## Slide 1: Mu2e Extinction Systems
Peter Kasper
NuFACT 2012

## Slide 2: Extinction
Ratio of “out-of-time” to “in-time” beam

## Slide 3: Overview: Proton Delivery
Booster
Main Injector/Recycler
Delivery Ring (formerly pBar Debuncher)
Mu2e
One Booster batch (4x1012 protons) is injected into the Recycler.
It is divided into 4 bunches.
These are extracted one at a time to the Delivery Ring
  Period = 1.7 msec
As a bunch circulates, it is resonantly extracted to produce the desired beam structure.

## Slide 4: Extinction Systems
In ring
  Beam delivery technique automatically gives good extinction < 10-5 going into the Delivery Ring
  May degrade to 10-4 during the spill
In beam line
  System of dipoles and collimators
  Additional factor of 10-7 should be possible
Monitoring
  Need to show that 10-10 has been achieved

## Slide 5: Delivery Ring
Start with < 10-5 level of extinction going into the Delivery Ring, so the issue is how will it grow during the spill.
Effects considered
  RF noise
  Intrabeam scattering
  Beam loading
  Beam-gas interaction
  Scattering off of extraction septum Dominant

## Slide 6: Septum Simulation
Study how the septum affects beam in the delivery ring

## Slide 7: Septum Simulation
Before septum
After septum
Out of Mu2e bucket will not recirculate
In Mu2e bucket and can migrate out-of-time
In Mu2e bucket and will remain in-time
Preliminary estimate: Extinction of < 10-4

## Slide 8: Extinction Beam Line
Delivery Ring
Extinction Beam Line
Mu2e Experiment

## Slide 9: Beam Line Modules
Upstream of extinction dipole
  Collimation to define beam line admittance to 50 p-mm-mr
AC dipole region
  Bend plane: b=250m
  Non-bend plane: waist
Extinction collimation
  Minimize transmission of scraping particles
Post-extinction
  High dispersion region for momentum collimation.

## Slide 10: Extinction Beam Line Optics
Momentum collimation
AC Dipole section
Collimation section
Momentum collimation and targeting optics

## Slide 11: Generic Extinction Analysis
Beam fully extinguished when deflection equals twice full admittance (A) amplitude
At collimator:
Angle to extinguish beam
Assume beam occupies entire admittance
Assume pulsed kicker that deflects out-of-time beam into a collimation system
Assume that the beam line admittance is equal to the collimation channel’s admittance
At kicker:

## Slide 12: Magnet Considerations
Complexity scales with stored energy
Bend strength to extinguish:
Stored Energy:
Large bx, long weak magnets
- Assume bx=250m, L=6m
- Factor of 4 better than bx=50m, L=2m

## Slide 13: AC Dipole Wave Form
Of the options considered:
½ harmonic – (2/17) * 17/2 harmonic seems most promising
Bunch length
Transmission window

## Slide 14: Proton flux vs time of flight
Time (ns)
Extinction Region
Collimator Material:
Extinction < 5x10-8 over range of interest for optimized collimators
This is multiplied by the Delivery Ring factor to produce a total extinction of < 5x10-12

## Slide 15: Monitor Requirements
Demonstrate 10-10 extinction
  Assume ≈ 3 x 107 protons/bunch
  Not possible measure 10-10 with a single bunch
     Integrate over many bunches
  Integration time should be < ≈ 1 hour
Only protons hitting the target can cause backgrounds
  Monitoring beam itself will lead to a potentially large over estimate of the background to the experiment
   Monitor target interaction products

## Slide 16: Filter + Detector Strategy
Filter
  Selects a sample of suitable secondaries and delivers them to the detector
  Sets the per proton detector signal rate
  Shields the detector from unwanted interaction products
Detector
  Measure “in-time” and “out-of-time” signal rates with equal or known relative efficiency
  Must have LOW “out-of-time” backgrounds compared to signal rate

## Slide 17: Two Schemes Under Consideration
Pixel Tracker
  Located above and behind the proton absorber
  Samples 3 to 4 GeV/c positive charged secondaries
  Pixel detectors reconstruct and count straight tracks with a well defined direction in 25ns time bins
Mini Spectrometer
  Located beside the proton absorber
  Samples ~ 1 GeV/c positive charged secondaries
  Magnetic spectrometer with 4 scintillator stations measures dE/dx, time of flight, and momentum of identified particle tracks

## Slide 18: Filter for Pixel Monitor
Production solenoid
Target
(too small to see)
Primary beam absorber
Entry and exit collimators
Filter magnet
Monitor
(too small to see)
20 m
Proton Beam

## Slide 19: Pixel Detector
3 x 2 stations of Atlas style pixel detectors.
Each station is comprised of 4 2 x 2 cm FE-14 sensor chips with 26,880
250 x 50 μm pixels per chip
Exit collimator opening

## Slide 20: Pixel Detector Features
Filter
  Filter magnet is an existing permanent dipole
    No cost and no maintenance
  Locates detector outside target hall
    Easy access for detector maintenance
    Lots of room for shielding
    Low radiation levels for detector + electronics
Detector
  Mature technology
    Can piggy-back on ATLAS purchases
  Simple reconstruction
    Possible to reconstruct every signal track from every bunch in real time?

## Slide 21: Mini Spectrometer Option
Production solenoid
Entry collimator
Spectrometer
Primary beam absorber
Iron shielding
Concrete shielding

## Slide 22: Mini Spectrometer Option
Iron lined with zirconium hydrate poly shielding
Brass collimators
8 scintillator strips per detector station read out by MPPC’s with 0.05 ns time resolution
Entry collimator
Filter magnet
Spectrometer magnet
Front detector stations
Rear detector stations

## Slide 23: Mini Spectrometer Features
Located inside target hall
  Reduces civil construction costs
Filter and spectrometer magnets obtained by cutting up an existing permanent dipole
Detector provides more measurables
  dE/dx + time of flight distinguishes π‘s and p’s
  Momentum measurement rejects low momentum background

## Slide 24: Choice
Based on how well each design meets a comprehensive list of requirements
Studies well advanced but have yet to be completed and documented

## Slide 25: Requirements: Signal Rate
Determined from beam intensity
  3 x 107 protons/bunch
  Bunch rate: 0.6 MHz @ 33% duty factor
   2 x 1016 in-time p.o.t./hr
  10-10 extinction  2 x 106 out-of-time p.o.t./hr
To set a 90% C.L.
  Need 2.3 expected out-of-time signal/hr
   1.2 x 10-6 signal events per p.o.t.
Pixels: 1.6 x 10-6 (limited by detector area)
Spectrometer: 1.0 x 10-6 (pile-up effects)

## Slide 26: Requirements: Background
Out-of-time background << a few events/hr
Background sources
  Cosmic rays
    Pixels: 0.03 evts/hr Spectrometer: negligible
  Late hits from in-time interactions
    Flux is 1,000 times higher for Spectrometer but it can more easily reject them
    Pixels can reject low momentum with a track quality and angle cuts
  Induced radioactivity
    Initial calculations suggest that it is negligible
  Electronic noise
    Pixels: negligible
    Spectrometer: radiation damage may be an issue

## Slide 27: Requirements: Reliability
Sensitivity to protons missing the target
  Out-of-time beam is flat over defining aperture
    Possibly only about 1% will hit the target
    Rest don’t make experiment backgrounds
  Both options insensitive if beam does not scrape on the Production Solenoid’s heat and radiation shield
In-time measurement linearity w.r.t. p.o.t./bunch must be well understood
  Noise rates, Pile-up, Reconstruction errors and efficiency
  Pixels expected to be linear
  Spectrometer preliminary reconstruction has ~15% inefficiency and finds ~15% fake tracks

## Slide 28: Requirements: Practicality
Sensitivity to design parameters
  Alignment tolerances
  Production solenoid field strength
  Pixel filter more vulnerable since collimators are embedded in bulk concrete but designed to accommodate placement errors of ~3 inches
Diagnostics
  Real time (low sensitivity) measurement
  Background monitoring
  Averaged bunch structure measurements
  Sanity checks
  Spectrometer provides more information and has better time resolution but will have to pre-scale in-time bunches
Feasible : cost, construction, operating and maintenance
  Pixels: Detector is cheaper, simpler, and easier to maintain
  Spectrometer: Cheaper civil construction

## Slide 29: Summary
Looks feasible
Need better understanding of out-of-time beam distribution at the production solenoid
Will choose between monitor options in the couple of months