## Slide 1: Horn studies for the CERN to Fréjus neutrino Super Beam
Nikolas Vassilopoulos (on behalf of EUROnu WP2), IPHC/CNRS

## Slide 2: Target station, service galleries
Design includes:
Proton Driver line
Experimental Hall: 4 MW Target Station, Decay Tunnel, Beam Dump
Maintenance Room
Power supply, Cooling system, Air-Ventilation system
Waste Area

## Slide 3: Horn evolution
evolution of the horn shape after many studies:
triangle shape (van der Meer) with target inside the horn : in general best configuration for low energy beam
triangle with target integrated to the inner conductor : very good physics results but high energy deposition and stresses on the conductors
forward-closed shape with target integrated to the inner conductor : best physics results, best rejection of wrong sign mesons but high energy deposition and stresses
forward-closed shape with no-integrated target:
best compromise between physics and reliability
4-horn/target system to accommodate the MW power scale
details in WP2 notes @ http://www.euronu.org/

## Slide 4: Horn shape and SuperBeam geometrical Optimization I
studies by A. Longhin, C. Bobeth
parameterise the horn and the other beam elements as decay tunnel dimensions, etc...
parameters allowed to vary independently
minimize the δcp-averaged 99%CL sensitivity limit on sin22θ13

## Slide 5: Horn Shape and SuperBeam geometrical Optimization II
fix & restrict parameters then re-iterate for best horn parameters & SuperBeam geometry

## Slide 6: Horn Stress Studies
horn structure
  Al 6061 T6 alloy good trade off between mechanical strength, resistance to corrosion, electrical conductivity and cost
  horn thickness as small as possible: best physics, limit energy deposition from secondary particles but thick enough to sustain dynamic stress
horn stress and deformation
  static mechanical model, thermal dilatation
  magnetic pressure pulse, dynamic displacement
  COMSOL, ANSYS software
cooling
  water jets

## Slide 7: Packed-bed target
He Temperature
He Velocity
transversal cooling
stresses levels manageable

## Slide 8: Energy Deposition from secondary particles @1.3 MW
Ptg = 105kW
Ph = 62kW
9.5kW
2.4kW
1.7kW
1.3kW
36kW, t=30mm
2.5kW
target Ti=65%dTi , RTi=1.5cm
8.6kW, t=35mm
radial profile of power density kW/cm3
max

## Slide 9: Stress Analysis
G. Gaudiot, B. Lepers,
F. Osswald, V. Zeter/IPHC,
P. Cupial , M. Kozien, L. Lacny,
B. Skoczen et al. /Cracow Univ. of Tech.
  Smax = 63 MPa
  Smax = 6 MPa
stress minimized when horn has uniform temperature
cooling TAl-max =60 0C,
cooling TAl-uniform =60 0C
umax = 1.12 mm
umax = 2.4 mm
Thermo-mechanical stresses:
  secondary particles energy deposition and joule losses
  T=60ms, (worst scenario, 1horn failed) ,τ0I=100μs, electrical model: I0 = 350kA, f=5kHz, Irms=10.1kA

## Slide 10
displacements and stress plots just
before and on the peak
  stress on the corner and convex region
  stress on the upstream inner due to pulse
  uniform temperature minimizes stress
peak magnetic field each T=80ms (4-horns operation)
Stress due to thermal dilatation and magnetic pressure
  Smax = 30 MPa
modal analysis, eigenfrequencies
f = {63.3, 63.7, 88.3, 138.1, 138.2, 144.2} Hz
2) cooling TAl-uniform = 60 0C
umax = 2.4 mm
  Smax = 60 MPa
1) cooling TAl-max = 60 0C,
umax = 1.12 mm
inner
outer
t= 79.6 ms
t= 80 ms
t= 80 ms

## Slide 11: Horn cooling
cooling system
planar and/or elliptical water jets
30 jets/horn, 5 systems of 6-jets longitudinally distributed every 600
flow rate between 60-120l/min, h cooling coefficient 1-7 kW/(m2K)
longitudinal repartition of the jets follows the energy density deposition
{hcorner , hhorn, hinner , hconvex}= {3.8, 1, 6.5, 0.1} kW/(m2K) for TAl-max = 60 0C
power distribution on Al conductor
secondary particles (66%) + joule (34 %)

## Slide 12: horn lifetime
6 – 60 MPa expected
highly conservative
1.25 108 pulses = 200 days = 1 year

## Slide 13: Power Supply
P. Poussot, J. Wurtz/IPHC

## Slide 15: Four-horn support
displacement (m)
foreseen design

## Slide 16: conclusions
Al 6061 T6 alloy for radiation, reliability and cost
convex shape defined for optimum physics
low stress on inner conductor when uniform cooling is applied < 30 MPa
horn lifetime > 108 cycles (1 year)
highly conservative
support designed
power supply & cooling R&D needed

## Slide 17: 4-horn system for power accommodation