## Slide 1: Development of μRGroove detectors
UTSC-MPGD Group
If there are questions, please contact :
Yi Zhou, zhouyi@cern.ch
20-02-2026

## Slide 2: Outline
Introduction
Large area μRGroove
  50cm×50cm detector
  100cm×50cm detector
Beam test of Cylindrical μRGroove @ 1Tesla
Summary & Outlook

## Slide 3
    Decoupled X&Y readout strips, avoided induced charge sharing effect, increased signal amplitude
    Easier to process due to its open geometry
    Easy clean, important for the end user.
    Lower material budget
micro-Resistive Groove
μRGroove
Drift HV
DLC HV
V readout
U readout
Drift
μRGroove
Small prototype
Cylindrical μRGroove
Large area
Suitable for cylindrical geometry and large-area tracking application.

## Slide 4
The Large-area μRGroove
A4 paper
2 readout strips are replaced by a PEP GND line in each 128 readout strips;
Active area:
50 cm × 50 cm
100 cm × 50 cm
PEP fast grounding line, divided into 10/20 sub-regions of 5 × 10 cm each
Dead Area (TOP): 2/128 = 1.5625%
Simple structure, easy installation

## Slide 5
The signal gain is relatively low (<3000) due to insufficient matching capacitance of ORTEC.
The Gas gain is similar with that in small μRGroove
Pretty uniformity, approximately 7%.
50cm × 50cm: Signal gain and uniformity
Ar/iso-C4H10 (95/5), DLC: 415V, Drift -500V

## Slide 6
50cm × 50cm: Rate capability
Read out the current from the top electrode and calculate the “current gain” to obtain the G/G₀ curve.
Scan different irradiation spot diameters.
For an 8 mm irradiation diameter with 8.1 keV X-rays, the counting rate capability (at 90%) is approximately 300 kHz/cm².
By converting the energy deposition to that of a MIP, the corresponding counting rate capability is about 2.4 MHz/cm².
Irradiated area: (6,5)

## Slide 7
50cm × 50cm: spatial reso & efficency
CERN SPS-H4
150GeV/c muon
APV25 + SRS + mmDAQ
2024.04
Work gas: Ar/iC4H10(90/10)
The combined efficiency is >96%
Spatial resolution is ~93μm for X readout and ~81μm for Y readout

## Slide 8
50cm × 50cm: New beam test
CERN SPS-H4
150GeV/c muon
APV25 + SRS + mmDAQ
Rotatable around the X-axis
Work gas: Ar:CF4:CO2/45:40:15. Better gas parameters but smaller gain
The efficiency is >95%
Spatial resolution is ~56μm for X readout and ~62μm for Y readout
2025.11
Better resolution is related to gas parameters such as smaller gas diffusion.
More μTPC-related analyses are underway.

## Slide 9
100cm × 50cm: spatial reso & efficency
CERN SPS-H4
150GeV/c muon
APV25 + SRS + mmDAQ
Work gas: Ar:CF4:CO2/45:40:15.
The efficiency is >96%
Spatial resolution is ~90μm for X readout and ~80μm for Y readout
More detailed tests about uniformity and rate capability are ongoing
2025.07

## Slide 10
Spatial Resolution： 52μm to 78μm
(small bending on sector4)
Detection Efficiency：95%
Muon
Spatial Resolution： 50μm to 53μm
Detection Efficiency： 96%
Pion (Ultra High Rate: ~1.73MHz/cm2)
50μm
53μm
100cm × 50cm: New beam test
2025.11
Work gas: Ar:CF4:CO2/45:40:15
APV25 + SRS + mmDAQ
Muon
Muon
Pion
Pion
Pion

## Slide 11: The low-mass Cylindrical μRGroove
1st C-μRGroove prototype:
Size of active area: D=131.0mm, L=100.0mm;
Material budget of active area: ~0.23% X0
Out cylinder is drift and inner is μRGroove-PCB
Detachable mechanical design
Prototype
2021.09 - 2024.05: design and production
2024.07：Beam test
2024.11: 1st beam test under magnetic field
One of the options for STCF inner tracker

## Slide 12
Beam test in magnet
Goliath magnet at SPS-H4, B = 1T
Trackers: μRGroove, Ar/iC4H10(98/2), 3kV/cm drift field, Lorentz angle: ~6°
c-μRGroove: Ar/CF4/CO2(45/40/15), 0.5kV/cm drift field, Lorentz angle: ~22°
APV25 + SRS + mmDAQ
2025. 07
B = 1T
Slimulatoin@B=1T

## Slide 13
Spatial resolution @B = 0T
  B = 0T
Tracker:
the sigma of Tracker2 is ~148μm, So that its resolution is ~115μm
Track error is ~66μm
c-μRGroove：
Sigma: μTPC (23°) ~120μm, CC (0°) ~92μm
Resolution without track error: μTPC (23°) ~100μm, CC (0°) 64μm
Alignment of trackers
Reconstruction Methods for c-μRGroove:
Charge centroid (CC) for tracks at small angles
Micro-Time projection chamber (μTPC) for tracks at big angles

## Slide 14
Spatial resolution @B = 1T
  B = 1T
Tracker:
the sigma of Tracker2 is ~217μm, So that its resolution is ~169μm
Track error is ~98μm
c-μRGroove：
Lorentz angle ~23°
Sigma: μTPC (0°) ~160μm, CC (Theta – Lorentz angle = 0°) ~125μm
Resolution without track error: μTPC ~127μm, CC ~78μm
Alignment of trackers

## Slide 15: Summary
50cm×50cm planar μRGroove
  Pretty gain uniformity: better than 7%.
  Rate capability: 300kHz/cm2@8mm diameter@8.1keV X-ray.
  New beam test: Spatial resolution is ~60μm.
100cm×50cm planar μRGroove
  Efficiency is > 96%.
  Spatial resolution is better than 60μm(except the bending area).
Cylindrical μRGroove
  Lorentz angle is ~ 23° @1T @Ar/CF4/CO2(45/40/15), 0.5kV/cm drift field.
  Spatial resolution @0T: μTPC (23°) ~100μm, CC (0°) ~64μm (track error deducted).
  Spatial resolution @1T: μTPC (0°) ~127μm, CC (Theta – Lorentz angle = 0°) ~78μm (track error deducted).

## Slide 16: Outlook
Detailed test of 100cm×50cm μRGroove
Develop μTPC algorithm based on several beam tests
Analyze new beam data of large area μRGrooves
Optimize the detector structure, such as groove structure and readout, etc.

## Slide 17: Backup

## Slide 18
Test setups | Signal gain
Full size connected； Bottom is readout | 1749
Central 10cm×10cm area connected Bottom is readout | 1872
Central 10cm×10cm area connected Top is readout | 1905
By reducing the connected area, the signal gain only increased by 7%.
Under the same setups, the top and bottom maintain similar amplitudes.
Capacitance measurement:
  small μRGroove, 5 × 5 cm connected: 1.53 nF
  Large μRGroove, 5 × 5 cm connected : 7.66 nF
  Large μRGroove, 45 × 50 cm connected : 9.02 nF
Influence of capacitance
Irradiated area: (6,5)，DLC: 415 V; Drift: -500 V
.
Small μRGroove
5×5cm connected
45×50cm connected
It is necessary to determine the effect of capacitance by comparing with a small-area μRGroove.

## Slide 19
Test setups | “Current gain” | Signal gain | Gsig/Gcur
Large μRGroove 5×5cm (6,5) connected； Top readout | 7573 | 2139 | 3.54
Small μRGroove 5×5cm connected Top readout | 8914 | 5079 | 1.76
Further check between large and small detectors
5mm
The difference in current gain between the large and small detectors is relatively minor, where the difference in signal gain is substantial.
This suggests that the electron multiplication is likely similar, but the reduced signal result from insufficient matching capacitance in the ORTEC preamplifier.
“Current gain” refers to the “gain” based on the current read out from the top electrode.
Although it’s not the total current on the DLC, it is still suitable for comparative analysis.

## Slide 20
C-μRGroove: Low-Mass Electrode
LM Drift & GND are both made
Zhou Lin, RD51 Collaboration Meeting, 21/06/2023
DLC: Diamond Like Carbon

## Slide 21
C-μRGroove: Manufacture
Drift electrode
Rohacell foam
Kapton/GND
Kapton/GND
Rohacell foam
V strip film
Det.&U-strip film
Total material budget: ~0.23%X0

## Slide 22
C-μRGroove: Electrodes design
μRGroove/U Strips
V Strips
Layer stack of μRGroove
Layer stack of V readout
U/V 2D strip-readout, pitch of U strips is 0.4mm, Pitch of V strips is 0.8mm, angel between UV is 15

## Slide 24
Gain and energy spectrum measurement
Setup：
  Gas: Ar:iC4H10/95:5
  Source: 55Fe
  Readout from X strips (cathode)
  V strips are grounded
  Ortec142AH/671 + MCA
  Gain measured by signal amplitude spectrum
Energy resolution: 26%;
Effective gain: 4000~10000;
Similar signal amplitude on X&V readout strips;
Good stability if the humidity can keep low enough;
~1h@gain : 5100
3 sectors not work (8 sectors in total);
Bad gain uniformity, caused by the gas(flow);