## Slide 1: CDet Analysis Status
Benjamin Spaude

## Slide 2: Kin3 Cross Target – Timing Checks
Run 3575 cross target @ 1uA, Ecal singles
~4 hits per event
Raw meaning no cuts
Clear Timing Peak
“Flat” background
Leading Edge Time (ns)
Time-over-Threshold (ns)
Trailing Edge Time (ns)

## Slide 3: Kin3 Cross Target – CDet & ECal pos check
Note, peaks on ecal x align with points on XECalCDet
Also, discrepancy on entries – there is a reason!
+/-1m xdiff from Ecal projected to CDet
CDet x1
CDet x2
ECal x
ECal x

## Slide 4: Kin3 Cross Target – Timing Checks w/ Cut
+/-10cm cut on ECal*-Cdet xdiff
“Flat” background goes away
*Projected back to cdet
Leading Edge Time (ns)
Time-over-Threshold (ns)
Trailing Edge Time (ns)

## Slide 5: Kin3 LH2 Timing Checks
LH2 @ 22uA, ~600 hits per event
Dominated by background
Background shape is same as cross target
Leading Edge Time (ns)
Time-over-Threshold (ns)
Trailing Edge Time (ns)

## Slide 6: CDet Occupancy from LH2 – Layer 1
Ave Occupancy calculation ignores missing pixels & “bad” PMTs
Computed for each side of each module

## Slide 7: CDet Occupancy from LH2 – Layer 2
Ave Occupancy calculation ignores missing pixels & “bad” PMTs
Computed for each side of each module

## Slide 8: Kin3 LH2 Timing Checks w/ ECal x cut
+/- 10cm ecal/cdet xdiff cut
Still background dominated
Need to optimize timing cut
Cross target data should help
Trailing Edge Time (ns)
Leading Edge Time (ns)
Time-over-Threshold (ns)

## Slide 9: CDet Layer 1 vs 2 Comparisons

## Slide 10: Hit Pairing Strategy
Split hits into layers by using pixel ID
Each hit in layer 1, check all layer 2 hits and compare dt and dx
Store all potential pairs passing accepted dt and dx, sort by best
Only works for events with at least 1 hit in both layers
cm
1ns

## Slide 11: CDet-ECal Comparisons from Cross Target

## Slide 12: Conclusion
LH2 suffers from high background rates in CDet
No clear peak with LH2
Significant occupancy variation tube-to-tube
Cross target data has a clean peak and good x correlation
Should be useful in calibrating to extract LH2 peak

## Slide 13: Backup Slides

## Slide 14: CDet-ECal Comparisons from LH2

## Slide 15: CDet Layer Comparison on LH2