## Slide 1
Status of Polarimeters and Polarized Targets: what are the plans for development of polarized targets to meet the needs of the Day 1 and future experimental physics program?

## Slide 2
Answer to the question
”Discuss in accelerator breakout: Status of polarimeters and polarized targets; what are the plans for development of polarized targets to meet the needs of the Day 1 and future experimental physics program?”
Day 1: we don’t have any experiments requiring polarized target
  Hall A high-luminosity polarized 3He target: FY19 (maybe FY18)
  Hall B Longitudinally NH3/ND3 polarized target: FY19
  Hall C polarized target: polarized 3He target FY19
  Hall D polarized target: not in the program so far
Earliest Experimental program that needs polarized targets:
Status of polarimeters and polarized targets – next slides

## Slide 3
Hall C – Polarimetry during Qweak
Compton polarimetry uncertainty: 0.59%, Moller polarimeter uncertainty: 0.85%

## Slide 4
Hall C – Polarimetry @ 12 GeV
Compton polarimetry uncertainty as determined during Qweak experiment: 0.59%
Limitation due to data acquisition and background  we believe we can reach well below 0.5% and aim for 0.4% (see next slide)
Moller uncertainty dominated by current extrapolation (Moller measurements only possible at low beam currents) - also some Levchuk effect, beam position, target polarization.
Current extrapolation remains main issue: one test during Qweak was a direct comparison of Compton and Moller at low currents. This was limited by Compton statistics to about 1%. With more time investment we can improve.
Present status: bad Moller (quadrupole) magnet coil has been replaced and two Moller magnets refurbished.
Expectation is that with Halls A and C having similar polarimetry, and by comparing systems with each other, we can reach the required polarimetry needs of MOLLER and SoLID with the Compton

## Slide 5: Precision Polarimetry in Hall A - MOLLER, SOLID require precision ≤ 0.5%
Qweak achieved design goal of ΔP/P ≤ 1%
Larger analyzing power at higher energy, DP/P < 0.5% within reach at 11 GeV
Strategy: use 2 independent polarimeters
Compton polarimetry, new developments and recent running:
- Continuous, non-invasive.
- New high-gain optical cavity for improved resolution and analyzing power
- Diamond microstrip detectors (Qweak)
- Integrating photon analysis (PREX)
Existing < 1% Hall C Møller polarimeter:
- Low beam currents, invasive.
- Known analyzing power provided by Fe foil in a 3.5 T field
- Create duplicate capability in Hall A (Temple, Kharkhov), new magnet at JLab

## Slide 6: Hall A/C: Polarized 3He Target
UVA convection gas cell successfully tested
 | Stage I | Stage II
Current | 30 mA on 40 cm | 60 mA on 60 cm
Luminosity | L ~ 2.2x1036 cm-2s-1 | L ~ 6.6x1036 cm-2s-1
Polarization | ~60% | ~60%
Cell | Glass cell | Glass cell metal window
 | convection gas flow pumping chamber 3.5” | convection gas flow pumping chamber 4.4”
Polarimetry (~ 3%) | Pulse NMR/AFP NMR | Pulse NMR/AFP NMR
Hall A/C compatibility | Significant engineering needed to fit into Hall C | Large gradient from SBS fringe field  Magnet shield box
Experiments | A1n Hall A d2n Hall C | A1n Hall C GEn Hall A
JLab CE projects includes:
Stage I) Lasers, optical fibers from laser house to Hall C, NMR for polarization measurements
Stage II) mechanical work to modify for a higher-FOM target
“High Impact” Exp.”
UVA/W&M : developing target cell, filling target cell, contribution to precision polarimetry

## Slide 7: Hall B – Long. Polarized Target
7
Expected polarization:
≥ 90% (p); ≥ 40% (d)
Electron beam current operation up to 30 nA.
DNP polarized NH3 /ND3 using the 5T magnetic field of the CLAS12 solenoid as a holding field
The base target components are developed with an NSF/MRI grant by ODU/CNU/UVA
It will serve 5 approved experiments (240 PAC days)
Target design highly modular  either single or double cells (with opposite pol.) can be utilized with little or no modification to the rest of the system
Status
Procurement of microwave, NMR, and pumping systems is complete (NSF/MRI)
Construction of outer vacuum chamber is complete
Design of refrigerator is 75% complete
Estimated completion date Spring 2017
JLab CE project: infrastructure to integrate the target into CLAS12 + design and engineering of the cryogenic system

## Slide 8: Hall B – HDice Target for transverse config.
8
It will serve three C1 approved “High Impact” Experiments
Solid HD material placed into a frozen spin state
- requires only modest (~1 T)short (~15 cm) field
to hold spin in-beam  minimizes sheet of flame
Operating performance with electrons beams requires further beam tests plan to use upgrade of the injector test facility: Ee =5 – 10 MeV (~10 MeV beam will test the HD performance at 11 GeV!)
JLab CE project: modifications required to operate the target in transverse polarization mode in the CLAS12 Solenoid, whose strong long. magnetic field must be locally repelled.
Status of ongoing work:
Transport design for 10 MeV rastered ITF beam
R&D for a new “passive” SC diamagnetic shield
to hold spin transverse to beam within solenoid
Improving NMR system for target polarization
measurement
• Design and build new HD gas purification factory