## Slide 1: CLAS12 Run Groups C and G Status and Outlook Tensor SIDIS Workshop and b1/Azz Collaboration Meeting June 3-5, 2026
Sebastian Kuhn, Old Dominion University
for the Run Groups and the CLAS collaboration
Beamline
Raster Magnets
1 K Refrigerator
Electronics
Vibration isolated pump cart
Inserted in CLAS12
Target Sample Insertion Port

## Slide 2: Overview
Science goals of RG-C and G
  Inclusive DIS -> g1, A1, b1?
  Semi-inclusive DIS
    TMDs, Tensor observables?
    Fracture Functions
    Two-hadron production
  Exclusive Channels – DVMP, DVCS
  Nuclear Binding modification of SSFs
Status and Expected Data
Status of Polarized Target
Outlook

## Slide 3: RG C Goals:
Measure inclusive spin structure functions (A1, g1) of the proton (NH3) and deuteron (ND3) for PDF fits and sum rules; Combine with flavor tagging (π±, K±) to extract Dq in the valence and moderate-x sea regions, constrain DG
Measure spin- and transverse momentum-dependent (TMD) PDFs (SIDIS)
Study novel fracture functions and two-hadron production
Measure target single and beam/target double spin asymmetries in proton and neutron DVCS, pion and J/y production, and TCS (e+ e-)
RG G Goals:
Measure inclusive spin double-spin asymmetries and spin-dependent cross section differences for polarized electron scattering on polarized 7Li (7LiD)
Compare with p (NH3) to extract POLARIZED EMC EFFECT on bound p in 7Li

## Slide 4: Overview of RG-C
8 experiments with a total of “916 PAC days worth” of proposed new data
Due to simultaneous data collection for all channels with CLAS12, originally approved request was 185 PAC days
  Including 120 PAC days on NH3 originally requested for pDVCS (E12-06-119(b))
  Plus 60 more PAC days on ND3 originally requested for nDVCS (E12-06-109A)
120 PAC days reapproved by Jeopardy PAC48 in 2020, scheduled for 244 calendar days in June 2022 – March 2023
Due to extensive accelerator downtimes and major equipment failure (solenoid magnet power supply) only 80 PAC days of data collected. Jeopardy PAC in 2024 re-approved remaining 40 days, to be run consecutively with RG-G
Additional channels under analysis: Time-like Compton Scattering, Diffractive Vector Meson Production (e.g., r) + 2 CAAs:
Measurements of J/ψ Polarization Observables (K. Gates)
Spin 1 Transverse Momentum Dependent Tensor Structure Functions in CLAS12 (J. Poudel) arXiv:2502.20044 [hep-ph]

## Slide 5: Overview of RG-G
Experiment 12-14-001 approved by Jefferson Lab PAC 42 for 55 days
Jeopardy PACs in 2020 and 2024 reaffirmed goal and increased rating to A-
By running together with RG-C, minimize overhead and share data (NH3, auxiliary targets)
Only difference: Need standard RG-C target cell with 7LiD irradiated material, modified NMR
First EMC puzzle: SFs of bound nucleons ≠ free nucleon SFs (suppressed at high x)
2nd EMC puzzle: Sum of spins carried by quarks ≠ nucleon spin (DS is only 30% of total)
EMC2: Is spin fraction carried by quarks reduced even further in nuclei (beyond “nucleons-only” state-of-the-art nuclear models)?
Ds Ratio  [N+-N-](7Li) / [N+-N-](p)
A|| Ratio  A||(7Li) / A||(p)

## Slide 6: DIS: Valence quark polarization at high x
Full Data set (combined with Hall C 3He data already in hand) will significantly constrain valence + sea quark and gluon PDF fits, higher twist effects and sum rules
C. Cocuzza, W. Melnitchouk, A. Metz, and N. Sato, Phys. Rev. D 106,
L031502 (2022).
6 of 20
Notes: indicate continuing high interest.

## Slide 7: Preliminary Data from CLAS12 RG-C - DIS
Proton
Deuteron
W > 2; Q2 > 1
RGC
Courtesy: Derek Holmberg (W&M)
SU(6)
VERY
PRELIMINARY!
Courtesy: Darren Upton (ODU)
Notes: Averaged over all bins in - No radiative corrections - All errors show are purely statistical; no systematics
Averaged over all bins in 𝑄^2 −"Red line is a parameterization of the previous world data" - No radiative corrections - All errors show are purely statistical; no systematics

## Slide 8
Extraction of spin-asymmetries in the production of exclusive mesons with a longitudinally polarized target
Timothy B. Hayward, Harut Avakian, Maggie Kerr
HERMES p+
• The low statistics measurement from HERMES
shows a large negative asymmetry in the exclusive
region.
• CLAS(12) BSA measurements had shown positive
asymmetry.
• Traditionally BSA ~ TSA.
Observation of negative AULsinf for low xB by HERMES is confirmed

## Slide 9
SIDIS Dihadron Production:
 | U | L | T
U | f1 |  | e
L |  | g1 | hL
T |  | gT | h1
Collinear PDFs
– Twist-2
– Twist-3
DIS2026

## Slide 10: TSA in Timelike DVCS
Summer22: approx 4mC accumulated charge
Full RGC dataset scaled to 13.06mC accumulated charge
Additional PAC days includes 20 additional days on NH3
Summer 2022 statistics too low for multidimentional binned analysis, but more statistics can allow for this for a better understanding of shape
Dilution factor = 34%
Fiducial cuts as defined in RGA
All final state particles in the forward detector
2500 events pass cuts
Statistical errors dominate systematic
Statistical errors too large to extract meaningful TSA at present

## Slide 12: Polarized Target
1 K Refrigerator
Electronics
Vibration isolated pump cart
Raster Magnet
Superconducting CLAS12 Magnet
Irradiated

## Slide 13: Target performance
PROTON (NH3)
DEUTERON (ND3)
Notes: D: Initial polarization for “fresh” target material often only 25%; later up to 35% routinely. (FoM: nearly 2x)

## Slide 14: Target Status and Prospect for 2027-8
Polarized target has performed well with a few exceptions:
  Initial polarization of some material was very low
  Some material was rather old and of unknown quality => Need new material, better irradiation facility, ability to test polarizability on location - SEE 
Target is in storage and can be reused with few to no modifications (remove mothballs and test all components). Present Plan: Summer/Fall 2027
Will work for both RG-C and RG-G (just replace NH3/ND3 cells with 7LiD)
LiD: Tsuneo Kageya (pol. Fusion project) + new staff scientist Hao Lu
See talk by Chris Keith earlier this afternoon
Will need ERR in 2027 to run in 2028
Irradiation: UITF?
Irradiate target materials with 1-10 µA electrons
Variable temperature cryostat and sample holder: Target Group
Helium transfer line
Variable temperature cryostat (3 – 300 K)
Target Development Lab
Measure polarization of irradiated target samples
Develop and test new NMR & microwave equipm.
Target Group
Cryogen-free 5 tesla superconducting magnet
Closed-cycle 1 K evaporation refrigerator
(under construction)
Start irradiation in Fall 2026?

## Slide 15
Notes: March 27 version of long-term run plan presented by Jlab Management.

## Slide 16: Summary And Outlook
RG-C combines several highly rated experiments that will make crucial contributions to the core 12 GeV program at Jefferson Lab. Main Observables: AUL, ALL
Tensor observables can be extracted by comparing ND3 runs with different absolute polarization |Pz|, averaging over both signs.
RG-G will measure spin structure functions of bound protons for the first time
The longitudinally polarized target is mostly ready (tremendous investment by Lab and collaborators, including NSF MRI), but waiting for completion of all parts of 7LiD production and irradiation. Some modifications to NMR planned.
More statistics are crucial for multi-dimensional binning, statistics-starved channels (DVCS, TCS, K-SIDIS), and all Deuteron asymmetries
Remaining runtime for Run Group C (40 additional PAC days) was approved by Jeopardy PAC in 2024.
Best guess at this time: ERR sometime in CY 2027, scheduling request late in 2027. Potential run (total of 95 PAC Days = 6 months) in 2028.
Note: To optimize extraction of tensor observables, it might be good to request an additional PAC week or 2 of zero-polarized ND3 running!
Notes: PLUS higher beam energy will benefit highest x! Also: a 30% reduction in error bar can turn a 3.5-sigma ”tension” into a 5-sigma discovery!

## Slide 17: Backup Slides

## Slide 20
  No luck yet finding these compounds with these specific isotopes
  6Li (>95%) and 7Li (>99%) metals are commercially available
  Lithium hydride is produced by heating lithium in a hydrogen atmosphere to 600-700 ℃ (anyone interested?)
For optimum polarization, LiH should be irradiated with electrons at 180-190 K to a fluence of a few 1017 e-/cm2
  Where to irradiate? (CEBAF injector? Offsite?)
  Requires a new, variable-temperature irradiation cryostat
Based on SLAC-E143 experience (6LiD)
Expected polarizations at 1K, 5T (NMR freq.)
  Deuteron: 30% (
  Lithium-6: 30%
  Lithium-7: 60% (212.9 MHz)
  Proton: 70% (educated guess) (212.9 MHz)
  Polarization is slower, but the radiation resistance is at least 5x better than ammonia.
  Can be annealed at 185 K for 20 minutes, albeit with diminishing returns.
Nuclear spins in lithium hydride conform to the
Equal Spin Temperature model
  Measure one polarization, calculate the other
Bueltmann: 1K, 5T
6 days @ 8 nA, ⌀2cm
S. Bueltmann, SLAC-PUB-7904 (1998)
NMR Freq. @ 5 T
Proton: 212.9 MHz
Lithium-7: 82.7 MHz
Deuteron: 32.7 MHz
Lithium-6: 31.3 MHz
What about the required Li-hydride/deuteride target material?
Requires 3 different NMR coils
D Polarization
Dose [1015 e-/cm2]
Notes: We will likely have coils integrated with cells so we can swap them. One Li7 and D, the other H (and Li6?). Can use 14NH3 instead of Li6H if necessary.

## Slide 21
DNP of Lithium Hydride
Under 1K/5T conditions, 7Li has been polarized to about 80% and 6Li to 30%.
Optimal polarization requires pre-irradiating the samples in a narrow temperature band around 185 K.
This can be performed at the UITF, using a custom-built, variable-temperature irradiation cryostat.
Photos and drawings: Scott Reeve, U. Bonn.

## Slide 22: PDF uncertainties WITHOUT INCLUSIVE RG-C data
E.R. Nocera, arXiv:1410.7290v2 [hep-ph] 23 Jan 2015
E.R. Nocera: Impact of Recent RHIC Data on Helicity-Dependent Parton Distribution Functions,
arXiv:1702.05077v1 [hep-ph] 16 Feb 2017
JAM’22

## Slide 23: Improvement in PDF uncertainties from INCLUSIVE RG-C data
Relative uncertainties on polarized PDFs with various data sets (Courtesy N. Sato)
Notes: Includes both statistics and estimated systematic uncertainties

## Slide 24
JAM 2017
J. J. Ethier, N. Sato, W. Melnitchouk Phys. Rev. Lett. 119, 132001 (2017), arXiv:1705.05889 [hep-ph]
Notes: Future plan: Include RHIC and Tevatron data (W, jets,…)

## Slide 25: PDFs from SEMI-inclusive RG-C data
Only K- production on D is uniquely sensitive to Ds (Du and Dd largely cancel)
Notes: Note: Existing data are of course pitiful; this is just to illustrate how HIGH statistics data on the d can have a very big impact.

## Slide 26
Longitudinally Polarized Target for CLAS12
Slow Controls + EPICS
NMR
Pumping System
1K Refrigerator
Microwaves
5 T Solenoid (FROST)
The target is > 90% complete and has been successfully tested at JLab on three occasions.
Additional cool-down tests are scheduled for 2020 and 2021. Full “dress rehearsal” September 2021 in the EEL. Ready for installation immediately after Summer Run 2021 (RG-M) ends.
13 of 20
Notes: mention MRI

## Slide 27
Longitudinally Polarized Target for CLAS12
Horizontal 1 K refrigerator: constructed and tested.
Meets or exceeds all design parameters.
  Stable & reproducible operation;
  Base temperature below 1 K;
  Cooling power of 0.6 W at 1.0 K, 1 W at 1.1 K
  Max. helium consumption < 5 liters/hr
14 of 20

## Slide 28
Longitudinally Polarized Target for CLAS12
Polarizations are measured using prototypes of a new NMR Q-meter developed by the JLab Target and Fast Electronics Groups
  Meets or exceeds performance of the 40-yr old Liverpool Q-meter
  Has remote-control capabilities not present on Liverpool version
  Modular for easy repair, modification, and upgrading
  R&D will continue on new version with faster, higher-resolution ADCs
  All-digital version is under design
We have dynamically polarized ⌀2 x 4 cm2 samples of 5-min. epoxy doped with TEMPO radical
(chosen for convenience) ➔ 30%-40%
Switch to butanol and NH3 for upcoming tests
15 of 20

## Slide 29
Longitudinally Polarized Target for CLAS12
The CLAS12 5 T solenoid will be used to polarize the target
  Field uniformity is ok for protons – should be improved to optimize the deuteron polarization
  Superconducting shim coils will be installed inside the the 1 K cryostat
  Demonstrated the efficacy of this approach
Pump Cart
(on rails)
Electronics Cart
Support & adjustment frame
(on rails)
Target insertion cart for CLAS12: ~75% complete.
  Fast, easy insertion and removal of target cryostat
  Six-axis adjustment
16 of 20

## Slide 30: Møller Shield

## Slide 31: Polarized target
Standard CLAS12 longitudinally polarized target
  two-cell design to minimize systematic errors for SSAs
  here: use one cell for 7LiD, the other for reference (either 6LiH or 14NH3).
  Measure ratios of cross section differences (s↑↓ - s↑↑) and of asymmetries (A||) to minimize systematic errors
  half-way through experiment, exchange target materials to further reduce systematic effects (different acceptance, NMR response, …)
  Measure polarization via NMR and via (quasi-)elastic scattering 7Li(e,e’p), H(e,e’p)
  Use software cut on vertex to minimize and determine DF (will be large for 7Li!)
Goertz: 0.3 K, 2.5 T
Notes: NOTES: Experience at SLAC (E143, E155x) and JLab show that one can measure Pt for protons to about 2.5% with embedded coils and careful attention to beam depolarization. Furthermore, we have a totally independent method using quasi-elastic (2-3%) and elastic (1% precision) scattering. An upper limit of 3% for either method for the ratio seems appropriate. (Note that a lot of the uncertainties cancel, e.g. target temperature and B-field for TE measurements, as well as some cancellation from exchanging the target material). Including nuclear uncertainties and other lingering doubts, after cross checking the 2 methods we should have at most 3% rel. syst. error on the ratio g1Li/g1p or A||Li/A||p .