## Slide 1: RF Separation Status
Mark Wissmann
July, 2015

## Slide 2: Outline
History
Update Of Three Tasks:
  • Resonant Control
  • Cavity Tuning
  • IOT Power Output Adjustment/Test

## Slide 3: Spring History
During the spring run we extracted ~9.6 GeV beam
and problems and concerns were uncovered.
Large Frequency Shift During Operations
- Water Control System Limited
- Cavity Tuning Not Optimized
The IOT Amplifier Near Its Set Power Limit.
A bit Less Separation Than Expected

## Slide 4: Water Controls Update
Preliminary test was performed for two weeks after suspending machine operations.
FINDINGS: (Tomasz Plawski’s ELOG 3343104)
- Operated 2.2 kW into a cavity.
- The cavity was controlled using an upgraded
heater chassis.
- Startup and operation to 2.1 power achieved
- Build of upgraded water system scheduled for completion by mid-August

## Slide 5: TEST Water Enclosure

## Slide 6: Cavity Setup Update
After water controls testing, all four cavities were removed for bench tuning and setup.
  Tasks:
  - Establish field flatness in each cell
  - Install a second pickup loop
  - Fiducialize each cavity
  - Reinstall Cavities

## Slide 7: Simulation Results
E-Field at Crest

## Slide 8: Simulation Results
H-Field at Crest

## Slide 9: Typical Spring Run Cavity Setup

## Slide 10: Cavity Setup With Fields Flat

## Slide 11: RRFAE00A’s Final Bench Setup

## Slide 12: Bead Pull In RF Structures Lab
RRFAE00A Setup For Beadpull
Notes: On the highlights slide you mentioned that this was done with ARRA funds. They may miss that or they may not remember at this point. Please add the “part of ARRA project” into the first bullet.
In first bullet you mention “high power testing”. In the 2nd bullet you say “rf measurements”. My brain assumed you were talking about high-power “rf measurements”. I suggest you add “low-power” in the 2nd bullet.

## Slide 13: Cavity Setup Update
  - Establish field flatness in each cell
  RRFAE00A set and in high power test
  RRFAE00D set and soon on Alignment Stand
  RRFAE00B & RRFAE00C awaiting Pickup Loops
  - Install a second pickup loop
  RRFAE00A, RRFAE00B and RRFAE00C need pickups. They arrived from MDC yesterday.
  - Fiducialize each cavity
  RRFAE00A, RRFAE00B and RRFAE00C complete.
  - Reinstall Cavities
  Plan to be ready by first week in August

## Slide 14: IOT Power Update
  - Goal is 14 kW Steady Power
  To do this the HVPS needs to provide ~24 kV
  The transformer taps where changed and the power supply is at 22 kV.
  At 22 kV 14 kW has been achieved but it drifts.
  This drift is believed to be from IOT Cavity heating
  Drift can also be addressed by IOT tuning
  Possible HVPS transformer tap change

## Slide 15: IOT Power RUN

## Slide 16: Summary
Resonance Control Test complete and construction of chassis on schedule for Mid August Delivery
Cavity tuning optimization on schedule but benefit is in question.
IOT power upgrade is still in progress and it appears power is achievable and can be stabilized with IOT tuning at the higher powers.
Questions?

## Slide 17: Inside A Separator Cavity
Tuning Plate Removed

## Slide 18: 750 MHz Cavity Couplers

## Slide 19: Prototype Under High Power Test

## Slide 20: Temperatures in the Power Coupler

## Slide 21: RESONANCE CONTROL CRITERIA
Chart: Frequency over Time
| 41052.576388888891 | 41052.581944444442 | 41052.58263888894 | 41052.601388888885 | 41052.602777777778 | 41052.605555555558 | 41052.607638888891 | 41052.611111111073 | 41052.613194444442 | 41052.614583333336 | 41052.615277777782 | 41052.618055555562 | 41052.621527777774 | 0.62500000000000056 | 0.62569444444444555 | 0.62847222222222221 | 0.63194444444444531 | 0.63541666666666652 | 0.63611111111111163 | 0.63888888888888984 | 0.64236111111111105 | 0.64583333333333415 | 0.6479166666666667 | 0.6506944444444458 | 0.65277777777777835 | 0.65625000000000056 | 0.65972222222222265 | 0.66319444444444531 | 0.66666666666666663 | 0.67013888888888973 | 0.67361111111111194 | 0.67847222222222225 | 0.68055555555555569 | 0.68402777777777779 | 0.6875 | 0.69097222222222221
 | 499.015 | 499.014 | 499.013 | 499.009 | 498.998 | 498.994 | 498.986 | 498.98 | 498.975 | 498.973 | 498.967 | 498.961 | 498.956 | 498.949 | 498.942 | 498.939 | 498.933 | 498.928 | 498.919 | 498.911 | 498.903 | 498.9 | 498.889 | 498.88 | 498.873 | 498.867 | 498.86 | 498.857 | 498.853 | 498.851 | 498.849 | 498.847 | 498.847 | 498.847 | 498.847 | 498.845
Chart: Power over Time
| 41052.576388888891 | 41052.581944444442 | 41052.58263888894 | 41052.601388888885 | 41052.602777777778 | 41052.605555555558 | 41052.607638888891 | 41052.611111111073 | 41052.613194444442 | 41052.614583333336 | 41052.615277777782 | 41052.618055555562 | 41052.621527777774 | 0.62500000000000056 | 0.62569444444444555 | 0.62847222222222221 | 0.63194444444444531 | 0.63541666666666652 | 0.63611111111111163 | 0.63888888888888984 | 0.64236111111111105 | 0.64583333333333415 | 0.6479166666666667 | 0.6506944444444458 | 0.65277777777777835 | 0.65625000000000056 | 0.65972222222222265 | 0.66319444444444531 | 0.66666666666666663 | 0.67013888888888973 | 0.67361111111111194 | 0.67847222222222225 | 0.68055555555555569 | 0.68402777777777779 | 0.6875 | 0.69097222222222221
Forward Power | 47.2 | 100 | 213 | 446 | 1261 | 1262 | 1633 | 1663 | 1671 | 1675 | 2128 | 2149 | 2173 | 2183 | 2679 | 2741 | 2760 | 2786 | 3435 | 3548 | 3614 | 3631 | 4355 | 4571 | 4720 | 4699 | 4753 | 4699 | 4699 | 4720 | 4720 | 4677 | 4710 | 4666 | 4613 | 4699
Reflected Power | 0.052 | 0.107 | 0.234 | 0.485 | 1.318 | 1.309 | 1.694 | 1.738 | 1.746 | 1.746 | 2.203 | 2.239 | 2.244 | 2.239 | 2.661 | 2.741 | 2.698 | 2.691 | 3.148 | 3.311 | 3.311 | 3.357 | 3.784 | 3.963 | 3.981 | 4.083 | 4.15 | 4.102 | 4.036 | 4.073 | 3.944 | 3.715 | 3.311 | 3.548 | 3.388 | 3.019
Forward Power | 47.2 | 100 | 213 | 446 | 1261 | 1262 | 1633 | 1663 | 1671 | 1675 | 2128 | 2149 | 2173 | 2183 | 2679 | 2741 | 2760 | 2786 | 3435 | 3548 | 3614 | 3631 | 4355 | 4571 | 4720 | 4699 | 4753 | 4699 | 4699 | 4720 | 4720 | 4677 | 4710 | 4666 | 4613 | 4699
Reflected Power | 0.052 | 0.107 | 0.234 | 0.485 | 1.318 | 1.309 | 1.694 | 1.738 | 1.746 | 1.746 | 2.203 | 2.239 | 2.244 | 2.239 | 2.661 | 2.741 | 2.698 | 2.691 | 3.148 | 3.311 | 3.311 | 3.357 | 3.784 | 3.963 | 3.981 | 4.083 | 4.15 | 4.102 | 4.036 | 4.073 | 3.944 | 3.715 | 3.311 | 3.548 | 3.388 | 3.019
Cavity Temp and Frequency Response
Chart: Power over Time
| 41052.576388888891 | 41052.581944444442 | 41052.58263888894 | 41052.601388888885 | 41052.602777777778 | 41052.605555555558 | 41052.607638888891 | 41052.611111111073 | 41052.613194444442 | 41052.614583333336 | 41052.615277777782 | 41052.618055555562 | 41052.621527777774 | 0.62500000000000056 | 0.62569444444444555 | 0.62847222222222221 | 0.63194444444444531 | 0.63541666666666652 | 0.63611111111111163 | 0.63888888888888984 | 0.64236111111111105 | 0.64583333333333415 | 0.6479166666666667 | 0.6506944444444458 | 0.65277777777777835 | 0.65625000000000056 | 0.65972222222222265 | 0.66319444444444531 | 0.66666666666666663 | 0.67013888888888973 | 0.67361111111111194 | 0.67847222222222225 | 0.68055555555555569 | 0.68402777777777779 | 0.6875 | 0.69097222222222221
Forward Power | 47.2 | 100 | 213 | 446 | 1261 | 1262 | 1633 | 1663 | 1671 | 1675 | 2128 | 2149 | 2173 | 2183 | 2679 | 2741 | 2760 | 2786 | 3435 | 3548 | 3614 | 3631 | 4355 | 4571 | 4720 | 4699 | 4753 | 4699 | 4699 | 4720 | 4720 | 4677 | 4710 | 4666 | 4613 | 4699
Reflected Power | 0.052 | 0.107 | 0.234 | 0.485 | 1.318 | 1.309 | 1.694 | 1.738 | 1.746 | 1.746 | 2.203 | 2.239 | 2.244 | 2.239 | 2.661 | 2.741 | 2.698 | 2.691 | 3.148 | 3.311 | 3.311 | 3.357 | 3.784 | 3.963 | 3.981 | 4.083 | 4.15 | 4.102 | 4.036 | 4.073 | 3.944 | 3.715 | 3.311 | 3.548 | 3.388 | 3.019
Forward Power | 47.2 | 100 | 213 | 446 | 1261 | 1262 | 1633 | 1663 | 1671 | 1675 | 2128 | 2149 | 2173 | 2183 | 2679 | 2741 | 2760 | 2786 | 3435 | 3548 | 3614 | 3631 | 4355 | 4571 | 4720 | 4699 | 4753 | 4699 | 4699 | 4720 | 4720 | 4677 | 4710 | 4666 | 4613 | 4699
Reflected Power | 0.052 | 0.107 | 0.234 | 0.485 | 1.318 | 1.309 | 1.694 | 1.738 | 1.746 | 1.746 | 2.203 | 2.239 | 2.244 | 2.239 | 2.661 | 2.741 | 2.698 | 2.691 | 3.148 | 3.311 | 3.311 | 3.357 | 3.784 | 3.963 | 3.981 | 4.083 | 4.15 | 4.102 | 4.036 | 4.073 | 3.944 | 3.715 | 3.311 | 3.548 | 3.388 | 3.019
Chart: Temperature over Time
| 41052.576388888891 | 41052.581944444442 | 41052.582638888889 | 41052.601388888892 | 41052.602777777778 | 41052.605555555558 | 41052.607638888891 | 41052.611111111109 | 41052.613194444442 | 41052.614583333336 | 41052.615277777775 | 41052.618055555555 | 41052.621527777781 | 0.625 | 0.62569444444444444 | 0.62847222222222221 | 0.63194444444444442 | 0.63541666666666663 | 0.63611111111111118 | 0.63888888888888895 | 0.64236111111111105 | 0.64583333333333337 | 0.6479166666666667 | 0.65069444444444446 | 0.65277777777777779 | 0.65625 | 0.65972222222222221 | 0.66319444444444442 | 0.66666666666666663 | 0.67013888888888884 | 0.67361111111111116 | 0.67847222222222225 | 0.68055555555555547 | 0.68402777777777779 | 0.6875 | 0.69097222222222221
Temp. 1 | 31 | 31 | 31 | 31 | 31 | 31 | 33 | 34 | 35 | 36 | 36 | 37 | 39 | 40 | 41 | 41 | 43 | 45 | 45 | 47 | 49 | 50 | 52 | 52 | 54 | 56 | 58 | 59 | 60 | 62 | 62 | 64 | 64 | 65 | 66 | 67
Temp. 2
Temp. 4

## Slide 22: Powering A Cavity With Solid State Amp
Chart: Frequency(MHz) vs Time
| 7:00 | 7:15AM | 7:30 | 7:45 | 8:00 | 8:15 | 8:30 | 8:45 | 9:00 | 9:30 | 10:00 | 10:30 | 11:00 | 11:30
Frequency | 499.062 | 499.065 | 499.059 | 499.057 | 499.058 | 499.062 | 499.03 | 499.018 | 499.021 | 499.023 | 499.02 | 499.023 | 499.021 | 499.025
Chart: Vacuum vs Time
| 7:00 | 7:15AM | 7:30 | 7:45 | 8:00 | 8:15 | 8:30 | 8:45 | 9:00 | 9:30 | 10:00 | 10:30 | 11:00 | 11:30
Vac Reading Stop | 10 | 12 | 12 | 12 | 26 | 34 | 59 | 96 | 107 | 102 | 85 | 78 | 69 | 64
Chart: Fwd Pwr(dBm) vs Time
| 7:00 | 7:15AM | 7:30 | 7:45 | 8:00 | 8:15 | 8:30 | 8:45 | 9:00 | 9:30 | 10:00 | 10:30 | 11:00 | 11:30
Fwd Pwr @ A | 57.09 | 57.13 | 57.15 | 57.16 | 60.78 | 66.2 | 66.18 | 66.17 | 66.19 | 66.18 | 66.2 | 66.18 | 66.16 | 66.16
Chart: Fwd Pwr(dBm) vs Time
| 7:00 | 7:15AM | 7:30 | 7:45 | 8:00 | 8:15 | 8:30 | 8:45 | 9:00 | 9:30 | 10:00 | 10:30 | 11:00 | 11:30
Fwd Pwr @ A | 57.09 | 57.13 | 57.15 | 57.16 | 60.78 | 66.2 | 66.18 | 66.17 | 66.19 | 66.18 | 66.2 | 66.18 | 66.16 | 66.16

## Slide 23
Resonance Control
PLC Controller
Heater System
Cavity Temp. vs. Frequency Response
Heater Module