## Slide 1: Hall D Fast Feedback
Trent Allison
Ops StayTreat
2015

## Slide 2: Hall D FFB Overview
V
H
Data from 2 BPMs used to control 2 sets of correctors
  Locking position at 1 point does not stabilize the trajectory or downstream position, 2 points are needed
  Element locations are selected based on the optics
Main goal is to compensate for 60Hz line motion
V
H
X Y
X Y
Correctors
Correctors
BPM
BPM
Control Algorithm
60Hz
120Hz
Beam Motion

## Slide 3: Based on Halls A & C FFB
FFB Control Algorithm: Lebedev & Dickson circa 1996
Targets 60Hz line motion and harmonics
Auto calibration: kick beam, record response and calculate matrix coefficients
Feedback to 180Hz plus feedforward to 720Hz
Position and energy correction
…
BPM
BPM
(x8)
RF Mod
…
ADC
4
4
FFB IOC
RF Mod
IF Mod
…
IF Mod
Shared Memory
EPICS IOC
ADC
DAC
Filter
DAC
Trim
Rack/ Cards
Trim
Rack/ Cards
VME Crate
BSY Service Building
Magnet
Magnet
Magnet
Magnet
Magnet
Magnet
A/C Select
SL Service Building Zone 20
Vernier Control Chassis
Filter
Filter
Filter
Filter
RFCM 1&2
RFCM 3&4
RFCM 5&6
RFCM 7&8
Timing
n*60Hz
Beam Sync
3
3
3
3

## Slide 4: Hall D FFB
BT02
Cal Cell
Trim
Rack/ Cards
E2
BS04V
5C00V
5C00H
5C04H
BS04H
5C04V
NL Service Building Zone 26
Fiber to BNC
5C00
Cal Cell
5C02
Cal Cell
Hall D
Striplines
5C06
Cal Cell
5C07
Cal Cell
5C11B
Cal Cell
AD00C
Cal Cell
Active Collimator
5H01
5C11A
Cal Cell
AD00
Cal Cell
Cavities*
Tagger Service Building
BPM RX
BPM RX
BPM RX
BPM RX
BPM RX
BPM RX
BPM RX
BPM RX
BPM RX
Beam Sync
LLRF 1
LLRF 2
LLRF 3
LLRF 4
LLRF 5
LLRF 6
LLRF 7
LLRF 8
FFB Chassis
VME ADC/ FPGA
Fiber RX
Altera Cyclone V
FPGA/
ARM Cortex-A9 dual-core
FFB IOC
Fiber TX
DACs
PC104 EPICS IOC
Beam Sync
Beam Sync
* There are only 8 fiber inputs so the Cavity BPMs will replace 2 Striplines
Correctors

## Slide 5: Hall D FFB Chassis
FPGA/ARM
FFB IOC
PC104
EPICS IOC
Fiber I/O
DACs
Power Filtering
Beam Sync
IOC RS232/Net
LEDs

## Slide 6: Stripline BPMs
Used instead of M15 antenna BPMs
  Easier & more precise manufacturing
  No hand bending of antennas
  Better sensitivity
  50 ohm devices
Position calculated as difference-over-sum
Each characterized with Goubau Line BPM Test Stand
26 Striplines
IPMBS00
IPMBS01
IPMBS02
IPMBS03
IPMBS04
IPMBE01
IPMBE02
IPMBE03
IPMBE04
IPMBT01
IPMBT02
IPMBT03
IPM5C00
IPM5C01
IPM5C02
IPM5C03
IPM5C04
IPM5C05
IPM5C06
IPM5C07
IPM5C08
IPM5C09
IPM5C10
IPM5C11
IPM5C11B
IPMAD00C
Y Stepper
Goubau Line
BPM
Ladder
X Stepper

## Slide 7: Stripline Bandwidth vs Resolution
Chart: Stripline BPM Performance
| 0.1 | 1 | 60 | 120 | 180 | 240 | 300
10um | 94.8683 | 300 | 2323.79 | 3286.3353 | 4024.9224 | 4647.58 | 5196.1524
100um | 9.4868 | 30 | 232.379 | 328.6335 | 402.4922 | 464.758 | 519.6152
430um | 2.2136 | 7 | 54.2218 | 76.6812 | 93.9149 | 108.4435 | 121.2436
 | 100um | 430um
BW Hz | Beam nA | Beam nA
0.1 | 9 | 2
1 | 30 | 7
60 | 232 | 54
120 | 329 | 77
180 | 402 | 94
240 | 465 | 108
300 | 520 | 121
100um resolution at 330nA with 120Hz BW
Error at 7 & 30nA
Beam Position (mm)
IPM2H00.XPOS
IPM2H02.XPOS
IPM2H00.YPOS
IPM2H02.YPOS
430um
100um
Beam Current (nA)
7nA
30nA
Current Ramp from 0 to 100nA with 1Hz Bandwidth

## Slide 8: Cavity BPMs
IPM5C11A at shield wall, IPMAD00 at Goniometer
Positions go as X/I & Y/I
Electromagnetic field excited by beam
  BCM: TM010 Mode
  BPM: TM110 Mode
    Signal disappears at boresight
Tuning port for centering at 1497MHz
  Temperature stabilized
Better sensitivity than Striplines
Tuners
I
X
Y
Probes & Test Ports
Blanket w/ Heat Tape
Foot

## Slide 9: Active Collimator
IPC5H01 in Hall D Alcove
Intercepts photon beam
  Tungsten pin-cushion wedges
  Current output
Difference-over-sum used on inner wedges for FFB (region 1)
Works at low beam currents
mm

## Slide 10: Hall D FFB Algorithm
Correctors up to 1kHz
Hall A&C FFB @ 10uA
  Hall D: 5nA to 500nA
  SEE: 20um @10uA
  Striplines: 100um @ 330nA/120Hz BW
  Use Cavity BPMs & Active Collimator for lower currents
Plan A: Hall A&C style feedback and feedforward
  1.8ksps data & DACs (due to hardware limitations in A&C)
Plan B: High bandwidth feedback (no feedforward)
  Take advantage of 30ksps fiber data and 1MHz DACs
  Must have low latency and good signal-to-noise
Plan C: 60Hz line-locked feedforward only (last run)
5C03H Corrector
5C03V Corrector
Gunk

## Slide 11: Hardware Testing
Hardware was verified using beam
  Fiber data to FFB
  Magnet controls
Magnet locations mapped correctly
Good response at 5.5GeV with headroom for 12GeV
IPM5C07 Stripline Frequency Response
BS04H
BS04V
5C00H
5C00V
5C04H
5C04V
60Hz
Active Collimator plot of time domain response to 1kHz FFB magnet kick at BS04V
1kHz kick on top of 60Hz @ Active Collimator

## Slide 12: 60Hz Suppression (Plan C)
Line-synchronized 60Hz Feedforward suppression algorithm used last 2 days of the run
Also engaged slow EPICS position locks to steady the beam
IPM5C07 Stripline Frequency Response
60Hz Suppression
OFF
60Hz Suppression
ON
60Hz Line Frequency Wanders ~0.14Hz
60.07
59.93
Hz

## Slide 13: Hall D FFB To Do
Implement Hall A&C FFB algorithm (Plan A)
  Translate into the new electronics
  Incorporate Active Collimator
  Incorporate Cavity BPMs
Commission Cavity BPMs (beam time)
  Finish firmware and software
  Measure bandwidth & current limitations
Commission Active Collimator (beam time)
  Measure bandwidth & current limitations
Iterative FFB testing and tweaking (beam time)

## Slide 14: Hall D Fast Feedback
Questions?
Hall D FFB Team: Trent Allison, Brian Bevins, Keith Cole, John Musson, Todd Satogata & Scott Windham

## Slide 15: Hall D Fast Feedback
Backup Slides…

## Slide 16: Bandwidth vs Resolution
Improving the signal-to-noise improves performance
Filtering down to 1 Hz instead of 10 Hz gives an improvement factor of about 3.2
This square root of bandwidth improvement holds true as long as the noise is Gaussian
~30 nA @ 1 Hz
~30 nA @ 10 Hz
Position map improves by tightening bandwidth
250 um
Step Scan

## Slide 17: FFB Component Locations
IPMAd00
Magnets
Stripline BPMs
Cavity BPMs

## Slide 18: FFB Component Locations
Stripline BPM
Active Collimator