## Slide 1: Sept 30 meeting updates
Explains past work and updates on box design

## Slide 2: Previous 14C work
Goal: to compare hotspots of activity in 11C PET labeling to 14C Hotspots on film.
  14C adds resolution and corroborates 11C result
  Additional spatial information from added resolution informs interpretation of PET

## Slide 5: Box iterations
Eventually landed on a design with a gasket within a groove that is pressed in by the door.
Used a piece of aluminum foil as a spacer so the film would not compress soil surface
Foam tipped tubing provides aeration to soil

## Slide 6: Labeling
Placed rhizobox into an empty 11C labeling pot
Sealed soil surface from air
Plastic acts as shielding during pulse labeling
Downside: was difficult to get box into pot

## Slide 7: Labeling
I designed an adapter for our existing circular labeling chamber but it was difficult to get a good seal.
Could be revived and perfected.

## Slide 8: Proposed Labeling Approach 1
Design a chamber for the aboveground portions of the plant that fits exactly onto the top of the labeling box
Downside: This would not leave room for larger leaves- may have to taper.

## Slide 9: Proposed Labeling Approach 2
Use larger labeling chamber as we are not constrained by PET detector aperture
Downside: Larger volume = longer assimilation time = less sharp pulse

## Slide 10: Film
Gafchromatic LD-V1 from Ashland Specialties
  Low dosage film
  Most sensitive version
  Has 122 micron polyester layer protecting active layer
  We did not successfully delaminate the film

## Slide 11: 2 trials with live plants
No registration on film either time
Wetness of film on one of the trials

## Slide 12: Potential issues
Compromised protective layer or condensation within that layer?
Carbon budget: is enough 14C reaching the surface of these roots to be registered in the time frame
Biggest issue: Film sensitivity – this film was not designed for dosages this low even though this is the most sensitive version

## Slide 13: Solution: High sensitivity water resistant phosphor screens
Phoshpor crystals store radiation energy and reemit it when exposed to a laser scanner
Higher sensitivity and high resolution

## Slide 14: Phosphor screen testing
Were able to register radiation during a 10 hr exposure to 25 micro curies soaked into a cotton radiation swipe with conventional saran wrap (~15 microns).

## Slide 15: Previously proposed work with phosphor screen
Continue the exposure testing to get a sense of the necessary exposure times for registering roots
Do a plant test with cut down version of phosphor screen

## Slide 16: Current Progress
Redesigned Rhizo-box for our current project dimensions
Redesigned gasket bevel so soil will come to the edge of the box

## Slide 17: Current Progress
Testing of first print of rhizo-box
Ordering new gasket material
Add more screw holes for tighter fit

## Slide 18: Upcoming work on box
Cut gasket to fit
Slope upper wall of the window so that roots don’t have to fight right angle
Check seal

## Slide 19: Upcoming work on setup
Finish transfer of 14C to UCSC
Test single pixel diodes for sensitivity