## Slide 1
CLAS12 Longitudinally Polarized Target R&D Update
Chris Keith

## Slide 2
Polarizing
Magnet
Pumping system
Microwaves
(140 GHz @ 5T)
NMR
1K Refrigerator
CLAS12 Solenoid (not to scale)
UVA/JLab
ODU
ODU
CNU
ammonia
Field
PolTar12: components for a dnp target
Beam

## Slide 3
Polarizing
Magnet
Pumping system
Microwaves
(140 GHz @ 5T)
NMR
1K Refrigerator
CLAS12 Solenoid (not to scale)
UVA/JLab
ODU
ODU
CNU
ammonia
Field
PolTar12: components for a dnp target
Magnet
Microwaves
Target Sample

## Slide 4
PolTar12: magnet
CLAS12 solenoid design specs
  5.0 tesla
  DB/B ≤ 10-4 (Ø2.5 x 4 cm central volume)
DB/B = 10-3
Proton reduced ~20%
Deuteron reduced ~50%
DB/B = 10-4
negligible effect
Polarization v. field dependence for NH3 and ND3 @ 136 GHz M. Seely, Yale 1982
If necessary we can add small shim coils inside the target cryostat to improve the uniformity…

## Slide 5
PolTar12: magnet
Sebastian Kuhn: We can also use internal, superconducting coils to adjust the polarizing field for two target samples, and take data on both polarizations simultaneously.
Beam
Coil 1 & 1A
Coil 2 & 2A
Target 1
(-80 gauss)
Target 2
(+80 gauss)
1K LHe
5 Tesla
Carbon Foil
Heat shield
Vacuum can
Question: Can we uniformly irradiate both samples with one microwave source?
Pumping tube

## Slide 6
PolTar12: microwaves
And how can we do it if there is no room for a microwave horn?

## Slide 7
PolTar12: microwaves
Measure the
frequency (137 GHz)
Measure the
REFLECTED power
2 ft WR-6 rect. waveguide
3 ft oversized circular waveguide
Various cavities
(copper, aluminum, etc)
Liquid crystal film
Liquid crystal film changes color according to temperature.
Three sensitivities:
  25 C
  30 C
  35 C

## Slide 8
Radiation pattern from a conical horn. Reflected power ~2 mW.
Radiation pattern from unterminated waveguide.
Reflected power ~2 mW.
PolTar12: microwaves

## Slide 9
Attempts to make slotted-style antennae in the circular waveguide were unsuccessful. Very little power transmission, and very large reflected power.
 Waveguide “reflectors” worked much better.
Radiation pattern from the wedge.
Reflected power ~ 2 mW.
Wedge-shaped reflector soldered into the circular waveguide.
PolTar12: microwaves
LC film

## Slide 10
Using a metal cavity makes a tremendous difference. The power is much more uniformly distributed, and reflected power continues to be minimal.
Radiation pattern after a 15 s exposure, 25 C film (most sensitive). Note the two “hot spots”.
Wedge-shaped reflector inside a copper cavity, OD ~ 4.5 cm
LC Film
PolTar12: microwaves

## Slide 11
Microwave pattern can be tailored to the desired target geometry.
Aluminum cavity w/ hemispherical end cap, diameter ~ 7.5 cm
60 s exposure on 35 C film (least sensitive)
Approximate size of two 2.5 x 2.0 cm target cells, w/ 2 cm separation
PolTar12: microwaves

## Slide 12
The next step is to make more quantitative measurements
  Use a grid of 8 thermocouples to map the power distribution inside a 6 cm aluminum cavity
  Thermocouple junctions are covered by a microwave absorber
  Assembly is complete
  Tests are underway
PolTar12: microwaves

## Slide 13
PolTar12: target insert
Ammonia samples are placed into the target cryostat with a sample insert.
It usually contains the microwave and NMR services as well.
The UVa polarized target

## Slide 14
PolTar12: target insert
A major obstacle in the design of the CLAS12 polarized target is its overall length, almost 3 meters.
This will make installation and replacement of the target sample very unwieldy and more subject to damage and frost.
James Brock has introduced a new design that has the potential to alleviate this problem. A proof-of-principle prototype has been constructed and looks very promising.

## Slide 15
PolTar12: target insert
In the new design a single, removable insert is replaced by two inserts that remain inside the cryostat.
1. NMR & Microwave insert: a hollow tube with NMR cables & coils, microwave waveguide, and a beam entrance window at the warm end.
To pumps
Outer vac. can
Helium pumping tube
1K refrigerator
LHe fill tube
NMR coil & cable
Waveguide
Microwave cavity
4K LHe
Helium vapor (gray)
Beam
window

## Slide 16
PolTar12: target insert
In the new design a single, removable insert is replaced by two inserts that remain inside the cryostat.
2. Sample insert: small container for ammonia sample(s) and liquid helium, with a re-entrant beam window.
To pumps

## Slide 17
PolTar12: target insert
Preloaded ammonia “cartridges” are placed into the sample insert in the retracted position via a dedicated loading port.
To pumps
The sample is then moved into the center of the microwave cavity and NMR coil.

## Slide 18
PolTar12: target insert
The sample insert is fill with 1K LHe from the refrigerator and the ammonia is dynamically polarized.
To pumps
Beam
Ready for beam!

## Slide 19
PolTar12: target insert
To pumps
The sample is unloaded and replaced by a fresh sample in the same manner.
Repeat as necessary…

## Slide 20
PolTar12: summary
Most recent activity on PolTar12 has been on the microwave & target insert subsystems
Good progress on the microwaves
 results are very promising for the double-cell design
New insert design promises to make sample loading and unloading easier
 prototype has been constructed & successfully tested
Work will now focus on other subsystems
 NMR system (remote frequency tuning, optimize coil design)
 1 K refrigerator (finalize design & engineering)

## Slide 21
PolTar12: microwaves
EIO microwave tube
  136.5 ± 2 GHz (4.87 ± .07 tesla)
  34 W max power!
  No tuning motor
Power v. Frequency (CNU measurements)
Graph by Sarah Clark