## Slide 1: CLAS12 Tracking Overview and Progress
CLAS 12 First Experiment Workshop
Veronique Ziegler
First Experiment Workshop

## Slide 2: Central Vertex Tracker Reconstruction
New package clasrec-CVT contains algorithms to reconstruct events using BMT and SVT
  SVT can be run stand alone
  Raw data translation for both systems
    tested on raw data with BMT + SVT hits
  new algorithms to use BMT cluster positions
    improved BMT (also FMT) clustering algorithm under development (Saclay- Maxime Defurne)
  Validation flags can be turned on  layer efficiencies
Alignment code development using Millepede (J. Gilfoyle)
Geometry implementation in common tools package (P. Davies)
Ongoing validation (next slides)

## Slide 3: BMT hit info used in pattern recognition
C-detector cluster position  z information (phi calculated from track )
Z-detector cluster position  phi information (used in fit in xy plane)
C-detector z information used for reconstructing theta

## Slide 4: New Banks
CVTRec  reconstruction banks using both BMT + SVT

## Slide 5: CVT Offline Monitoring and Validation
CVT Validation suite
Histogram selection menus added
MVT histograms added
Cut selection menu implemented
Event skimming added
Unbiased centroid residuals added
Efficiencies and resolutions implemented
Hipo and root output format
Validations performed
Reconstruction release validation v0.1 - v0.6
Single track reconstruction
  Geantinos, muons, pions
  Straight (0T) and helical tracks
Gemc 2.3
Geometric acceptance
Discriminator thresholds
Resolutions (momentum, angular)
Efficiencies (track finding, hit finding)
Occupancies
Work in progress
Misaligned geometry
Multiple tracks
Electronic noise
Local reconstruction
Lorentz angle
Documentation
Track finding efficiency, %
Y. Gotra

## Slide 6: CVT Online Monitoring
Strip Plots/Tracker Maps
2d plot, sensor vs. channel (132x256)
channel status (green: good, yellow: masked, red: noisy)
occupancy in percent vs. the strip number
average strip pulse height in ADC counts
width of pulse height distribution in ADC counts
new bad strip (red: strip marked by data quality algorithm but not marked)
chip status map
Component Plots
Selection of component (sensor) in Detector View, 1D
occupancy, vs. the strip number
ADC
BCO
cluster charge
corrected cluster charge (by cos of the track angle)
strip multiplicity
unbiased centroid residual
local track phi
local track theta
local track 3D angle
Statistics Plots
Mean value and RMS (as error bar) vs. sector, by layer
ADC
occupancy
cluster charge
strip multiplicity
unbiased centroid residual
Summary/Combined Plots
Per layer/region, total
hit finding efficiency, occupancy, norm. by nb of strips (event-by event)
ADC
cluster charge
corrected cluster charge (by cos of the track angle)
unbiased centroid residual
strip multiplicity
hit multiplicity
cluster multiplicity
cross multiplicity
Tracker Object Plots
track p, pt, φ0, θ0, z0, d0
track φ0 vs. track θ0
track normalized χ2,
track multiplicity
path length
hits per track
Views:
Summary
Report
Shift
Expert
Monitoring Plots:
long-term (statistics accumulated in the run)
short-term (during the last few minutes or over a few most recent events)
history plots (time history of any quantity with long/short-term plot)
periodic plots (averaged over a fixed number of events)
tracker maps
6

## Slide 7: Alignment of the SVT
* Geometry implementation in Java framework & validation ongoing (P. Davis [U. Surrey])
J. Gilfoyle

## Slide 8: DC Reconstruction
Realistic time smearing and intrinsic inefficiencies in MC
  using doca RMS in fit
Time-to-distance parametrization (M. Mestayer & K. Adhikari [U. Miss.])
Improved noise rejection algorithms
  secondaries pruner
  LR ambiguity resolver
Development of improved Hit-based track parameters (in development)
  using KF fitting method
  using segment dictionary & Neural Net (D. Heddle [CNU], M. Catelli [CNU student], L. Lorenti [CNU student])

## Slide 9
Three sources of inefficiency:
  Intrinsic (applies to all wires) – cells don’t always fire,
  Equipment malfunction-related (applies to specifc wires),
  Background-related (unavoidable knock-on electrons)
Improved digitization in GEMC
  parameters added to CCDB: SQlite
  intrinsic inefficiency (distance dependent) is added in GEMC
The intrinsic inefficiency function:
where X = doca/docaMax & docaMax = 2 dlayer
not yet calibrated
Inefficiency =
0.000125/(x^2+0.05)^2 + 0.0025/((1-x)+0.15)^2
Inefficiency
X=doca/docaMax
θ=30
θ=0
Hit times generated by GEMC digitization routine will be smeared by a random number with position-dependent magnitudes as given by above intrinsic inefficiency function.
Same inefficiency function and parameters are used by the track reconstruction software to form error matrix in the Kalman-filter.
Simulation of intrinsic wire inefficiencies
Notes: In the case of a track which passes very close (within 1-2 mm) of the wire, the ionization electrons arrive individually, spread out over a long time, and the signal voltage may fail to exceed the discriminator level and so result in no signal.
In case of a track passing close to x=1 (i.e near the hexagon vertices/corners or near field wires), only some ionization electrons will arrive (with most or a lot of them lost to the neighboring cells), thus reducing the signal voltage to have similar effect as near the wire.

## Slide 10: Tuning inefficiencies in MC
inefficient wire

## Slide 11
Simulation of doca resolution
Resolution in mm =
1.0(0.16 + 0.005/(0.1+x)^2 + 0.8*x^8)
X=doca/docaMax
Resolution in mm
used to smear docas in GEMC
used in reconstruction in measurement error
in Kalman Gain calculation
Functional form: M. Mestayer & K. Adhikari
GEMC implementation: M. Ungaro
Notes: In the case of a track which passes very close (within 1-2 mm) of the wire, the ionization electrons arrive individually, spread out over a long time, and the signal voltage may fail to exceed the discriminator level and so result in no signal.
In case of a track passing close to x=1 (i.e near the hexagon vertices/corners or near field wires), only some ionization electrons will arrive (with most or a lot of them lost to the neighboring cells), thus reducing the signal voltage to have similar effect as near the wire.

## Slide 12
Cosmic data
Gemc data
GEMC data
Cosmic data
X=doca/docaMax
X=doca/docaMax
Residual in cm
Residual in cm
Superlayer - 1
Superlayer - 2
Residuals (calcDoca – trkDoca) in 40 trkDoca bins.
Double Gaussian fits on the residuals
Standard deviation of the central/narrower Gaussian taken as the resolution for that bin.
DC-resolution for Cosmics & GEMC
K. Adhikari
Notes: Double Gaussian fits (red and green represent the two gaussian components and the blue is for the overall double gaussian). The central/narrower gaussian was used to represent the resolution in the given doca bin.

## Slide 13
Superlayer 1
Superlayer 2
Superlayer 1
Superlayer 2
Superlayer 1
Superlayer 2
Superlayer 1
Superlayer 2
Superlayer 1
Superlayer 2
Superlayer 1
Superlayer 2
Inefficiency
Inefficiency
Inefficiency
Inefficiency
Inefficiency
Inefficiency
Layer 5
Layer 1
Layer 3
Layer 4
Layer 6
Layer 2
Layer (In)efficiency as function of track DOCA
(Cosmic data)
K. Adhikari
Notes: Fluctuation in lnefficiency: due to low statistics as some dead areas? (Mac)

## Slide 14
Studied distance dependence of layer inefficiency for COSMIC data
  Except of layer 4 in SL1, inefficiency is about 3 to 4 %
  Layer 4 in SL1 has high inefficiency (about 12%) which seems to be due to voltage issues in some of the channels.
  Corrections for equipment status (dead channels) not applied yet
  Time-to-distance function not calibrated yet. (Linear function being used in reconstruction).
Corresponding study on GEMC data yet to be done.
not yet calibrated
Inefficiency =
0.000125/(x^2+0.05)^2 + 0.0025/((1-x)+0.15)^2
Inefficiency
X=doca/docaMax
Layer inefficiencies
M. Mestayer & K. Adhikari
Notes: https://www.jlab.org/Hall-B//secure/eg4/adhikari/myHomeLinked/MyHm/Shared/spikyEvents.txt

## Slide 15: Time-to-distance parameterization
Distance (cm)
Time (ns)
Region 1
Region 3
Region 2
B=2T
B=1T
B=0T
Distance (cm)
Distance (cm)
Time (ns)
local angle = 00
local angle = 300
inflection point
Distance  Time
-local-angle and B-field dependence
-consistent with GARFIELD
-inversion done numerically
-thicker wire  more linear
 easier to calibrate
Initial parameters & method in software now
M. Mestayer

## Slide 16: Time-to-distance parameterization
Starting equation for 30 degree tracks:
Very preliminary fits on 30 degree & 0 degree tracks respectively
K. Adhikari

## Slide 17: Noise rejection algorithm improvements
secondaries produce this type of clusters mostly in Region 3
negative times indicating inefficient cell  not used In reco.
MC sample 4.5 GeV e- @ f =0o, q = 10o
Effect of noisy clusters on the reconstruction

## Slide 18: Noisy clusters that do not affect tracking
detached secondary hits
Removed by pruning algorithm

## Slide 19: Noisy Clusters
New algorithm:
look for double hits for which the sum of the docas is less than some predefined cut (to be optimized, 1.75*cell-size)
refit the cluster for all combinatorials of hits choosing one of the hits in such doublets
select the best cluster
  requires to a priori redo hit-based fits as the LR assignment can be wrong
not used In reco.
MC sample 4.5 GeV e- @ f =0o, q = 10o

## Slide 20: After algorithm implementation
Cross correctly reconstructed

## Slide 21: LR ambiguity not resolved for tracks at ~30o in superlayer local coordinate system
LR ambiguity resolved using doublet hits in layers 1--3
LR ambiguity not resolved
New algorithm:
using docas calculated from times save the following segment candidates:
  if doca sizes are ~ equal
    2 candidates : LR = 1, LR =-1
  if docas larger at ends of segment
    2 candidates
save all candidates and select the one yielding the best track fit when combined with segments from other regions (for current cosmic sample  save all segment candidates)
DC cosmic data sample: Region 1 Chamber

## Slide 22: Allowing both segments and picking the correct one
2 crosses  only 1 yields well reco. track
2 track solutions
retain track solution with best chi2

## Slide 23: DC new algorithms and code restructuring
ClusterCleaner utility class
  called by ClusterFinder
    HitBased level
      hit list pruner
      find clusters
        look for // clusters or X clusters  cluster splitter
    TimeBased level
      recompose HitBased Clusters  read from HB bank
      secondaries remover  using sum-docas algorithm
      LR ambiguity resolver
      Final fit  cluster line  used in cross calculation
Status word for cluster:
  Array:  Can be used in analysis to reject poorly reconstructed segments when high sample purity is required…
layer  | 1 | 2 | 3 | 4 | 5 | 6
nb hits in layer | 0,1,2 | 0,1,2 | 0,1,2 | 0,1,2 | 0,1,2 | 0,1,2
LR ambiguity sum | -1,0,1 | -1,0,1 | -1,0,1 | -1,0,1 | -1,0,1 | -1,0,1
Ave. nb hits passing residual cut (350 m) | 0,1,2 | 0,1,2 | 0,1,2 | 0,1,2 | 0,1,2 | 0,1,2

## Slide 24: Hit-based Tracking Improvements
Previously hit-based tracking used only to select a track candidate.
Very rough estimate of track parameters using a simple approximation (next slide)  very poor momentum resolution
Redesign code to improve hit-based track parameters estimates to use them to match track to outer detectors and get start time

## Slide 25
x
x
x
x
x
x
DC Reconstruction Algorithms
(reminder)
Obtain a trajectory from hit-based track segment
reconstruction
  Fits to the wires  extended to a plane
   point & direction
Gives a “cross” object a position and direction vector
Add raw timing information to refine the hit position
Fit to the crosses to obtain a trajectory  Initial parameters to KF
 Quadratic fit
25
Notes: Segments are linked into region-segments using a wire index proximity condition formula (find another seg within certain number of wires). From this region-segments a point (similar to BST algorithm) is determined. The fit to the wires in each superlayer can be extended to form a plane. Since the orientation of the wires in each superlayer at at +/- 6 degrees stereo angles w.r.t. each other, the 2 planes with intersect. Hence from this intersection a line is formed to yield a direction, and a point can be obtained from the intersection of that line with the plane that lies inbetween the superlayers – so-called middle-plane. This object ( point & direction unit vector ) is what we call a cross. For a good track there are 3 crosses, from which a track trajectory can be estimated.

## Slide 26: Test of implementation
2 GeV e- @ 15 deg q, at midplane
Set times to zero (i.e. hit-based) and run KF using wire positions & hit uncertainties of cell-size/sqrt(12)  did not work
Set times to zero and run KF using segment fit values at measurement plane (fixed z)  kinda worked (except for phi)
Time-based
Hit-based
Dp/p res = 0.45%
q res = 0.046 deg
Dp/p res = 1.33%
q res = 0.12 deg

## Slide 27
Tracking Timeline
Central Tracking: tracker alignment code ready SVT + BMT (4+1) code optimization (unbiased residuals, angular resolution improvements) SVT + BMT (3+3) configuration implementation (geometry & reconstruction) Forward Tracking : Time-to-distance calibration & implementation in reconstruction Hit-based tracking parameters improvements (needed for Event Builder) use of all calibration constants and status tables in reconstruction integration with FMT in reconstruction alignment code and magnet mapping ready FW Trkg & PID: FT-Trk java code ready and integrated with FT system Event Builder: event reconstruction chain ready (e- or hadron id, start time from hit-based tracking, detector matching, full PID using all available detector responses) | 4th quarter 2016 3rd quarter 2016 2nd quarter 2017 4th quarter 2016 3rd quarter 2016 4th quarter 2016 3rd quarter 2016 1st quarter 2017 4th quarter 2016 3rd quarter 2016