## Slide 1: Progress in Electron Cooling Simulations and Code Development
He Zhang
JLEIC Collaboration Meeting, 03/29/2016

## Slide 2
Staged cooling scheme
Simulation results
Simulation program development
Outline

## Slide 3
I. Staged cooling scheme

## Slide 4
MEIC Design Strategy
The JLEIC conceptual design aims for reaching ultra high luminosity up to 1034 cm-2s-1 per interaction point
The JLEIC luminosity concept is based on high repetition rate crab- crossing colliding beams.
This design concept relies on strong cooling of protons & ions
  Achieving small transverse emittance (small spot size at IP)
  Achieving short bunch (with strong SRF)
  Enabling ultra strong final focusing (low β*) and crab crossing
  Suppressing IBS, expanding high luminosity lifetime
JLEIC design adopts traditional electron cooling
JLEIC design adopts a multi-phase cooling scheme for high cooling efficiency

## Slide 5
Staged Cooling Scheme
JLEIC ion complex layout
Multi-phased scheme takes advantages of high electron cooling efficiency at low energy and/or small 6D emittance
Low energy DC cooler at the booster:
  Reduce the emittance
  2GeV/u ion beam, 1.6 MeV electron beam
High energy bunched cooling at the collider ring:
  Maintain the emittance
  Up to 100 GeV/u ion beam, 55 MeV electron beam

## Slide 6
DC Cooler and Bunched Beam Cooler
MEIC needs two electron coolers
DC cooler (within state-of-art, a 2 MeV cooler is in commissioning at COSY)
Bunched beam cooler (Needs R&D):
  ERL single pass cooler (Qe = 420 pC/buncn, baseline design, no circulator ring)
  ERL circulator cooler (Qe = 2 nC/bunch, lower emittance, higher luminosity)
Challenges of the high energy bunched cooler
Cooling by a bunched electron beam
Making and transport of high current/intensity magnetized electron beam
ion bunch
electron bunch
circulator ring
Cooling section
solenoid
Fast kicker
Fast kicker
SRF Linac
dump
injector
ion bunch
electron bunch
Cooling section
solenoid
SRF Linac
dump
injector
energy recovery
Cooling section

## Slide 7
II. Electron cooling simulation results

## Slide 8
DC Cooling at the Booster
Proton beam:
KE = 2 GeV
Emit = 2.15 mm mrad
dp/p = 0.001
N = 2.8E12
Electron beam:
I = 2 A
Ttr = 0.1 eV, Ts = 0.1 eV
DC cooler:
L = 10 m
B = 1 T
 |  | IBS | ECOOL | IBS+ECOOL
RH | 1/s | 3.86E-4 | -9.05E-3 | -9.10E-3
RV | 1/s | 3.86E-4 | -9.00E-3 | -8.71E-3
RL | 1/s | 2.27E-4 | -15.3E-3 | -15.3E-3

## Slide 9
Strong Cooling at the Collider Ring (Qe = 2 nC)
Proton beam:
KE = 30/60/100 GeV
Emit = 0.45/0.35/0.35 mrad
dp/p = 5/4/4
= 2.5/2.75/2.75 cm
N = 6.56E9
Electron beam:
Qe = 2 nC
Ttr = 0.5 eV, Ts = 0.1 eV
Bunched cooler:
L = 302 m
B = 1 T
 |  | IBS | ECOOL
RH | 1/s | 4.74E-3 | -8.05E-3
RV | 1/s | -1.59E-5 | -8.05E-3
RL | 1/s | 2.10E-3 | -1.31E-2
KEp=30 GeV

## Slide 10
Strong Cooling at the Collider Ring (Qe = 2 nC)
 |  | IBS | ECOOL |  | IBS | ECOOL
RH | 1/s | 6.21E-3 | -3.78E-3 |  | 4.43E-3 | -2.65E-3
RV | 1/s | -4.08E-5 | -3.75E-3 |  | -1.53E-5 | -2.60E-3
RL | 1/s | 2.00E-3 | -8.65E-3 |  | 0.97E-3 | -7.29E-3
KEp=60 GeV
KEp=100 GeV

## Slide 11
Weak Cooling at the Collider Ring (Qe = 420 pC)
Proton beam:
KE = 100 GeV
Emit_x = 1.2 mrad
Emit_y = 0.6 mrad
= 2.5 cm
N = 6.56E9
Electron beam:
Q = 420 pC
Ttr = 0.5 eV, Ts = 0.1 eV
= 0.035 cm
= 0.84 cm
Bunched cooler:
L = 60 m
B = 1 T
Lower electron beam current, within the state-of-art technique.
Electron bunch smaller than the proton bunch.
Higher proton beam emittance, lower IBS.
Larger proton beam momentum spread.
Horizontal expansion rate decreases as dp/p increases, with = 2.5 cm |  |  |  |  |  |  |  |  | 
dp/p (1E-4) | 5 |  |  | 8 |  |  | 12 |  | 
IBS (1E-4 1/s) | 5.03 | 0 | 2.26 | 3.39 | 0.01 | 0.63 | 2.35 | 0.01 | 0.20
Cool (1E-4 1/s) | -1.01 | -1.40 | -4.14 | -0.85 | -1.25 | -2.45 | -0.71 | -0.98 | -1.34
Total (1E-4 1/s) | 4.02 | -1.40 | -2.10 | 2.54 | -1.24 | -1.82 | 1.64 | -0.97 | -1.14
dp/p (1E-4) | 5 |  |  | 8 |  |  | 12 |  | 
IBS (1E-4 1/s) | 5.03 | 0 | 2.26 | 3.39 | 0.01 | 0.63 | 2.35 | 0.01 | 0.20
Cool (1E-4 1/s) | -1.01 | -1.40 | -4.14 | -0.85 | -1.25 | -2.45 | -0.71 | -0.98 | -1.34
Total (1E-4 1/s) | 4.02 | -1.40 | -2.10 | 2.54 | -1.24 | -1.82 | 1.64 | -0.97 | -1.14
Proton beam: Parkhomchuk formula

## Slide 12
Weak Cooling at the Collider Ring (Qe = 420 pC)
dp/p=8E-4
dp/p=1.2E-3
1.5h
2.8h
time to double
Np = 3.3E9
10% 4h
10% 8h
Np = 3.3E9
20% transverse coupling
dp/p=1.2E-3
dp/p=1.2E-3

## Slide 13
Weak Cooling at the Collider Ring (Qe = 420 pC)
dp/p=1.2E-3
Np = 5.5E9
10% 3.7h
10% 7.6h
Not easy to find a stable solution.
Horizontal emittance increases due to cooling in the other two directions.
The proposed parameters of the ERL cooler is in reasonable range.
Needs more study.
20% transverse coupling
3.5h
dp/p=1.2E-3
dp/p=1.2E-3
Friction force: Derbenev-Skrinsky-Meshkov formula

## Slide 14
III. Electron cooling simulation program development

## Slide 15
Goals and Approach
Goals:
Enhance the simulation capability for electron cooling in JLEIC project
Different scenarios: DC cooling, bunched electron to bunched ion cooling, bunched electron to coasting ion cooling
More flexibility, higher efficiency.
Approaches:
Following the models in BETACOOL whenever applicable
Revise the models whenever needed
Improve the efficiency by strategically arrange the computation
Take advantage for modern multi-core hardware
Formulas and models implemented:
IBS: Martini model (no vertical dispersion lattice)
Friction force: Parkhomchuk formula (magnetized cooling)
Cooling rate: single particle model, Monte Carlo model
Cooling dynamics: RMS method (with single particle model or Monte Carlo model), model beam method

## Slide 16
New Model: Small e- Bunch to Coasting Ion Beam
How to sample the coasting beam in the longitudinal direction
Sample the ions in the center plate (Single particle model in BETACOOL)
  Ions only see a piece of the
  electron beam
  Do not include the effect of the
  profile of the electron beam
Sample the ions along the ring (MC model in BETACOOL)
  Electron beam length << the circumference of the ring
  Moderate number of ion samples,
  e- bunch CANNOT catch any ion.
  Too many ion samples means
  a lot of redundant calculation.

## Slide 17
How to sample the coasting beam in the longitudinal direction
Only sample the ions that interact with one electron bunch
Calculate the cooling rate in the sampled region
Adjust the cooling rate w.r.t. the duty factor
Random (uniform distribution) longitudinal position in the sample area.
Avoid redundant calculation
Take account the electron bunch profile
New Model: Small e- Bunch to Coasting Ion Beam

## Slide 18
New Model: Correlated e- Bunch
Uncorrelated
Correlated
How will the correlation affect cooling rate?

## Slide 19
New Model: Correlated e- Bunch
Parkhomchuk formula:
Ion beam
Electron beam
Lp also depends on
If the longitudinal momentum is not correlated with longitudinal position, we use the rms of for all the ions.
If the longitudinal momentum is correlated with longitudinal position, the local momentum spread is still , but the electrons have a drift momentum or velocity, which is determined by its longitudinal position.
In the local electron beam frame, the ion get a drift velocity. is replaced as , with the drift velocity.

## Slide 20
Efficiency: Avoid Redundant Calculation
Martini model for IBS rate calculation (No vertical dispersion, Transverse Gaussian distribution)

## Slide 21
Efficient calculation of the IBS expansion rate using Martini model
  Calculate and the rates for each element
  Take average over the whole ring
  In function , are the sample points one selects to numerically calculate the integration. They do NOT depend on the TWISS parameters and the beam property.
  Significant parts in and only depend on and . They have the same value for all the elements. So we only need to calculate them once.
  It improves the efficiency of the program to avoid the redundant calculation.
Efficiency: Avoid Redundant Calculation

## Slide 22
Good efficiency of the serial code, so not necessary to run the code on a cluster machine.
Further improve the efficiency for shared memory structure hardware: GPU, Intel Xeon Phi, or just a multi-core PC.
Parallelization is based on thrust, a parallel algorithm library that supports CUDA, TBB (Threading Building Blocks) and OpenMP.
IBS calculation, 100100100 grid:
NVidia GTX 660 ti GPU: 6 s
CPU: 62 s
Efficiency: Parallelization

## Slide 23
Benchmark
IBS of coasting ion beam
IBS of bunched ion beam

## Slide 24
Benchmark
DC Cooling for JLEIC booster ring:
I. RMS dynamic single particle model
II. RMS dynamic Monte Carlo model
III. Model beam method

## Slide 25
Benchmark
Bunched cooling for JLEIC collider ring:
I. RMS dynamic single particle model
II. RMS dynamic Monte Carlo model
III. Model beam method

## Slide 26
Benchmark
DC cooling and IBS for JLEIC booster ring with KE = 800 MeV
Time cost 133 s (BETACOOL 3060 s)
Bunched cooling and IBS for JLEIC collider ring with KE = 100 GeV
Time cost 30.7 s (BETACOOL 422 s)

## Slide 27
Summary
Staged cooling scheme:
  Traditional electron cooling
  DC cooling reduce the emittance at 2 GeV (booster)
  Bunched cooling maintain the emittance at collision energy (collider)
Simulation suggests the design parameters are achievable.
Need more study on the weak cooling with low electron current.
ERL cooler design is in progress.

## Slide 29
Backup

## Slide 30
Weak Cooling at the Collider Ring (Qe = 420 pC)
dp/p=8E-4
dp/p=1.2E-3
60 m
cooler
30 m
cooler
1.5h
2.8h
1.2h
2.0h
time to double

## Slide 31
Weak Cooling at the Collider Ring (Qe = 420 pC)
Proton beam:
KE = 100 GeV
Emit_x = 1.2 mrad
Emit_y = 0.6 mrad
= 2.5 cm
N = 6.56E9
Electron beam:
Q = 420 pC
Ttr = 0.5 eV, Ts = 0.1 eV
= 0.036/0.036 cm
= 0.84 cm
Bunched cooler:
L = 3060 m
B = 1 T
Lower electron beam current, within the state-of-art technique.
Electron bunch smaller than the proton bunch.
Lower proton beam current, lower IBS.
Larger proton beam momentum spread.
Horizontal expansion rate decreases as dp/p increases, with = 2.5 cm |  |  |  |  |  |  |  |  | 
dp/p (1E-4) | 5 |  |  | 8 |  |  | 12 |  | 
IBS (1E-4 1/s) | 5.03 | 0 | 2.26 | 3.39 | 0.01 | 0.63 | 2.35 | 0.01 | 0.20
Cool (1E-4 1/s) | -0.54 | -0.73 | -4.80 | -0.38 | -0.50 | -2.69 | -0.25 | -0.29 | -1.32
Total (1E-4 1/s) | 4.49 | -0.73 | -2.66 | 3.01 | -0.49 | -2.06 | 2.10 | -0.28 | -1.30
dp/p (1E-4) | 5 |  |  | 8 |  |  | 12 |  | 
IBS (1E-4 1/s) | 5.03 | 0 | 2.26 | 3.39 | 0.01 | 0.63 | 2.35 | 0.01 | 0.20
Cool (1E-4 1/s) | -0.54 | -0.73 | -4.80 | -0.38 | -0.50 | -2.69 | -0.25 | -0.29 | -1.32
Total (1E-4 1/s) | 4.49 | -0.73 | -2.66 | 3.01 | -0.49 | -2.06 | 2.10 | -0.28 | -1.30

## Slide 32
Weak Cooling at the Collider Ring (Qe = 420 pC)
dp/p=8E-4
dp/p=1.2E-3
60 m
cooler
30 m
cooler
2.3h
3.5h
1.7h
3.0h
time to double