## Slide 1: Compensation of Detector Solenoid
G.H. Wei, V.S. Morozov, Fanglei Lin
JLEIC Collaboration Meeting Spring, 2016

## Slide 2: Contents
Detector solenoids Effect
Compensation Options
JLEIC Considerations & a Solution
Summary

## Slide 3: Detector Solenoid Effect
Coherent orbit distortion
Transverse betatron coupling
  Dynamic effect
    Coupling resonances
    Rotates beam planes at the IP
    Breaks Horizontal and vertical dispersion free
    Perturbation on lattice tune & W function of the first order chromaticity compensation
  Spin effect
    Breaks figure 8 symmetry
  Crab crossing
    Complicates the design if crab cavities are installed in a coupled region

## Slide 4: JLEIC and Detector Solenoids
Detector Solenoid | JLEIC
Length | 4 m
Strength | < 3 T
Crossing Angle | 50 mrad

## Slide 5: JLEIC and Detector Solenoids
Effects | e ring | ion ring
Coherent orbit distortion | N | Y
Coupling resonances | Y | Y
Rotates beam planes at the IP | Y | Y
Breaks H & V dispersion free | N | Y
Perturbation on lattice tune & W function | Y | Y
Breaks figure-8 spin symmetry | Y | Y
Effects on e ring & ion ring

## Slide 6: Vertical and horizontal orbit oscillations
Detector Solenoid 1 T: Closed orbit V: ~170 mm, H: ~30 mm
Detector Solenoid > 2 T: No closed orbit

## Slide 7: Coupling of X and Y betatron motion
Coupling beta ~ 5 % of nominal beta (Ion Ring, 60 GeV)

## Slide 8: Break of H & V dispersion-free
Left: detector solenoid off
Right: detector solenoid on

## Slide 9: Perturbation on lattice tune & W function
Tune (25.22, 23.16)  (25.20, 23.08)
Detector solenoid status: Left: off; Right: on
IP
IP

## Slide 10: Compensation Options
Detector Solenoid + Drift + Anti-Solenoid (a RHIC design)
  Pro: dynamically is the best
  Con: there seems to be no space in the IR of JLEIC
Detector Solenoid + + same-field-integral solenoid
  Cons: long locally coupled section, crab cavity issue, spin effect is not compensated
Detector Solenoid + + Anti-Solenoid
  Cons: long locally coupled section, crab cavity issue
V. Garczynsky, RHIC-Notes/AD-AP-37

## Slide 11: Compensation Options
Distributed skew quadrupole compensation
  Pro: less complicated optics than in options 2 & 3
  Cons: long locally coupled section, crab cavity issue, spin effect is not compensated
  a RHIC design, PEP-II
  3 ~ 6 skew quads on each side of IP
V. Garczynsky, RHIC-Notes/AD-AP-38

## Slide 12: Compensation Options
Solenoid + tilt Quads + Anti-Solenoid
  Pros: coupling is localized, no crab cavity problem, spin effect is compensated
  Con: more complicated final focus design
Super KEKB & DAFNE

## Slide 13
JLEIC Considerations & a Solution
Compensation constraints for both electron and ion rings
  Optics fixed and uncoupled at IP due to variety of solenoid fields and energies
  Coupling compensated locally and independently on each side of IP
  Optics fixed at the entrance into and exit from IR
  No coupling elements (for now) dispersive regions
  Cancel spin effect to keep figure 8 symmetry
Notes: 13

## Slide 14
JLEIC Considerations & a Solution
A solution: Solenoid + Quads(normal+skew) + Anti-Solenoid
Quads(normal+skew): a normal quad with an additional winding or a skew quad next to the normal quad
Dynamical rotation angle  of a normal quad (strength: kn) & a skew component (strength: ks)
Notes: 14

## Slide 15
JLEIC Considerations & a Solution
A solution: Solenoid + Quads(normal+skew) + Anti-Solenoid
Quads(normal+skew)
e-ring
Ion ring
IP
: Orbit corrector
Notes: 15

## Slide 16: Coupling of X and Y betatron motion
Coupling compensated locally and independently on each side of IP

## Slide 17: Vertical and horizontal orbit oscillations
Detector Solenoid 3 T: Closed orbit V: < 4 mm, H: < 0.5 mm

## Slide 18: Restoration of H & V dispersion
Left: before restoration
Right: after restoration, Dy < 0.3 m

## Slide 19: Summary
Detector solenoid gives effects of orbit distortion, transverse betatron coupling, Rotates beam planes at the IP, Breaks Horizontal and vertical dispersion free, Perturbation on lattice tune & W function of the first order chromaticity compensation, Spin effect to Break figure 8 symmetry.
A solution of ‘Solenoid + Quads(normal+skew) + Anti-Solenoid’ is used to compensate detector solenoid effects. Results are acceptable.
More study should be done on W function restoration.

## Slide 20: Thank you

## Slide 21: Perturbation on lattice tune & W function
Left: uncorrected; Right: corrected

## Slide 22: Detector Solenoids in LHC
Detector Solenoid | Old LHC | HL-LHC
Length | 5.3 m | 5.3 m
Strength | 2 T | 2 T
Crossing Angle | 285 rad | 590 rad

## Slide 23: Detector Solenoids in RHIC
Detector Solenoid | RHIC
Length | 6.2 m
Strength | 0.5 T
Crossing Angle | <1.7 mrad