## Slide 1: Status Report on Technology Evaluation for JLab Electron Ion Collider (JLEIC) Ion Linac
R.C. York
JLEIC Collaboration Meeting Spring 2016

## Slide 2: Outline
Problem – What technology for JLEIC Ion linac
  copper (Cu) or niobium (Nb)?
Preliminary Evaluation & Results
Summary
Next Steps

## Slide 3: JLEIC Ion Linac Parameters
Ion linac to provide ions to ion booster synchrotron – first step in chain
Ion linac output requirements being developed
  Ion booster performance evaluations as function of input beam parameters will determine necessary ion linac beam parameters output
Question now is what is best technology choice?
  Room Temperature (copper) based - RT
  Superconducting Radio Frequency (niobium) based - SRF
Historically two design points considered
  E_final protons ~285 MeV/u, 208Pb ~100 MeV/u
  E_final protons ~130 MeV/u, 208Pb ~40 MeV/u
Assumption – can reach decision (RT or SRF) that remains valid even as ion linac beam requirements refined
  Focus on E_final protons ~130 MeV/u, 208Pb ~40 MeV/u design point

## Slide 4: Parameters for Technology Choice Analysis
Design point considered
  E_final => protons ~130 MeV/u, 208Pb ~40 MeV/u
Other high level parameters are
  Duty factor of ~0.5% for RT
  Duty factor of ~2.5% for SRF (longer fill time)
  Example heavy ion 208Pb
    Stripped at ~13 MeV/u from 30+ to 67+ (stripping energy part of later optimization)

## Slide 5: Analysis Approaches
Primary metric is cost – either RT or SRF can delivery performance
SRF
2-gap (l/2 & l/4) structures
  Gives broad transit time for large Q/A range of ions
RT
2-gap (l/2 & l/4) structures
  Gives broad transit time but rf drive high
Multi-gap structures
  Narrower transit time but rf drive requirements reduced

## Slide 6: SRF Linac – [1]
ANL Design – P.N. Ostroumouv, et al., “Pulsed SC Ion Linac as Injector to Booster of Electron Ion Collider”, pg. 265-256, Proc. of SRF2015 (Whistler, BC, Canada).
E_final: Protons ~130 MeV/u & 208Pb ~40 MeV/u
Normal conducting section ~5 MeV/u
SRF cavities
  21 of QWR βopt ~0.15 at 100 MHz
  14 of HWR βopt ~0.3 at 200 MHz

## Slide 7: SRF Linac – [2]
SRF Costing - Assume normal conducting front end & stripping section same whether SRF or RT– look at differentials for remainder of linac
Cost tunnel - ~35k$/m x ~47 m ~1.7M$
SRF section - 35 SC cavities ~18.3M$
  21 of QWR βopt ~0.15 at 100 MHz ~7.8M$
    use cost of FRIB QWR βopt ~0.085 at 80.5 MHz ~$0.37M/cavity
  14 of HWR βopt ~0.3 at 200 MHz ~5.6M$
    use cost of FRIB HWR βopt ~0.29 at 322 MHz ~$0.40M/cavity
  RF (~$7/watt) ~4.9M$
    SRF cryoplant ~8.2M$
  heat load ~35 cavities x 9 W (at 4.5K)/cavity x 1.5 ~ 473 W
  M.A. Green, “The cost of Helium Refrigerators and Coolers for Superconducting Devices as a Function of Cooling at 4K”, http://dx.doi.org/10.1063/1.2908683 => scales as [kW]0.63
Total - tunnel & SRF & cryoplant ~28.2 M$

## Slide 8: RT Linac
Following from
Jiquan Guo (Jlab)

## Slide 9: RT Linac 2 gap – [1]
Normal Conducting
E_final: Protons ~130 MeV/u & 208Pb ~40 MeV/u
Normal conducting section ~5 MeV/u – same as SRF
Same as SRF – but use RT
  Cavity losses require high rf power – large expense – α gradient2 – mitigate by increasing cavities
Scale SRF solution – n x 35 RT cavities
  n x 21 of QWR βopt ~0.15 at 100 MHz
  n x 14 of HWR βopt ~0.3 at 200 MHz
  as n goes up, rf drive /cavity goes down – but – cost per rf watt goes up (~$7/W at ~10s kW to ~$0.5/W at few MW)
  => lowest cost for n=1

## Slide 10: RT Linac 2 gap – [2]
RT Costing - Assume normal conducting front end & stripping section same whether SRF or RT– look at differentials for remainder of linac
Cost tunnel - ~35k$/m x ~49 m ~1.7M$
RT section - 35 SC cavities ~55.2 M$
  ~100k$/m x 0.5 m/cavity = ~50k/cavity ~1.75 M$
  RF (~$0.3/W) ~52.9M$
    $0.3/W lower end – cost information ranged ~0.4±0.1 (25%) $/W
  Diagnostics etc (~10k$/m x 49m) ~0.5M$
Total - tunnel & RT section ~55.6 M$
Normal Conducting

## Slide 11: Multi-gap RT Approach
Following from
Professor Holger Podlech , Goethe Universitat

## Slide 12: Prof. Dr. H. Podlech
208Pb
Energy: 40 MeV/u or higher (e.g. 100 MeV/u)
Current: 0.5 / 0.25 emA (before/after stripping)
Stripping energy: 13 MeV/u (Pb30+ => Pb67+)
Protons
Energy: 130 MeV/u or higher (e.g. 285 MeV/u)
Current: 5emA (before/after stripping)
Other
Duty cycle for RT: 0.5%
Frequency choice will largely be driven by commercial availability of rf drive – following uses 80.5, and 161 MHz
Separate linacs for proton (deuteron) through lower (e.g. <5 MeV/u) energy
  Large Q/A range
  High proton current
Single linac for higher energies
  Multi-gap structures
LINAC Parameters Considered

## Slide 13
Prof. Dr. H. Podlech
Room Temperature Multi-gap Linac
Source
LEBT
RFQ
DTL (IH/CH)
Source
LEBT
RFQ
DTL (CH)
4-10 keV/u
0.4 MeV/u
13 MeV/u
30 keV/u
1.5 MeV/u
5 MeV/u
Stripper/
Charge state separator
DTL (CH)
40 MeV/u (208Pb)
130 MeV/u (proton)
Pb
p

## Slide 14: Prof. Dr. H. Podlech
Likely should be optimized for deuterons
Proton 5 MeV/u Injector
RFQ
f=161 MHz
L≈3 m
P≈130 kW
30 keV/u
1.5 MeV/u
5 MeV/u
Magnetic triplet
P(kW) ≈ 250
L (m) ≈ 1.0
f(MHz)= 161
RFQ
CH-1
MEBT

## Slide 15: Prof. Dr. H. Podlech
Pb30+ 5 MeV/u Injector
RFQ
RFQ
f=80.5 MHz
L≈3.5 m
P≈100 kW
CH-1
4-10 keV/u
0.4 MeV/u
MEBT
1.8 MeV/u
4 MeV/u
5 MeV/u
3 MeV/u
Magnetic triplet
P(kW) ≈ 300 250 250 250
L (m) ≈ 2.4 2 2 2
f(MHz)= 80.5 80.5 80.5 80.5
IH-1
IH-2
IH-4
IH-3

## Slide 16: Prof. Dr. H. Podlech
Linac – 2nd Half
5 MeV/u
Magnetic doublet or triplet – between every 2 to 4 Cavities
4 x CH-T1
7 x CH-T2
9 x CH-T3
12 x CH-T4
40 MeV/u (208Pb)
130 MeV/u (proton)
L (m) ≈ 0.9 0.65 0.78 0.92
f(MHz) = 161 161 161 161
l_opt = 0.184 0.225 0.274 0.35
# cells = 5 3 3 3
P(kW) ≈ 550 500 650 880
Ea (MV/m) cos j incl ≈ 5

## Slide 17: Prof. Dr. H. Podlech
Preliminary Costing
Hardware estimates - no manpower & contingency => estimates doubled to approximate
Proton 5 MeV/u Injector Hardware ~ 5M$
Pb 5 MeV/u Injector Hardware ~ 39M$
Remainder (>5 MeV/u) of Linac Costs
To be compared to SRF & RT 2-gap
Linac tunnel - 35$k/m x 58 m ~ $2M
Hardware ~ 62.4M$
  (2/3rd of cost is rf)
  Could be as low as ~50M$ (rf costs ±25%) OR similar to 2-gap
Total tunnel & hardware ~ 64.4M$

## Slide 18: Summary & Next Steps
Technology Choice
Both RT & SRF can deliver performance
Key decision metric is cost
SRF/RT 2-gap/RT multi-gap/ => ~28M$/~56M$/~64M$
RT is about 2x cost of SRF largely due to rf costs
Costing rough but ratio (RT to SRF) large enough to conclude
SRF (with RT front end) is preferred Solution
Next Steps
Final design awaits requirement specification from Booster analyses but start to:
Develop detailed RT front end design
  Large Q/A range for H- [1] to D+ [0.5] to 208Pb30+ [0.14]
    Possibly require two independent front ends through ~few MeV/u
Develop detailed SRF linac
  Develop choice of for RT to SRF transition point
  Stripping point for heavy ions
  Optimization of cavity choices (QWR/HWR, frequency, β_opt, etc)