## Slide 1: Data-Driven Machine Retuning
2016 StayTreat

## Slide 2: Run Until It Breaks (or Cries)
The operations paradigm at CEBAF seems to be (mostly) “Run Until It Breaks”
  A reasonable reactive paradigm for repairs
  Preventive maintenance occurs during SADs or opportunistically behind failures
  History: CEBAF used to be scheduled preventive maintenance
Corresponding optics paradigm: “Run Until They Cry”
  Users tasked with monitoring beam quality after setup
  No tuning until:
    Scheduled configuration change
    Hardware (or beam studies) breaks
    Users cry topic of this discussion
    Terry will cover tune time tracking in DTM

## Slide 3: Run Until They Cry
Is it the right paradigm for optics tuning?
Pros:
  Gives priority hall control over program
  Potentially long intervals between tuning
  Great (?) beam after aggressive tuning
Cons:
  Optics adopts a reactive stance
  Retuning mentality: “fix everything while we’re here”
    Possibly longer tune time when it occurs
    Retune usually a change that improves symptom
    Harder to identify root causes
  Users remember when they cry too much

## Slide 4: Daily Invasive Measurements
We currently (sometimes) perform some daily invasive optics measurements
  Daily QE measurements
  Daily fopts
    Useful to detect gross beam transport changes after 1S (but not injector)
    See next page for plot of fopt frequency
    Suggests that we did not do enough systematic tuning during January restoration
Routine fopts are probably not be cost-effective
  Can easily (even often) be degenerate
  Not precise enough to drive small optics changes
  Benefit: tracking medium-term dispersion

## Slide 5: Frequency of fopts
1/day
Winter SAD
Tuning
Tuning
End 12 GeV Run
Apr 5-7 restoration
Nov 9 restoration
Late Jan restoration
More than 1/day
PRad setup

## Slide 6: (Random) Degenerate fopt
SE A R L S E A R L S E A R L S E A
SE A R L S E A R L S E A R L S E A
Degenerate
Degenerate

## Slide 7: Daily Invasive Measurements: Profiles
Cost/benefit of daily beam profile data collection?
  Viewers: not precise enough
    Also not amenable to automated capture/analysis
  SLMs: archivable, parasitic at certain locations
    Need to be treated analytically: priority?
  Daily fast harp scans (3-5 mm/s) may be cost effective in finding/characterizing small drifts
    particularly correlated with fopt/rayTrace
    simple to automate: ~45s/harp of tune beam
  Routine profile measurements give precise tracking of transverse injector beam parameters
    Reinstitute 0L07-10 emittance measurements?

## Slide 8: Daily Invasive Measurements: rayTrace
Cost/benefit of daily rayTrace instead of fopt?
  Avoids fopt degeneracy
  With tool development, data acquisition time is about the same
    Analysis tools are being resurrected/developed
    Large potential to benefit startup/config change
  Potentially precise enough to
    drive fine retuning
    localize/identify drifting magnet power supplies
    characterize complete transport stability

## Slide 9: Issues and Open Questions
We are tasked with improving accelerator reliability
  How do we minimize “crying users” tune time?
Is the current “fix it when they cry” paradigm right?
Can daily/routine optics measurements and improved routine analysis catch optics problems before they are big enough to make users cry?
  If so, can we learn root causes well enough to fix them quickly (even routinely)?
  Can this also provide input to priorities in preventive maintenance?
  Can we raise priority of analyzed SLM data?
  Are routine rayTrace and/or harp scans cost-effective?