## Slide 1: C100 Activation Status and Projections JLab Ops Staytreat 2016
P. Degtiarenko, D. Hamlette, G. Kharashvili, V. Vylet, K. Welch, M. Washington
Radiation Control Department
Notes: Title Page

## Slide 2: concerns related to field emitted radiation
Activation:
  ALARA
  Complicates machine maintenance and other work in the affected areas
  Future accelerators
  Decommissioning
Radiation damage:
  Material degradation
  Damage to semiconductor electronics
JLab Ops Staytreat, 6/28/2016 Slide 2 of 24
Notes: Interior Page Design 1

## Slide 3: what happens to field emitted electrons
Low energy electrons below photonuclear reaction thresholds
Electrons capable of accelerating up to the full gradient
Iris
Electromagnetic cascade
҉
JLab Ops Staytreat, 6/28/2016 Slide 3 of 24
In C100s cascade can propagate from cavity to cavity
Notes: Interior Page Design 1

## Slide 4: C100
JLab Ops Staytreat, 6/28/2016 Slide 4 of 24
Notes: Interior Page Design 1

## Slide 5: 1L24 GRADIENTS JAN-APR 2016
Survey results:
  20 mrem/h at 30 cm ~1h after the end of the run
  6.3 mrem/h at 30 cm ~2 weeks after the end of run
JLab Ops Staytreat, 6/28/2016 Slide 5 of 24
99 MeV
94 MeV
Notes: Interior Page Design 1

## Slide 6: ALL C100s JAN-APR 2016
Survey results:
  Up to 37 mrem/h at 30 cm after ~1 hour of decay
  Up to 8 mrem/h at 30 cm after ~ 2 weeks of decay
Radiation areas (> 5 mrem/h) persisted for days and in some cases - weeks
JLab Ops Staytreat, 6/28/2016 Slide 6 of 24
Notes: Interior Page Design 1

## Slide 7: typical gamma spectrum near activated c100 cm
51Cr – 28 d
57Co – 271 d
58Co – 71 d
511 keV
54Mn – 312 d
56Co - 77 d
92mNb – 10.15 d
56Co - 77 d
56Co - 77 d
Other notable nuclides:
60Co – 5.27 y
57Ni – 35.6 h
56Ni – 6.1 d
52Mn – 5.6 d
24Na – 15 h
55Co – 17.5 h
48V – 16 d
44mSc – 58.6 h
JLab Ops Staytreat, 6/28/2016 Slide 7 of 24
Notes: Interior Page Design 1

## Slide 8: dose rates after 3-4 months of running
Chart: Dose rates after 1 hour, 8 hours, 2 days, 1 week, 4 weeks, and 8 weeks of decay Calculated rates are normalized to dose rates at 1L24 - 20 mrem/h after 1 hour decay
| 0.0416666666666667 | 0.333333333333333 | 2.0 | 7.0 | 28.0 | 56.0
Calculated | 19.9917 | 17.9898 | 14.2992 | 10.6679 | 7.676 | 5.9339
Measured 1L24 | 20 | 6.3
JLab Ops Staytreat, 6/28/2016 Slide 8 of 24
Notes: Interior Page Design 1

## Slide 9: 5 year projections
Chart: Time (months)
| 4.00136892539357 | 10.00136892539357 | 16.00136892539357 | 22.00136892539357 | 28.00136892539357 | 34.00136892539354 | 40.00136892539354 | 46.00136892539354 | 52.00136892539354 | 58.00136892539354
1 hour | 19.9917 | 22.8376 | 24.2902 | 25.1728 | 25.7465 | 26.1239 | 26.3756 | 26.544 | 26.655 | 26.7309
8 hour | 17.9898 | 20.8318 | 22.2825 | 23.167 | 23.7388 | 24.1163 | 24.3679 | 24.5345 | 24.6473 | 24.7232
48 hour | 14.2992 | 17.1193 | 18.5632 | 19.444 | 20.0121 | 20.3896 | 20.6394 | 20.8059 | 20.9188 | 20.9946
1 week | 10.6679 | 13.4256 | 14.848 | 15.7169 | 16.2802 | 16.6523 | 16.8997 | 17.0651 | 17.176 | 17.2504
4 week | 7.676 | 10.1937 | 11.5302 | 12.3553 | 12.8919 | 13.247 | 13.4833 | 13.6411 | 13.747 | 13.8182
8 week | 5.9339 | 8.1804 | 9.4141 | 10.185 | 10.6883 | 11.0217 | 11.2438 | 11.3922 | 11.4917 | 11.5589
RF ON/OFF | 5 | 5 | 0 | 0 | 5 | 5 | 0 | 0 | 5 | 5 | 0 | 0 | 5 | 5 | 0 | 0 | 5 | 5 | 0 | 0 | 5 | 5 | 0 | 0 | 5 | 5 | 0 | 0 | 5 | 5 | 0 | 0 | 5 | 5 | 0 | 0 | 5 | 5 | 0 | 0
Decay times:
RF: 4 months ON, 2 months OFF, 4 months ON, 2 months OFF, …
JLab Ops Staytreat, 6/28/2016 Slide 9 of 24
Notes: Interior Page Design 1

## Slide 10: projection of activation over next 5 years
If C100 field emissions remain at current levels, during the next 5 years:
  Short-term (< 2 days) dose rates will increase by ~30%
  Long-term (weeks) dose rates will increase by ~ factor of 2
All C100 zones are subject to becoming radiation areas on permanent basis
No high radiation areas are anticipated due to the field-emissions at current levels
JLab Ops Staytreat, 6/28/2016 Slide 10 of 24
Notes: Interior Page Design 1

## Slide 11: radiation damage
JLab Ops Staytreat, 6/28/2016 Slide 11 of 24
1E1 1E2 1E3 1E4 1E5 1E6 1E7 1E8 1E9 1E10 1E11 Gy
1E12 1E13 1E14 1E15 1E16 1E17 1E18 1E19 1E20 1E21 1E22 n/cm2
!!! Assumption !!! (depends on particle energy spectra) 1 neutron (1MeV) /cm2 ~ 3.3E-11 Gy
- no damage
- mild to severe damage
- destruction
Dose & Displacement Damage
Radiation Damage to Materials/Electronics
commercial COTS hardened electronics
accelerators
Semiconductors
Polymers
Ceramics
Metals and alloys
© Lockheed Martin
!!! A Rough Overview Only !!!
Notes: Interior Page Design 1

## Slide 12: high range passive dosimetry– march-april 2016
JLab Ops Staytreat, 6/28/2016 Slide 12 of 24
1L24 – 1L25 and 2L23 – 2L24 were monitored
Notes: Interior Page Design 1

## Slide 13
Location | 1L25 Dose (krad) | 1L25 Avg dose rate (rad/h) | 2L24 Dose (krad) | 2L24 Avg dose rate (rad/h)
C1 | 184 | 263 | 259 | 372
C3 | 202 | 288 | 290 | 416
C4 | 144 | 205 | 169 | 242
C6 | 172 | 246 | 274 | 394
C7 | 124 | 177 | 270 | 388
C9 | 146 | 209 | 299 | 430
C11 | 142 | 203 | 206 | 296
C12 | 142 | 203 | 209 | 300
C1
C7
C9
C11
C3
C4
C6
C12
Detector placement around C100 CM
JLab Ops Staytreat, 6/28/2016 Slide 13 of 24
Notes: Interior Page Design 1

## Slide 14
Location | Dose (krad)** | Avg dose rate (rad/h)
1L24 - B1 | 10,000 | 14,000
1L24 - B2 | 3532 | 5000
1L24 - B3 | 2916 | 4166
1L24 - B4 | 3614 | 5163
2L23 - B1 | 3243 | 4659
2L23 - B2 | 3123 | 4487
2L23 - B3 | 2334 | 3353
2L23 - B4 | 2961 | 4254
B1
B2
B3
B4
**All doses are above the range of the device
Detector placement around Beamline
JLab Ops Staytreat, 6/28/2016 Slide 14 of 24
Notes: Interior Page Design 1

## Slide 15: radiation damage
JLab Ops Staytreat, 6/28/2016 Slide 15 of 24
1E1 1E2 1E3 1E4 1E5 1E6 1E7 1E8 1E9 1E10 1E11 Gy
1E12 1E13 1E14 1E15 1E16 1E17 1E18 1E19 1E20 1E21 1E22 n/cm2
!!! Assumption !!! (depends on particle energy spectra) 1 neutron (1MeV) /cm2 ~ 3.3E-11 Gy
- no damage
- mild to severe damage
- destruction
commercial COTS hardened electronics
accelerators
Semiconductors
Polymers
Ceramics
Metals and alloys
© Lockheed Martin
10 Y
1 Y
5 Y
8 months per year @ 300 rad/h
Notes: Interior Page Design 1

## Slide 16: radiation damage
JLab Ops Staytreat, 6/28/2016 Slide 16 of 24
1E1 1E2 1E3 1E4 1E5 1E6 1E7 1E8 1E9 1E10 1E11 Gy
1E12 1E13 1E14 1E15 1E16 1E17 1E18 1E19 1E20 1E21 1E22 n/cm2
!!! Assumption !!! (depends on particle energy spectra) 1 neutron (1MeV) /cm2 ~ 3.3E-11 Gy
- no damage
- mild to severe damage
- destruction
commercial COTS hardened electronics
accelerators
Semiconductors
Polymers
Ceramics
Metals and alloys
© Lockheed Martin
10 Y
1 Y
5 Y
8 months per year @ 4000 rad/h
Notes: Interior Page Design 1

## Slide 17: damage projections in adhesives – c100 circumference
Source: CERN Rad. Damage Report, 2001 F. Guarino, C. Hauviller, M. Tavlet
10 Y
1 Y
5 Y
JLab Ops Staytreat, 6/28/2016 Slide 17 of 24
Notes: Interior Page Design 1

## Slide 18: damage projections in adhesives – warm regions between c100s
Source: CERN Rad. Damage Report, 2001 F. Guarino, C. Hauviller, M. Tavlet
10 Y
1 Y
5 Y
JLab Ops Staytreat, 6/28/2016 Slide 18 of 24
Notes: Interior Page Design 1

## Slide 19
Source: CERN Rad. Damage Data, 1982
10 Y
1 Y
5 Y
JLab Ops Staytreat, 6/28/2016 Slide 19 of 24
damage projections in materials – at C100 circumference
note that mylar superinsulation is almost certainly exposed to higher dose rates
Notes: Interior Page Design 1

## Slide 20: damaged db magnet – picture from david gelhaar
JLab Ops Staytreat, 6/28/2016 Slide 20 of 24
Notes: Interior Page Design 1

## Slide 21: active radiation monitoring around c100 cryomodules - g, n
Dose rates observed at 1 ft : ~100 rad/h g, ~10 rem/h n
JLab standard CARM probes do not survive for long
Need for radiation-hard Ionization Chambers with remote front-end and DAQ electronics, using long cables
Typical neutron proportional counters won’t work: long cables, high rates, sensitivity to gammas
Need for neutron-sensitive Ion chambers
Decline of sensitivity
Failure
Failure
Gammas
Neutrons
Probe #1
#2
JLab Ops Staytreat, 6/28/2016 Slide 21 of 24
Notes: Interior Page Design 1

## Slide 22
LND 50413 10Boron-lined IC: too big (18x40 cm), expensive
Other manufacturers?
Propose to use two small LND ICs, filled with 3He and 4He, placed together in a poly moderator, with lead or tungsten shield (1 atm gas)
3He and 4He: ~0.1 pA in 1 rad/h g
3He: ~10 pA in 1 rem/h n field
3He: $950 at 1 atm
4He: $750
Poly cylinder
Poly cylinder
Lead shield
4He
4He
3He
3He
LND 52120
JLab Ops Staytreat, 6/28/2016 Slide 22 of 24
Notes: Interior Page Design 1

## Slide 23: summary
JLab Ops Staytreat, 6/28/2016 Slide 23 of 24
Multiple attempts to monitor activation and dose rates:
  Useful data
  Detector failures due to high radiation fields
Attempts to relate the field emitted radiation to the operating parameters have not been successful
Current RadCon activities:
  Surveys
  Periodic monitoring of activation
  Occasional prompt dose rate measurements
Future continuous gamma and neutron monitoring:
  Gradient team (Bob Legg) is working on deployment of high range ion chambers
  We suggest to find or develop radiation hard neutron monitors
Field emitted radiation and activation should be taken into account in the gradient optimization process
Notes: Interior Page Design 1

## Slide 24: open issues / concerns
JLab Ops Staytreat, 6/28/2016 Slide 24 of 24
Material degradation
Inability to do real time monitoring
Upgrades and design of other machines
Notes: Interior Page Design 1