## Slide 1: Challenges to RHIC Availability
Peter Ingrassia
JLAB Staytreat
28 June 2016.

## Slide 2: Collider-Accelerator Department
TANDEMS
e-Lens
CeCPoP
polarimeter

## Slide 3
diode
dAu

## Slide 4: RHIC -- a “Capable” Hadron Collider
Run(FY) | B species | Y species | Eb [GeV/n] | Ey [GeV/n] |  | Run (FY) | B species | Y species | Eb [GeV/n] | Ey [GeV/n]
16-1 | Au | Au | 100 | 100 |  | 9-1A | p^ | p^ | 249.9 | 249.9
16-2A | d | Au | 101.3 | 99.4 |  | 9-1B | p^ | p^ | 100.2 | 100.2
16-2B | d | Au | 31.3 | 31.1 |  | 9-1C | p^ | p^ | 100.2 | 100.2
16-2C | d | Au | 9.8 | 9.8 |  | 8-1 | d | Au | 100.7 | 100
16-2D | d | Au | 19.6 | 19.4 |  | 8-2 | p^ | p^ | 100.2 | 100.2
15-1 | p^ | p^ | 100.2 | 100.2 |  | 8-3A | Au | Au | 4.6 | 4.6
15-2 | Au | p^ | 103.36 | 97.37 |  | 8-3B | Au | Au | 2.5 | 2.5
15-3 | p^ | Al | 103.36 | 98.64 |  | 7-A | Au | Au | 100 | 100
14-1A | Au | Au | 7.3 | 7.3 |  | 7-B | Au | Au | 4.6 | 4.6
14-1B | Au | Au | 100 | 100 |  | 6-1A | p^ | p^ | 100.2 | 100.2
14-2 | 3He | Au | 103.9 | 100 |  | 6-1B | p^ | p^ | 11.25 | 11.25
13 | p^ | p^ | 254.9 | 254.9 |  | 6-1C | p^ | p^ | 31.2 | 31.2
12-1A | p^ | p^ | 100.2 | 100.2 |  | 6-1D | p^ | p^ | 250 | 250
12-1B | p^ | p^ | 254.9 | 254.9 |  | 5-1A | 63Cu | 63Cu | 100 | 100
12-2 | 238U | 238U | 96.4 | 96.4 |  | 5-1B | 63Cu | 63Cu | 31.2 | 31.2
12-3 | 63Cu | Au | 99.9 | 100 |  | 5-1C | 63Cu | 63Cu | 11.2 | 11.2
12-4 | Au | Au | 2.5 | 2.5 |  | 5-2A | p^ | p^ | 100.2 | 100.2
11-1 | p^ | p^ | 249.9 | 249.9 |  | 5-2B | p^ | p^ | 204.9 | 204.9
11-2A | Au | Au | 9.8 | 9.8 |  | 4-1A | Au | Au | 100 | 100
11-2B | Au | Au | 100 | 100 |  | 4-1B | Au | Au | 31.2 | 31.2
11-2C | Au | Au | 13.5 | 13.5 |  | 4-2 | p^ | p^ | 100.2 | 100.2
10-1A | Au | Au | 100 | 100 |  | 3-1 | d | Au | 100.7 | 100
10-1B | Au | Au | 31.2 | 31.2 |  | 3-2 | p^ | p^ | 100.2 | 100.2
10-1C | Au | Au | 19.5 | 19.5 |  | 2-1A | Au | Au | 100 | 100
10-1D | Au | Au | 3.85 | 3.85 |  | 2-1B | Au | Au | 9.8 | 9.8
10-1E | Au | Au | 5.75 | 5.75 |  | 2-2 | p^ | p^ | 100.2 | 100.2
10-1F | Au | Au | 2.5 | 2.5 |  | 1-1A | Au | Au | 27.9 | 27.9
 |  |  |  |  |  | 1-1B | Au | Au | 65.2 | 65.2
 |  |  |  |  |  | 1-2 | p^ | p^ | 24.3 | 25.1

## Slide 5: This Presentation
Measuring Availability
  Availability arithmetic
  Run16 Availability
  RHIC Availability history from Run-2
Major System Reliability
    Tracking Reliability
    Working with system owners to improve reliability
    MTBF review from Run-7
Specific Issues to reach reliability goals
    Challenge I “Burn in” RHIC PS
  Challenge II Reproducibility
  Challenge III Abort kicker pre-fire
    Experiment protection -- bumps
    fec (front end computer & network switch) resets
  Challenge IV Intensity (Au) related issues
    Cryo PLC location
    Rf – beam loading

## Slide 6: Measuring Availability: DOE Availability Arithmetic
  Availability = (Research + Studies + Tuning/Setup) (Research + Studies + Tuning/Setup + Failure)

## Slide 7: Run16 availability 82.7%
Chart: 
| FY16-week 14: | FY16-week 15: | FY16-week 16: | FY16-week 17: | FY16-week 18: | FY16-week 19: | FY16-week 20: | FY16-week 21: | FY16-week 22: | FY16-week 23: | FY16-week 24: | FY16-week 25: | FY16-week 27: | FY16-week 28: | FY16-week 29: | FY16-week 30: | FY16-week 31: | FY16-week 32: | FY16-week 33: | FY16-week 34: | FY16-week 35: | FY16-week 36: | FY16-week 37: | FY16-week 38: | FY16-week 39:
availability | 0.93787 | 0.62504 | 0.74663 | 0.74946 | 0.84474 | 0.79042 | 0.90897 | 0.84153 | 0.37713 | 0.84444 | 0.8668 | 0.94315 | 0.79724 | 0.77536 | 0.8593 | 0.91143 | 0.91821 | 0.82889 | 0.90708 | 0.86101

## Slide 8: RHIC Availability History
Chart: 
| Run2 | Run3 | Run4 | Run5 | Run6 | Run7 | Run8 | Run9 | Run10 | Run11 | Run12 | Run13 | Run14 | Run15 | Run16
RHIC Availability by Run[%] | 0.825 | 0.779 | 0.801 | 0.847 | 0.802 | 0.698 | 0.833 | 0.803 | 0.829 | 0.763 | 0.854 | 0.837 | 0.868 | 0.879 | 0.827

## Slide 9: Systems Reliability
Tracking Reliability
  Operators make entries for each failure or state change to a database using OpLog application.
  Component level failures not recorded by operators – determination by the equipment owners.
  Oplog is used to generate reports of failure statistics
  All the charts in this talk use data from Oplog reports

## Slide 10: Working with system owners to improve reliability.
At the weekly “Time Meeting” availability and equipment reliability data are shown.
Daily “RHIC” meetings review significant faults for previous 24/48 hours.
Reliability Improvement by Embarrassment!
Dirty laundry is aired – no group wants to be cited.
Repeat offenders cannot hide.
System owners are proactive maintain high reliability rates with little prodding from management.

## Slide 11: RHIC + Injectors MTBF, MTTR, <Failure hours/da>
Chart: Hours (h)
| Run7 | Run8 | Run9 | Run10 | Run11 | Run12 | Run13 | Run14 | Run15 | Run16
MTBF (h) | 5.59 | 6.33 | 5.66 | 5.47 | 5.69 | 7.12 | 6.56 | 8.68 | 9.04 | 6.18
MTTR (h) | 1.98 | 1.21 | 1.29 | 1.04 | 1.24 | 1.09 | 1.23 | 1.31 | 1.14 | 1.38
<Failure h/da> | 6.3 | 3.8222 | 4.4171 | 3.6786 | 4.4588 | 3.1829 | 3.6929 | 3.026 | 3.1494 | 3.1544

## Slide 12: “Burn In”
Ken Baggett …’talk to how things may have changed after start up (i.e. was there a "burn in" period required before your availability hit a steady state)’.
Chart: RHIC Availability by Run[%]
| Run2 | Run3 | Run4 | Run5 | Run6 | Run7 | Run8 | Run9 | Run10 | Run11 | Run12 | Run13 | Run14 | Run15 | Run16
RHIC Availability by Run[%] | 0.825 | 0.779 | 0.801 | 0.847 | 0.802 | 0.698 | 0.833 | 0.803 | 0.829 | 0.763 | 0.854 | 0.837 | 0.868 | 0.879 | 0.827

## Slide 13: “Burn In” – Experiments trend in the wrong direction
Experiments are embedded in the lattice.
Evolved such that they are more complex and able to make measurements of greater precision.
Si components more sensitive to damage.
Run 16 CeCPoP
Chart: RHIC Experiment failure % of Scheduled Ops
| 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Experiments | 0.0036 | 0.0068754 | 0.0047451 | 0.0061323 | 0.012115 | 0.0068785 | 0.0097367 | 0.0093
#Species*#Energies | 2 | 12 | 3 | 6 | 8 | 20 | 1 | 6 | 9 | 10

## Slide 14: Challenge I -- RHIC Power Supplies
Supplies from vendors needed engineered improvements
“Off Trips”
Voltage Drop outs
Soft start circuit
  Doubled FET resistors
  Replaced FET fuses
  One PC board replacing 3 PC boards
Chart: RHIC Power Supply Failure % of Scheduled Ops
| 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16
PS_RHIC | 0.0639 | 0.024534 | 0.041589 | 0.026161 | 0.035143 | 0.02504 | 0.018504 | 0.019089 | 0.01565 | 0.0235
#Species*#Energies | 2 | 12 | 3 | 6 | 8 | 20 | 1 | 6 | 9 | 10

## Slide 15: “Burn In” -- RHIC Power Supplies
IR focus and steering
trim dipoles, sextupoles, octupoles etc.

## Slide 16: Challenge II – Reproducibility BLM Interlocks & Human Error
“Feedbacks”
    Tune/Coupling
    Orbit
  Made the RHIC more reproducible
  Reduced Tuning/Setup times
  Reduced number of failed ramp attempts
Chart: Rad Monitor Interlocks % of Scheduled Ops
| 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16
RadMonIntlk | 0.0041 | 0.0062103 | 0.017325 | 0.014694 | 0.0139 | 0.0058989 | 0.0094661 | 0.0005 | 0.0069153 | 0.0082
#Species*#Energies | 2 | 12 | 3 | 6 | 8 | 20 | 1 | 6 | 9 | 10
Chart: Human Error % of Scheduled Ops
| 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16
HumanError | 0.0079 | 0.016408 | 0.010188 | 0.014303 | 0.010431 | 0.014168 | 0.012613 | 0.0071595 | 0.005302 | 0.0072
#Species*#Energies | 2 | 12 | 3 | 6 | 8 | 20 | 1 | 6 | 9 | 10

## Slide 17: Challenge II – Reproducibility Controls
Controls plays a large role with regard to reproducibility.
Controls systems reliability is very good.
Controls (hardware) challenged by intensity issues (more in Challenge III)
Chart: Controls Failures % of Scheduled Ops
| 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Cntrls Hdwr RHIC | 0.009 | 0.0057322 | 0.0046263 | 0.0091796 | 0.0052866 | 0.0064
#Species*#Energies | 2 | 12 | 3 | 6 | 8 | 20 | 1 | 6 | 9 | 10

## Slide 18: Challenge III – Pulsed Power Abort Kicker Pre-Fire
Abort Kicker Pre-fire
  Power Supply charged (armed) for HOURS.
    21kA @ 33 kV
  Purpose to abort beam to protect RHIC (MPS) or prior to a re-fill
  Spontaneous discharge at the wrong time has caused damage to experiment detectors.
 |  |  | Summary of Abort Kicker Pre-Fire |  |  |  | <15/yr> |  | KAD | 
Ring | FY08 | FY09 | FY10 | FY11 | FY12 | FY13 | FY14 | FY15 | FY16 | Totals
Blue | 2 | 11 | 12 | 9 | 2 | 8 | 6 | 1 | 9 | 60
Yellow | 2 | 2 | 8 | 15 | 8 | 14 | 12 | 7 | 4 | 72
Chart: RHIC Pulsed Power Failures % of Scheduled Ops
| 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16
PPS_RHIC | 0.0173 | 0.0050909 | 0.0057183 | 0.0074398 | 0.010987 | 0.0048041 | 0.0087836 | 0.011285 | 0.005142 | 0.0062
#Species*#Energies | 2 | 12 | 3 | 6 | 8 | 20 | 1 | 6 | 9 | 10

## Slide 19: WHY PROTECTION BUMPS? PHENIX RUN15 MPC Damage
19050
May 11
Damaged South
Impacted North
19116/18
May 28
We got lucky
No addt’l damage
19134
June 1
The end of the MPC in Run 15
South
North
Store
Matin L. Purschke

## Slide 20: Abort Kicker Pre-fire Protection Bump
Bump generated in 11 o’clock arc pushes orbit to -21mm. In a pre-fire condition bunches kicked by the pre-firing module will crash into the cryostat at that location, preventing damage to the experiments. In 1 o’clock arc is a compensation bump to adjust for off-center orbit in quads and sextupoles in the pre-fire bump.
Chronic losses in the arc are due to Au+78 beam created during collisions and off-momentum particles at the protection bump peak. The peak loss is located at g10-lm20 loss monitor, located just downstream of dipole 19 where the failure occurred

## Slide 21: Cryostat Cut Open
Cryogenic lines
Beam Pipe
End Volume
Containing Diode

## Slide 22: End Volume Cut Open

## Slide 23: Damaged Diode
When a magnet coil is no longer superconducting (beam heating) the diode “turns on” and routes electrical current around the normal conducting magnet in order to protect it.

## Slide 24: “RHIC Alcoves” are a feature -- (3 per sextant) house power supplies, front end computers, network switches, etc.

## Slide 25: Abort Kicker Pre-fire – Controls
Run16
Chronic Losses due to protection bumps
Plagued by trips radiation upsets of FEC memory
Band Aid work around – reset front ends prior to each fill
Top plot before Run16 diode failure

## Slide 26: Abort Kicker Prefire– Controls
Run16
Chronic losses due to protection bumps
Plagued by resets of network switches
Top plot before Run16 diode failure
Bottom plot after peak bump displacement relocated

## Slide 27: Increased circulating beam current
Chart: Au Ions per bunch -- evolution
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Au Ions/bunch | 700000000 | 1100000000 | 1100000000 | 1000000000 | 1100000000 | 1300000000 | 1300000000 | 1600000000 | 1600000000 | 2000000000
# bunches | 55 | 45 | 103 | 95 | 111 | 111 | 111 | 111 | 111 | 111

## Slide 28: Challenge IV Intensity –– Cryogenics
An early challenge
Some Cryogenic Controls were located in alcoves in the tunnel.
Too many radiation related upsets
Moved 66% of controls out of the tunnel.
Migration halted with added workload (ERL, 56MHz, CeC, sPHENIX)
Chart: RHIC Cryogenic Failures % of Scheduled Ops
| 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16
CryoRHIC | 0.0317 | 0.0054101 | 0.0074166 | 0.0077242 | 0.007227 | 0.006181 | 0.014357 | 0.0051
#Species*#Energies | 2 | 12 | 3 | 6 | 8 | 20 | 1 | 6 | 9 | 10

## Slide 29: Cryogenics cryo controls-free alcoves

## Slide 30: Intensity (Au) Effects – RHIC Rf (1)
RHIC Rf -- WARM
Primarily two Systems
B&Y Acceleration 2 each
B&Y Storage 5 each
Others
Landaus
9 MHz (proton ops)
SRF
56 MHz (gold ops)
CeCPoP (2)
Chart: RHIC Rf System Failures % of Scheduled Ops
| 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Rf_RHIC | 0.0222 | 0.011184 | 0.0054661 | 0.0097961 | 0.018702 | 0.0098861 | 0.014116 | 0.013348 | 0.0047944 | 0.0178
#Species*#Energies | 2 | 12 | 3 | 6 | 8 | 20 | 1 | 6 | 9 | 10

## Slide 31: Intensity (Au) Effects – RHIC Rf (2)
Run16
Plagued by trips of storage cavities – beam loading. Improvements did not keep pace with intensity increase.
Group focus was on SRF (56 MHz & CeCPoP 704MHz)
Lost focus – forgot to condition cavities after 19 day diode replacement outage.
Chart: RHIC Rf System Failures % of Scheduled Ops
| 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Rf_RHIC | 0.0222 | 0.011184 | 0.0054661 | 0.0097961 | 0.018702 | 0.0098861 | 0.014116 | 0.013348 | 0.0047944 | 0.0178
#Species*#Energies | 2 | 12 | 3 | 6 | 8 | 20 | 1 | 6 | 9 | 10

## Slide 32: Intensity (Au) Effects – Losses
Au ion losses at injection affected controls (alcove 5A) for power supplies.
Loss of control led to power supply trips and beam loss that caused a hole in a ceramic vacuum chamber associated with one of the injection kickers.
“Leak checking with a flashlight”.

## Slide 33: Issues and Open Questions
Ever Higher per bunch Intensities
  Machine Protection
  Abort Kicker Pre-fire
  Experiment protection
  Rf system and beam loading
Trying to do too many things…
  e.g. Rf & Cryogenic groups focused on SRF for new electron machines.
Electrical Infrastructure – lurking in the background
  AGS electrical feeders are decades old – Run11
    AGS first began operation in 1960