## Slide 1: Magnet Reliability
Joseph Meyers
Magnet Measurement Facility

## Slide 2: Magnet Agenda
Overview of the magnets in tunnel and spares on-hand
Magnet reliability
Notable events
Issues and open questions

## Slide 3: Overview of Magnet Inventory
Magnet Type |  | # In Tunnel | # Magnet Spares | Magnet Spare Comments
Box Supply Powered | DIPOLE | 443 | 12 | 1m(3), 2m(3), 3m(2), 4m(1)
 | SEPTUM | 25 | 8 | YA(1), YB(1), YR(6), ZA(0)
Trim Card Powered | QUAD | 853 | 27 | QA(7), QB(8), QC(8), QP(2), QR(2)
 | CORRECTOR | 1063 | 25 | BC(7), BT(8), BD(2), BM(2), DB(6)

## Slide 4: Overview of Coil Inventory
Magnet Type |  | Spare Coils
DIPOLE | ARC | 1m(~6), 2m(~12), 3m(12), 4m(0)
 | BCOM | 8-turn & 10-turn 1m(~30), trapezoidal-shaped(~10)
 | DOGLEG | BW/BY(8), CW/CV/CX(0)
SEPTUM | THIN | YA(0)
 | THICK | YB(0), YR(2), ZA(1 Right)
82 magnets have new coils
  72 dipoles (16%)
  10 septa (40%)
  386 magnets have original coils
  371 dipoles (84%)
  15 septa (60%)
  Over 82% magnets operate with original coil packs dating back to 1990’s.

## Slide 5: Magnet Agenda
Overview of the magnets in tunnel and spares on-hand
Magnet reliability
Notable events
Issues and open questions

## Slide 6: Magnet Reliability
Type | # of Failures* | R(5 yrs) | R(1o yrs) | MTTR (hrs) | Availability | Estimate # of Failures in 15 yrs**
DIPOLES | 2 | 99.77% | 99.54% | 76.1 | 99.9996% | 3.1
SEPTUMS | 2 | 95.99% | 92.14% | 290.9 | 99.9433% | 3.1
TRIM | 3 | 99.97% | 99.95% | 48.0 | 99.9999% | 1.5
* Data gathered from Downtime Manager (https://accweb.acc.jlab.org/dtm) and ATLis (http://opsweb.acc.jlab.org/CSUEApps/atlis/atlis.php)
** Operating 25 weeks per year

## Slide 7: Magnet Agenda
Overview of the magnets in tunnel and spares on-hand
Magnet reliability
Notable events
Issues and open questions

## Slide 8: Notable Event: MJC5A14 Shorted
Date: 02/09/2016
Cause: Insufficient work planning for in-situ repairs
Downtime: 76.1 hours
Repair: Replaced with spare JC magnet.
Mitigation: MMF technician will QC the magnets following in-situ repairs that require disassembly of any coil connections.
Magnet Reliability JSA Ops 2016 Stay Treat J. Meyers

## Slide 9: Notable Event: MZAAR03 Failure
Date: 04/15/2014
Cause: Magnet design allows debris get between coils and chamber.
Downtime: 245.8 hours
Repair: Replace damaged coil with spare ZA coil.
Mitigation: Added more insulation between coil and chamber. Attached longer coil support plate to prevent the coils from bowing. Caulked areas that would prevent debris from getting near coils.

## Slide 10: Magnet Agenda
Overview of the magnets in tunnel and spares on-hand
Magnet reliability
Notable events
Issues and open questions

## Slide 11: Issues and Open Questions:
Reliability improvements
  Do not exceed design currents.
  Keep LCW on.
    Proactive Action #1: LCW valves clearly labeled and are components of HCO.
    Proactive Action #2: Temperature monitoring with RTD’s on Septas.
  Invest in new coil spares.
Investigating leak at MYR6T02

## Slide 12: MYR6T02 Status
Found coil leak in January 2016.
Last measured in June 2013.
Fixing YR6T02 by replacing damaged coil with spare YR coil.
Investigate the cause of the leak.

## Slide 13
Thank you for your attention.
Many thanks to Randy Michaud, Dr. Ken Baggett, Tommy Hiatt, Sarin Phillip and Mike Beck for your help.