## Slide 1: Electron Cooling Code Development and Simulation Studies
He Zhang, He Huang, Rui Li, Jie Chen, Li-Shi Luo
JLEIC Collaboration Meeting, 10/06/2016
Newport News, VA

## Slide 2
Outline
Two–stage electron cooling scheme for JLEIC
A new electron cooling simulation program
Electron cooling simulation for JLEIC
Particle tracking simulation for electron cooling
Summary

## Slide 3
JLEIC Staged Cooling Scheme
JLEIC ion complex layout
Multi-phased scheme takes advantages of high electron cooling efficiency at low energy and/or small 6D emittance
Low energy DC cooler (Within state-of-art) at the booster:
  Reduce the emittance
  2GeV/u ion beam, 1.6 MeV electron beam
High energy bunched beam cooler (needs R&D) at the collider ring:
  Maintain the emittance
  Up to 100 GeV/u ion beam, 55 MeV electron beam
  ERL single pass cooler (Qe = 420 pC/buncn, baseline design, no circulator ring)
  ERL circulator cooler (Qe = 2 nC/bunch, lower emittance, higher luminosity)

## Slide 4
A New Electron Cooling Simulation Code
Goals:
Fulfill the specific needs for JLEIC electron cooling scheme
Different scenarios: DC cooling, bunched beam cooling
More flexibility, higher efficiency.
Use for electron cooling simulation and further code development
Approaches:
Following the models in BETACOOL whenever applicable
Revise the models whenever needed
Improve the efficiency by strategically arrange the computation
Adaptive to the modern multi-core platform
Formulas and models implemented:
IBS: Martini model (no vertical dispersion lattice)
Friction force: Parkhomchuk formula (magnetized cooling)
Cooling rate: single particle model, Monte Carlo model
Cooling dynamics: Four-step procedure
Other formulas and models can be added in future
Codes and a tutorial are available online:
https://github.com/zhanghe9704/electroncooling

## Slide 5
Electron Cooling Rate
  Single particle model: sample the ion beam with particles with the same dynamic invariant (single particle emittance)
  Sample the ion beam on a regular grid
  Calculate the electron charge density around each ion
  Convert into beam frame
  Calculate the friction force on each ion (Parkhomchuk formula)
  Convert back to lab frame
  Each ion feels a kick as .
  Calculate the new dynamic invariant and thus the emittance for each ion (as in the previous page) and take average on all of them.
  Calculate the cooling rate (the change of emittance in a unit time)

## Slide 6
  Monte Carlo model : sample the ion beam with particles of Gaussian distribution
    Sample the ions as described in the previous page
  Calculate the electron charge density around each ion
  Convert into beam frame
  Calculate the friction force on each ion
  Convert back to lab frame
  Each ion feels a kick as .
    Emittace is calculated statistically as
    Calculate the cooling rate (the change of emittance in a unit time)
Electron Cooling Rate

## Slide 7
Cooling Dynamic
  Four-step procedure:
  Create sample ions
  Calculate the expansion rate under the IBS and/or electron cooling effect
  Update the beam parameters and the sample ions, and
  repeat from the second step till the end time
The RMS dynamic method and the model beam method in BETACOOL fit into this four-step procedure.

## Slide 8
Cooling Dynamic
  RMS dynamic method in the four-step procedure:
  Create sample ions (using the single particle model or Monte Carlo model) w.r.t. the given emittance
  Calculate the expansion rate under the IBS and/or electron cooling effect
  Update the beam parameters using , create new sample ions w.r.t. the new emittance, and
  repeat from the second step till the end time

## Slide 9
Cooling Dynamic
  Model beam method in the four-step procedure:
  Create sample ions with the given initial distribution
  Calculate the IBS rate and/or the friction force.
  Apply the IBS kick on each particle as
  , ,
  Gaussian random number ; apply the electron cooling kick as
  ;
  apply a random phase advance for each particle; calculate new emittance and expansion rate; and
  4. repeat from the second step till the end time.

## Slide 10
Benchmark with BETACOOL
Thoroughly benchmarked with BETACOOL (a few examples below)
RMS dynamic
Single particle
RMS dynamic
Monte Carlo
Model beam
Model beam

## Slide 11
Benchmark
DC cooling and IBS for JLEIC booster ring with KE = 800 MeV
Time cost 133 s (BETACOOL 3060 s)
Bunched cooling and IBS for JLEIC collider ring with KE = 100 GeV
Time cost 30.7 s (BETACOOL 422 s)

## Slide 12
Good efficiency of the serial code, so not necessary to run the code on a cluster machine.
Further improve the efficiency for shared memory structure hardware: GPU, Intel Xeon Phi, or just a multi-core PC.
Parallelization is based on thrust, a parallel algorithm library that supports CUDA, TBB (Threading Building Blocks) and OpenMP.
IBS calculation, 100100100 grid:
NVidia GTX 660 ti GPU: 7.76 s
CPU AMD Phenom™ II X4 840T Processor 2.9GHz: 62 s
Electron cooling
200,000 samples: GPU 0.03 s CPU 0.151 s
40,000 samples: GPU 0.024 s CPU 0.023 s
Parallelization

## Slide 13
DC Cooling at the Booster
Proton beam:
KE = 2 GeV
Emit = 2.15 mm mrad
dp/p = 0.001
N = 2.8E12
Electron beam:
I = 2 A
Ttr = 0.1 eV, Ts = 0.1 eV
DC cooler:
L = 10 m
B = 1 T
 |  | IBS | ECOOL | IBS+ECOOL
RH | 1/s | 3.86E-4 | -9.05E-3 | -9.10E-3
RV | 1/s | 3.86E-4 | -9.00E-3 | -8.71E-3
RL | 1/s | 2.27E-4 | -15.3E-3 | -15.3E-3

## Slide 14
Strong Cooling at the Collider Ring (Qe = 2 nC)
Proton beam:
KE = 30/60/100 GeV
Emit = 0.45/0.35/0.35 mrad
dp/p = 5/4/4
= 2.5/2.75/2.75 cm
N = 6.56E9
Electron beam:
Qe = 2 nC
Ttr = 0.5 eV, Ts = 0.1 eV
Bunched cooler:
L = 302 m
B = 1 T
 |  | IBS | ECOOL
RH | 1/s | 4.74E-3 | -8.05E-3
RV | 1/s | -1.59E-5 | -8.05E-3
RL | 1/s | 2.10E-3 | -1.31E-2
KEp=30 GeV

## Slide 15
Strong Cooling at the Collider Ring (Qe = 2 nC)
 |  | IBS | ECOOL |  | IBS | ECOOL
RH | 1/s | 6.21E-3 | -3.78E-3 |  | 4.43E-3 | -2.65E-3
RV | 1/s | -4.08E-5 | -3.75E-3 |  | -1.53E-5 | -2.60E-3
RL | 1/s | 2.00E-3 | -8.65E-3 |  | 0.97E-3 | -7.29E-3
KEp=60 GeV
KEp=100 GeV

## Slide 16
Weak Cooling at the Collider Ring (Qe = 420 pC)
Proton beam:
KE = 100 GeV
Emit_x = 1.2 mrad
Emit_y = 0.6 mrad
= 2.5 cm
N = 6.56E9
Electron beam:
Q = 420 pC
Ttr = 0.5 eV, Ts = 0.1 eV
= 0.035 cm
= 0.84 cm
Bunched cooler:
L = 60 m
B = 1 T
Lower electron beam current, within the state-of-art technique.
Electron bunch smaller than the proton bunch.
Higher proton beam emittance, lower IBS.
Larger proton beam momentum spread.
Horizontal expansion rate decreases as dp/p increases, with = 2.5 cm |  |  |  |  |  |  |  |  | 
dp/p (1E-4) | 5 |  |  | 8 |  |  | 12 |  | 
IBS (1E-4 1/s) | 5.03 | 0 | 2.26 | 3.39 | 0.01 | 0.63 | 2.35 | 0.01 | 0.20
Cool (1E-4 1/s) | -1.01 | -1.40 | -4.14 | -0.85 | -1.25 | -2.45 | -0.71 | -0.98 | -1.34
Total (1E-4 1/s) | 4.02 | -1.40 | -2.10 | 2.54 | -1.24 | -1.82 | 1.64 | -0.97 | -1.14
dp/p (1E-4) | 5 |  |  | 8 |  |  | 12 |  | 
IBS (1E-4 1/s) | 5.03 | 0 | 2.26 | 3.39 | 0.01 | 0.63 | 2.35 | 0.01 | 0.20
Cool (1E-4 1/s) | -1.01 | -1.40 | -4.14 | -0.85 | -1.25 | -2.45 | -0.71 | -0.98 | -1.34
Total (1E-4 1/s) | 4.02 | -1.40 | -2.10 | 2.54 | -1.24 | -1.82 | 1.64 | -0.97 | -1.14
Proton beam: Parkhomchuk formula

## Slide 17
Weak Cooling at the Collider Ring (Qe = 420 pC)
dp/p=8E-4
dp/p=1.2E-3
1.5h
2.8h
time to double
dp/p=1.2E-3
Np = 4.4E9
Lower proton beam current or 20% transverse coupling
6.6h
4.0h
dp/p=1.2E-3

## Slide 18
Issues with Bunched Beam Cooling
Cooling with correlated electron beam
The momentum of the electron is correlated with its longitudinal position, modeled as
Friction force is calculated in the electron beam frame. Ions got a various velocity shift according to their positions.
 |  | Non-correlated |  |  | Correlated |  | 
 | eV |  |  |  |  |  | 
1 | 0.00511 | 1.59 | 1.59 | 1.66 | 1.60 | 1.60 | 1.60
2 | 0.02044 | 1.54 | 1.54 | 1.50 | 1.53 | 1.53 | 1.30
3 | 0.04599 | 1.48 | 1.48 | 1.34 | 1.43 | 1.43 | 1.02
4 | 0.08176 | 1.41 | 1.41 | 1.19 | 1.33 | 1.33 | 0.79
5 | 0.12775 | 1.34 | 1.34 | 1.06 | 1.23 | 1.23 | 0.61
 |  | Non-correlated |  |  | Correlated |  | 
 | eV |  |  |  |  |  | 
1 | 0.00511 | 1.59 | 1.59 | 1.66 | 1.60 | 1.60 | 1.60
2 | 0.02044 | 1.54 | 1.54 | 1.50 | 1.53 | 1.53 | 1.30
3 | 0.04599 | 1.48 | 1.48 | 1.34 | 1.43 | 1.43 | 1.02
4 | 0.08176 | 1.41 | 1.41 | 1.19 | 1.33 | 1.33 | 0.79
5 | 0.12775 | 1.34 | 1.34 | 1.06 | 1.23 | 1.23 | 0.61
Assume .

## Slide 19
Issues with Bunched Beam Cooling
Cooling rate vs. electron bunch size
Electron number per bunch is limited by the capacity of the cathode and the instability during transport
Two competing parameters affect the cooling rate: how many ions covered by the electron bunch & local electron density around an ion.
Calculate cooling rate for Gaussian ion bunch with cylindrical electron bunch of various sizes.
Best cooling rate at .

## Slide 20
Issues with Bunched Beam Cooling
Cooling rate vs Larmor emittance
Magnetic electron beam
Drift emittance , relates to the transverse bunch size
Larmor emittance , relates to the transverse temperature
Important parameter for cooler and electron source design

## Slide 21
Initial distribution
10,000 turn
20,000 turn
40,000 turn
80,000 turn
Turn by Turn Simulation

## Slide 22
Particle Tracking Simulation (in progress)
Simulate the motion of ions and electrons inside the cooler based on the first principles.
Focus on the interactions between individual particles.
Single pass, not the whole cooling process.
Friction force calculation.
Fast multipole method for Coulomb interaction using Cartesian tensor.
Fast multipole method for other non-oscillating interaction.
MPI based parallel integrators: (RK4 and Hermite)
Linear scale with particle number
Order | Relative error
2 | 
4 | 
6 | 
8 | 
10 | 
Order | Relative error
2 | 
4 | 
6 | 
8 | 
10 | 

## Slide 23
Summary
A new electron cooling and IBS effect simulation program has been developed. Code available on online
Benchmarked with BETACOOL.
Significant improvement in efficiency, which brings the possibility for more sophisticated physical model or algorithm
Actively implemented in JLEIC electron cooling simulations
Lowe energy DC cooling is within the state of art.
Bunched beam cooling at the collision energy is challenging, but possible.
A particle tracking program is in development