## Slide 1: Progress report on PIC simulations of a neutralized electron beam
James Gerity, Texas A&M University
Presented at JLEIC Fall collaboration meeting October 6, 2016
Slides available at http://www.github.com/jgerity/talks

## Slide 2: Electron cooling
Coulomb collision with ‘cold’ electrons drives velocity profiles to equilibrium
Effect is enhanced by magnetization
Ion beam seen from stationary (lab) frame
Ion beam seen from moving frame, with electrons

## Slide 3: Motivation
Bunched cooling is desirable to control IBS
  Many challenging R&D tasks are involved!
Conventional cooling is part of the baseline
  Any improvements to cooling would be beneficial
RadiaSoft and TAMU collaboration

## Slide 4: Cooling + stacking ring
Previously proposed: integrate a dedicated ring for cooling + stacking in the existing cryostat layout
Common cryostat
Collision ring
Cooling ring

## Slide 5: Space charge drift limit
With strong magnetization and high current, interaction causes beam to twist azimuthally
Effective heating  cooling limit

## Slide 6: Fermilab experiments (neutralization)
Initial cooling experiments at Fermilab included ionization of residual gas
  Magnetized beam at 1 kG
Space charge compensation also allowed for low-power collection of electrons

## Slide 7: Particle-in-cell (PIC) simulation
We have chosen to use the Warp PIC library for this work
  Python interface allows rapid simulation development, analysis
  No speed compromise, heavy lifting done in Fortran

## Slide 8
Slide courtesy of J.L. Vay from https://people.nscl.msu.edu/~lund/uspas/scs_2016/

## Slide 9: Misc. development
Tools for working with Warp:
  Extracting particle data from HDF5 files, converting velocities to angles, etc.
  Ionization class extension, allowing arbitrary emission energies
  Diagnostic output of fields/particles according to OpenPMD specification for offline analysis

## Slide 10: Simulation parameters
116 keV electron beam, 10 mA
1 meter drift as domain
Background H2 gas with realistic ionization cross-section
  In this work, density chosen to observe compensation reasonably quickly
Available on GitHub
  https://github.com/radiasoft/rscooler/

## Slide 14: Field suppression at center of beam

## Slide 15: Further work
Scale up current, aiming for ~ Ampere
  Use of NERSC likely
Replicate Fermilab beam properties
  “Electron wind” instability
Quantify dynamic friction for use in long-term study

## Slide 16: Thank you!

## Slide 17: Backup Slides

## Slide 18: Averaged field suppression