## Slide 1: Electron collider ring Chromaticity Compensation and dynamic aperture
Yuri Nosochkov, Yunhai Cai (SLAC)
Fanglei Lin, Vasiliy Morozov, Guohui Wei (JLab)
Min-Huey Wang
JLEIC Collaboration Meeting Fall 2016 Thomas Jefferson National Accelerator Facility Newport News, VA

## Slide 2: Introduction
Strong final focus (FF) quadrupoles near IP, where b-functions are very high, create large non-linear chromatic perturbations (~bKL)
  Large momentum tune spread increases exposure to betatron resonances
    reduced momentum range, beam dynamic aperture and lifetime
  Large momentum variation of b functions causes beam smear at IP
    may limit luminosity
Correction strategy
  Chromatic sextupoles placed at optimal phase near the FF for a local correction
  Special optics (e.g. –I sections) to cancel sextupole non-linear geometric (amplitude dependent) aberrations for maximum dynamic aperture
  Minimal impact on beam emittance
Previously studied
  Correction schemes based on the arc cell configuration
    preserves ring geometry
  Adequate chromaticity compensation and dynamic aperture
  Contribution to emittance is not small
New study
  Correction schemes for lower emittance
  Using electron ring design with 108° arc FODO cells

## Slide 3: Chromatic sextupoles in electron ring
e-
R=155m
RF
RF
Spin rotator
Spin rotator
Original CCB
Arc, 261.7
81.7
Forward e- detection
IP
Tune trombone & Straight FODOs
Future 2nd IP
Spin rotator
Spin rotator
CCB
CCB
Arc sextupoles
Arc sextupoles
Two dedicated chromaticity correction blocks (CCB) replace several arc cells nearest to the FF on either side of IP for local FF chromaticity correction
Two-family arc sextupoles arranged in groups of multiple of 10 cells (unit matrix) to cancel the remaining linear chromaticity while compensating sextupole geometric effects in 108° arc FODO cells

## Slide 4: Previously studied schemes
Several schemes: 1) original compact CCB with interleaved X & Y sextupoles, 2) non-interleaved –I sextupole pairs, 3) interleaved –I pairs, 4) no CCB
Based on arc cell configuration with the same dipoles  preserves geometry
Scheme with non-interleaved –I pairs provides a better performance
  Adequate chromaticity compensation and reasonable dynamic aperture
  But emittance increases from 8.9 nm (w/o CCB) to >15-20 nm at 5 GeV
-I
-I
SY
SY
SX
SX
ex = 19.4 nm with CCB b = 250/500 m
Scheme A
ex = 15.5 nm with 40% lower b
Scheme B

## Slide 5: Emittance
 Preservation of low emittance requires small CCB bending angles θb and small H-function (i.e. bx, hx) at the CCB dipoles
But CCB sextupoles require high dispersion and b functions  large H-function at dipoles leads to large contribution to emittance
H-function in scheme-A
arc
H-function in scheme-B with 40% lower b
arc
ex = 19.4 nm
ex = 15.5 nm

## Slide 6: SuperB type sextupole scheme
Remove dipoles from cells with high dispersion and bx
  Low H-function at the remaining dipoles if angle per dipole is not changed
  If the total CCB angle is kept the same as in the arc cells, then the dipole angle qb would increase a factor of 2 (to compensate for missing dipoles) increasing dispersion and the H-function
  A compromise is needed between the emittance, the CCB bending angles and ring geometry
SuperB IR
SY
SY
SX
SX

## Slide 7: Scheme-2
Two non-interleaved –I sextupole pairs per CCB with large b = 200 / 400 m at the sextupoles and np phase advance from the FF
Seven regular length CCB dipoles (Lb = Lb0 as in arc cells)
Increased angle per CCB dipole qb = 2.286 qb0 (B = 2.286 B0) relative to the arc dipole  to preserve the total bending angle
A larger CCB H-function compared to the arc due to strong dipoles
ex = 22.8 nm at 5 GeV (MAD8 calculation)  too large compared to 8.9 nm without CCB  need to reduce the bending angle per dipole
SY
SY
SX
SX
-I
-I
match
H-function
arc

## Slide 8: Scheme-4
Seven short half-length dipoles (Lb = 0.5 Lb0) plus one regular arc dipole
Shorter CCB with a smaller angle per dipole qb = 1.286 qb0 relative to scheme-2 (still a strong field B = 2.572 B0)  same total bending angle as in the arc
Factor of 3 smaller dispersion and H-function relative to scheme-2
np phase advance from FF to CCB sextupoles and b = 200 / 400 m at CCB x/y sextupoles
ex = 10.3 nm at 5 GeV  a factor of 2 reduction compared to scheme-2
arc
H-function
Scheme-4 optics

## Slide 9: Scheme-6
Seven short dipoles (Lb = 0.592 Lb0) plus one regular arc dipole
Smaller angle per dipole qb = 0.714 qb0 (B = 1.206 B0) compared to scheme-4  very small dispersion and H-function  smaller bending angle compared to the arc  affects ring geometry
Make similar angle reduction on the other side of arc (for symmetry) and add 4 regular cells in each arc to restore the total arc angle  longer circumference
b = 200 / 400 m at CCB x/y sextupoles
Optimized phase advance (np + Dm) between FF and CCB sextupoles
ex = 8.3 nm at 5 GeV  smaller than without CCB
H-function
Scheme-6 optics

## Slide 10: Arc adjustment in scheme-6
Scheme-6 CCB has a smaller bending angle than in the original arc optics  this makes arc asymmetric
To minimize asymmetry, a similar angle reduction is made at the other arc end by replacing 4 regular arc cells with 2 dispersion suppressors (with half-angle) which are optically already matched
To restore the full arc angle, 4 regular cells are added to each arc
 ~140m longer circumference
DS
2 AC
2 AC
Arc Cells
DS
-DS
DS
Arc Cells
Original end of arc: DS + 4 arc cells
Modified: 3 dispersion suppressors

## Slide 11: IR optics with two CCBs (scheme-6)
my=9p
mx=7p
mx=13p
my=18p
CCB
CCB
FF
FF

## Slide 12: Complete electron ring optics (scheme-6)
* Ring geometry is not yet matched
CCB
CCB
IP
arc
arc

## Slide 13: Schemes summary
Scheme | No CCB | 1 | 2 | 3 | 4 | 6
ex (nm) @ 5 GeV | 8.9 | 29.3 | 22.8 | 12.2 | 10.3 | 8.3
qb / qb0 | 1 | 2.286 | 2.286 | 1.429 | 1.286 | 0.714
Lb / Lb0 | 1 | 1 | 1 | 0.5 | 0.5 | 0.592
b at CCB sext, x/y | --- | 300 / 600 | 200 / 400 | 200 / 400 | 200 / 400 | 200 / 400
K2Lmax (m-2) CCB | 0 | 0.78 | 1.04 | 3.06 | 3.44 | 3.53
K2Lmax (m-2) arcs | 3.09 | 2.94 | 2.84 | 1.87 | 1.90 | 2.53
Natural x, x/y | -113 / -120 | -129 / -147 | -123 / -136 | -132 / -155 | -132 / -156 | -135 / -152
Tune, x/y | 44.22 /47.16 | 44.22 /45.16 | 44.22 /45.16 | 45.22 /47.16 | 46.22 /47.16 | 48.22 /50.16
C (m) | 2185.5 | 2182.8 | 2182.4 | 2181.7 | 2181.7 | 2327.2
Comment | 60x2 arc sextupoles | Thin trombones for match, 40x2 arc sextupoles | Thin trombones for match, 40x2 arc sextupoles | Thin trombones for match, 60x2 arc sextupoles | Thin trombones, for match, 60x2 arc sextupoles | No trombones, longer arc, 60x2 arc sextupoles
* Ring geometry is not yet matched in these CCB schemes

## Slide 14: Chromaticity correction performance
Momentum range ~10sp with optimization of CCB-to-FF phase advance
Scheme-6, ex = 8.3 nm
with phase adjustment
Scheme-4, ex = 10.3 nm
with exact np CCB-to-FF phase

## Slide 15: Dynamic aperture
Comparable chromaticity correction performance in studied CCB schemes
Adequate dynamic aperture and momentum range
No magnet errors yet included
Scheme-3, ex = 12.2 nm
(should be similar to scheme-4, ex = 10.3 nm)
Elegant
Dp/p from 0 to ±9sp
±23sx
72sy
Scheme-6, ex = 8.3 nm
LEGO
Dp/p from 0 to ±11sp

## Slide 16: Summary & conclusions
Low emittance schemes for FF chromaticity correction have been studied, based on SuperB IR design, using non-interleaved –I sextupole pairs
A low emittance is achieved using shorter CCB with smaller bending angles (still comparable to arc dipole angles)
Chromaticity compensation is adequate providing momentum range of ~10sp, with optimization of CCB-to-FF phase advance
A sufficient dynamic aperture of >20s is achieved without magnet errors
Different positions of the CCB dipoles, as compared to the arc, result in some geometry mismatch which was not fixed in this study
The lowest emittance scheme required ~140 m longer ring due to smaller CCB bending angle than in the arc
Next steps:
  Match ring geometry
  Select CCB scheme
  Study dynamic aperture with magnet errors

## Slide 17
Thank you for your attention!