## Slide 1
Demonstration of Cooling of Ions by A Non-DC Electron Beam
Yuhong Zhang
For the JLab-IMP Cooling Collaboration
JLEIC Collaboration Meeting Fall 2016
October 5 to 7, 2016

## Slide 2: The JLab-IMP Cooling Collaboration
Andrew Hutton, Kevin Jorden, Tom Powers, Michael Spata, Haipeng Wang, Shaoheng Wang, He Zhang, Yuhong Zhang (Jefferson Lab)
Jie Li, Xiaomin Ma, Lijun Mao, Youjin Yuan, He Zhao, Hongwei Zhao, (Institute of Modern Physics, Chinese Academy of Science)
Supported by JLab LDRD (2015) and CEBAF Operation Fund, and
Chinese Academy of Science International Collaboration Fund
JLEIC Collaboration Meeting, Fall 2016
2

## Slide 3: Outline
Introduction
Evolution of the Idea of Proof-of-Principle Experiment
Experimental Setup: Making of A Pulsed Beam
Experimental Results
Interpretation of the Data
What is the Next?
Summary
JLEIC Collaboration Meeting, Fall 2016
3

## Slide 4: Introduction: Bunched Beam Cooling Is Essential for JLEIC
JLEIC relies on electron cooling of proton/ion beams for delivering ultra high luminosities (exceeding 1034 cm-2s-1 at each detector)
It is essential to perform cooling during collision in order to compensate IBS induced emittance growth. The electron energy is up to 55 MeV which can only be provided by a SRF linac, thus the cooling electron beam is bunched
All electron cooling to this day were performed using a DC electron beam. The technology is mature.
It is generally believed ions can be cooled by a bunched electron beam, however this has never been demonstrated experimentally before, nor its physics has been systematically studied
We proposed and carried out an experiment at Institute of Modern Physics (IMP) of China to demonstrate cooling in a new parameter region. Success of this experiment will retire one major technical uncertainty of the JLEIC design
JLEIC Collaboration Meeting Fall 2016
4

## Slide 5: Development of An Idea of Proof-of-Principle Test
Presently, there is no existing bunched beam electron cooler for a proof-of-principle (P-o-P) experiment. BNL is constructing a multi-MeV bunched beam cooler for the low energy RHIC operation, however, the expected completion date of construction is beyond 2018, and no P-o-P experiment has been planed.
An idea of utilizing an existing DC cooler for a P-o-P experiment was proposed (A. Hutton). It suggested replacing a thermionic gun by a photo-cathode gun, using the driven laser to control the bunch length (very short) and bunch rep. rate (very high).
A collaboration was initiated between JLab (A. Hutton) and IMP (H. Zhao).
The idea further evolved to utilizing a method of modulating the grid voltage of a thermionic gun to generate a pulsed electron beam with pulse length as short as ~100 ns (H. Zhao). The advantages are least invasive to the IMP DC cooler and requiring a minimum funding.
We received a JLab LDRD grant (Y. Zhang as the PI) to further develop and design the experiment. At the same time, IMP received a grant from Chinese Academy of Science (CAS) for supporting international collaboration (L. Mao as the PI)
JLEIC Collaboration Meeting Fall 2016
5

## Slide 6: Prediction of Bunching Effect by Cooling
Though electron cooling is fundamentally a thermodynamically phenomena (flow of heat/entropy), for bunched beam cooling, there could be intriguing effects associated to ultra-relativisitic motion and phase space distribution
One such an effect, grouping of ions, was suggested (A. Hutton). It is due to reduction of ion beam longitudinal emittance. We would like to verify this effect
Particle density
Before cooling
Particle density
After cooling
A coasting ion beam cooled by a bunched electron beam
Electron bunch
Electron bunch
A bunched ion beam cooled by a bunched electron beam
Electron bunch
Electron bunch
Particle density
Before cooling
Particle density
After cooling
Must be synchronized
JLEIC Collaboration Meeting Fall 2016
6

## Slide 7: IMP DC Cooler on CSRm
DC cooler
HIREL@IMP
Thermionic gun
cathode
electrode
Pulser
JLEIC Collaboration Meeting Fall 2016
7
CSRm ring

## Slide 8: Making of Pulsed Electron Beam
Option 2: An RF amplifier (IMP)
Option 1: A HV pulser (JLab)
Pulse modulation + DC Bias Scheme
JLEIC Collaboration Meeting Fall 2016
8

## Slide 9: The Experiment Setup
Place for JLab pulser
collector
Cathode filament
anode and suppressor
DC grid
>95% beam transmission
JLEIC Collaboration Meeting Fall 2016
9

## Slide 10: Experiment Design Parameters
 | Variables | Value | Value | Unit
12C6+ | Kinetic energy | 7 | 30 | MeV/u
 | Particle γ | 1.007 | 1.032 | 
 | Particle β | 0.121 | 0.247 | 
 | Geometric emittance | 5 | 5 | µm
 | Bunch length | Coasting or 13.4 (RMS) |  | m
 | Energy spread | 4 | 4 | 10-4
e- | Number of particles | 5 | 5 | 108
 | Kinetic energy | 3.8 | 16.3 | keV
 | Radius | 2.5 | 2.5 | cm
 | Average current | 30 | 70 | mA
 | Pulse length | DC to 60 (FWHM) |  | ns
 | Temperature | 0.05 | 0.1 | eV
Rap Rate | For h=2 synch w/ delay | 0.45 | 1.38 | MHz
JLEIC Collaboration Meeting Fall 2016
10

## Slide 11: Beam Diagnostic for Cooling Experiment
Measurement | EC35-electron | CSRm-ions | Data-acquisition
average beam current | dc readings on PSs, sampling resistors | DCC(current)T (transformer)s | existing calibra. and DAS
peak beam current and pulse length | mod. freq. fm Pearson coil on e-collector | rf or harmonic freqs n*f0 | fiber optical link readout
Beam position | capacitive BPMs | capacitive BPMs | Re-calibra. and DAS put new attenuator
Beam trans.-profile | capacitive BPMs (off-line screen) | residual gas BPMs | DAS
Beam long.-profile | BPMs on BPMs | BPMs on BPMs or DCCTs Stochastic cooling pickup | fast scope and on-line DAS
Cooling rates | n.a. | Schorttky resonator and pickups | fast scope and on-line DAS Off-line side-band signal analysis
existing
Modified for the experiment
new installation (in 2016)
JLEIC Collaboration Meeting Fall 2016
11

## Slide 12: 1st Bunched Beam Cooling Experiment
Beam cycle
  Carbon (12C6+) ions were injected at 7 MeV/u from a cyclotron and stored in the CSRm ring
  The ion beam was either coasting or captured into two long bunches h=2 by a RF w/ 450 kHz;
  each bunch occupied about 1/2 of the CSRm ring
  The pulsed electron beam was turned on
  Pulsed beam cooling proceeded very fast in time scale of 1 second
  At 7 second, the stored beam was dumped, then restarted the cycle
Cooling tests:
  Pulsed electron beam cooled the coasting ion beam, both beams were not synchronized
  Pulsed electron beam cooled the coasting ion beam, both beams were synchronized
  Pulsed electron beam cooled the bunched ion beam, both beams were synchronized
Cooling electron beam
  Pulse length varies from 2.2 µs (half of the ring circumference) to 60 ns (limit of the pulser),
  Corresponding to 79.2 m to 2.2 m FWHM pulse length (relativistic β = 0.12)
  The pulse current was kept constant, thus the average current decreased with the pulse length
(IMP, May 17-22, 2016)
JLEIC Collaboration Meeting Fall 2016
12

## Slide 13: Experiment Observations
Test 1: Long pulsed (~5 µs) electron beam cools a coasting ion beam, two beams were not synchronized
We observed a rapid ion loss at beginning of cooling;
Loss was too fast such that cooling effect could not be observed
Exact mechanism of the ion loss is still unknown, but it is suspected raise/fall of the electron pulse might act as a large transverse kicker which knocks ions out piece-by-piece
It is also suspected the electron beam and ion beam were not perfectly aligned
Test 2: Long pulsed electron beam cools a coasting ion beam, two beams were synchronized
We observed a modest to small ion loss
We observed a rapid cooling effect (longitudinal cooling)

## Slide 14: Experiment Observations
Test 3: Pulsed (~2 µs) electron beam cools a bunched ion beam, two beams were synchronized
Only one of two ion bunches were cooled
Electron bunches are longer than the ion bunches;
Ion loss is very small; we postulate the raise/fall of pulsed electron beam did not see ions so no ions were kicked out
We observed cooling effect (longitudinal cooling)
Test 4: Pushing short pulse length of electron beam and use it to cool a coasting ion beam, two beams were synchronized
The electron (FWHM) pulse length was pushed as short as 100 ns (~3.6m)
No cooling were observed with electron pulse length short than 150 ns (~5.4 m); Longitudinal diffusion is too slow to spread cooling along the coasting beam
With a little longer electron pulse length, we observed cooling effect.
At 400 ns pulse length, ions were lost rapidly which could not be explained. It is suspected the ion beam had hit some instability
JLEIC Collaboration Meeting Fall 2016
14

## Slide 15: Observation of Cooling of Bunched Ion Beam by a Pulsed Electron Beam
Two long ion bunches in the ring, only one of them was cooled
After cooling, the cooled ions has a much smaller energy spread, then the ions were more concentrated around center of the RF bucket
Experiment data observation on BPMs
cooled ion bunches
uncooled ion bunches
Electron bunches
Ring circumference
JLEIC Collaboration Meeting Fall 2016
15

## Slide 16: Evolution of Ion Longitudinal Density Profile
Sum of BPM Signals are Used to Show Longitudinal Ion Density Profile
dI/dt peak envelop signal of ion BPMs
A
Ion BPM dI/dt  integration  Iion
A
B
C
1µs
Uncooled bunch
Cooled bunch
Ie=15 mA
12C+6
1µs
Ie=15 mA
1µs
Ie =15 mA
RF OFF
1 s
5 s
Vrf = 600 V
A
B
C
RF on
e-pulse on
RF off
C
B
JLEIC Collaboration Meeting Fall 2016
16

## Slide 17: A Closed Look of Pulsed Beam Cooling
2 µs
time
cooled
Un cooled
1 µs
cooled
Un cooled
1 µs
1 µs
We must admit that these figures are not from one beam store (data have lot of noises)
These figures illustrate reduction of the energy spread
2 µs
0.5s
0.75s
2 µs
2s
0.4s
0.6s
2.2s
JLEIC Collaboration Meeting Fall 2016
17

## Slide 18: A Closed Look of Pulsed Beam Cooling
0.8 µs
cooled
Uncooled
time
0.875s
0.8 µs
2.825s
0.8 µs
3.05s
0.6 µs
0.6 µs
0.675s
0.55s
0.6 µs
3.30s
cooled
Uncooled
JLEIC Collaboration Meeting Fall 2016
18

## Slide 19: Observation of Cooling of A Coasting Beam and Bunching Effect By A Pulsed Electron Beam
2 µs
Ion beam profile follows electron pulse profile, ions can see only electron potential well
This potential has a flat bottom, so no narrow core spike will appear
1 µs
0.15 µs
ions
electrons
4.20s
4.30s
0.3 µs
JLEIC Collaboration Meeting Fall 2016
19

## Slide 20: Observation of Cooling of Coasting Beam By A Very Short Pulsed Electron Beam
zoom in
Beam synchronization between electron pulse and ion bunch is critical
Both electron and cooled ion have the same bunch length ~150ns
Without fine tune the electron pulser’s frequency with the ion revolution frequency, the cooling effect can be lost
150 ns
ions
electrons
150 ns
JLEIC Collaboration Meeting Fall 2016
20

## Slide 21
Fit by a Bi-Gaussian distribution
+
Data Analysis And Modeling
May 21’s data with RF on
RMS bunch length needs to be standardized
RMS bunch length definition
JLEIC Collaboration Meeting Fall 2016
21

## Slide 22
Evolution of the RMS Bunch Length
JLab Algorithm
Use the first integral of the BPM signal as the beam density function.
Make the start and the end point of the first integral to be zero to remove DC slope.
If any value is less than zero after the slope adjustment, make it zero.
The rms bunch length is calculated using the following formula:
t (s)
dz (s)
Cooling reach equilibrium at about 1.5 s.
May 21’s data with RF ON
Blue: uncooled ion bunch
Red: cooled ion bunch
JLEIC Collaboration Meeting Fall 2016
22

## Slide 23: Preliminary Results and Explanations
Ion synchrotron motion enhances effectiveness of cooling since it is much fast than cooling process, therefore cooling works even electron pulse is shorter than ion bunch length;
With cooling, ion bean energy spread becomes smaller and smaller. RF potential well constrains those cooled ions around the center of the bucket, thus a core spike in the density profile is formed
Height and width of the core spike is determined by a balance of IBS and cooling, it also depends on the electron temperature;
Although width of the electron pulse does not affect width of the cooled core spike, it does affect the cooling rate with given peak electron beam current;
1D beam dynamic modeling
The cooled ions are trapped at the RF potential well bottom, forms the spike core. In this simulation, RF voltage is on with electron bunch cooling.
Space charge force of the electron pulse does form an additional potential, but it is quite small (10% compared the RF voltage at 600 V). Therefore it shouldn’t blur the pulsed cooling process. In the IMP experiments, it only manifest itself when VRF is turned off.
JLEIC Collaboration Meeting Fall 2016
23

## Slide 24: Consideration for the 2nd Stage Experiment
The second bunched e-cooling experiment is planned (5 days) near end of Nov.
The primary goal of this second experiment is machine studies, including hardware (beam diagnostics) improvement and software development, tentatively, they are
  Preparation of ion BPMs on bench and in situ calibrations
  Software and hardware for BPM, DCCT and Schottky signals data acquisition systems
  Software and hardware improvement for the gun trigger and RF synchronization of high rate of data recording during single injection cycle
  Beam instrumentation checkup with 40Ar+15 beam at CSRm in high energy
We also plan to demonstrate pulsed beam cooling at 30MeV/u to study the weak effect of electron bunch potential well both with and without RF
JLEIC Collaboration Meeting Fall 2016
24

## Slide 25: Summary
The first experiment of cooling of ions by a non-coasting electron beam was carried this May at a DC Cooler at IMP by a JLab-IMP collaboration team
The pulsed electron beam with 2 µs to 60 ns FWHM pulse length was generated in the thermionic gun of the IMP DC cooler using a method of modulating the grid voltage
In this experiment, cooling of ions (either bunched or coasting) by a pulsed electron beam was observed through BPM measurements.
The grouping/bunching effect of pulsed beam electron cooling was also observed in the case of coasting ion beam
The team has collected a large amount of experiment data, they are primarily BPM data. Analyses of these experiment data is in progress.
1D longitudinal dynamic modeling with/without RF and the pulsed electron cooling is under development with promised results to explain observed experiment data
JLEIC Collaboration Meeting Fall 2016
25

## Slide 26: Acknowledgements
I want to thank Haipeng Wang and Shaoheng Wang for their assistance in preparing for this presentation

## Slide 27
Backup Slides

## Slide 28: HIREL-CSR Layout & Performance Specification
EC-35 cooler
separated-sector cyclotron
Sector Focusing Cyclotron

## Slide 29: EC-35 DC Cooler and Commissioned Performance
1—electron gun, 2—electrostatic bending plates, 3—toroid, 4—solenoid of cooling section, 5—magnet platform, 6—collector for electron beam, 7—dipole corrector, 8—vacuum ﬂange for CSRm. Two BPMs placed in the cooling station, one is at upstream of electron beam at gun side in position 9, another one is at downstream collector side in the mirror symmetric position relative to 9.
vacuum 21011 mbar,
high voltage 20 kV,
electron beam current 1.5 A,
collector efﬁciency >99.99%,
angle of magnetic ﬁeld line in cooling section <210-5
Recommissioned in March 2016
Single plate of this BPM has been used for the bunched e-beam measurement

## Slide 30
Cavity Schottky Pickup RF harmonic signal

## Slide 31
Algorithm:
Integrate the BPM signal and find the peak of the cooled beam.
Select the range of half period, centered at the peak, as the whole cooled beam.
Make the start and the end point of the first integral to be zero to remove DC slope, and calculate the second integral.
Select the following half period as the uncooled beam, and calculate the second integral in the same way.
Calculate the rate between two second integrals of the cooled and the uncooled beam.
First integral of the BPM signal charge density function
Second integral of the BPM signal total charge
t=0.025 s
t=0.45 s
t=1.7 s
t (s)
Rate
Rate of the two 2nd integrals
1st Integral
1st Integral
1st Integral
t (s)
t (s)
t (s)
Evolution of the RMS Bunch Length
JLEIC Collaboration Meeting Fall 2016
31