## Slide 1: JLEIC Configuration and Parameter Management
Michael Spata
October 7, 2016

## Slide 2: Outline
Synchronous Information Flow
Lattice Configuration Control
JLEIC Requirements and Parameters
Region Definitions
JLEIC Element Database
Conclusion

## Slide 3: Synchronous Information Flow
Accelerator Physics
Lattice Design
High Level Applications
Engineering
Hardware Development:
3-D Models
Survey & Alignment
Magnet Group
Installation Group
Vacuum Group
Electrical Group
Operational Development:
Production Je-Di+ Database
Song Sheets
Control Screens
Machine Checkout
Nomenclature edits
Non-beam elements
Physical Parameters
Element coordinates
Field strengths
Generic element names
TWISS Parameters
Elegant Parameters
High Level Requirements and Specifications
Design Iteration
Simulation Cycle

## Slide 4: Synchronous Information Flow
Accelerator Physicist (CASA) responsibilities:
  Develop high level parameter tables for EIC complex consistent with requirements of Nuclear Physics
  Develop beam specification tables for protons and lead for all machine segments
    Ensure seamless flow of parameter space between segments
  Develop lattice files for each segment
    Includes all components that interact with the beam
      Magnets, RF structures, Diagnostics, …
    Version controlled in our subversion repository
  Conduct all relevant simulations to validate designs
  Develop documentation for each machine segment for input into conceptual design report
  Output information to stakeholders
    Mechanical information to Engineering group
    Optics information to High Level Applications group
    Write conceptual design report chapter

## Slide 5: Synchronous Information Flow
Mechanical Engineering responsibilities:
  Modify component names from lattice files to have the proper nomenclature for implementation in the Je-Di+ database
  Compile hardware specific information such as magnet field strength limits, physical lengths, gaps, pole width, powering configurations ….
  Add non-beam components that are not included in lattice files such as vacuum valves, ion pumps, bellows, support structures, …
  Convert element data into 3-dimensional models to identify any potential mechanical interferences
  Update costing information based on updated layouts

## Slide 6: Synchronous Information Flow
High Level Applications group responsibilities:
  Develop and implement a comprehensive element database for JLEIC (Je-Di+) analogous to the CEBAF Element Database (CED)
  Implement optics information in Je-Di+ from lattice files provided by CASA
  Implement component information in Je-Di+ provided by Mechanical Engineering group
  Apply proper sequencing to all components
  Maintain device catalog and device definitions in Je-Di+

## Slide 7: Lattice Configuration Control
All lattice files for the entire complex are managed in a version control environment
Top-level interface shows directory structure for JLEIC, revision numbers for each machine, last modification date, person making the change, and log information
Most directories populated. Need transfer lines and ERL Cooler uploaded to system.

## Slide 8: Lattice Configuration Control
Lattice designers import a local copy of files which are kept synchronized with the server
Changes are committed to the server along with a description of changes in a log file
Notification is sent to all lattice designers as modifications to the system are made
System provides capability to view differences between versions and to merge changes

## Slide 9: JLEIC Requirements and Parameters
Wiki developed to collect all JLEIC information – Requirements, Parameter Tables, Supporting Documentation, Simulation Results, Conceptual Design Report Draft Chapters

## Slide 10: JLEIC Requirements and Parameters
JLEIC Accelerator Complex segmented into logical blocks with identified owners for each:
Highest Level Requirements Overview [Y. Zhang]
CEBAF Requirements and Parameters for JLEIC [Roblin]
Electron Transfer Line Requirements and Parameters [Roblin]
Electron Collider Ring Requirements and Parameters [Lin]
Ion Source Requirements and Parameters [Sy]
Ion Linac Requirements and Parameters [Satogata]
Ion Linac to Booster Transfer Line Requirements and Parameters [Satogata]
Ion Booster Ring Requirements and Parameters [Bogacz]
Ion Booster to Collider Transfer Line Requirements and Parameters [Bogacz]
Ion Collider Ring Requirements and Parameters [Morozov]
Ion Booster DC Electron Cooler Requirements and Parameters [He Zhang]
Collider Electron Cooler Requirements and Parameters [Benson]
Collider Interaction Region I Requirements and Parameters [Morozov]
Detector Requirements and Parameters [Physics TBD]
Conceptual Design Report Document Template [Krafft]

## Slide 11: JLEIC Requirements and Parameters
LINAC Parameters for Protons and Lead

## Slide 12
Region
1 eA1
2 e Straight1
3 e Arc2
4 e Straight2
Electron Collider Ring
REGION T1: Transfer Line #1- Electrons;(T1)
REGION 3: Arc2;( eA2)
REGION 2: Straight1;(eS1)
REGION 1: Arc1;(eA1)
REGION 4: Straight2;(eS2)
IP #1
Future IP #2
T1 Transfer Line #1- Electrons from CEBAF
See next page for NOMENCLATURE
Electrons from CEBAF
JLEIC Machine Region Definition

## Slide 13
JLEIC Machine Region Definition
Electron Collider Ring Segmentation

## Slide 14
(Quadrupole Magnet)
eA1-MQPX-005-X
Element Type(Quad, Dipole, Sextapole, etc.)
Element Specifics (2 or 3 characters)
Ring Descriptor (e, i, b or c)
Q022
Q022
Q022
Q022
Q022
SASD1
Element Sequence Number (3 characters)
eA1-MSAX-001
( Sextapole Magnet)
SASD1
SASD2
SASD3
Sextapole
Quadrupole
eA1-BPMX-002 (Button Position Monitor)
Disambiguation Code-(alpha Character), e.g. H, V, A, B, etc.
Region (A1, S1, A2, S2 or T1, T2, etc.)
Position Monitor
Electron Collider Ring Segment
JLEIC Machine Region Definition

## Slide 15
Ion Collider Ring
Region
4 i Arc2
3 i Straight2
2 i Arc1
1 i Straight1
REGION T2: Transfer Line #2; (iT2)
REGION 2: Arc1; (iA1)
REGION 3: Straight2; (iS2)
REGION 4: Arc2; (iA2)
REGION 1: Straight1; (iS1)
Future IP
T2 Transfer Line #2 - Ions
Ions from Booster
JLEIC Machine Region Definition

## Slide 16
(Quadrupole Magnet)
iA2-MQPX-005-X
Element Type(Quad, Dipole, Sextapole, etc.)
Element Specifics (2 or 3 characters)
Ring Descriptor (e, i, b or c)
Q022
Q022
Q022
Q022
Q022
SASD1
Element Sequence Number (3 characters)
SASD1
SASD2
SASD3
Sextapole
Quadrupole
iA2-MSAX-001 (Sextapole Magnet)
Disambiguation Code-(alpha Character), e.g. H, V, A, B, etc.
Region (A1, S1, A2, S2 or T1, T2, etc.)
Position Monitor
Ion Collider Ring Segment
JLEIC Machine Region Definition

## Slide 17
REGION 1: Ion Source and Linac; (bIJ)
Ion Linac
Ion Source
Ion Booster Ring
Region:
2 (B Arc1)
3 (B Straight1)
4 (B Arc2)
1 ( Ion Injector Source and Linac)
5 (B Straight2)
T2 (Ion Transfer Line)
REGION T2: Ion Transfer Line; (iT2)
REGION 2: Arc1; (bA1)
REGION 5: Straight2; (bs2)
REGION 4: Arc2
REGION 3: Straight1; (bS1)
JLEIC Machine Region Definition

## Slide 18: JLEIC Element Database
Je-Di+ is a comprehensive database containing all machine elements, beam parameters, coordinate information, physical properties, powering scheme, ….
Presently populated with baseline layouts for Ion Ring, Electron Ring and Booster

## Slide 19: JLEIC Element Database
Je-Di+ is a comprehensive database containing all machine elements, beam parameters, coordinate information, physical properties, powering scheme, ….
Expanded to show major segments for the three machines that are in the system

## Slide 20: JLEIC Element Database
Je-Di+ is a comprehensive database containing all machine elements, beam parameters, coordinate information, physical properties, powering scheme, ….
Expanded to show elements for the A1 segment of the Electron Collider

## Slide 21: JLEIC Element Database
Je-Di+ populated with baseline layouts for Ion Ring, Electron Ring and Booster
Component count to date:

## Slide 22: JLEIC Element Database
Example from CEBAF Element Database (CED) of fully populated system:
Coordinates – 6-D positional information of an element

## Slide 23: JLEIC Element Database
Example from CEBAF Element Database (CED) of fully populated system:
Design – Twiss parameters, elegant parameters, coordinate in beam following system

## Slide 24: JLEIC Element Database
Example from CEBAF Element Database (CED) of fully populated system:
Physical – Powering, Physical Dimensions, LCW Connectivity, Shape

## Slide 25: Conclusion
Synchronous Information Flow from highest level requirements
Subversion repository created to track lattice file development and simulation parameters in a version-controlled environment
Wiki established to collect relevant information about the baseline JLEIC design to ultimately write Conceptual Design Report
Interface to Engineering and High Level Applications to:
  Complete engineering layouts and costing of the JLEIC Accelerator Complex
  Collect all information of the baseline JLEIC design in the Je-Di+ database
Much work has been done to establish a framework to guide us towards a comprehensive and solid baseline design for JLEIC
Thank You!