## Slide 1: “High-Power” THz Sources and Applications
Eric Bryerton
Virginia Diodes, Inc.
Charlottesville, VA USA

## Slide 2: My Background
B.S. University of Illinois 1995
Ph.D. University of Colorado 1999
  “High-Efficiency Switched-Mode Circuits for Spatial Power Combining”
  Nothing above 10 GHz
National Radio Astronomy Observatory (NRAO) 1999-2013
  ALMA local oscillator development for 84-950 GHz
  Cryogenic MMIC LNA design and testing
Virginia Diodes, Inc. (VDI) 2013-
  Integrated sources and downconverters, mm-wave radiometers, new projects

## Slide 3
Frequency [GHz]
ALMA Development (~1998-2007)
66 Antennas
  12 m & 7 m diameter dishes
2 Receivers for each band
12 VDI THz multiplier chains in each antenna
VDI

## Slide 4: ALMA Front End
Warm Cartridge Assembly with LO YIG Tuned Oscillator and Driver Stage (up to ~120 GHz)
Morgan, 2005 CSIC Digest
Cryogenic Front End
4K Stage with SIS Mixers
VDI Multipliers on 77K Stage
Driver contains integrated multi-chip modules taking ~12-24 GHz YTO output to 65-122 GHz output

## Slide 5: ALMA Front End Cryostat

## Slide 6: ALMA Operation Support Facility (2900m)

## Slide 7: ALMA Chajnantor Site (5000m)

## Slide 8
ALMA Chajnantor Site (5000m)

## Slide 9: ALMA Science
ALMA image of the young star HL Tau and its protoplanetary disk. This best image ever of planet formation reveals multiple rings and gaps that herald the presence of emerging planets as they sweep their orbits clear of dust and gas. Credit: ALMA (NRAO/ESO/NAOJ); C. Brogan, B. Saxton (NRAO/AUI/NSF)

## Slide 10
Applications
Spectroscopy
Imaging
Communications
Molecular Spectroscopy
Radio Astronomy, Atmospheric
EPR/NMR/DNP
Plasma Diagnostics
Weather Monitoring
General Test & Measurement
ALMA (NRAO)
Nafradi et al (EPFL)
THz VNA Extenders

## Slide 11: 680 GHz Integrated Polarimeter
VDI funded through NASA SBIR Phase 2 for compact low-power 680 GHz polarimeters (e.g. for Cubesats)
1.50” x 1.50” x 0.75”, ~3W required DC

## Slide 12: THz Orthomode Transducer
OMT used in polarimeters, to separate dual-polarized input into two orthogonal polarizations
To do in waveguide split-block requires very precise machining tolerances (widths and depths): e.g. +/- 2um at 600 GHz
Can laser micromachining do this better?

## Slide 13: High Power Applications
Steady need for high-powered THz sources
Radio Astronomy
  Focal Plane Array LO Sources
Spectroscopy
  Electron Spin Resonance
  Dynamic Nuclear Polarization
Plasma Diagnostics
  ITER
http://www.astro.uni-koeln.de/
Bruker
ITER

## Slide 14: VDI Core Technology: Use the nonlinearity of diodes to extend the frequency range of traditional microwave electronics
X3
Microwave Technology
VDI Technology
X8
40 GHz
16.7 GHz
320 GHz
40 GHz
3 W
50 mW
Triquint
Herley-CTI
Schottky Diode
GaAs MMIC
Synthesizer

## Slide 15: Schottky Diode Frequency Multipliers
X2
100 GHz
200 GHz
Diode Multiplier
Frequency Doubler

## Slide 16: Power from Multipliers

## Slide 17: 263 GHz Source for ESR/DNP
High power source for Electron Spin Resonance and Dynamic Nuclear Polarization experiments
Peak power 120 mW
  Higher power version under development
Nafradi et al (EPFL)

## Slide 18: Sources for ESR and DNP

## Slide 19: Sources for ESR and DNP

## Slide 20: Sources for ESR and DNP
Need high-power sources to saturate the sample
  The shorter the pulse, the more power needed
Standard DNP frequencies: 263 GHz, 395 GHz, 527 GHz (based on magnetic field)
Can start to do interesting things at >100mW
  Can do even more with tens of Watts

## Slide 21: 1 mW at 1 THz

## Slide 22: THz Sources for SOFIA
SOFIA Observatory
Meas. At Room Temp.

## Slide 23: 1.9 THz AMC
N = 144
x2Amp/x2/x2/x2/x3/x3
Two types of multipliers
Self-biased triplers
High power varactor doublers
Power amplifier is < 40 GHz.

## Slide 24: 2.67 THz Solid-State Source
4 uW at 2.67 THz

## Slide 25: Future Goal – 200mW at 264GHz
Chart: AMC 573 Output Power Performance
| 258.99599999999998 | 259.49760000000003 | 259.99680000000001 | 260.49599999999998 | 260.99760000000003 | 261.49680000000001 | 261.99599999999998 | 262.49760000000003 | 262.99680000000001 | 263.49599999999998 | 263.99760000000003 | 264.49680000000001 | 264.99599999999998 | 265.49760000000003 | 265.99680000000001 | 266.49599999999998 | 266.99760000000003
 | 43.9209 | 72.337 | 96.9495 | 105.244 | 116.282 | 120.258 | 117.934 | 107.477 | 104.094 | 96.3794 | 86.4233 | 83.6957 | 82.3029 | 87.3297 | 85.4028 | 94.1107 | 92.0428

## Slide 26: Recent High Power Result at 210 GHz

## Slide 27: Other high-power applications
Plasma diagnostics
Molecular spectroscopy
Cloud radar
Imaging (medical, security, etc.)
???