## Slide 1: NGLS Outline and Needs in Superconducting RF Materials Development John Corlett SRFMW, July 16, 2012
Office of Science

## Slide 2
What is the NGLS?
≤1 to ~100 femtoseconds
~ microseconds
An array of high average power X-ray lasers with intense, ultrafast, coherent X-ray pulses at high repetition-rate
time
X-rays
~ 100 microjoule
A CW superconducting accelerator with high rep-rate injector provides the high brightness and high-power electron beam
EUXFEL
Free electron lasers (FELs)produce intense, ultrafast, coherent, X-ray pulses

## Slide 3: What is the NGLS? Comparison with existing light sources
NGLS
~ microseconds
≤1 to ~100 femtoseconds
Intense coherent pulses at high rep rate – high average power
~100 microjoule
Weak pulses at
high rep rate
Today’s storage ring x-ray sources
~ nanoseconds
~10 to 100 picoseconds
~nanojoule
Intense pulses at
low rep rate
~ milliseconds
~10 to 100 femtoseconds
Today’s x-ray laser sources
~millijoule
…
…
Notes: Storage rings and FELs provide beamlines with about 1 Watt average power (0.1% BW)
Next generation superconducting-linac-driven FELs can provide hundreds of Watts, and with flexibility in X-ray pulse characteristics
Orders of magnitude more average power in coherent beams, with many (10) orders of magnitude greater peak brightness than storage rings

## Slide 4: What is the NGLS? Approach
CW superconducting linac,
laser heater, bunch compressors
High-brightness, high rep-rate gun and injector
Beam spreader
Array of independent FELs
X-ray beamlines and endstations
More energy per unit bandwidth
More photons per second
Shorter pulses
Controlled trade-off between time and energy resolution
CW pulse train

## Slide 5
High repetition rate soft X-ray laser array
  Up to 106 pulses per second
  Average coherent power up to ~100 W
Spatially and temporally coherent X-rays (seeded)
  Ultrashort pulses from ≤1 fs to ~100 fs
  Narrow energy bandwidth to 50 meV
Tunable X-rays
  Adjustable photon energy from 270 eV – 1.2 keV
    higher energies in the 3rd and 5th harmonics
  Polarization control
  Moderate to high flux with 108 – 1012 photons/pulse
Expandable
  Capability
  Capacity
What is the NGLS?
Capabilities

## Slide 6
Seeded / self-seeded
2 color seeded
Self-seeded
10 μs
5 – 250 fs
High resolution
Trade-off time/energy resolution
1011 – 1012 ph/pulse
10-3 – 5x10-5 bandwidth
10 μs
~1– 25fs
Ultra-fast
≤ fs pulse capability
2 color
108 ph/pulse
≤100 fs
Three nominal initial X-ray lasers
≤1 μs
5 – 250 fs
Highest rep rate
High flux
1011 - 1012 ph/pulse
100 W

## Slide 7
300 pC bunches
1 MHz rep-rate
2.4 GeV
~16 MV/m gradient
27 ~12-m long cryomodules
7 RF cavities per module
2 bunch compressors
1 laser heater
3 initial identical spreader beamlines
3.9
CM01
CM2,3
CM04
CM09
CM10
CM27
BC1
210 MeV
BC2
685 MeV
GUN
1 MeV
Heater
100 MeV
L0
Ipk = 50 A
L1
Ipk = 50 A
Lharmonic
L2
Ipk = 150 A
L3
Ipk = <600 A
SPRDR
2.4 GeV
~700 m
to spreader end
Linac schematic layout

## Slide 8: NGLS cryomodule concept
“TESLA” cavities in JLAB-style housing
  Cold/warm transitions on each cryomodule
  Distribute 5 K liquid, cool to 1.8 K at cryomodule
  Warm magnets, diagnostics & HOM absorbers
  RF power distribution options under study
Planning workshop on “CW SCRF Linac for X-ray Lasers” – September

## Slide 9: NGLS project status
LBNL submitted a CD-0 proposal in December 2010
DOE approved “Mission Need” for the Next Generation Light Source

## Slide 10: Planning assumptions
15
16
17
18
19
20
13
14
CD-2/3a, 3b
12
CD-1
21
CD-4a,b
11
23
22
FY
Defining
Building
Commissioning
Today
Refining
CD-0
We need to define what NGLS “is” in this timeframe
Use existing technology where it works
Develop performance improvements and cost reductions where they have the biggest impact

## Slide 11: Charge to this workshop
For a CW accelerator, with modest accelerating field ~15–20 MV/m:
  What materials and fabrication processes could be developed to increase Qo to the highest reliably achievable value?
  What materials and fabrication technique developments might lead to reduced costs and improved production yield?
Notes: High repetition rate
  Injector (APEX)
  Spreader
Advanced FEL operation
  Seeding
  Lasers
  Undulators
  Instrumentation & diagnostics
  Timing & synchronization
High average power
  Beam dumps
Superconducting accelerator developments
  High Qo
  Higher order mode power
  Field emission
  Harmonic cavity