## Slide 1: Preparation of the CLAS12 First Experiment Status and Time-Line
CLAS Collaboration – CLAS12 Workshop
Jefferson Lab
March 28-31, 2017
Latifa Elouadrhiri
Jefferson Lab

## Slide 2: Outline
CLAS12 Technical Design
KPP Run
Engineering/Physics Run Preparation
Summary

## Slide 3
Optimized for exclusive and semi-inclusive reactions
Large coverage in J and f angles
Small angle capabilities
Capable of operating at luminosity of
1035 cm-2s-1
Particle ID up to high momentum for e-/π-, π/K/p, γ/πo separation
Good momentum & angle resolution for use of missing mass techniques
Operate Polarized Target
CLAS12 Technical Scope

## Slide 4
CLAS12 – Baseline Equipment
Forward Detector (FD)
  TORUS Magnet
  HT Cherenkov Counter
  Drift Chamber System
  LT Cherenkov Counter
  Forward TOF System
  Pre-shower Calorimeter
  E.M. Calorimeter
Central Detector (CD)
  SOLENOID Magnet
  Silicon Vertex Tracker
  Central TOF System

## Slide 5: CLAS12 - Upgrade Equipment
- Central Neutron Detector
  MicroMegas
  Forward Tagger
  RICH detector
  Polarized target
Forward Detector (FD)
  TORUS Magnet
  HT Cherenkov Counter
  Drift Chamber System
  LT Cherenkov Counter
  Forward TOF System
  Pre-shower Calorimeter
  E.M. Calorimeter
Central Detector (CD)
  SOLENOID Magnet
  Silicon Vertex Tracker
  Central TOF System
Upgrade Detectors
  Forward Tagger (FT)
  Ring-Imaging Cherenkov Counter (RICH)
  Micro-Megas Detector (MM)
  Central Neutron Detector (CND)

## Slide 6: CLAS12 Technical Specifications
CLAS12:
CEBAF Large Acceptance Spectrometer 12 GeV
 | Forward Detector | Central Detector
Angular Range |  | 
Tracks | 5o  35o | 35o  125o
Photons | 3o  35o | 
Resolution |  | 
dp/p | 1% @ 5 GeV | < 5%
dq | 1 mrad | 10 – 20 mrad
df | 3 mrad | 5 mrad
Photon Detection |  | 
Energy | > 150 MeV | n.a.
dq | 4 mrad @ 1 GeV | n.a.
Neutron Detection |  | 
Neff | < 70% (EC+PCAL) | 10%
Particle ID |  | 
e/p | Full range | n.a.
p/p | < 6 GeV | < 1.5 GeV
p/K | < 3 GeV | < 0.7 GeV
K/p | < 5 GeV | < 1.0 GeV
p0, h  gg | Full range | n.a.

## Slide 7: CLAS12 KPP Configuration
KPP configuration:
Do not wait for the solenoid arrival, fully assembled forward detector, SVT and CTOF installed upstream of the target (CTOF on a temporary support) and run with ~100 times lower luminosity (e.g. 5 nA beam on a 0.5 mm thick 12C target)
Detector operational: events recorded with a > 2 nA electron beam at > 6 GeV beam energy (3 passes)
KPP Demonstration:
Detector running for 8 hours recording data from all subsystems.
Screenshots of beam status and/or accelerator e-log.
Plots showing relative timing of calorimetry, time-of-flight, and Cherenkov detectors.
Event displays showing correlated particle hits in the Forward Detectors.
Plots of reconstructed particle trajectories showing target position.
Particle identification plots using signals from calorimetry and Cherenkov detector.

## Slide 8: KPP Run Success!!
KPP – Run Period Feb. 3 – Feb. 6, 2017. Data taking with the full detector readout:
-Beam current: 5 nA electron beam - Target: 0.5 mm carbon wire - Torus: 50% B-field
-Trigger:
  Hit-based trigger, ORed from 6 sectors
  FADC-based trigger, ECAL INNER cluster finding with different thresholds
Production runs
& calibration runs
Reverse polarity
Torus Field = 0
DC (HV and Threshold scans)
Random trigger2
Different trigger threshold
2 type of trigger
2 target positions
Low luminosity run

## Slide 9: CLAS12 Engineering/First Experiment Run
Engineering/First Experiment configuration:
The entire CLAS12 is operational
Engineering October/November 2017, followed by Physics data taking
Run at 2.2 GeV (1 pass) and 11 GeV (5 passes) with LH2 target
Commission at low luminosity using loose trigger configuration
Study detector performance as a function of luminosity, define luminosity limits – the goal is L=1035 cm-2 sec-1 (75 nA beam on 5 cm long LH2 target)
Record data for physics analysis
Perform special runs (e.g. alignment ...)

## Slide 10: Timeline
TASK |  |  |  |  | 2016 |  |  | 2017 |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | Oct. | Nov. | Dec. | Jan. | Feb. | Mar. | Apr. | May | June | July | Aug. | Sept | Oct. | Nov. | Dec.
SIMULATION |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RECONSTRUCTION |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CALIBRATION |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EXP. SCHEDULE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
New release with full central detector (MM)
Ready for KPP
New release with full central detector
Ready for Physics
KPP Run
Engineering Run
Full Chain Test
Coordinated Calibration
Challenge

## Slide 11: Extend KPP Strategy to the engineering Run
Full Chain Complete from simulation to cosmic data taking to documentation
  Commissioning plan revised
  CLAS12 first experiment final configuration simulation complete
  SC Torus and Solenoid ready and field maps produced
  All detectors and corresponding electronics ready
  DAQ/Trigger firmware and hardware ready
  Beam polarization
  Experiment normalization
  Online monitoring for shift taker and for experts
  Online reconstruction, fully tested ready
  Data base complete with detector calibration
  Detector alignment
  Offline data processing and offline shift training
  Offline data calibration ready and exercised on calibration challenge
  Event selection framework completed and tested on KPP and simulations
  Final data processing to general DST
  Skimming to produce DST for the first specific experiments
Analysis note based on KPP data Ready

## Slide 12
THANK YOU for Successful KPP run
Looking forward to successful engineering run and the start of physics data taking!