## Slide 1: Challenges in the eRHIC IR Magnet Design
Brett Parker

## Slide 2: eRHIC IR Magnet Challenges: Presentation Plan
Brief introduction (physics & accelerator drivers).
Outline a basic list of eRHIC IR magnet issues.
Review these issues in the historical context of R&D progress we have made to date.
Examine more closely a few of the more interesting examples from the zoo of eRHIC IR magnets.
Conclude with some thoughts for our next steps.

## Slide 3: eRHIC Ring-Ring IR Layout
22 mrad total crossing angle
Initial efforts were to develop an IR design for a linac-ring scenario.
Ring-Ring IR geometry has 4.5 m detector space with crab crossing.
Magnets quite different forward/rear due to physics requirements.
22 mrad total crossing angle
22 mrad total crossing angle
Initial efforts were to develop an IR design for a linac-ring scenario.
Bob Palmer is heading an effort to develop and validate an IR design for our eRHIC ring-ring based accelerator concept.
Forward hadron magnets have large apertures; the electron magnets have smaller apertures.
The side with the outgoing hadron and incoming electron beams is denoted the forward side (neutron and charged particle detectors).
For eA physics, B0, B1 bends separate forward charged particles and 4 mrad neutron cone; we need large hadron magnet apertures with large coil fields... from which the electron beam must be shielded.
“B0”
“ZDC”
For eA physics, B0, B1 bends separate forward charged particles and 4 mrad neutron cone; we need large hadron magnet apertures with large coil fields... from which the electron beam must be shielded.
“B0”
“ZDC”
Physics example: Kinematic regions for DVCS protons that must be detected in either a spectrometer (B0) or downstream Roman Pots.
We use large hadron magnet apertures to pass the charged particles not detected inside B0 on through to the Roman Pots RP1 and RP2.
Not shown here are two Roman pots RP3 and RP4 that are after the crab cavities and located in a low-beta, high-dispersion section.
“B0”
“ZDC”
Rear side hadron magnets have smaller apertures; the electron magnets have larger apertures.
The side with the incoming hadron beam is denoted the rear side.
Outgoing electron beam, rear side, has e-tagger and lumi monitor.
Rear hadron apertures are much smaller than on the forward side.
Electron rear side has separation bends for tagger and lumi monitor.
BH-s
Pair conversion with vertical spectrometer
Weak Bends
REAR
Ring-Ring IR geometry has 4.5 m detector space with crab crossing.
Magnets quite different forward/rear due to physics requirements.
22 mrad total crossing angle

## Slide 4: Basic List of eRHIC IR Magnet Issues
Magnet Zoo: Just within ±20m of the IP we need 12 different styles of superconducting magnets, most of which require closely spaced, double apertures or low-field shielded regions.
  We want to avoid having to create unique tooling for each style.
A few of these magnets, i.e. on the forward hadron side, must have very large apertures with relatively strong quad gradients or strong dipole guide fields.
  Large coil fields/coil dimensions make external field shielding difficult.
  We should consider a range of coil and yoke topologies/schemes.
  We can benefit greatly by investing in shielding R&D (test facility).
Even when we can use a “traditional solution for magnetic shielding,” i.e. cutting holes in magnetic yokes to get reduced field regions, some of the resulting yokes are monster sized.
  With limited resources, we must then carefully consider what R&D prototypes are needed to validate performance goals (test facility).

## Slide 5: Need a Flexible Magnet Production Technique.

## Slide 6
Electron Ion Collider − eRHIC
Winding the SuperKEKB
b5 Cancel Coil
25 September 2013
B. Parker, et.al., "THE SUPERKEKB INTERACTION REGION CORRECTOR MAGNETS,"
Contribution TUPMB041 to Proceedings of IPAC2016, Busan, Korea, May 2016, pp. 1193-1195.
B. Parker, et.al., "SUPERCONDUCTING CORRECTOR IR MAGNET PRODUCTION FOR SUPERKEKB,"
Contribution THPBA07 to Proceedings of PAC2013, Pasadena, CA USA, pp. 1241-1243.
B. Parker, et al., “Direct Wind Superconducting Corrector Magnets for the SuperKEKB IR,”
Contribution WEEPPB013, to IPAC12, New Orleans, USA, May, 2012.
Coil design to cancel a rapidly
changing non-linear external field
component; for more information see the first
backup slide at the end of this presentation.

## Slide 7: eRHIC Linac-Ring IR “Sweet Spot” Magnets†
†Brett Parker, "SWEET SPOT DESIGNS FOR INTERACTION REGION SEPTUM MAGNETS," Contribution TUPMB042
to Proceedings of IPAC2016, Busan, Korea, May 2016, pp. 1196-1198.
6.2 T Field @ Main Coil
Only a few Gauss here

## Slide 8: A Prototype Dipole Sweet Spot Test Magnet
At present time we are almost finished with production of a 1 m long dipole sweet spot coil prototype.
The field is around 4.5 T in the main aperture where the eRHIC hadron beam goes but should be of order a few gauss inside the shielded region for the electron beam.
Coil pattern used for the inner coil is shown to the right.
When this prototype is complete, it becomes a facility for testing different magnetic shielding configurations.
BNL Direct Wind R&D

## Slide 9: eRHIC Magnet R&D Accomplishments and Work Presently In Progress
Have successfully upgraded Direct Wind machine to handle 1.6 mm cable for more than twice capacity of the previous 1 mm cable (i.e. design with single strand wire and 1 mm or 1.6 mm cable).
  Now able to make large diameter coils with half as many cable layers.
The dipole Sweet Spot coil nearing its completion has coil sizes comparable to the Ring-Ring requirements and the prototype is designed to be operated at even higher field.
  So we gain direct experience with large coils and 1.6 mm dia. cable.
  For the R&D prototype, inner/outer coils independently powered; we can run in both Sweet Spot and the active cancellation configurations.
We can provide a wide range of field strengths and varieties of field configurations over the “Sweet Spot test region.”
  Opportunity to test passive magnetic/superconducting shield designs as well as Direct Wound, corrector-like active compensation schemes.

## Slide 10: Need Special Coil and New Yoke Configurations.

## Slide 11: What Changes with Ring-Ring Vs Linac-Ring
Sweet Spot coils are well matched to Linac-Ring requirements because both the crossing angle and electron beam apertures are small (i.e. need to use space close to main coil but this is easier to do if we only need reduced field over a small region).
For Ring-Ring both the electron beam emittance is larger and we pay more of a penalty with large betas and chromaticity; we must use large aperture superconducting electron IR quads, interleaved with hadron magnets, rather than using warm quads further from the IP in the warm region beyond the hadron quads.
Fortunately with the present eRHIC Ring-Ring 22 mrad total crossing angle, we can now fall back on previous work for the ILC final focus where we have produced and tested compact actively shielded coil configurations.

## Slide 12: Design for Compact Superconducting Magnet Used in the ILC 14 mr Layout.
14 mr crossing angle via compact self-shielded QD0 coil windings.
Extracted beam passes just outside coil into separate focusing channel.
Cryostat to fit within limited space inside detector at L* = 4.1 m.
QD0 with active shield off/on
On
Off
Incoming Beam
Outgoing Beam

## Slide 13: Q1PF, First Forward Side Proton Quad
3D End View
Q1PF, active external field cancelation coil.
90 T/m gradient, clear bore is 86 mm ID.
Peak field about 4.5 T with essentially zero external field outside body of the bare coil.
Small cancellation undershoot/overshoot near the coil ends is handled via the use of a thin passive magnetic shield.
3D calculation done for bare coils, run in series.

## Slide 14: Q1PF, First Forward Side Proton Quad
3D Side and End Views
(additional 5 mm thick passive shield is shown as translucent)
First pass Q1PF coil design has a slight mismatch with inner/outer coil ends that yields a small cancellation over/under shoot.
This can be improved when we re-optimize the coil ends and total pattern lengths.
3D calculation done for bare coils, run in series.

## Slide 15: B0 Spectrometer Dipole Concept
(m)
(m)
(m)
3D View
Region for protons, neutrons and forward charged particles
Electrons
Dipole Cancel Coil
Warm Yoke
Superconducting Racetrack coil
B0, a Superferric C-magnet.
1.7 T Field, 1.3 m long.
Gives access for detectors.
Use a Direct Wind dipole cancel coil to buck most of main field and then use passive shielding inside.
x (mm)
Y (mm)
B0 Shielded Region Detailed View
Cancel coil keeps inner passive shield from saturating
Passive shields
Coil
Model by H. Witte

## Slide 16: Lets View Some of the Monsters in the Zoo.

## Slide 17: B1PF, Forward Side Proton Dipole
Protons
Electrons
Unlike the original Linac-Ring design (10 mrad x-ing), the 3.5 T B1 Ring-Ring dipole (22 mrad x-ing), does not seem to require either Sweet Spot or Active Cancellation coils and a simple yoke cutout suffices for the electron beam.
B1 seems like a simple extrapolation, but with 4.8 m length and 1.05 m OD it does not fit in a BNL test dewar (horizontal test??).
3D Oblique View
(yoke is shown translucent)
Roughly 250 gauss field in cutout can be handled by additional passive shielding.
250 mm ID Clear Bore
B1PF can use same 1.6 mm cable as the BNL Sweet Spot R&D prototype.
(IP end shown)

## Slide 18: Q2PF, Forward Side Proton Quadrupole
Protons
Electrons
3D Oblique View
(yoke is shown translucent)
At 17.9 T/m gradient, Q2PF can use a yoke cutout for e-beam.
But like B1PF, it is a monster with 3.72 m length and 1.3 m OD yoke, so it also does not fit in existing BNL vertical test dewars.
We can always put it in a cryostat and do a horizontal test, but this seems a very expensive way to make/test any prototypes.
400 mm ID Clear Bore
Q2PF can use same 1.6 mm cable as the BNL Sweet Spot R&D prototype.
(IP end shown)

## Slide 19: Other Ring-Ring IR Magnets are not Monsters
FORWARD
REAR
Rear side hadron magnets do not need large apertures and their coil peak fields are modest.
And the electron IR dipoles and quadrupoles coil peak fields are much less than those of their hadron counterparts.
The main challenge, which then applies to all of the IR magnets, is how best to accommodate them, with closely spaced side-by-side, apertures in common cryostat structures.
0.2 T Dipoles
Small aperture hadron quads
Monsters
Warm quads

## Slide 20: Look at Some Modest Next Steps

## Slide 21: What (Should) Happen Next
The Ring-Ring IR magnet parameters discussed here are only recently frozen during preparation for our Ring-Ring technical design review that is yet to be held this week.
So there is a fair amount of work yet to be done to carefully go though the design details for all the Ring-Ring IR magnets.
Soon we will be ready to wind the last coil set for the Sweet Spot dipole R&D prototype and can then complete its assembly with its yoke in a vertical cryostat.
Once this dipole is in operation, we will have the capability to carry out a rich test program with tests of different passive magnetic shielding solutions as well as superconducting active and passive shielding.

## Slide 22: And What Could be Points of Common Interest?
I am not presently familiar with the details of JLEIC IR magnets but from this slide, sent to me today by C. Montag, I do see some things of special interest.
I am familiar with the work developing this CIC conductor and have long been interested in using it in some IR magnet designs... especially for the LHeC project being studied at CERN.
While a top goal of the present eRHIC Ring-Ring design study is to “reduce risk,” we should also consider ways in which using novel technology in a few key magnets might be helpful to improve both the accelerator and experimental detector physics performance.
BNL has relevant experience in these areas, along with design work on a Force Neutral Anti-Solenoid for the ILC QD0 Final Focus and the BEPC-II and the SuperKEKB (i.e. locally cancel Belle-II detector field) anti-solenoids.

## Slide 23: Backup Slides

## Slide 24
Electron Ion Collider − eRHIC
35 correction coils and 8 cancel coils are integrated with the main IR quadrupole and must fit within very limited available space.
The first IR quadrupoles have no magnetic yoke and create external field at nearby beam.
The cancel coil shown during winding on an earlier slide has to match a rapidly changing non-linear field in order to cancel it out.
All of the SuperKEKB corrector coils were wound for KEK using the computer controlled Direct Wind technology developed at BNL.
SuperKEKB Interaction Region Corrector Magnets
Belle−II Detector
SuperKEKB IR Magnets

## Slide 25: The Sweet Spot Coil Principle
The magnetic field reverses on opposite sides of a given conductor. So somewhere inside the conductor there is a field zero.
If we now separate the conductor block into two parts, we see that there is a region of low field strength about a central Sweet Spot, zero-field crossing point.
In the low field region in the immediate vicinity of the Sweet Spot, we can place additional magnetic shielding without the shielding becoming overly saturated.
Note if a simple split coil geometry leaves too much field to be handled via a thin passive shield, we can further reduce the magnitude of the field in the vicinity of the Sweet Spot by placing some conductor above and below the desired low field region.

## Slide 26: SuperKEKB QCS Anti-Solenoids for Compensating the Belle-II Detector Field (Slide from Norihito Ohuchi, KEK)