## Slide 1: JLEIC R&D Review: Other R&D
Cooling, SRF, Magnets, Physics discussed elsewhere
Other CTE areas in Fulvia’s original R&D review presentation
First I discuss these, then broader implications for other R&D from table and summary in R&D report from Feb 2017

## Slide 2: INJ2: Booster Space Charge
JLEIC Booster injection is space charge dominated
  Laslett tune shift for design parameters ~0.15
  Conventional DC cooling limited by SC limit
  Proton single-turn injection limited by SC
  Ion multi-turn injection limited by ion source performance
Leverage existing tools and experience
  e.g. FNAL Booster, CERN PS Booster SC limit studies
  SC tracking with realistic superferric magnet multipoles
    Synergia is preferred tool, c.f. FNAL Booster
  Design resonance compensation schemes, multi-turn ion injection scheme

## Slide 3: INJ2: R&D Plan
Add superferric multiples to Synergia design lattice
  Modeling of realistic errors from TAMU TOSCA models
  Include symmetry-driven structure resonances
Produce loss maps and frequency map analysis
  Evaluate halo formation due to resonance crossing
  Evaluate growth times with/without cooling
Evaluate lattice design for resonance correction
  Linear/nonlinear chromatic control
  Optimization for high-intensity injection/acceleration

## Slide 4: INJ3: Ion Bunch Formation
JLEIC luminosity concept requires short ion bunches
  Many modest-intensity (~1e10 p) bunches for 0.75 A
  Acceleration velocity, frev swing requires lower h, frf
Approaches for ion bunch (re)formation
  Preferred: Multiple adiabatic bunch splits
  Alternative: Barrier bucket “debunch”, rebunch
Notes: eRHIC concept: 8 cm sigma_z with about 1.5e11, a bit more aggressive than we are

## Slide 5: INJ3 R&D Plan: Barrier Bucket
Impedance models are also fundamental to this effort
  Smaller RF requirements, less impedance, but higher uncertainty
Develop barrier bucket models
  BLonD/ESME for cross-code verification
  Estimate impedance requirements/thresholds
  Inverse problem to FNAL bunch compression, high intensity
Consult with barrier bucket experts
  Determine feasibility of study at existing facility
  Experimental comparison to model development

## Slide 6: INJ6: Test of CEBAF as JLEIC Injector
Proposed JLEIC injection scheme
  1497/22 MHz trains with pulse length 3.7 us
  Interval 10s of ms to match storage ring damping time
  Pulsed transient beam power 5.5 MW (1 MW each pass)
  Provides 15 min fill time at 3 GeV with longest damping time
Pulsed beam transients a problem unless addressed
  Beam loading/droop exceeds 2e-3 arc momentum acceptance
  Substantial risk in LLRF control, injector performance
LLRF feedforward can be tested in C100/R100 digital LLRF
  Existing digital controls can be modified
  Possible tests in CEBAF, injector R100, UITF with new QCM

## Slide 7: Report R&D Priorities: High
Report Table 1: (somewhat) prioritized list of R&D activities
High / Medium / Low priorities
  Sub-priority C: correlated to most important identified R&D concepts
  The panel assigned very high priority to tests of CEBAF in injector mode for JLEIC
Identifier | Title | JLab Priority | Panel Priority | Panel Sub-Priority
BDD1 | Spin tracking in ion and electron rings | First | High | 
BDD2 | Beam-beam simulation and gear changing | First | High | C
INJ6 | Test of CEBAF injection mode | Third | High | C
IRS1 | IR design and detector integration | Second | High | 

## Slide 8: Report R&D Priorities: High
Spin “likelihood of success appears rather high”
  Risk mainly arises vs investment and NSAC EIC goal needs
  JLEIC performance is more limited by SR power
Noted assumption of CEBAF as full-energy injector
  JLEIC requirement quite different than CEBAF ops
  “An early demonstration of JLIEC injector mode operation would mitigate this risk entirely”, a “significant technical risk”
Large section of CTE feasibility (III.B) discussed simulations
  Gear changing/crabbing/beam-beam collaboration encouraged
  Raised to level of highest priorities in report

## Slide 9: Report R&D Priorities: Medium
Identifier | Title | Our Priority | Panel Priority
BDD3 | Nonlinear beam dynamics | Second | Medium
BDD4 | Instabilities and feedback systems | Second | Medium
BDD5 | Large dynamic range BPM | Third | Medium
INJ2 | Space charge in ion complex | First | Medium
INJ3 | Ion beam formation | First | Medium
IRS2 | Ion and electron ring background and vacuum | Second | Medium
The committee agreed with some of our self-assessments on medium-priority R&D items
  Booster space charge (INJ2) and ion beam formation (INJ3) lowered a bit
  Short JLEIC hadron bunches not specifically critiqued
  Opportunity for hadron BPM diagnostic development (LDRD?)

## Slide 10: Diagnostics and Feedback

## Slide 11: Report R&D Priorities: Low
Identifier | Title | Our Priority | Panel Priority
BDD6 | Large dynamic range luminosity monitor | Third | Low
BDD7 | Electron polarimetry | Third | Low
BDD8 | Ion polarimetry | Third | Low
INJ4 | Alternative ion injector complex design | Third | Low
INJ1 | SRF linac high power operations | Third | Low
INJ5 | Ion sources | Third | Low
IRS3 | Collimation and machine protection | Third | Low
The committee agreed with our self-assessments on nearly all low-priority R&D items
  Exception: CEBAF injection mode (INJ6)  high
  Exception: Large dynamic range BPM (BDD5)  medium
  Polarized 3He source separately identified as common high priority

## Slide 12: Charge Element III High Level
Three major items fall into “other R&D”
These can be interpreted as “musts” from the R&D report
  High-bandwidth feedback (instability/impedance input)
  Gear changing synchronization and simulations
  CEBAF as a JLEIC injector

## Slide 13: Table 1 R&D Priorities: JLEIC