## Slide 1: Polarization Studies
V.S. Morozov, Ya.S. Derbenev, F. Lin, Y. Zhang – Jlab, Newport News, VA D. Barber – DESY, Hamburg, Germany A.M. Kondratenko, M.A. Kondratenko – Zaryad, Novosibirsk, Russia
Yu.N. Filatov – MIPT, Dolgoprudny, Russia
Zgoubi support: F. Meot – BNL, Upton, NY
JLEIC Collaboration Meeting, JLab
April 3-5, 2017
Notes: F. Lin
1

## Slide 2: Outline
Electron polarization
  Design strategy
  Universal spin rotator
  Monte-Carlo simulations of electron polarization lifetime
    SLICK/SLICKTRACK
    Zgoubi
Ion polarization
  Figure-8 concept
  Ion polarization control in the ion collider ring
    Stability criterion
    3D spin rotator
    Suppression of imperfection effect on the ion spin
    Spin flip
  Acceleration of polarized ion beam in the ion collider ring
    Lattice
    Imperfection effect as a function of energy
    Transition energy crossing
    Start-to-end simulation of acceleration

## Slide 3: Electron Polarization Strategies
Highly vertically polarized electron beams are injected from CEBAF
  avoid spin decoherence, simplify spin transport from CEBAF to MEIC, alleviate the detector background
Polarization is designed to be vertical in the JLEIC arc to avoid spin diffusion and longitudinal at collision points using spin rotators
Universal spin rotator (fixed orbit) rotates the electron polarization from 3 to 12GeV
Desired spin flipping is implemented by changing the source polarization
Polarization configuration with figure-8 geometry removes electron spin tune energy dependence, significantly suppress the synchrotron sideband resonance
Continuous injection of electron bunch trains from the CEBAF is considered to
  preserve and/or replenish the electron polarization, especially at higher energies
Spin matching in some key regions is considered to improve polarization lifetime
Compton polarimeter provides non-invasive measurements of the electron polarization
…
…
…
…
Empty buckets
Empty buckets
2.1 ns
476 MHz
Polarization (Up)
Polarization (Down)
bunch train & polarization pattern (in arcs)
IP
Spin Rotator
Magnetic field
Polarization
Polarization configuration

## Slide 4: Universal Spin Rotator (USR)
Solenoid decoupling & Lattice function
Parameters of USR for JLEIC
P. Chevtsov et al., Jlab-TN-10-026
IP
Arc
E | Solenoid 1 |  | Arc Dipole 1 | Solenoid 2 |  | Arc Dipole 2
 | Spin Rotation | BDL | Spin Rotation | Spin Rotation | BDL | Spin Rotation
GeV | rad | T·m | rad | rad | T·m | rad
3 | π/2 | 15.7 | π/3 | 0 | 0 | π/6
4.5 | π/4 | 11.8 | π/2 | π/2 | 23.6 | π/4
6 | 0.62 | 12.3 | 2π/3 | 1.91 | 38.2 | π/3
9 | π/6 | 15.7 | π | 2π/3 | 62.8 | π/2
12 | 0.62 | 24.6 | 4π/3 | 1.91 | 76.4 | 2π/3
Half
Solenoid
Half
Solenoid
Quad. Decoupling Insert
Dipole set
Dipole set
2nd sol. + decoup. quads
1st sol. + decoup. quads
Schematic drawing of USR

## Slide 5: Polarization w/ Continuous Injection
Polarization w/ continuous injection
Equilibrium polarization
A relatively low average injected beam current of tens-of-nA level can maintain a high equilibrium polarization in the whole energy range.

## Slide 6: Spin Tune Scan
SLICK/SLICKTRACK allows one to insert a zero length spin tuning magnet to move the spin tune away from zero. Such magnet in the code only rotates the spin, leaving the orbit intact.
Longitudinal field spin tuning solenoid in one straight where the polarization is longitudinal
  Only moves the spin tune away from zero
  Does not change the spin direction
  Breaks the current spin matching condition in the straight
IP
Spin Rotator
e-
Magnetic field
Polarization
Spin tuning solenoid

## Slide 7: Close Orbit in SLICK/SLICKTRACK
SLICK/SLICKTRACK
  Before orbit correction
    MAX.ORB.DISTORTN: DXMAX = 13.01533955 MM.
    DYMAX = 44.66292770 MM.
    DSMAX = 0.19756703 MM.
    DEMAX = 0.00201231 MEV.
    RMS ORB.DISTORTN: DXRMS = 1.96592282 MM. DXVQRMS = 1.96711965 MM. DXVCRMS = 1.93201011 MM.
    AT QUADS DYRMS = 9.13466663 MM. DYVQRMS = 9.08943471 MM. DYVCRMS = 9.08811068 MM.
    DSRMS = 0.03628817 MM.
    DERMS = 0.00200462 MEV.
    DYPRMS = 1.96765921 MRAD
    DYABS = 6.16746947 MM.
    DYBEND = 22121.34052348 MM.
  After orbit correction
    MAX.ORB.DISTORTN: DXMAX = 1.70784426 MM.
    DYMAX = 0.37412418 MM.
    DSMAX = 0.02578462 MM.
    DEMAX = 0.00024464 MEV.
    RMS ORB.DISTORTN: DXRMS = 0.23823080 MM. DXVQRMS = 0.23807316 MM. DXVCRMS = 0.23333431 MM.
    AT QUADS DYRMS = 0.05731394 MM. DYVQRMS = 0.06759153 MM. DYVCRMS = 0.03287557 MM.
    DSRMS = 0.00419851 MM.
    DERMS = 0.00024370 MEV.
    DYPRMS = 0.07774984 MRAD
    DYABS = 0.03486573 MM.
    DYBEND = 0.29488997 MM.

## Slide 8: Spin Tune Scan @ 5 GeV
Quadrupole vertical misalignment with a rms value of 0.2mm and dipole roll with a rms value of 0.2 mrad. The orbit is corrected with correctors around the ring.
First order spin resonance occurs when
500 electrons in the Monte-Carlo simulation
Optimum Spin Tune 0.0267
  Spin-orbit depolarization time increases by a factor of 2.6 in the optimized baseline design
Optimum Spin Tune 0.0249
Baseline design optics
Optimized baseline design optics

## Slide 9: Closed Orbit Distortion in ZGOUBI
Closed orbit distortion due to random quadrupole misalignments
FFQs’ misalignments are included.
FFQs’ misalignments are not included.
This scenario is used for the spin tracking in ZGOUBI using 20 particles.

## Slide 10: Spin Tune
Longitudinal spin component vs. turn
  w/ quads misalignments
  w/o spin tune solenoid setting
Spin tune induced by the closed orbit distortion: 6.7×10-4
Longitudinal spin component vs. turn
  w/ quads misalignments
  w/ spin tuning solenoid providing a spin precession of 9.6
Spin tune induced by the spin tuning solenoid: 0.027
Longitudinal spin component vs. turn
  w/ quads misalignments
  w/ spin tuning solenoid providing a spin precession of 13.7
Spin tune induced by the spin tuning solenoid: 0.038

## Slide 11: Emittances
Spin tune at 0.027
Spin tune at 0.038
20 particles were used for tracking, ~ 2 days for 7 damping time of ~ 600 ms (80000 turns)
After 7 damping time, the horizontal emittance is close to the analytical value of 9 nm-rad. The non-zero vertical emittance is caused by the coupling of particle motions in the solenoids in the spin rotators, due to the closed orbit distortion.
The emittances in two cases do not change because only spin precession is adjusted by the spin tuning solenoid.

## Slide 12: Spin Motion
Three average spin components of 20 particles vs. time (ms)
~ 7x,y
Qualitatively, simulation results in ZGOUBI agree well with that in SLICK/SLCIKTRACK
  Long depolarization time for s =0.027, short time for s =0.038
Quantitatively, the depolarization time is about 5 times shorter in ZGOUBI than SLCIK/SLICKTRACK, might due to
  Large closed orbit distortion in ZGOUBI
  Coupling in solenoids due to the closed orbit distortion

## Slide 13: Spin Motion in Figure-8 Ring
Properties of a figure-8 structure
  Spin precessions in the two arcs are exactly cancelled
  In an ideal structure (without perturbations) all solutions are periodic
  The spin tune is zero independent of energy
A figure-8 ring provides unique capabilities for polarization control
  It allows for stabilization and control of the polarization by small field integrals
  Spin rotators are compact, easily rampable and give no orbit distortion
  It eliminates depolarization problem during acceleration
    Spin tune remains constant for all ion species avoiding spin resonance crossing
  It provides efficient polarization control of any particles including deuterons
  It is currently the only practical way to accommodate polarized deuterons
  Electron quantum depolarization is reduced due to energy independent spin tune
  It makes possible ultra-high precision experiments with polarized beams
  It allows for a spin flipping system with a spin reversal time of ~1 s
n = 0

## Slide 14: Zero-Integer Spin Resonance & Spin Stability Criterion
The total zero-integer spin resonance strength is composed of
  coherent part due to closed orbit excursions
  incoherent part due to transverse and longitudinal emittances
Spin stability criterion
  the spin tune induced by the 3D spin rotator must significantly exceed the strength of the zero-integer spin resonance
  for proton beam
  for deuteron beam

## Slide 15: Polarization Control in Ion Collider Ring
3D spin rotator: control of the radial, vertical, and longitudinal spin components
Module for control of the radial component (fixed radial orbit bump)
Module for control of the vertical component (fixed vertical orbit bump)
Module for control of the longitudinal component
IP
ions
3D spin rotator

## Slide 16: Spin Dynamics in Ion Collider Ring
100 GeV/c figure-8 ion collider ring with transverse quadrupole misalignments
Example of vertical proton polarization at IP. The 1st 3D rotator:  = 10-2 , ny=1. The 2nd 3D rotator is used for compensation of coherent part of the zero-integer spin resonance strength
Zgoubi
2nd 3D rotator for compensation
1st 3D rotator for control
with compensation
without compensation

## Slide 17: Spin Flipping
Adiabaticity criterion: spin reversal time must be much longer than spin precession period
 flip >> 1 ms for protons and 0.1 s for deuterons
Vertical (hy) & longitudinal (hz) spin field components as set by the spin rotator vs time  Spin tune vs time (changes due to piece-wise linear shape)
Vertical & longitudinal components of proton polarization vs time at 100 GeV/c

## Slide 18: Injection Mode
* increased by a factor of 30 to (3 m, 0.6 m), max reduced by a factor of ~26
Betatron tunes: x = 24.22, y = 23.16

## Slide 19: Crossing Scheme: Simple Phase Jump
On-momentum particle
Particle with =

## Slide 20: Proton Spin during Transition Crossing
On-momentum particle
Particle with =

## Slide 21: Impact of Synchrotron Phase
On-momentum particle
Five particles uniformly distributed on an ellipse with =

## Slide 22: Proton Resonance Strength
Analytically calculated proton incoherent spin resonance strength for  Need a spin tune of
Analytically calculated proton vertical orbit excursion due to quadrupole misalignments and resulting coherent spin resonance strength

## Slide 23: Start-to-End Proton Acceleration
Three protons with and accelerated at ~3 T/min in lattice with 100 m rms closed orbit excursion,
Coherent resonance strength component
Zgoubi simulation
Analytic prediction

## Slide 24: Deuteron Resonance Strength
Analytically calculated deuteron incoherent spin resonance strength for  Need a spin tune of
Analytically calculated deuteron vertical orbit excursion due to quadrupole misalignments and resulting coherent spin resonance strength

## Slide 25: Start-to-End Deuteron Acceleration
Three protons with and accelerated at ~3 T/min in lattice with 100 m rms closed orbit excursion,
Deuteron spin is highly stable in figure-8 rings, which can be used for high precision experiments

## Slide 26: Summary and Future Work
Electron polarization design is complete
Electron spin tracking simulations with distorted closed orbit are in progress using SLICK/SLICKTRACK and Zgoubi with good results
Ion polarization control and spin flip in the ion collider ring demonstrated
Start-to-end simulation of polarized ion beam acceleration with transition energy crossing completed
Ongoing and future studies
  Electron spin tracking in the presence of coupling and closed orbit distortion
  Electron spin matching
  Compensation of detector solenoid effect on the ion polarization
  Effect of coupling on the ion polarization
  Higher-order resonances
  Effects of crab crossing, beam-beam interaction, and electron cooling

## Slide 27: Backup

## Slide 28: Transition Energy Crossing Scheme
Constant acceleration rate
Transition energy jump according to the below picture
RF phase flip at the instant of crossing during the jump

106.6
12.45
8.53
0
60
t (s)
2.4
t = 0.612 s
 = 1
= 0.5
tr
t = 60 ms

## Slide 29: Transition Energy Modification
Scheme by W. Hardt (1974)
Two quadrupole doublets are used in one arc
  Horizontal and vertical betatron phase advances between the quadrupoles in each pair are 
  Horizontal and vertical betatron phase advances between the pairs are 
The doublets excite dispersion wave around the ring thus modifying the transition energy
The betatron tunes and chromaticities change very little during the jump.
tr = 11.452
tr = 12.453

## Slide 30: Proton Spin During Crossing
On-momentum particle
Particle with =