## Slide 1: JLEIC SRF and fast harmonic kicker update
Bob Rimmer for SRF team
04-3-2017

## Slide 2: RF cavities for JLEIC
IP
Future IP
Ion Source
Booster
JLEIC
Collider
Rings
12 GeV CEBAF
Halls A, B, C
Electron Injector
Hall D
SRF Linac
e-RF
i-SRF +
NCRF
Crab
Crab
Cooling
e-RF
476.3 MHz e-ring
(NCRF PEP-II)
952.6 MHz i-ring
(SCRF)
952.6 MHz cooler ERL (SCRF)
952.6 MHz crab
(SCRF)
Harmonic Fast kicker for cooling ring
ODU
952.6 MHz booster
(SCRF)
Not including ion acceleration and bunch formation

## Slide 3: Outline
Storage ring cavities
Gap transient mitigation
Cooler ERL Linac and injector
Harmonic fast kicker
Cooling experiment support (Geoff Krafft)
Ion bunch formation scheme (Todd Satogata)
Crab cavities (Jean Delayen, ODU)
Modular cryostat – no change

## Slide 4: Storage ring cavities
e-ring based on PEP-II RF at 476.3 MHz
i-ring uses new SRF cavities at 952.6 MHz
Large contributions to impedance budgets
or
PEP-II raft assembly from SLAC
New on-cell damped cavity
2-cell end-group damped cavity

## Slide 5: 952.6 MHz SRF: Current status
1) 3WG. 2) 3 x coax dampers. 3) enlarged beam pipes (ref) 4) on-cell dampers
Cooler needs 5-cells in the ERL, 1-cells in the injector.
Ion ring might use 2-cells
New 952.6 MHz high-current cavity shape developed
1-cell prototype in progress on existing EIC R&D funds
HOM damping schemes under evaluation
Full RF system parameter tables defined

## Slide 6: Heavily-Damped Collider Ring Cavity
Progress has been made to design of a heavily damped 952.6 SRF single-cell cavity with on-cell waveguide dampers
The effective and broadband HOM damping with a similar arrangement of three waveguide dampers is well proven with normal-conducing cavities (e.g. BESSY 500 MHz cavity and PEP-II 476 MHz cavity)
The magnetic field enhancement at the surface (openings) can be limited to a factor of ~2 compared to standard elliptical cavities, around ~15 MV/m are feasible
F. Marhauser, “Next Generation HOM-damping”, Special Issue on Superconducting RF for Accelerators, to be published

## Slide 7: Example: Transverse Wakefield
Transverse wakefields are damped within ~15 m behind the leading bunch
Extremely small transverse impedances (several factors better than PEP-II or BESSY cavity)
well balanced dipole impedances
with highest Rtr
Fine-tuning of design is ongoing exploring a multi-dimensional parameter space
Goal: Finding compromise between longitudinal and transverse damping as well as the magnetic surface field enhancement, while accounting for ease of fabrication utilizing standard Nb sheet deep-drawing and port necking techniques

## Slide 8: Collider Ring Impedance Thresholds
Broadband damping of HOMs with on-cell dampers better than with any other design including enlarged tubes to un-trap low frequency modes
No costly beam tube absorbers are needed between cavities (risk mitigation and real estate savings)
F. Marhauser, “Next Generation HOM-damping”, Special Issue on Superconducting RF for Accelerators, to be published

## Slide 9
BEPC-II Electron Positron Collider Synchrotron Storage Rings at IHEP, Beijing, China
RF Transient Compensation Test at IHEP
H. Wang

## Slide 10: Transient beam loading
Experimental beam based studies for the future EIC to study the luminosity loss caused by the transient beam/SRF system interaction
Using the bunch-by-bunch RF feedback system build by Dimtel for BECP-II, we have obtained preliminary data set of different filling patterns and compensation technique by modulating bunch charge around the gap
Additional tracking simulations using JLab/LBNL/Dimtel/IHEP codes are under the way. The benchmarked tools will be used for future EIC designs
preliminary
Beam Loading & Instability Study at BEPC-II by IHEP/JLab/LBNL/Dimtel Collaboration
gap
gap
Even fill
Modulated fill
Phase
transient
reduced
transient
gap
Compensation
H. Wang

## Slide 11: Harmonic fast kicker
Strong cooling now the baseline (see Steve Benson’s talk)
ERL supplies bunches to circulator ring with 10-20 turns
Reduces average current in ERL/Injector but not peak charge
Requires fast and clean exchange of bunches
Strong cooling scheme as imagined by Dave Douglas

## Slide 12: 952.6 MHz cooler cavity prototype
Preliminary engineering analysis is complete
Cell and beam tube dies (110mm) have been fabricated
Test blanks have been pressed
End group design will be chosen based on simulations
Impedance requirements (Q spec)
HOM power (i-ring, e-ring, ERL)
Will produce single-cell first (possibly using ingot material)
σe,max = 15.2 MPa
F. Fors
J. Henry
L. Turlington
F. Fors
Notes: Red Interior Page Design 1

## Slide 13: First test pressings

## Slide 14: HOM Coupler Technology
The HOM power is distributed evenly among the coaxial couplers with the chosen Y-configuration
At these power levels the inner HOM coupler hooks need to be cooled actively (not done for JLab/Tesla-type coaxial coupler), which requires R&D on the coaxial coupler design (synergy with CERN cavity project)
Waveguide dampers are adaptable to higher power levels, high current (HC) design exists
5-cell cavity with one endgroup
utilizing 3 coaxial dampers
5-cell cavity with one endgroup
utilizing 3 HC waveguide dampers
Some of the power is propagating through beam tubes, yet the HOM power level extracted by the coupler is still significantly high
F. Marhauser

## Slide 15: HOM Power in ERL Cooler Cavities
Individual HOM power values
are summed up
Note that the spectral lines are weighted by the nominal 20 mm flattop bunch length, which produces the roll-off at the high frequency end (beyond 10 GHz however there will be a ripples due to the beer-can distribution, i.e. peak currents will raise again to some extent)
The monopole HOM power up to 9.5 GHz is 137 Watts @ 2nC bunch charge.
The HOM power is 350 Watts @ 3.2nC bunch charge
952.6 MHz
F. Marhauser

## Slide 16
~ns
~10 of ns
Few kV
Few mrad
CCR scheme required fast bunch swap out every 10-20 turns
Pulsed power supplies, especially with these characteristics are beyond state of the art.
An alternative driving method is summing simple cosine waves at sub-frequencies of the final beam repetition frequency to generate a continuous waveform.
Harmonic fast kicker
Y. Huang

## Slide 17: Kick Waveforms to Kick Every 10th Bunch
Chart: Bunch Distance (m)
Bunch | 55 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 55
Chart: Bunch Distance (m)
Bunch | 55 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 55
Chart: Bunch Distance (m)
Bunch | 55 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 55
Chart: Bunch Distance (m)
Bunch | 55 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 55
10 Harmonics+DC offset
9 Harmonics+DC offset
Y. Huang, J. Guo

## Slide 18: Kicker Cavity Model
5 harmonics 47.63MHz1,3,5,7,9
3 harmonics 47.63MHz2,6,10
1 harmonics 47.63MHz4
1 harmonics 47.63MHz8
Mode (MHz) | FFT Kick Voltage (kV) | CST Trans. Shunt Impedance (Ω) | Dissipated Power (W)
47.63 | 13.711 | 7.13E6 | 26.37
95.26 | 12.462 | 1.14E7 | 13.62
142.89 | 10.532 | 4.09E6 | 27.12
190.52 | 8.1290 | 1.35E7 | 4.89
238.15 | 5.5030 | 3.14E6 | 9.64
285.78 | 2.9170 | 6.09E6 | 1.40
333.41 | 0.6300 | 2.65E6 | 0.15
381.04 | -1.2090 | 1.65E7 | 0.09
428.67 | -2.4320 | 2.40E6 | 2.46
476.3 | -3.0110 | 4.57E6 | 1.98
DC | 8.2760 |  | 
Total | 55.508 | 3.56E7 | 87.72
Y. Huang

## Slide 19: Two Kicker Tracking Result
Flat-Top
Zero-Gradient
Equal-Amplitude
Least-Modes
Monitor 1
Monitor 1
Monitor 1
Monitor 1
Monitor 2
Monitor 2
Monitor 2
Monitor 2
Monitor 3
Monitor 3
Monitor 3
Monitor 3
Y. Huang

## Slide 20
Emittance Growth During Recirculation
Chart: Turn-by-turn Normalized Horizontal Emittance for Two-Kicker Scheme
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Flat-Top | 1.0741e-06 | 1.0741e-06 | 1.0741e-06 | 1.0741e-06 | 1.0741e-06 | 1.0741e-06 | 1.0741e-06 | 1.0741e-06 | 1.0741e-06 | 1.0741e-06
Zero-Gradient | 1.126e-06 | 1.1261e-06 | 1.1261e-06 | 1.1261e-06 | 1.1261e-06 | 1.1261e-06 | 1.1261e-06 | 1.1261e-06 | 1.1261e-06 | 1.1262e-06
Least-Modes | 1.0885e-06 | 1.0885e-06 | 1.0884e-06 | 1.0884e-06 | 1.0884e-06 | 1.0884e-06 | 1.0884e-06 | 1.0884e-06 | 1.0884e-06 | 1.0884e-06
Equal-Amplitude | 1.3266e-06 | 1.3273e-06 | 1.327e-06 | 1.3271e-06 | 1.3271e-06 | 1.3271e-06 | 1.327e-06 | 1.3272e-06 | 1.3269e-06 | 1.3275e-06
Y. Huang

## Slide 21: JLEIC Harmonic fast Kicker Development
Built a half-scale 5-mode copper prototype;
RF bench tests match well with the simulation;
Demonstrated combination of 5 harmonics.
Ph.D thesis of Yulu Huang, IMP
Y. Huang

## Slide 22: High-power model
Vacuum model concept in progress
Can test in UITF, LERF or ???
Need to settle on a baseline kicking scheme (angle, frequency) to go to the next step.
Eagerly anticipating new postdoc position
Need to study multi-turn effects with magnetized beams
J. Henry

## Slide 23
Take the best features of previous JLab designs
Modular approach to hold various different cavities
Design suitable for industrial production
Simple concepts, low parts count to reduce costs
476.3 MHz Crab cavity
Waveguide damper concept
Cooler ERL, 5-cell cavities
b=0.6 650 MHz cavity
Modular cryostat

## Slide 24: RF R&D roadmap
 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4
RF systems design and specification |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
952 MHz cavities: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ERL cooler 5-cell |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ERL booster 1-cell |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Storage ring bunching cavity |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Crab cavities (ODU) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Harmonic kicker cavity |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Ancillary components (windows, tuners, HOMs, etc.) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Integrated cooler test ? |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Modular cryostat |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LLRF and Bunch by bunch feedback systems, kickers |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2017
2018
2019
2020
2021
NP base
VA funds
FOA?
💰
💰
💰
💰?
📕?
ODU

## Slide 25: Conclusions
Storage ring cavities under development, meeting Impedance requirements.
Gap transient mitigation first test looks promising
Cooler ERL Linac and injector under development
Harmonic fast kicker proof of principle model successful, ready for vacuum model
Modular cryostat waiting for attention
Roadmap for base and VA funding, awaiting FOA.

## Slide 26: Back up

## Slide 27: Transient effects seen from frequency domain
With a uniformly spaced bunch chain, the bunch frequency is same as the RF generator frequency (frf), hence, the RF cavity of resonance frequency fres is a damped driven oscillator. Two solutions exist:
And the transient solution can be ignored. Hence, we will see only the steady-state solution with driving frequency, frf, and its harmonics.
With a gap, the frequency spectrum is complicated, the beam spectrum has fres component, which drives the fres oscillation in non-gap time period. At the same time, the continues generator current still produce the steady-state solution of frf . Because of the small frequency difference with frf , the sum of the two oscillations exhibits a periodic phase and amplitude variation, the transient effect.
Gap and double shoulders on ends of bunch chain. The spectrum changed, the fres component has a much lower amplitude, hence the transient effect is allevitated.
H=6832, gap = 5%
H=6832, gap = 5%, double shoulder
S. Wang