## Slide 1
Berkeley Lab Modeling Tools for Electron Cloud Build-Up and Effects on Beam Transport
Jean-Luc Vay, Miguel Furman
April 5, 2017
JLEIC Collaboration Meeting Spring 2017

## Slide 2
LBNL ATAP home of Accelerator Modeling Program
Chad
Mitchell
Ji
Qiang (deputy)
Rob
Ryne
Jean-Luc Vay (lead)
Rémi
Lehe
Kilean Hwang
Postdocs
Scientific Staff
Greg
Penn
Admin. Support
Lucky
Cortez
ATAP Collab.
Carlo
Benedetti
BELLA
Stepan
Bulanov
Hiroshi
Nishimura
Changchun
Sun
BELLA
ALS
ALS
William
Fawley
LBNL/SLAC
Alex
Friedman
Miguel
Furman
Brendan
Godfrey
LLNL
LBNL
U. Maryland
David
Grote
LLNL
Axel
Huebl
Manuel
Kirchen
Steven
Lund
U. Dresden
U. Hamburg
Michigan State U.
Affiliates
Guillaume Blaclard
Patrick
Lee
Students
Yue
Tao
Zhicong
Liu
Chuwen Luo
U. Paris-Saclay
Olga Shapoval
Jaehong Park
Maxence
Thevenet
Henri
Vincenti
CEA
(M. Curie Fellow)
Notes: Berkeley has a lot to offer with a unique collection of tools

## Slide 3: Maintains the “BLAST” simulation toolset for conventional & advanced concepts accelerators
blast.lbl.gov
State-of-the-art codes:
BEAMBEAM3D*, WARP, POSINST, IMPACT, FBPIC, INF&RNO, AMBER.
Wide set of physics & components:
beams, plasmas, lasers, structures, ...
linacs, rings, injectors, traps, …
Supporting many accelerators:
across U.S. DOE (HEP, BES, NP, FES, DNN) and beyond (CERN, DESY, KEK, …).
At the forefront of computing:
novel algorithms: boosted frame, etc.
part of SciDAC, NESAP & DOE Exascale.
*presentation Ji Qiang right after this talk.

## Slide 4: Electron Cloud Effects for EIC*
Panel priority: high.
Electron-cloud effects will have quite different characteristics for each of the proposed options.
The JLEIC ion beam may trap and accumulate electrons liberated by gas ionization, possibly leading to a classical electron-proton two-stream instability that might be counteracted by feedback.
The BNL rings will create an electron cloud by beam-induced multipacting. Copper coating might mitigate this, but it is not obvious that copper will provide a lower secondary emission yield than stainless steel.
*Report of the Community Review of EIC Accelerator R&D for the Office of Nuclear Physics - Feb. 2017

## Slide 5: The tools that we have at LBNL to study e-cloud effects
Posinst: build-up of e-cloud.
Warp: effect on beam dynamics.
Warp+Posinst: build-up & beam dynamics self-consistently.

## Slide 6: POSINST is a code for e- cloud build studies
  2-D electrostatic PIC.
  Advanced phenomenological SEY model with Monte Carlo generation of electrons with realistic energy-angle emission spectrum*.
  POSINST has been used to study electron cloud buildup in many accelerators around the world.
true sec.
back-scattered
elastic
re-diffused
Monte-Carlo generation of electrons with energy and angular dependence.
    *SEY model is a self-contained module. It has been imported into other codes for study of electron clouds and spacecraft charging.

## Slide 7: Example of simulation of e- buildup in CERN SPS
E-cloud distribution can be fed to a beam dynamics code.

## Slide 8: Warp: A Particle-In-Cell framework for accelerator modeling
Geometry: 3-D (x,y,z) axisym. (r,z) + FFT(q) 2-D (x,z) 2-D (x,y)
Reference frame: lab moving-window Lorentz boosted
        z z-vt (z-vt); (t-vz/c2)
Field solvers
electrostatic/magnetostatic - FFT, multigrid; AMR; implicit; cut-cell boundaries
Fully electromagnetic – Yee/nodal mesh, arbitrary order, spectral, PML, MR
Accelerator lattice: general; non-paraxial; can read MAD files
  solenoids, dipoles, quads, sextupoles, linear maps, arbitrary fields, acceleration.
Particle emission & collisions
  particle emission: space charge limited, thermionic, hybrid, arbitrary,
  secondary e- emission (Posinst), ion-impact electron emission (Txphysics) & gas emission,
  Monte Carlo collisions: ionization, capture, charge exchange.
y
z
x
Z (m)
R (m)
Automatic meshing around ion beam source emitter
Versatile conductor generator accommodates complicated structures

## Slide 9: Warp quasi-static mode used for e-cloud studies
2-D slab of electrons
3-D beam
s
proc 1 2 N/2 N/2+1 N-1 N
Station n n+1 n+N/2-1 n-N/2 n+N-2 n+N-1
Warp quasi-static model similar to HEADTAIL, PEHTS, QuickPIC, CMAD.
parallellized using pipelining
Beam ions
Electrons
Warp’s mesh refinement & parallelism provide efficiency

## Slide 10: Warp-POSINST integrated to model build-up & effect on beam
Beam ions
Electrons
Spurious image charges from irregular meshing controlled via guard cells
true sec.
back-scattered
elastic
re-diffused
Posinst provides advanced secondary electrons model
Monte-Carlo generation of electrons with energy and angular dependence.
Warp’s mesh refinement & parallelism provide efficiency
2-D slab of electrons
3-D beam
s
proc 1 2 N/2 N/2+1 N-1 N
Station n n+1 n+N/2-1 n-N/2 n+N-2 n+N-1
Warp quasistatic model similar to HEADTAIL, PEHTS, QuickPIC, CMAD.
parallellized using pipelining

## Slide 11: Example of multi-bunch e-cloud simulation of SPS*
11
  Code WARP+POSINST: 3D, parallel, multibunch, with feedback
  SPS at E=26 GeV (injection)
  3 batches of 72 bunches each (tb=25 ns, tbatch=200 ns)
  includes SEY model from POSINST (dmax=1.18)
  Bunch-to-bunch feedback (g=0.1) in horizontal plane (no V feedback)
  Ecloud was reinitialized to 0 at the beginning of every turn
    Seed mechanism: ionization of residual gas
  But proton density was allowed to evolve continuously for all turns
  Full run was for 1000 turns
  9,600 CPUs on Franklin supercomputer (NERSC) in 2011-2012
  *J.-L. Vay, IPAC12-WEPPP076

## Slide 12: Simulation parameters for SPS at injection, t=25 ns
12
  Bunch
    energy W=26. GeV
    population Np=1.11011
    RMS length z=0.23 m (Gaussian profile)
    momentum spread p/p=210-3
    transverse normalized emittance x= y=2.8 mm.mrad
    longitudinal normalized emittance z=0.3 eV.s
   : continuous focusing
    beta functions x,y= 33.85, 71.87
    betatron tunes  x,y= 26.13, 26.185
    chrom. Qx,y=0.,0.
  // : continuous focusing
    momentum compaction factor =1.9210-3
    cavity voltage V = 2 MV
    cavity harmonic number h = 4620.
  assumed 100% dipole
  10 interaction stations/turns

## Slide 13: Simulation gives insight in e-cloud/bunch interactions
Beam direction
1. Electrons from previous bunch or injected here from Posinst dump
Beam density (x1015) at t=0 (bunches 35-36 = buckets 176-181)
chamber wall
3D view
Bunch 35
Bunch 36

## Slide 14: Simulation gives insight in e-cloud/bunch interactions
14
2. Electrons are focused by bunch
chamber wall
3D view
Electron density (x1012m-3) at turn 1 (bunches 35-36 = buckets 176-181)

## Slide 15: Simulation gives insight in e-cloud/bunch interactions
15
3. High-density spikes eject electron jets
chamber wall
3D view
Electron density (x1012m-3) at turn 1 (bunches 35-36 = buckets 176-181)

## Slide 16: Simulation gives insight in e-cloud/bunch interactions
16
4. Secondary emission from impact of e- jets on walls
chamber wall
3D view
Electron density (x1012m-3) at turn 1 (bunches 35-36 = buckets 176-181)

## Slide 17: Simulation gives insight in e-cloud/bunch interactions
17
5. Electrons fill the chamber
chamber wall
3D view
Electron density (x1012m-3) at turn 1 (bunches 35-36 = buckets 176-181)

## Slide 18: Simulation gives insight in e-cloud/bunch interactions
18
6. Electrons interact with next bunch
chamber wall
3D view
Electron density (x1012m-3) at turn 1 (bunches 35-36 = buckets 176-181)

## Slide 19: Simulation gives insight in e-cloud/bunch interactions
19
Electron density (x1012m-3) at turn 500 (bunches 35-36 = buckets 176-181)
3D view

## Slide 20: Simulation gives insight in e-cloud/bunch interactions
20
chamber wall
Beam density (x1015m-3) at turn 500 (bunches 35-36 = buckets 176-181)
3D view
Bunch 35
Bunch 36

## Slide 21: Self-consistent evolution of e-cloud buildup and effects for 3 consecutive beams of 72 bunches in SPS
Bunch by bunch evolution at fixed station
Turn 1
Proton density
Electron density
Electron density
Turn 600
Proton density

## Slide 22: Electron density 50-100% larger with Warp+Posinst than with Posinst only
Substantial density rise in
tails of batches between turns 0 and 800.
Average electron cloud density history at fixed station
J.-L. Vay, et al, IPAC12 Proc., (2012) TUEPPB006
Conclusion: ne is ~50-100% larger at end of batch than if
computed via a build-up code with “static” beam

## Slide 23: Comparison with experimental measurements -- collaboration with SLAC/CERN
Fractional tune
Good qualitative agreement: separation between core and tail with similar tune shift.
Warp also applied to study of feedback control system (R. Secondo in collaboration with SLAC)
Warp-Posinst2
Bunch 29, Turn 100-200
head
tail
head
tail
Fractional tune
Bunch slice
Experiment1
Bunch 119, Turn 100-200
Nominal fractional tune=0.185
Bunch slice
1J. Fox, et al, IPAC10 Proc., p. 2806 (2011)
2J.-L. Vay, et al, Ecloud10 Proc., (2010)

## Slide 24: Summary
Posinst can simulate build-up of e-cloud
Warp can simulate effect on beam dynamics
Warp+Posinst can simulate both self-consistently
Warp open source at warp.lbl.gov
Posinst available upon request
  Send email to MAFurman@lbl.gov or JLVay@lbl.gov.
Could also use IMPACT & Marylie-IMPACT in combination, for more detailed tracking in lattice.