## Slide 1
Integration and Cold Testing of the CW ERL Cryomodule at Daresbury
Shrikant Pattalwar
ASTeC, STFC, Daresbury Laboratory (UK)
On behalf of
ERL Cryomodule Collaboration

## Slide 2
Introduction
The aim – To build and test the ERL Cryomodule
with beam on ALICE
Accelerator and Lasers
in Combined Experiment
Dimensioned to fit on the ALICE ERL facility at Daresbury:
  Same cryomodule footprint.
  Same cryo/RF interconnects.
  ‘Plug Compatible’ with existing cryomodule
2 Shrikant Pattalwar TTC meeting Nov 5-8, 2012 J-Lab

## Slide 3
Existing Cryomodule on ALICE
ERL (New) Cryomodule
Parameter | Target
Frequency (GHz) | 1.3
Number of Cavities | 2
Number of Cells per Cavity | 7
Cavity Length (m) | 0.807
Cryomodule Length (m) | 3.6
R/Q () | 762
Eacc (MV/m) | >20
Epk/Eacc | 2.23
Hpk/Eacc | 46.9
CM Energy Gain (MeV) | >32
Qo | >1010
Qext | 4 x 106 - 108
Max Cavity FWD Power (kW) | 20 SW
The ERL Cryomodule
3 Shrikant Pattalwar TTC meeting Nov 5-8, 2012 J-Lab

## Slide 4
High Power Input couplers
Saclay II tuners
3. HOM absorbers
4. Several thermal transitions
Major Variations in the Design
80-5-2
2-5-80
2-5-80-5-2
2
5
80
4 Shrikant Pattalwar TTC meeting Nov 5-8, 2012 J-Lab

## Slide 5
Radiation Shield, HOMs and thermal intercepts cooled with GHe
6. Additional thermal management scheme
7. Additional Instrumentation
Major Variations in the Design
5 Shrikant Pattalwar TTC meeting Nov 5-8, 2012 J-Lab

## Slide 6
Check the cryogenic performance
Understand the processes and establish commissioning and operating procedures
Validate instrumentation
Make the task of integration with ALICE easier
Identify and resolve any unknown issues
Off - line cold tests
6 Shrikant Pattalwar TTC meeting Nov 5-8, 2012 J-Lab

## Slide 7
Parameters | Measured* | Specification
Static Heat Load at 80K (HOMs, Thermal shield and intercepts.) | ~ 7 W | 20W
Static heat losses for the cavities at 80K | ~ 3.5 W | 15 W at 4K
Delta T across thermal shield at equillibrium | < 5K | <10K
Delta T across the two cavities during cooldown | < 5K | < 5K Currently 50K to 60K for ALICE
Cavity Temperatures
Results
Phase -1 Cool down to 80K (Cryogenics)
12 hrs
Calibration error
7 Shrikant Pattalwar TTC meeting Nov 5-8, 2012 J-Lab

## Slide 8
Results
Phase -1 Cool down to 80K (RF)
Tuner for cavity -2 freezes for T< 220K
Additional thermometry was added to
various locations on tuner assembly
Camera was inserted inside the isolation
chamber to observe the physical
movement of the motor
Cold tests were repeated but were
inconclusive
We decided to dismantle the cryomodule
(Clean room operation)
One of the shafts on the tuner assembly
was found to be misaligned
8 Shrikant Pattalwar TTC meeting Nov 5-8, 2012 J-Lab

## Slide 9
Bearing spacer installed rotated out of position. Shaft not correctly seated. And so 2.5mm high.
9 Shrikant Pattalwar TTC meeting Nov 5-8, 2012 J-Lab

## Slide 10
Independent Cold Tests on Tuner
10 Shrikant Pattalwar TTC meeting Nov 5-8, 2012 J-Lab

## Slide 11
Results
Phase -2 Cool down with LHe4
Chart: Motor Steps (x1000)
A
B
Lowest temperature ~ 8K
QL1=9x106
QL2=12x106
Resonant frequencies slightly out of range by ~400 KHz
Line A is expected to be at Line B (need to be adjusted manually)
One motor wired in the opposite direction
11 Shrikant Pattalwar TTC meeting Nov 5-8, 2012 J-Lab

## Slide 12
dT ~ 60K
Lowest temperature ~ 8K
Large Temperature gradient between the two cavities
Helium Reservoirs do not fill together
.......
Most of the issues can be attributed to high static heat load
( ~ 50W ) present during the tests
due to non ideal conditions and floating components
Heat leak will be much lower (< 5W) during actual
operation
COOL Down to ~ 4K
50
150
100
0
T_C1
T_C2
12 Shrikant Pattalwar TTC meeting Nov 5-8, 2012 J-Lab

## Slide 13
Cold Tests - Conclusions
Off Line Cold tests have proved to be important
Sufficient data has been collected that will help to reduce the cryomodule installation and commissioning period with an increased level of confidence
Most of the difficulties in the cryogenic tests can be attributed to non ideal conditions which will not be present during actual operation on ALICE.
The major issue with the operation of the tuner has been understood and resolved
Few minor problems relating mainly to errors in the sensor calibration or incorrect wiring, which have been identified and will be resolved before installation
13 Shrikant Pattalwar TTC meeting Nov 5-8, 2012 J-Lab

## Slide 14: ALICE Cryomodule Integration Scheduled in January 2013
TCF 50
2K BOX
1500 L Dewar
NEW LINAC
BOOSTER
COOL-IT
14 Shrikant Pattalwar TTC meeting Nov 5-8, 2012 J-Lab

## Slide 15
2007
2012
2013
2010
2009
2010
2010
2011
15 Shrikant Pattalwar TTC meeting Nov 5-8, 2012 J-Lab
Thank You