## Slide 1
Polarized Ion Beams with JLEIC
V.S. Morozov, Ya.S. Derbenev, F. Lin, Y. Zhang – JLab, Newport News, VA A.M. Kondratenko, M.A. Kondratenko – Zaryad, Novosibirsk, Russia
Yu.N. Filatov – MIPT, Dolgoprudny, Russia
Zgoubi support: F. Meot – BNL, Upton, NY
Workshop on polarized light ion physics with EIC
Ghent University, Ghent, Belgium, February 8, 2018

## Slide 2: Outline
Overall layout of JLEIC
Vector and tensor beam polarizations
Polarized ion sources
Polarimetry
Polarization rotation and its experimental demonstration
Figure-8 concept
Polarized beam acceleration in the JLEIC booster
Polarized beam acceleration, control and spin-flip in the JLEIC ion collider ring
Polarization measurement strategy
Summary and future work

## Slide 3: JLEIC Layout
3-12 GeV
8-100(400) GeV
8 GeV
2015
arXiv:1504.07961
Electron complex
  CEBAF
  Electron collider ring
Ion complex
  Ion source
  SRF linac (285 MeV/u for protons)
  Booster
  Ion collider ring
Optimum detector location for minimizing background
May 17 update:
https://eic.jlab.org/wiki/index.php/Main_Page
SRF Linac &

## Slide 4: Key Design Concepts
High luminosity: high collision rate of short modest-charge low-emittance bunches
  Small beam size
    Small β*  Short bunch length  Low bunch charge, high repetition rate
    Small emittance  Cooling
  Similar to lepton colliders such as KEK-B with L > 21034 cm-2s-1
High polarization: figure-8 ring design
  Net spin precession zero
  Spin easily controlled by small magnetic fields for any particle species
Full acceptance primary detector including far-forward acceptance
Beam Design
High repetition rate
Low bunch charge
Short bunch length
Small emittance
IR Design
Small β*
Crab crossing
Damping
Synchrotron radiation
Electron cooling

## Slide 5: JLEIC Energy Reach and Luminosity
CM Energy (in each scenario) | Main luminosity limitation
low | space charge
medium | beam-beam
high | synchrotron radiation

## Slide 6: JLEIC Parameters (3T option)
CM energy | GeV | 21.9 (low) |  | 44.7 (medium) |  | 63.3 (high) | 
 |  | p | e | p | e | p | e
Beam energy | GeV | 40 | 3 | 100 | 5 | 100 | 10
Collision frequency | MHz | 476 |  | 476 |  | 476/4=119 | 
Particles per bunch | 1010 | 0.98 | 3.7 | 0.98 | 3.7 | 3.9 | 3.7
Beam current | A | 0.75 | 2.8 | 0.75 | 2.8 | 0.75 | 0.71
Polarization | % | 80% | 80% | 80% | 80% | 80% | 75%
Bunch length, RMS | cm | 3 | 1 | 1 | 1 | 2.2 | 1
Norm. emittance, hor / ver | μm | 0.3/0.3 | 24/24 | 0.5/0.1 | 54/10.8 | 0.9/0.18 | 432/86.4
Horizontal & vertical β* | cm | 8/8 | 13.5/13.5 | 6/1.2 | 5.1/1.0 | 10.5/2.1 | 4/0.8
Ver. beam-beam parameter |  | 0.015 | 0.092 | 0.015 | 0.068 | 0.008 | 0.034
Laslett tune-shift |  | 0.06 | 7x10-4 | 0.055 | 6x10-4 | 0.056 | 7x10-5
Detector space, up/down | m | 3.6/7 | 3.2/3 | 3.6/7 | 3.2/3 | 3.6/7 | 3.2/3
Hourglass(HG) reduction |  | 1 |  | 0.87 |  | 0.75 | 
Luminosity/IP, w/HG, 1033 | cm-2s-1 | 2.5 |  | 21.4 |  | 5.9 | 

## Slide 7: Interaction Region Concept
Courtesy of R. Yoshida
Ion beamline
Electron beamline
Possible to get ~100% acceptance for the whole event
Central Detector/Solenoid
Dipole
Dipole
Forward (Ion) Detector
Scattered Electron
Particles Associated
with Initial Ion
Particles Associated with struck parton

## Slide 8
Detector Region
Integrated detector region design developed satisfying the requirements of
  Detection – Beam dynamics – Geometric match
GEANT4 detector model developed, simulations in progress
Forward hadron spectrometer
low-Q2 electron detection
and Compton polarimeter
p
(top view in GEANT4)
e
ZDC
IP
e
ions
forward e detection
Compton polarimetry
dispersion suppressor/
geometric match
spectrometers
forward ion detection

## Slide 9: Spin Density Matrix
Consider spin-1 state
Mathematical expectation of an operator
Mathematical expectation for an ensemble of particles
where is the fraction of particles in the state.
Due to randomness of the spin phases, is diagonal in an accelerator

## Slide 10: Beam Polarization
Cartesian vector and tensor spin operators ( is the quantization axis)
Density matrix representation
For a diagonal , the only non-zero expectation values are the “vector” and “tensor” polarizations

## Slide 11: Polarized Ion Sources
ABPIS: Atomic Beam Polarized Ion Source (IUCF, COSY)
OPPIS: Optically-Pumped Polarized Ion Source (RHIC)
Demonstrated technology
ABPIS has similar performance with polarized
There are ideas for modification of ABPIS to produce polarized and
 | (units) | Desired value | ABPIS+ | OPPIS*
Charge status |  |  |  | 
Pulse current | mA | 2 | 3.8 | 4 (0.7)
Pulse length | ms | 0.5 | 0.17 | (0.3)
Charge per pulse | μC | 1 | 0.65 | 
Protons per pulse | 1012 | 6.24 | 4.03 | 
Polarization | % | 100 | 91 | 85
 | (units) | Desired value | ABPIS+ | OPPIS*
Charge status |  |  |  | 
Pulse current | mA | 2 | 3.8 | 4 (0.7)
Pulse length | ms | 0.5 | 0.17 | (0.3)
Charge per pulse | μC | 1 | 0.65 | 
Protons per pulse | 1012 | 6.24 | 4.03 | 
Polarization | % | 100 | 91 | 85
+[Belov et al., Rev. Sci. Instrum. 77, 03A522 2006]
*[Zelenski et al., Rev. Sci. Instrum. 87, 02B705 (2016)]
-Linac parameters in parentheses; 85% polarization at 200 MeV
[Belov et al., Rev. Sci. Instrum. 77, 03A522 (2006)]
[Belov et al., Rev. Sci. Instrum. 67 (3) (1996)]

## Slide 12: Polarized Deuteron Source
COSY’s polarized ion source
Deuterium hyperfine states
(in strong magnetic field)

## Slide 13: Polarimetry
Differential spin-dependent cross-section (using lab-frame polarizations)
, for protons , for deuterons
Polarizations extracted using azimuthal count rate dependence and effective analyzing powers , .
For fast measurement, one can calibrate in terms of “left-right” scattering asymmetry and in terms of “left-right- top-bottom” asymmetries

## Slide 14: Tensor Polarization Dynamics
Preservation and control of vector polarization = preservation and control of tensor polarization
Spin wave function of spin- particle can be formally composed of spin wave functions of independent spin- particles
  Description of spin- dynamics in electric and magnetic fields reduces to description of spin-
  Demonstration of preservation and control of spin- polarization at the same time demonstrates preservation and control of spin- vector and tensor polarizations
Polarization rotation

## Slide 15: Experimental Demonstration
Sweeping an rf magnet’s frequency through a spin resonance can rotate the polarization
Spin rotation and Froissart-Stora formula
Demonstrated experimentally at COSY

## Slide 16: Ion Polarization Requirements
Major JLEIC ion complex components
Polarization design requirements
  High polarization (~80%) of protons and light ions (d, 3He++, and possibly 6Li+++)
  Both longitudinal and transverse polarization orientations available at all IPs
  Sufficiently long polarization lifetime
  Spin flipping
Ion
source
SRF linac
Booster
285 – 7062 MeV
(accumulator ring)
Ion collider ring
8-100 GeV/c
Cooling
Cooling

## Slide 17: Ion Polarization
Figure-8 concept: Spin precession in one arc is exactly cancelled in the other
Spin stabilization by small fields: ~3 Tm vs. < 400 Tm for deuterons at 100 GeV
  Criterion: induced spin rotation >> spin rotation due to orbit errors
3D spin rotator: combination of small rotations about different axes provides any polarization orientation at any point in the collider ring
No effect on the orbit
Polarized deuterons
Frequent adiabatic spin flips
n = 0

## Slide 18: Zero-Integer Spin Resonance & Spin Stability Criterion
The total zero-integer spin resonance strength is composed of
  coherent part due to closed orbit excursions, causes coherent spin tune shift (due to imperfections)
  incoherent part due to transverse and longitudinal emittances, causes spin tune spread (proportional to beam emittance)
Spin stability criterion
  the spin tune induced by a spin rotator must significantly exceed the strength of the zero-integer spin resonance
  for proton beam
  for deuteron beam

## Slide 19: Pre-Acceleration & Spin Matching
beam from Linac
Booster
to Collider Ring
BIIL
Polarization in Booster stabilized and preserved by a single weak solenoid
  0.6 Tm at 8 GeV/c
  d / p = 0.003 / 0.01
Longitudinal polarization in the straight with the solenoid
Conventional 8 GeV accelerators require B||L of ~30 Tm for protons and ~100 Tm for deuterons

## Slide 20: Spin Dynamics in Booster
Acceleration in figure-8 booster with transverse quadrupole misalignments
0.1 Tm (maximum) spin stabilizing solenoid
Spin tracking simulation using Zgoubi (developed by F. Meot, BNL)
protons
x0 = y0 = 1 cm
p/p =0
deuterons
x0 = y0 = 1 cm
p/p = 0

## Slide 21: Polarization Control in Ion Collider Ring
3D spin rotator: control of the radial, vertical, and longitudinal spin components
Module for control of the radial component (fixed radial orbit bump)
Module for control of the vertical component (fixed vertical orbit bump)
Module for control of the longitudinal component
IP
ions
3D spin rotator

## Slide 22: Spin Dynamics in Ion Collider Ring
100 GeV/c figure-8 ion collider ring with transverse quadrupole misalignments
Example of vertical proton polarization at IP. The 1st 3D rotator:  = 10-2 , ny=1. The 2nd 3D rotator is used for compensation of coherent part of the zero-integer spin resonance strength
Zgoubi
2nd 3D rotator for compensation
1st 3D rotator for control
with compensation
without compensation

## Slide 23: Spin Flipping
Adiabaticity criterion: spin reversal time must be much longer than spin precession period
 flip >> 1 ms for protons and 0.1 s for deuterons
Vertical (hy) & longitudinal (hz) spin field components as set by the spin rotator vs time  Spin tune vs time (changes due to piece-wise linear shape)
Vertical & longitudinal components of proton polarization vs time at 100 GeV/c

## Slide 24: Start-to-End Proton Acceleration
Three protons with and accelerated at ~3 T/min in lattice with 100 m rms closed orbit excursion,
Coherent resonance strength component
Zgoubi simulation
Analytic prediction

## Slide 25: Start-to-End Deuteron Acceleration
Three protons with and accelerated at ~3 T/min in lattice with 100 m rms closed orbit excursion,
Deuteron spin is highly stable in figure-8 rings, which can be used for high precision experiments
Analytic prediction

## Slide 26
Ion Polarimeter Location
Ion polarization in the straight section upstream of the IP is the same at the IP, however:
  Polarimeter target would generate detector background
  Polarimeter only measures transverse polarization, placing polarimeter upstream does not help with measurement of the longitudinal polarization
Polarization is rotated at any other potential polarimeter location
Determining polarization at IP becomes a question of knowing
  Polarization rotation angle from IP to polarimeter
  Polarization orientation at the polarimeter
  Calibration of the spin rotator
IP
e
ions
forward e detection
Compton polarimetry
dispersion suppressor/
geometric match
spectrometers
forward ion detection
80 m
ion polarimeter

## Slide 27: Polarimetry with Short Bunch Spacing
2. Accumulating coasting beam
3. Capture to bucket
4. Accelerate and cool
DC cooler
DC cooler
5. Bunch compression to ~56m
Step 6/7. Bucket-to-bucket transfer to the collider ring and BB cooling, repeat 26 times (Nh=28)
BB cooler
2x80m gaps
It is difficult to resolve individual bunches in a polarimeter with JLEIC’s short bunch spacing
It may be possible to measure polarizations of individual bunch trains
  There are 26 trains of 128 bunches each
  Individual bunches within each train have identical polarizations because of the way they are formed
  Polarimeter data may be gated during transitions between trains
JLEIC bunch formation
  26 bunches are injected into the ion collider ring
  Beam is accelerated to collision energy
  Each bunch is split in half 7 times, i.e. into 128 smaller bunches

## Slide 28: Summary and Future Work
It has been experimentally demonstrated that ion sources can provide vector and tensor polarizations of about 80% and potentially even higher
Figure-8 ring configuration should provide complete preservation and efficient control of the polarization; this has been verified by start-to-end simulations of polarized ion beam acceleration in JLEIC ion rings
Ion polarization control system has been developed and verified by simulations for the JLEIC ion collider ring; any polarization orientation can be adjusted at the IP
Adiabatic spin-flip has been demonstrated in simulations
Polarimetry concepts have been developed
Effects of detector solenoid, betatron coupling, and nonlinearities have been studied and understood
Ongoing and future studies
  Effects of crab crossing, beam-beam interaction, and electron cooling
  Benchmarking simulations against available data

## Slide 29: Backup

## Slide 30
Extracting Polarization at IP
Polarization rotation from IP to the polarimeter
should be small, e.g. polarimeter placed in the straight downstream of IP
Polarization orientation at the polarimeter and spin rotator calibration
Experimentally measure as a function of and and extract calibration of in terms of and