## Slide 1: Update on the BigBite Gas Ring Imaging Cherenkov (GRINCH) Detector for SBS
Todd Averett
Department of Physics
The College of William and Mary
Williamsburg, VA USA
Hall A Meeting
22-Jan-2018
In collaboration with:
C. Ayerbe-Gayoso, William and Mary
B. Wojtsekhowski, Jefferson Lab
Ahmidouch, S. Danagoulian, NC A&T
I. Niculescu, G. Niculescu, JMU
J. Annand, Glasgow
Physics Department at William and Mary
Wiki: http://wm-jlab.physics.wm.edu/mediawiki/index.php/Bigbite_Gas_Cherenkov
Email: tdaver@wm.edu

## Slide 2: Motivation: SBS High Rate Running
Heavy Gas threshold Cherenkov detector for pi/e separation.
For SBS: expect 4-5x increase in total luminosity over previous BigBite running.
Assume 4-5x larger background rate.
30 degree scattering angle
Segmented PMT array (qty= 512, 29mm tubes)
Search for timing clusters/rings in 5-10 ns window.
No ADCs—timing only
Magnetic shielding between rows.
Locate PMT array on large angle side away from beam line.
C4F10 heavy gas at 1 atm**

## Slide 3
BigBite Detector Stack – 12 GeV
Cherenkov
GEM x 4
GEM
Shower
PreSh
Hodo

## Slide 4
Mirror
Mirror
Frame
PMT
Array
Incoming
Particles
Top View of Geometry

## Slide 5: Design—S. Esp, JLab
Vessel Weldment
Front View
Complete Assembly
Front View

## Slide 6
Mirrors and Frame
Front View
Mirrors Out of Vessel
Rear View

## Slide 7: Mechanical Assembly Status
Vessel complete, windows installed, 120 um Al
Mirrors installed, aligned according to
E. Fuchey simulation
All PMTs tested, gain matched, installed
Light catcher cones installed
Gas system complete, in use
Removable door is leaking-work in “progress”

## Slide 8: Pictures
Entrance Window
Exit Window and Gas Panel
Mirror Frame

## Slide 9: Pictures
Nino front end cards
PMT array
PMT between iron & mu metal
PMTs with light catcher cones

## Slide 10: DAQ Status
Front-end NINO cards installed, PMT cables complete.
Power supply distribution board complete.
DAQ—VME-based VETROC system for timing, possible online cluster finding trigger.
VME ADCs for 15% of tubes.
64 Channel DAQ system testing ongoing with prototype detector.
Trigger up to 10 kHz.

## Slide 11: DAQ Info

## Slide 12: Gas Possibilities
C4F10 looks prohibitively expensive. Largest loss is through leakage based on Hall A and B experience.
Measuring index of refraction and UV absorbance of 3 less-expensive gases: SF6 , C4F8 , C3F8.
Possibility of using CO2 for GMn experiment which only needs 10:1 pion rejection. But CO2 gives a factor of three fewer photons.
Non-toxic, non-flammable; all are greenhouse gases
W&M interferometer for measuring refractive index

## Slide 13: Jlab WLS Paint Studies—S. Barcus, B. Wojtsekhowski
PMTs not sensitive to UV but Cherenkov spectrum most intense UV
Try using WLS paint that is used successfully in HRS Cherenkov
Using quartz rod with cosmics—seems to work

## Slide 14
JMU ADC using UV LED— Clear improvement
W&M results using D2 lamp and
Spectrometer—Paint not working
WLS Studies

## Slide 15: Plans
Seal leaking door
Continue DAQ tests with prototype
Install all cables
Assemble full DAQ
Finish testing gases
Full detector checkout
Estimate completion Fall 2018