## Slide 1: C75 LLRF
Curt Hovater
Also Contributing: Tomasz Plawski, Rama Bachimanchi, Dave Seidman and Clyde Mounts

## Slide 2: Outline
Existing C20/50 & C100 LLRF
LCLSII LLRF
Path to New Digital LLRF
C75 LLRF
  RF Front End
  Digitizer
  FPGA Carrier
  Interface to Controls
Questions/Comments/Thoughts

## Slide 3: Where We Have Been …Analog…Digital
Analog LLRF
  Circa 1992
  The present Analog RF system is labor intensive to maintain and repair
  System has obsolete and hard to find parts
  Crates are dying
C75s can utilize the existing analog LLRF systems but gradient and operability will be reduced because of Lorentz detuning.
C100 Digital LLRF System
  Been a workhorse
  But…next slide
Obsolete
Parts
Analog LLRF

## Slide 4: Unfortunately Continuing with C100 LLRF is Impossible
Design is 10 years old (hard to believe)
  Parts are difficult to obtain or not recommended for new design/production
    PC104 version is not available
    FPGA: Cyclone Three is not for “new” designs
    ADCs are 15 year old design …better components out there now
Design has flaws
  Channel Isolation barely met specification, limiting our gain and field control
  Clock chip can over heat and the modification is not optimum
  Lack of digital board (ADC/DAC/Clock and FPGA share same board) modularity makes it difficult to upgrade
  PC104 while a workable solution in 2006 is now cumbersome …there are better ways of doing this
At the time this was a good design and digital flexibility has allowed us to make up for some of the operational C100 flaws. It has become a work horse for SRF cavity testing

## Slide 5: A Sample of Obsolete Parts
Part | number | Board | Comment |  | 
Attenuator | TVA0200N05 | RF | All 4 of these attenuators are very hard to get and install. |  | 
Attenuator | TVA0300N03 | RF |  |  | 
Attenuator | TVA0600P08 | RF |  |  | 
Attenuator | TVA1000N07 | RF |  |  | 
FPGA | EP3C55F484C8 | Digital | Getting very hard to find. Will be phased out soon. FPGA - Cyclone III 3491 LABs 327 IO |  | 
Resistor | EZA-DT21AAAJ | Digital | Obsolete. Resistor Networks & Arrays Resistor-Cap Network Chip 4 RC's 1206 |  | 
Transformer | MABACT0034 | Digital | Obsolete. Audio Transformers / Signal Transformers 4.5-3000MHz Imp 1:1 50 and 75 Ohm |  | 
Memory | EPCS64SI16N | Digital | End of life. FPGA - Configuration Memory IC - Ser. Config Mem Flash 64Mb 40 MHz |  | 
Memory | MT48LC16M16A2TG-75:D | Digital | Obsolete. IC SDRAM 256MBIT 133MHZ 54TSOP |  | 
Processor | PC104 | Digital | Chad is working on a solution or we need to re-qualify another PC104 for our Network |  | 

## Slide 6: Which Way Next …
XFEL: Just completed …first light
  mTCA …compact but noisy for high performance RF receivers
  Good for taking a lot of signals in …like with a 32 cavity vector sum.
  Single cavity single source operating CW …not so much.
SLAC: Mission Readiness (replacing legacy LLRF) is prototyping with ATCA (big brother to mTCA).
  Design is having a hard time meeting isolation/noise specifications.
LCLSII: Going into production, design meets specification. …hmm…
An optimized hybrid of the LCLSII design using JLAB field control requirements.

## Slide 7: Leveraging LCLSII LLRF
JLAB has been in the LCLSII LLRF collaboration for four years. Its time that relationship pays off!
  System was designed by SLAC/LBNL/FNAL/JLAB
  C100 LLRF Functional Requirements were the basis for the LCLSII LLRF requirements.
It’s a great design both for performance and economic reasons.
LCSLII RF specifications and CEBAF RF specifications are similar.
1.497 GHz and the LCLSII cavity, 1.3 GHz, share some common components.
It’s been reviewed by system experts
  Final design review was held in July 2017
It’s been prototyped and tested on LCLSII cryomodules
It’s modular, so in 10 years if we need to change the FPGA carrier board we can with out upsetting the HW or SW.
It was designed with EPICS in mind.

## Slide 8: LCLSII Design Philosophy…We will CO-OPT
Requirements (0.5o/0.04%) demand ultra low noise design.
  Keep noise generators far from critical components i.e. no fans in RF chassis!
  Channel to channel isolation very good > 70 dB
    Isolate cavity signals from forward, reverse and drive signals
  Receiver noise floors < -150 dBc/Hz
  High gain system requires low group delay
Value Engineering: Build upon what has been done in the immediate past and what is commercially available.
  Designs based on LBNL/FNAL/JLAB recent work
  Components (Mixers/ADCs/Amps) commercially (Mini-circuits/ADI/TI) available.
  NAD system based around a common carrier board
Resources: Make the best use of available resources

## Slide 9: LCLS-II/CEBAF LINAC RF Requirements
LCLSII
Required Field Control is derived from the linac energy spread and beam jitter tolerances at the undulator.
CEBAF
Required Field Control is derived from the linac energy spread and based on the NP users requirements.
Both CEBAF and LCLSII dp/p is similar ~ 1e-4
LCLS-II LINAC
Courtesy Paul Emma
LCLSII Cavity Field Control Design Specification
For the time period > 1 Hz : 0.01% and 0.01o
For the time period < 1Hz: 5.0% and 5.0o
CEBAF Field Control Design Specification
  For the time period > 1 Hz : 0.04% and 0.5o (the tough one for CEBAF has been 0.04%)
  For the time period < 1Hz: ~ 3.0% and 3.0o

## Slide 10: Key Parameter Comparison Table
Parameter | CEBAF Specification | C100 LLRF Measured (rms.) | LCLSII LLRF Measured (rms.)
Phase Control | 0.5 | 0.2* | 0.002
Amplitude Control | 0.044% | 0.04%-0.05% | 0.003%
Channel Isolation | 60 dB | < 60 dB | 80 dB
The most important parameter in reaching our field control specification has been the channel to channel isolation. The original CEBAF specification was 60 dB which was based on the C20 cavity to cavity isolation. At the time (1990) this was a reach for RF electronics. The C100 had higher cavity to cavity isolation, but we stuck with the original specification for the electronics. As you can see from the table above the LCLSII isolation is much higher and this is reflected in the amplitude field control.
My suggestion is that we should raise the isolation specification (~ 70 dB) so that the we can achieve better amplitude field control, ultimately leading to lower energy spread.
*phase control is determined by our reference oscillator

## Slide 11: LCLSII LLRF Architecture*

## Slide 12: CEBAF LLRF (assumes one cavity/chassis)
EPICS
Timing
Beam Feedback
Resonance Control
Stepper
RF Station
Feedback Algorithms
Exception Handling
Forward &
Reverse Power
8 kW
Klystron
1.497 GHz Superconducting Cavities
GigE
Tunnel
Gallery
Cavity Signal
No PRC
Piezo Control

## Slide 13: LCLSII RF Station/Precision Receiver Chassis
Chassis tested at all LBNL and all partner laboratories
Tests have exceeded specifications – data later
Full documentation package has been developed
  Gerber files for all PCBs
  Cable drawings for all internal cabling
  BOMs for boards and chassis parts: heat sinks, filters, connectors, etc.
  Mechanical drawings for chassis enclosure, mounting plates, etc.
  Schematic Diagrams

## Slide 14: LLRF Architecture
  Field Control Chassis (RF Station)
    Receiver/Transmitter
      One cavities/chassis
      Probe, Forward, Reverse and Drive power
      Klystron Amplifier Drive
      IF Processor and FPGA
    Channel Isolation in the RFS is better (~80 dB) than the 60 dB we designed to 10 years ago, so it easily meets our specification
    Greatly simplifies design
      One RFS can control one/two C75 cavities
  Resonance Control
    Stepper Motor Control
      Eight cavities per chassis
      Same FPGA/carrier as RFS
    Fiber communication with RF station
  Interlocks (Modified Design)
    Similar to C100
      Eight cavities per chassis
      Same FPGA/carrier as RFS
    Fiber communication with RF station
  HPA Controller (Modified Design)
    Similar to R100
      Eight klystron per chassis
      Same FPGA/carrier as RFS
    Fiber communication with RF station

## Slide 15: Where We Are …
RF Front End: Tomasz is investigating what can, what needs modification and what can’t be used from the LCLSII RR front end.
  Presently prototyping a three channel receiver to test
  As we get further along it appears that while we can use the LCLSII RF as a guide, we will need to build our own receiver.
FPGA Carrier Card: Rama is taking the LCLSII Xlinx carrier card design and investigating Intel (Altera) FPGA for our use.
  Low start up costs, Initial tests can be done with evaluation boards
  Goal is to develop the UDP between the FPGA and the EPICS IOC (this has already been done for LCLSII, and in use in the CMTF and LERF).
  Big Incentive: Eliminates PC104 and reduces the EPICS IOC count/zone from 11 to 1!

## Slide 16: RF Front End
RF boards key features
Standard heterodyning architecture with passive, level 13 mixers
CEBAF 70 MHz IF – although we are still investigating the possibility to use lower IF frequency (35 MHz)
Single DAC transmitter with the oversampling (280 MHz) and heterodyning
LCLS-II Similarities
Aluminum cooling plate underneath the RF boards instead of forced air flow above
Separated boards for the receivers and the transmitters
6 channel receiver and 2 channel transmitter in one chassis (not decided yet)
High quality RF shielding
Some PCB solutions , Rogers laminates (?) , very similar layout
Power supply outside of the LLRF chassis

## Slide 17: Digitizer Board
Modular design
High speed ADC
High speed DAC
Clock distribution
GPIO and diagnostic ADC/DAC
CAD: Altium (what JLAB uses)
Plan: Take the LCLSII design add frequency correct transformers (for ADC) and go from there.
LCLSII Digitizer Board

## Slide 18: FPGA Board
Generic FPGA board with Ethernet PHY (10/100/1000 Mbps) and SFP (Small form-factor pluggable transceiver) capability
HSMC (High Speed Mezzanine Card) connector for Altera FPGA
FMC (FPGA Mezzanine Card) connector for Xilinx FPGA
Faster time to develop a system with a generic FPGA board
  Will reduce time and cost for one of a system e.g. 4 Laser
  Don’t have to design a board with FPGA every single time
  Cost and complexity will be lower for systems
Interfaces to network switch over copper/fiber
Compatible with test boards from manufacturers (TI, ADI etc.)

## Slide 19: EPICS IOC
One IOC per zone (e.g. computer)
  Now we have 11+ IOCs/zone!
All the FPGAs are connected to IOC over a private LAN (copper/fiber)
UDP for communication between IOC and FPGA
  Being used for resonance and interlocks in the CMTF Now!
This architecture eliminates the need to have one IOC per chassis
  Allows hardware to be moved from zone to zone easier …

## Slide 20: RF Racks
  General Rack area needs to be temperature controlled between 20 and 25C (basically what we have now)
    This is needed for noise issues. There are no fans planned for the FCC chassis.
  Rack Components
    LO and RF Signals
    Field Control Chassis
    Resonance Control
    Power Supply
    Cavity/Cryomodule Interlocks
    HPA Controller
  RF signals (cavity, forward, reflected) are brought to the front panel.
20
L
L
L
L
L
L
L
L
L
LO Distribution
FCC 1
Power Supply
Switch
FCC 2
FCC 6
FCC 7
FCC 8
FCC 5
FCC 3
FCC 4
Interlocks
Resonance
HPA Controller
Power Supply
Switch

## Slide 21: System Q&A
Three Design Reviews
  Preliminary
  Final
  Production Readiness
Production Test Benches/Stands
  Similar to C100 LLRF
  All chassis tested automatically using EPICS
  Individual boards tested on bench
Zone/Commissioning Tests
  Similar to C100 with a complete interlock, calibration and RF performance checkout.

## Slide 22
SUMMARY
New LLRF has a solid design foundation
Flexible: Meets the needs of C75s and all/aging LLRF systems elsewhere in the CEBAF LINACs
Modular design allows for continual production as parts become obsolete
Fits into existing “two-rack” footprint
Allows C75s to meet their operational expectations
Thank you for your time
Questions, Comments and Thoughts