## Slide 1: Accelerator Technology Transfer Opportunities
Jefferson Lab Technology Transfer Workshop:
Fostering Market Pull on Technologies
CEBAF Center, F113
R. Rimmer, SRF R&D dept.

## Slide 2: Accelerator technology transfer opportunities
Outline
What we do
How we do it
Opportunities for wider use of the technology
Barriers to adoption
What are we doing about it?
Conclusions

## Slide 3: Accelerator technology transfer opportunities
What we do
  Big accelerators for discovery science
  CEBAF, SNS, LCLS-II, ILC, JLEIC, FCC
  Specializing in SRF re-circulating and energy recovery linacs

## Slide 4: Big Accelerators for Discovery Science
New Hall
Add arc
Enhanced capabilities
in existing Halls
Add 5 cryomodules
Add 5 cryomodules
20 cryomodules
20 cryomodules
New Hall
Add arc
Enhanced capabilities
in existing Halls
Add 5 cryomodules
Add 5 cryomodules
20 cryomodules
20 cryomodules
New Hall
Add arc
Enhanced capabilities
in existing Halls
Add 5 cryomodules
Add 5 cryomodules
20 cryomodules
20 cryomodules
New Hall
Add arc
Enhanced capabilities
in existing Halls
Add 5 cryomodules
Add 5 cryomodules
20 cryomodules
20 cryomodules
New Hall
Add arc
Enhanced capabilities
in existing Halls
Add 5 cryomodules
Add 5 cryomodules
20 cryomodules
20 cryomodules
New Hall
Add arc
Enhanced capabilities
in existing Halls
Add 5 cryomodules
Add 5 cryomodules
20 cryomodules
20 cryomodules
CEBAF linac
CEBAF Linac
SNS
ILC
12 GeV CEBAF

## Slide 5: RF cavities for JLEIC
IP
Future IP
Ion Source
Booster
JLEIC
Collider
Rings
12 GeV CEBAF
Halls A, B, C
Electron Injector
Hall D
SRF Linac
e-RF
i-SRF +
NCRF
Crab
Crab
Cooling
e-RF
476.3 MHz e-ring
(NCRF PEP-II)
952.6 MHz i-ring
(SCRF)
952.6 MHz cooler ERL (SCRF)
952.6 MHz crab
(SCRF)
Harmonic Fast kicker for cooling ring
ODU
952.6 MHz booster
(SCRF)

## Slide 6: Accelerator technology transfer opportunities
What we do
  Big accelerators for discovery science
  CEBAF, SNS, LCLS-II, ILC, JLEIC, FCC
  Specializing in SRF re-circulating and energy recovery linacs
How we do it
  Develop optimized accelerator solutions for emerging needs
  Prototype in house
  Utilize industry for large scale production
  Qualification and integration in house up to now

## Slide 7: A sampling of JLab’s Cavity R&D
HC 5-cell1.5 GHz C75 Cavity (CEBAF)
CEBAF 750 MHz separator
Beta-matched 2-cell for new injector CM
For CEBAF
1.5 GHz ERL twin-axis cavity
5-cell 802 MHz ERL main linac cavity (PERLE/Orsay & LHeC/CERN)
750 MHz compact SRF-based environmental accelerator
For SPPs and R&D
2-cell 952.6 MHz ion ring cavity
First 952.6 MHz cavity parts
JLEIC 5-cell 952.6 MHz ERL cooler
Harmonic kicker magnetization cavity
For JLEIC

## Slide 8: Accelerator technology transfer opportunities
What we do
  Big accelerators for discovery science
  CEBAF, SNS, LCLS-II, ILC, JLEIC, FCC
  Specializing in SRF re-circulating and energy recovery linacs
How we do it
  Develop optimized accelerator solutions for emerging needs
  Prototype in house
  Utilize industry for large scale production
  Qualification and integration in house up to now
Opportunities for wider use of the technology
  Spin off applications
  FEL’s, isotopes, compact light sources, e-beam sources, ADS

## Slide 9: JLab IR/UV FEL Light Sources
E = 135 MeV
Up to135 pC pulses @ 75 MHz
20 μJ/pulse in (250)–700 nm UV-VIS
120 μJ/pulse in 1-10 μm IR
1 μJ/pulse in THz
The first high current ERL
14 kW average power
Ultra-fast (150 fs)
Ultra-bright
Now converted to LERF
Possible location for isotope production
and other accelerator R&D

## Slide 10: Compact X-ray Light Source Concept
SRF Gun
Emittance exchange line for coherent ICS
ICS x-ray generator
Project scope includes:
beam simulation,
cavity design and fabrication,
cryostat design and fabrication,
development of Nb3Sn coatings
Jefferson Lab: inexpensive SRF linac operating at 4.5K
Clean sheet design, cavity and cryostat!

## Slide 11: Accelerators for Isotope Production
Low Energy Recirculator Facility (LERF) is proposed for isotope production in non-ERL or ERL mode
  Up to 150 MeV energy electron beam
  Up to 100 kW beam power
A. Hutton, R. Johnson, AccApp’17 Quebec City

## Slide 12: Compact high-power CW SRF accelerator for industrial application
1-year design collaboration among JLAB, AES, General Atomics
Funded by DOE-HEP (Accelerator Stewardship)
Use in wastewater and flue-gas treatment
1 MeV, 1 A electron beam
~6 m
Nb3Sn/Nb/Cu b=0.5 single-cell cavity, conduction cooled with four 1.5 W cryocoolers
Patent on Cryomodule design filed on 01/29/18

## Slide 13: Compact, scalable normal-conducting e-beam source
The source uses new technology developed at JLab as well as established components
Scalable in size (frequency) and power
Additional units could be stacked for higher energy
Gridded electron gun
Vacuum pumping
Magnetron RF source
Compact graded-b copper linac
Focusing coils
Deflecting system
Horn
Exit window
915 MHz 100 kW

## Slide 14: Accelerator Driven System: MYRRHA Concept
Accelerator
(600 MeV – ≤ 4 mA proton)
Reactor
Subcritical mode (~85 MWth)
Critical mode (~100 MWth)
Subcritical reactor
Neutrons from spallation target
Lead-Bismuth cooled or molten salt reactor
Can destroy surplus weapons grade Pu
Can burn spent fuel from conventional reactors or Thorium

## Slide 15: Accelerator technology transfer opportunities
What we do
  Big accelerators for discovery science
  CEBAF, SNS, LCLS-II, ILC, JLEIC, FCC
  Specializing in SRF re-circulating and energy recovery linacs
How we do it
  Develop optimized accelerator solutions for emerging needs
  Prototype in house
  Utilize industry for large scale production
  Qualification and integration in house up to now
Opportunities for wider use of the technology
  Spin off applications
  FEL’s, isotopes, compact light sources, e-beam sources, ADS
Barriers to adoption
  High capital cost of SRF-based systems, despite efficiency
  Perception of high maintenance, questionable reliability
  Lack of industry base for long term support

## Slide 16: Accelerator technology transfer opportunities
What we do
  Big accelerators for discovery science
  CEBAF, SNS, LCLS-II, ILC, JLEIC, FCC
  Specializing in SRF re-circulating and energy recovery linacs
How we do it
  Develop optimized accelerator solutions for emerging needs
  Prototype in house
  Utilize industry for large scale production
  Qualification and integration in house up to now
Opportunities for wider use of the technology
  Spin off applications
  FEL’s, isotopes, compact light sources, e-beam sources, ADS
Barriers to adoption
  High capital cost of SRF-based systems, despite efficiency
  Perception of high maintenance, questionable reliability
  Lack of industry base for long term support
What are we doing about it?
  R&D on cost reduction, new materials, modular systems, RF power sources

## Slide 17: What are we doing about it?
R&D on cost reduction:
  New materials, 4.5K operation
  Cheaper, more efficient RF power sources
  Modular systems
  Safer, cheaper processing methods
Focus on improving CEBAF reliability
  Conservative design for reliability
Outreach to industry (SBIR/STTR etc.)

## Slide 18: What are better SRF Materials?
Tc [K] | ρn [μΩcm] | Δ [meV] | Hc(0) [T] | Hsh(0) [T] | Hc1(0) [T] | (0) [nm] | Material
9.25 | 0.1 | 1.45 | ~ 0.2 | ~ 0.24 | ~ 0.17 | 40 | Nb
17.2 | 70 | 2.6 | ~ 0.23 | ~ 0.19 | ~ 0.02 | ~ 200 | NbN
17.5 | 35 | 3.0 | ~ 0.28 | ~ 0.24 | ~ 0.03 | ~ 151 | NbTiN
18.3 | 5 | 3.1 | ~ 0.54 | ~ 0.45 | ~ 0.05 | ~ 85 | Nb3Sn
40 | 2 | 2.3/7.1 | ~ 0.43 | ~ 0.27 | ~ 0.03 | ~ 140 | MgB2
s-wave superconductor
large energy gap
high HSh
low normal conducting resistivity
Material | Nb | Nb3Sn
Tc [K] | 9.25 | 18.3
ρn [μΩcm] | 0.1 | ~ 5
Hsh(0) [T] | 0.24 | ~ 0.45
Δ [meV] | 1.45 | ~ 3.1
QBCS @ 2K | ~ 5·1010 | ~ 5·1014
QBCS @ 4K | ~ 5·108 | ~ 5·1010
Eacc [MV/m] | ~ 50 | ~ 100

## Slide 19: JLab Nb3Sn 5-cell progress
Reasonable low-field Q0, but a strong Q-slope, similar to the one measured in 5-cell cavity coated at Wuppertal University. Medium field Q-slope is likely due to equator features.
Nb3Sn coating is present, but is not uniform. The top of the cavity seems “shinier” than the bottom
New 17” OD x 40” furnace insert
The new configuration was commissioned up to 1250 °C on May 4, 2017.
Looking from the top
C50
2K spec
Original CEBAF 2K spec
IA007(no end-groups)
Nb3Sn grain structure
G. Eremeev early career award
preliminary
More 5-cell cavity tests coming soon!

## Slide 20: Nb3Sn: Towards cryomodule testing
Nb3Sn??
A quarter cryomodule with Nb cavities was tested at 4 K in CEBAF injector. The module accelerated the beam to the nominal energy. There was no discernible difference in the beam quality between 4 K and 2 K.
CEBAF injector quarter cryomodule
The layout of the Upgraded Injector Test Facility (UITF)
Plan to test 2 cavities with beam in the next 2-3 years

## Slide 21: JLab R&D on magnetron RF source
L3 13 kW klystron
National 1.2kW oven magnetron
L3 20-80kW magnetron
Why?
Klystron: Space-charge effect in electron bunch forming process in linear motion dominates the efficiency. Spent energy deposits in the collector.
Magnetron
forms bunches in spoke-on-hub process in circular motion. Beam-to-RF cavity interaction in multiple passes. Much less wasted energy.
Varian 5 kW klystron
12.2
H. Wang

## Slide 22: 2.45GHz Magnetron R&D Test Stand with SBIR-II Fund
2.45GHz Magnetron RF Test Stand
Digital RF FPGA Control Chassis
2.45GHz RF Front End Controller
CST magnetic circuit design with +-10% trimming coils on cooker magnetron

## Slide 23: Modular Cryostat
Take the best features of previous JLab designs
Modular approach to hold various different cavities
Design suitable for industrial production
Simple concepts, low parts count to reduce costs
476.3 or 952.6 MHz Crab cavity
952.6 MHz Ion ring concept
Cooler ERL, 5-cell cavities
476.3 MHz 1-cell?

## Slide 24: Lowering the entry point for Commercial SRF production
Partnering with small electrochemistry innovation company
Developing low-hazard niobium polishing chemistry
  Reduce/avoid the use of dangerous hydrofluoric acid
  Safer, greener, cheaper process
Bring general-service metals processing companies into the game
Weak sulfuric acid or even salt water will do the job.
E. J. Taylor, M. E. Inman, T. D. Hall
"Electrochemical system and method for electropolishing superconductive radio frequency cavities"
U.S. Pat No. 9 006 147, April 14, 2015.
SBIR success story, started with small sample exploration and JLab-supplied scientific analysis
Faraday Technology Inc. has secured international patents.

## Slide 25: Conclusions
Many promising concepts and technologies at JLab
Active R&D on cost reduction, performance improvement
Engaged in SBIR/STTR partnerships
Keen to see new and non-traditional uses for the technology
How to transition from concepts to first applications?

## Slide 26
Back up

## Slide 27: 2K and 4K JLab Technology Development Areas
3x Power Reduction
20-25% Power Reduction
2008 12 GeV PED
Dana Arenius
Large machines are getting more efficient
Difference between 2K and 4K does not make up for BCS losses

## Slide 28: Scalability
The size and power may be simply scaled according to available source frequencies. Higher energies may be obtained using pulsed operation or by stacking additional modules in series.
  915 MHz 1497 MHz 2450 MHz
  ~100 kW 10-50 kW 1-5 kW
  0-1MeV 0-500 keV 0-250 keV
Stationary Applications mobile “portable”

## Slide 29: Scale up
For factory processing of sheets prior to installation a larger static installation is preferable. For wide mill runs it may be more convenient to stack multiple compact units in parallel.
Direction of
sheet travel
Static installation
Beam fan

## Slide 30: State-of-the-Art Gradient Results
As a result of continued SRF cavity R&D at CERN, Cornell, DESY, JLAB, KEK, SACLAY and other labs, modern 9-cell TTF-style cavities increasingly exceed 35 MV/m at Q0 P 8109. Gradient in the range of 40-43 MV/m demonstrated and confirmed independently in real 9-cell (and 7-cell) cavities, corresponding to a surface magnetic field of 160-180 mT.
ILC 500 GeV
R&D Gradient Goal

## Slide 31
The Intensity Frontier for Protons
Central challenge at the beam power frontier is controlling beam loss to minimize residual activation
1 nA protons at 1 GeV, a 1 Watt beam, activates stainless steel to 80 mrem/hr at 1 ft after 4 hrs
High beam current
  BBU control (HOMs)
  Low Frequency large aperture cavities
  High power, high efficiency RF sources
J. Wei , “China Spallation Neutron Source Design”, APAC 2007, Indore, India

## Slide 32
Capital and operation cost saving for CEBAF in RF power
Low cost of magnetron device
DC-to-RF efficiency from klystron to magnetron improves from ~35% to ~90%
2.22MW of DC power saving
$2.8 million saving in power bill, if 41 weeks/year of CEBAF in 6-12GeV operation
Technology demonstration for all SRF accelerators in the DOE complex
Magnetron RF source, the potential impact
References:
[1] A. C. Dexter, G. Burt, R. G. Carter, I. Tahir, H. Wang, K. Davis and R. Rimmer, PRST-AB, 14, 032001 (2011).
[2] M. Nuebauer, A. Dudas, R, Rimmer, H. Wang, An Efficient RF Source for JLab, PAC 2013, Pasadena, CA, USA.
[3] H. Wang, T. Plawski, R. Rimmer, Simulation Study Using Injection Phase Locked Magnetron as an Alternative Source for SRF Accelerators , IPAC 2015, May 3-8, 2015, Richmond, VA, USA .
[4] H. Wang, T. Plawski, R. Rimmer, M. Neubauer, A. Dudas, Simulation and Experimental Studies of a 2.45GHz Magnetron Source for an SRF Cavity with Field Amplitude and Phase Controls, IPAC 2016, May 8-13, 2016, Busan, Korea
2.45GHz Magnetron RF Test Stand

## Slide 33
1000 Apmturns=10% B field trimming
Magnetic field coil current
Moving working point along the fixed frequency line when changing the output amplitude
Magnetron trim coil modulation experiment

## Slide 34
FY2018 Accelerator Stewardship Proposal for DOE National Lab 18-1879
More than 85% efficiency of magnetron in mass production
is commercial available