## Slide 1
EIC Accelerator Collaboration Meeting October 29 - November 1, 2018
Beam Dynamics in the CCR
Speaker: Chris Tennant, Jefferson Laboratory
Collaborators: Slava Derbenev, David Douglas, Fay Hannon, Andrew Hutton, Rui Li, Bob Rimmer, Yves Roblin, Chris Tennant, Haipeng Wang, He Zhang, Yuhong Zhang

## Slide 2: Outline
Why a CCR?
  transition from weak to strong cooling
What is the CCR?
  cooling channel
    drives system requirements (beam energy, emittance, match, distribution, etc.)
  recirculation arcs
    intersection of many beam dynamical processes
  beam exchange
    possible with development of fast kickers
Summary
  current status
  path moving forward

## Slide 3: Background
initial design effort focused on “weak cooling”
  single pass ERL
  moderate charge (420 pC)
  preliminary injector design developed
  generated ERL design with acceptable performance with “ideal” injected beam
in late 2016 the specifications were changed to “strong cooling”
  extremely high charge (3.2 nC)
  extremely high current via CCR (1.5 A)
  retain the ERL solution as a driver for CCR
    relaxes average current burden on ERL in exchange for increased bunch charge

## Slide 4: Weak Cooling
Parameter | Value
Injected momentum | 5 MeV/c
Momentum at cooling channel | 55 MeV/c
RF fundamental frequency | 952 MHz
Bunch repetition frequency | 476 MHz
Bunch charge | 420 pC
Bunch length at cooling channel (full) | 2 cm / 66.7 ps / 22.9°
Energy spread at cooling channel (rms) | 3×10-4
Cooling solenoid strength | 1 T
Normalized horizontal drift emittance | 36 mm-mrad
Normalized Larmor emittance | <19 mm-mrad
arc
arc
solenoid
solenoid
flip
magnetized gun
booster
linac
de-chirper
chirper
ion beam
cooling solenoid
beam dump
cooling solenoid
magnetization flip

## Slide 5: Strong Cooling
harmonic kicker exchanges every 11th CCR bunch between ERL and CCR
Beam Exchange (side)
CCR
ERL
DC & RF kicker
chirper
chirper
injected bunch orbit
extracted bunch orbit
dipole
dipole
DC & RF kicker
CCR (top)
ion beam
cooling solenoids
magnetization flip
septum
magnetization flip
DC & RF kicker
DC & RF kicker
ERL (bottom)
magnetized gun
booster
linac
beam dump
chirper
chirper
dipole
dipole

## Slide 6: Background
top level requirements are “standard” for an ERL
  generate, accelerate, and deliver to user a properly configured beam
  recover (possibly degraded) beam after use
  preserve beam quality, avoid instabilities and limit losses
unique features of JLEIC cooling system:
  magnetized beam
    axially symmetric transport
  high charge
    collective effects aggravated
  long bunch
    samples large(r) part of RF waveform
  small momentum spread
    susceptible to wake-induced distortion

## Slide 7: Recirculation Arcs
ERL has 360° of bending
CCR has 11 × 360° of bending
the CCR arc has the following requirements:
  local axial symmetry – preserve magnetization
  globally isochronous – longitudinal match
  locally isochronous - manage CSR and mBI
  locally achromatic – manage CSR and mBI
  high periodicity – suppress aberrations and error sensitivities
  moderate size – avoid space charge degradation
not easy to satisfy all conditions simultaneously

## Slide 8: Arc Layout
design by D. Douglas (JLAB-TN-18-009)
do not force the conditions of
  high periodicity
  local axial symmetry
start with a simple baseline arc, analyze and determine level of increased complexity required
sextupole
quadrupole
dipole

## Slide 9: Microbunching Gain
needs to be less than unity for multiple passes
  total gain goes as gain(1-turn)Number Passes
consider the gain for multiple turns in a “CCR ring” (two arcs put together)
modest gain for 1-arc ~ 5

## Slide 10: Effect of CSR on Longitudinal Phase Space
no CSR
CSR
CSR “corrected”

## Slide 11: RF Correction for 20 Turns
after 20 turns
initial
cannot compensate head/tail effects
will need to explore collimation schemes

## Slide 12: CSR Shielding
shielding of CSR is effective when the full aperture size is less than where R is the bend radius and sz is the rms bunch length
for R = 0.53 m and sz = 4.95 mm, the (full) aperture needs to be less than ~2 inches (5.04 cm)
for sz = 4.95 mm
with CSR + shielding
with CSR

## Slide 13: TStep – Multiturn Tracking
space charge only

## Slide 14: elegant – Multiturn Tracking
CSR only

## Slide 15: elegant – Multiturn Tracking
CSR with csrdrifts

## Slide 16: Bmad – Multiturn Tracking
CSR with csrdrifts and with CSR shielding (5 cm)

## Slide 17: Putting It All Together: “S2E”
Simple Arc
pathlength = 194.5973 m ~ 618lRF
solenoid
solenoid
solenoid
solenoid
15 m
15 m
15 m
15 m
4.8 m
4.8 m
5.4 m
Simple Arc
-40 -20 0 20 40
Z (m)
0
-10
X (m)
incorporate beam exchange, recirculation arcs, cooling solenoids, magnetization flips
track distribution through entirety of the CCR
use reduced charge (1.6 nC)

## Slide 18: RMS Beam Sizes

## Slide 19: (x,y) Phase Space
exit turn 1
exit turn 2
exit turn 3
exit turn 5
exit turn 6
exit turn 7
exit turn 9
exit turn 10
exit turn 11
exit turn 4
exit turn 8
CCR entrance

## Slide 20: (t,p) Phase Space
exit turn 1
exit turn 2
exit turn 3
exit turn 5
exit turn 6
exit turn 7
exit turn 9
exit turn 10
exit turn 11
exit turn 4
exit turn 8
CCR entrance

## Slide 21: Summary: Beam Dynamics Issues
CSR, space charge, mBI: machine lives in unique part of parameter space
beam breakup (BBU): well understood, need full system to assess impact
halo: serious problem, not yet addressed, need good simulation statistics
  halo formation effects: IBS, Touscheck, beam dynamical processes
ion trapping: potential problem
environmental wakes, impedances, etc.
collimation
  not demonstrated in high power, CW operation
other…

## Slide 22: Summary
system design has proceeded in a piecemeal fashion  time for iterations
ERL was designed around a 420 pC solution
  short injected bunch, use longitudinal match to stretch and de-chirp before cooling channel
strong cooling requires 8x higher bunch charge (3.2 nc)
  forces injector solution to much longer bunch length
consequently,
  need lower frequency RF for sufficient phase acceptance (476 MHz)
  require different momentum compaction tunings for arcs (isochronous)
  need large momentum acceptance
  (longer bunch  larger projected energy spread  exacerbates chromatic aberrations)

## Slide 23: Path Forward
process of iterating/re-working has begun
have initial designs for all of the major cooler sub-systems
identify appropriate ERL arc
  low mBI gain
  large momentum acceptance
  isochronous
explore options for mitigating CSR-induced insult to beam (ERL and CCR arcs)
  longer bunch length
  CSR shielding
put all the pieces together, begin S2E tracking studies and evaluate performance

## Slide 25: BACKUP

## Slide 26: Cooling Channel
the ion beam and electron beam co-propagate through the channel where thermal energy is transferred from the ions to the electrons and are “cooled”
separate the 60 m active cooling length into 4 × 15 m solenoid sections
B < 0
magnetization flip
B > 0
B > 0
B < 0
magnetization flip
I-transform
Parameter | Value
Energy | 55 MeV
Charge | 3.2 nC
CCR Pulse Freq. | 476.3 MHz
Bunch Shape | Beer can
Bunch Length | 2 cm (full)
Thermal emittance | <19 mm-mrad
Parameter | Value
Norm. Tran. Drift Emittance | 36 mm-mrad
RMS Energy Spread (uncorr.) | 3x10-4
Energy Spread (p-p corr.) | <6x10-4
Solenoid Field | 1 T
Electron Beta in Cooler | 0.37 m
Solenoid Length | 4x15 m

## Slide 27: Magnetization Flip Transformation
preserving ion polarization requires running solenoids with opposite signs
however, electron beam has a specific sign of angular momentum which must be matched to the sign of the solenoid
need to flip the magnetization between solenoids and ensure appropriate transverse match
entrance
exit

## Slide 28: Magnetization
quantify the magnetization (or lack thereof) as a function of turn number

## Slide 29: Charge Scan
0.4 nC
0.8 nC
1.6 nC
3.2 nC

## Slide 30: Beam Exchange v1.0
reference orbit defined by injected/extracted beams
  septum bending field lies on axis of exchange region (septum wall above axis)
  all bunches are deflected upward - with DC kicker - to clear elevated septum wall
  exchanged bunches kicked downward via RF kicker back onto axis
sequence for recirculated beam
  DC kick up + extraction kicker at (near) zero kick
  bunches follow orbit offset through exchange, clear septum, return to CCR axis at node downstream
  DC kick up + injection kicker at (near) zero kick at node and re-steers bunch train to CCR reference orbit
    IK cancels any remnant (x’-t) correlation from EK
DC & EK
IK & DC
ERL
injected bunch orbit
extracted bunch orbit
dipole
dipole
CCR

## Slide 31: Beam Exchange v1.0
sequence for injected beam
  DC kick up + “pre-kicker” down
    pre-compensates any (x’t) correlation induced by IK
  on-axis through vertical achromatic translation up to plane of CCR → cross septum to bend onto CCR axis
  on-axis transport to IK (down) and DC kick (up), merging with circulating beam
sequence for extracted beam
  DC kick up + extraction kick down → on-axis transport to septum
  bend down and vertical achromatic transport to plane of ERL, bending onto plane of ERL
  “post-kicker” down + DC kick up
    post-kicker cancels any bunch distortion (x’t correlation) due to EK
Beam Exchange (side)
CCR
ERL
DC & EK
injected bunch orbit
extracted bunch orbit
dipole
dipole
IK & DC
DC & pre
post & DC

## Slide 32: Twiss Parameterization
CCR back leg
ERL to CCR

## Slide 33: Probing the Parameter Space
DIMAD
  lattice design
elegant
  CSR
GPT
  space charge
  CSR
Bmad
  CSR
  CSR shielding
Vlasov-Solver
  microbunching
TStep
  space charge
  CSR

## Slide 34: Why Magnetized Electron Cooler?
Tremendous reduction (by a factor 20 – 30) of the regional and global deleterious Space Charge transverse impact to dynamics in CCR (tune shift)
Strong mitigation (suppression) of the CSR microbunching/ energy spread growth
Suppression of deleterious impacts of high electron transverse velocity spread and short-wave misalignments to cooling rates (thanks to ion collisions with “frozen” electrons at large impact parameters)
At cathode immersed in solenoid, a gun generates almost parallel (laminar) beam state of a large size (electron Larmor orbits are very small compared to beam size)
This beam state is then transplanted to the solenoid in cooling section
(while preserving the canonical emittances: the drift and the Larmor
emittances)
The solenoid field can be controlled to make e-beam size properly match the ion beam size
Magnetization results in the following critical advantages
(compared to a non-magnetized gun/cooling solenoid):
Notes: At cathode immersed in solenoid, one can generate almost parallel (laminar) beam state after the gun

## Slide 35: CCR Backleg
qccrm1
qccrm4
qccrm5
qccrm6
qccrm8
qccrm7
qccrm3
qccrm2
qccrm1
qccrm4
qccrm5
qccrm6
qccrm8
qccrm7
qccrm3
qccrm2
qccr1
qccr1
qccr1
qccr2
qccr2
qccr1
DC kicker
RF kicker
CSR correction
collimation
85.0 m
septum
requires idealized systems and mitigation schemes to transport bunch 11-turns
  CSR correction cavity modeled as a matrix to fix longitudinal phase space (R65 = 0.025 m, T655 = 2.5 m) plus an energy shift (33 keV)
  “collimator” used to filter high energy tails (deltaLimit = 3×10-3)

## Slide 36: Multi-Turn Tracking with Kickers
DC kickers only
11 revolutions in CCR
1 2 3 4 5 6 7 8 9 10 11
1 2 3 4 5 6 7 8 9 10 11
1 2 3 4 5 6 7 8 9 10 11
harmonic kickers only
DC + harmonic kickers
1st bunch is extracted

## Slide 37: Beam Exchange v2.0
(courtesy D. Douglas)