## Slide 1: eRHIC Accelerator Design Overview
Christoph Montag, BNL
October 29, 2018

## Slide 2: RHIC
Two superconducting storage rings
3.8km circumference
Energy up to 255GeV protons, or 100GeV/n gold
110 bunches/beam
60% proton polarization – world’s only polarized proton collider
6 interaction regions, 2 detectors
In operation since 2001
Exceeded original design luminosity by factor 50 – unprecedented performance

## Slide 3: Requirements
eRHIC is designed to meet the following requirements:
High luminosity: L = (1033-1034) cm-2sec-1
Large range of center-of-mass energies Ecm= (29-140) GeV
Polarized beams with flexible spin patterns
Favorable condition for detector acceptance such as pT =200 MeV
Large range of hadron species: protons ….Uranium
Collisions of electrons with polarized protons and light ions (h3He, hd,…)

eRHIC meets or exceeds the requirements formulated in the
White Paper on EIC

## Slide 4: Facility layout
Electron complex to be installed in existing RHIC tunnel – cost effective

## Slide 5: Beam parameters at highest luminosity ()
Many bunches (up to 1320)
High beam currents (1A p, 2.5A e)
Flat beams
Short hadron bunches (5cm with cooling, 7cm without)
Crossing angle collisions with crab crossing
High luminosity: 10.1*with cooling, 4.4*without

## Slide 6: Luminosity versus Center-of-Mass Energy
Strong hadron cooling improves luminosity by factor 2.3 at and beyond, and by factor 6-7 at lower energies

## Slide 7: Beam-Beam Physics (Y. Luo, Y. Hao)
Operate electron ring just above integer resonance to benefit from dynamic focusing and to stay away from half-integer spin resonance
Concerns:
Slow hadron emittance growth,
examined using long term weak-strong
simulations
No evidence in head-on collisions
Crab crossing studies still in progress
Coherent beam-beam instability,
examined by strong-strong simulations
using several codes
Threshold found
at twice the design intensities

## Slide 8: Hadron Ring Dynamic Aperture
Requirement: DA> 5 s (RHIC experience)
Long terms tracking in eRHIC hadron ring
with beam-beam effect
with multipole errors
Beam-beam has a strong impact on DA
Systematic multipole errors in the IR should not
exceed 2 units of 10-4 @ 25mm
High demand on IR magnet design
No attempts to improve DA by nonlinear corrections yet
No study of random errors yet
Dynamic aperture comparable to present RHIC

## Slide 9: Electron Ring Dynamic Aperture
Requirement: DA > 10 s in all three planes (lifetime)
Main issue: 2nd order chromaticity (local IR xx,y = -30)
Sextupole scheme: A-B-E-A-B-A-B-C-A-B-C-A-B-E-A-B
Off-momentum DA still limited at 0.8% (12s) by
2nd order vertical chromaticity
On-momentum DA ~ 20 s, limited by tune shift with
amplitude
No results with beam-beam and imperfections yet
No optimization of non-chromatic sextupoles yet

## Slide 10: Dynamic Aperture with 2 IRs
On-momentum dynamic aperture with 2 IR and 2 family sextupole correction exceeds 20 s in tracking studies
Off-momentum: Arrange phase advances between IRs such that IR-induced β-beats compensate each other
 need only 2 sextupole families (one per plane)
HERA-II experience with this concept:
- Without IR-IR compensation, no DA at desired working point
With IR-IR compensation  sufficient on-and off-momentum DA
Need to confirm with systematic tracking

## Slide 11: Collective Effects (M. Blaskiewicz)
Electrons:
Single bunch instabilities checked with standard code and appear to be stable.
Transverse coupled bunch modes appear to be stable.
Might need a longitudinal damper for coupled bunch instabilities.
We consider the possibility of removing the 3rd harmonic RF system ($$)
Fast ion instability is expected to be present but manageable at SuperKEKB vacuum levels.
Feedback noise might affect hadrons  still needs to be studied and noise specs
need to be defined
Hadrons:
Electron cloud is most worrisome Cu and amorphous carbon coating of stainless steel vacuum chamber needed (prepared and planned)
IBS: 2 hour emittance growth time horiz. and long.  need strong hadron cooling
Coherent instabilities appear to be absent at top energy
Might need a narrowband damper to control coupled bunch instabilities at injection.

## Slide 12: Electron Storage Ring Polarization (E. Gianfelice-Wendt, V. Ptitsyn)
Physics program requires bunches with spins parallel ↑ ↑ and antiparallel ↑↓ to main dipole field simultaneously.
Sokolov-Ternov would slowly flip all bunches into antiparallel orientation
Need to replace bunches with parallel spin ↑ ↑ with a rate much faster (5 min) than Sokolov-Ternov time constant (>30 min)
Performed spin tracking to determine equilibrium polarization:
Equilibrium polarization P∞ = 50% in eRHIC sufficient
to maintain polarization with <P> = 63% (spin ↑↓ 80%)
Polarization with BB not studied yet
Conclusion:
Polarization ok so far
More improvements expected by longitudinal spin matching, harmonic bumps, BBA, etc.

## Slide 13: IR Layout (B. Palmer)
Design meets all requirements
 Very constrained systems, requires novel types of magnets in the IR
IR design requirements:
  Small b* for high luminosity
  Limited IR chromaticity contributions
  Large final focus quadrupole aperture
  Large detector acceptance
   Large quadrupole aperture, limited beam divergence
  Accommodate spectrometer in the low-b optics
  No accelerator magnets +/-4.5 m
  25 mrad crossing angle (increased from 22 mrad to ease magnet design), crab crossing, crab cavities 90° from IP
  Avoid synchrotron radiation:
  - no electron bends on the forward side
  - absorb SR far from IP
  - need mask against backscattered SR photons
  Accommodate spin rotators, spin matching
  Space for luminosity monitor, neutron detector, “Roman Pots”

## Slide 14
Multi-stage separation:
Electrons from protons
Protons from neutrons
Electrons from Bethe-Heitler photons (luminosity monitor)

## Slide 15
IR Magnets (B. Parker)
1.3 T Cancel Coil Detail
Q1EF

## Slide 16: Electron Storage Ring (V. Ptitsyn)
Composed of six FODO arcs with 60º /cell for 5-10 GeV
90º /cell for 18 GeV
Super-bends for 5-10 GeV for emittance control
5 straight sections with simple layout, plus IR straight
Radiate approx. 10 MW for maximum luminosity parameters at 10GeV
 12 superconducting 2-cell RF cavities
Storage
Ring

## Slide 17: SR Vacuum System
Vacuum chamber from CuCrZr alloy
Good thermal properties
Weldable
Brazable
Easily available
Reasonable price
Thermal SR power load
ok
Maximum temperature 173°C
well below yield strength limit
Pumping based on
integrated NEG Pumps
RF bellows:
Critical element of the vacuum system
Improved NSLS-II bellow with outside
CuCr fingers good candidate
Silver plated sleeve
Contact spring
Copper fingers
RF spring groove

## Slide 18: Rapid Cycling Synchrotron (V. Ranjbar)
eRHIC requires a full energy polarized injector for rapid electron bunch replacement
A rapid cycling synchrotron is the most cost effective solution
High periodicity and proper tune choice ensures polarization preservation on the ramp
Straight sections designed as unit matrices
Simulations show good robustness of spin preservation against machine errors (alignment, field errors, …)

## Slide 19: Rapid-Cycling Synchrotron Polarization
Blue asterisk: 200 ms ramp time
High quasi-symmetry
 Good spin transparency properties

## Slide 20: Polarized Electron Source (E. Wang)
Need to provide 10 nC of polarized electrons/second
SLC Gun with 16 nC 120 Hz operation is the existence proof
eRHIC polarized gun is based on the JLAB inverted gun
Design verified by PIC beam dynamics simulations
400 MeV injector linac will be a SLAC type S-band linac.
Beam transport simulated and found to be ok for eRHIC beams.
Wien filter, polarimeter design already in fairly large detail

## Slide 21: Hadron Storage Ring
YELLOW RHIC ring will serve as eRHIC hadron ring
In-situ beam pipe coating with copper for improved surface conductivity, and amorphous carbon to reduce SEY
BLUE arc from IR6 to IR4 as transfer line extension to new injection area
BLUE inner arc between IRs 12 and 2 for circumference matching during 41 GeV low-energy operation

## Slide 22: Strong Hadron Cooling
Challenges:
2 hour IBS growth times require strong hadron cooling
100 mA CW electron source is beyond state of the art
Hadron chicane to compensate for electron delay in the micro-bunching chicanes is a considerable effort (need several Blue ring s.c. RHIC magnets)
Unexplored:
Short bunches might boost the cooling rate, reduce the electron current and reduce number of amplifications.
To Do:
3-D model
Simulation including space charge and drifts
Optimization of parameters for short bunches

## Slide 23: Summary
eRHIC design reaches a peak luminosity of
L= 1.05·1034cm-2s-1
with 2 hour IBS growth times
However, this can only be achieved with strong hadron cooling, which is beyond state of the art, and is a topic of ongoing R&D.
Without hadron cooling a peak luminosity of
L= 0.44·1034cm-2s-1
is reached, with IBS growth times of 9 hours
eRHIC design has progressed very well and a tremendous amount of design work was accomplished.
There are still critical beam dynamic issues which require more effort. They could have an impact on achievable luminosity but do not constitute a risk of missing the EIC White Paper Requirement
While a large amount of work is still ahead to arrive at a Conceptual Design, we believe that the present state of the eRHIC design matches well the expectations of a Pre-Conceptual Design

## Slide 24
Pre-Conceptual Design Report was delivered to DOE (publication pending)
~800 pages, with many subsystems already beyond pre-conceptual stage
Active R&D program on strong hadron cooling