## Slide 1: eRHIC polarized electron source and pre-Injector
Erdong Wang
Collider accelerator department eRHIC R&D
Brookhaven National Laboratory
EIC Collaboration meeting 2018

## Slide 2: Outline
Polarized electron source and pre-injector requirements
eRHIC polarized DC electron gun concepts
Pre-injector concepts
Spin considerations
Laser, RF and Diagnostics
R&D activates
Summary
Outline

## Slide 3: eRHIC pre-injector specifications
Low repetition rate, high charge
1Hz for 5nC and 10 nC
Short bunch length
3-6 ps for 2.856 GHz Linac
High peak current >2 kA
Good emittance
20 mm-mrad for high luminosity

## Slide 4: eRHIC pre-injector parameters
 | Nominal: High luminosity with cooling | Moderate luminosity without cooling
Bunch charge [nC] | 5 | 10
RMS Bunch length [ps] | 6 | 6
RMS Emittance [mm-mrad] | 20 | 55
Frequency [Hz] | 1 | 
Energy [MeV] | 400 | 
Polarization [%] | 80%-85% | 

## Slide 5: Overview of polarized electron DC guns
Laboratory | Photocathode | Polarization | Voltage | Bunch charge | I_pk | Repetition Frequency | I_avg
JLab[1] | GaAs-GaAsP | 85% | 100, 200kV | 2 or 2.7pC | 67~53mA | 1.5 GHz | 1~4mA
SLC[2] | GaAs-GaAsP | 86% | 120kV | 16nC max | 5 A | 120 Hz | 2uA
MAMI[3] | AlGaAs/InAlGaAs | 85% | 100kV | 0.02pC |  | 2.45 GHz | 50 uA
Bonn-ELSA[4] | AlGaAs/InGaAs | 80% | 50kV | 100nC | 100mA | 50 Hz | 5 uA
MIT-BATES[5] | GaAsP | 50-80% | 60kV | 250nC | 12mA | 600 Hz | 20 or 200uA
Nagoya[6] | GaAs-GaAsP | 92% | 200kV | 3.2 nC | 3.2 A | 20 Hz | 50 uA
NIKHEF[7] | InGaAsP | 80% | 100kV | 2 nC | 2 mA | 10 Hz | 0.04uA
BNL | GaAs-GaAsP | 85% | 350kV | 10 nC | 5 A | 1 Hz | 10 nA
In operation
Shut down
In design
16 nC was achieved by SLC DC gun. It is beyond our nominal injector design.
Can we make it better?
Minimize beam loss
Simplify maintenance

## Slide 6: Superlattice GaAs photocathode
Recent results from SVT/JLab using DBR super lattice GaAsP photocathode.
QE is greater than 5%.
Achieved 86% polarization at the peak.

## Slide 7: Existing Gun concepts for eRHIC injector
First load-locked gun used at an accelerator
High bunch charge, low avg. current, very long operating lifetime 。
4 days to replace photocathode. No separate load lock...
Inverted shape has less out gassing surface and eliminated field emission to ceramic
High average current, long operating lifetime.
Separate load-lock for cathode replacement.
10 -12 torr scale vacuum
SLC PES 120 kV gun
JLab 350 kV inverted gun

## Slide 8: Comparison of guns
 | SLC | Inverted gun (JLab) | Inverted gun in fabrication (BNL)
Voltage [kV] | 120 | 350 | 350
Gradient [MV/m] | 1.8 | 3.4 | 4.2
Cathode size [cm2] | 3 | 1.13 | 4.98
Bunch charge [nC] | 16 | 0.003 | 10
Average current [uA] | 5 | 4000 | To be measured
Charge lifetime[C] | <1 | 80 | To be measured
In-situ Cs evap. | Y | N | N
Biasable Anode | N | Y | Y

## Slide 9: R&D Gun and cathode preparation
Cathode preparation system
HV DC Gun
Gun electrode
The final gun will be similar to the R&D gun, except
Optimized gun chamber
Pumps locations and sizes
Optimized Pierce shape (similar to SLC gun)
Larger cathode

## Slide 10: 400 MeV pre-injector
SLC linac
12 nC
200 MeV
NSLS II linac
500 pC
200 MeV

## Slide 11: Pre-injector Linac frequency choice
Frequency | RF | Aperture | Solenoid | Beam quality | In operation | Cost
563 MHz | SRF | Large | Compensated | Good | NA | High
1.3 GHz | NRF | Moderate | Compensated | Moderate | ANL … ✔ | Moderate
2.856 GHz | NRF | Small | Continuous | Acceptable | SLAC, BNL… ✔ | Low ✔
Considering the technical maturity and lower cost,
2.856 GHz Linac is our choice.

## Slide 12: 400 MeV beam line set up
350 kV gun
114MHz buncher
570 MHz buncher
3GHz buncher
2.856 GHz buncher TWP (8 tanks)
Coil solenoids
Mott polarimeter
Corrector
Laser
Both bunch charge 5n C and 10 nC cases have been simulated by Parmela 3.38.
 meets all the requirements.

## Slide 13: 5nC: High luminosity with cooling
RMS bunch length 2 mm
RMS N_ε x,y:17mm-mrad
Beam Energy:400MeV
RMS beam size

## Slide 14: 10 nC :Moderate luminosity
Beam Energy:400 MeV
RMS bunch length 2 mm
N_ε x,y:55mm-mrad
RMS beam size

## Slide 15: Spin considerations in pre-injector
Wien filter
Quads triplets
Quads triplets
Gun
 | Energy Range | Energy acceptance | Realizable
Dipole+solenoid | >100 MeV | Small | SLC
Wien filter | < 400 KeV | Large | Jlab, Mainz(small charge and small energy)

## Slide 16: Wien filter
Parameter | Value
Bunch charge | 10 nC
Energy | 350 KeV
L | 0.5 m
Ex | 0.98 MV/m
By | 0.00407 T
Electrode gap | 5 cm
Three-segment Wien filter has been studied to rotate electron spin by 90°

## Slide 17: Mott polarimeter
Parameter name | value
Beam energy | 300-350 keV
Beam bend degree by spin rotator | 143°
Voltage of spin rotator | 244.5 d/R kV
Scattering degree, | 136°
Detector count rate | 1.69e3 Hz/(nA.um)
Corresponding time for P = 0.1% | 1.36 s
High voltage Mott polarimeter placed at gun diagnostic beamline where beam energy is 300-350 keV.
Can be simplified if using Wien filter to rotate the spin.

## Slide 18: High pulse energy hybrid Laser
100 uJ
Parameter | Value
Pulse energy | 16 uJ
Length | 1-2.5 ns
Rep. Rate | 1 Hz ,up to 27.8 MHz
Wave length | 780 nm
Two lasers will be placed.
One for operation; another one for hot spare.

## Slide 19: Linac cavities
 | 114 MHz | 571 MHz | 2.856 GHz | 2.856 GHz
Rep. Freq | 1Hz |  |  | 
Function | Buncher |  |  | Booster
Shape | Capacitor loaded | Re-entrance | Traveling wave | Traveling wave
Gap voltage | 500 kV | 600 kV/500 kV | 15 MV | 50 MV
Duty factor | 0.02% |  |  | 
Peak power | 52 kW | 35 kW |  | 

## Slide 20: Potential R&D topics
Extremely high vacuum studies
Cathode lifetime modeling and experiments
Large cathode gun experiments
Beam halo induced beam loss, Beam dynamics studies
New high polarization cathode and related simulation
From EIC Collaboration meeting 2017

## Slide 21: Lifetime study on Cs2Te(CsO) coated GaAs
O. Rahman, J. Biswas, M. Gaowei, W. Liu, E. Wang
540 ºC heat treatment
Roughness:1.8-3.9 nm
2e-11 torr
7e-11 torr
x6
Te source in Saes dispenser
Cathode
Anode
GaAs
Trying GaAs/GaAsP and CsI coating now.

## Slide 22: Extend the lifetime by kicking electrons
O. Rahman, E.Wang, J. Skaritka, J. Biswas
Paper in preparation
Lifetime will be at least doubled with off-center anode scheme.
Emittance increases only 20% compare to centered laser/anode.

## Slide 23: MC simulation of heterojunction GaAs cathode
Simulated photoemission spectrum response, matchs to experimental results well.
Considered the heterojuction between GaAs/AlGaAs, and surface barrier.
Once consider the spin dynamics, could simulate other spin electronics.
Thinner and lower dopant density samples provide short electron bunches
W. Liu M. Poelker, C. Sinclair, E. Wang
Paper in preparation

## Slide 24: Summary
The eRHIC polarized electron source needs to generate high charge (10nC) and high polarization of the electron beam. Both SLC PES gun and JLab inverted guns are being considered. 12.5 nC bunch charge has been demonstrated from a DC gun using SL-GaAs photocathode.
400 MeV pre-injector has been simulated. Meets the requirements.
All electron spin requirements have been integrated into pre-injector design.
The gun R&D activates are in progress.
eRHIC source design has no risks:
Dr. Charles Sinclair: “If the ring-ring eRHIC parameters are really 10 nC and 1 Hz, then I think you will have no problem at all. Several laboratories have demonstrated performances well above this level”.

## Slide 25
Thank you for your attention !

## Slide 26: Back up

## Slide 27: Retarding field Mott polarimeter
Measure the photocathode emission electrons polarization.
Place at preparation chamber.
Commercially available.
Parameter name | value
Beam energy | 20 keV
Beam bend degree | 90°
Scattering degree, | 120°
Detector count rate | 3.8e5 Hz/(nA.um)
laser
beam
Electric lens
Cathode

## Slide 28: Electron transportation-scattering angle
For isotropic scattering processes:
For anisotropic scattering processes:
C. Jacoboni and L. Reggiani, Rev. Mod. Phys. 55, 645 (1983)
D. Vasileska and S.M. Goodnick, https://nanohub.org/resources/9109

## Slide 29: Electron transportation-energy flow
Electrons obtain energy from photon
Electrons exchange energy with holes and crystal lattice
Electron reach a steady-state distribution after a series of scattering
Notes: the width of the arrows indicates the relative size of each energy-flow channel

## Slide 30: Polarized gun R&D
The polarized gun R&D goal:
High average current (6~50 mA), high bunch charge (5.3 nC) large cathode inverted gun for L-R eRHIC source.
High bunch charge (50 nC) for R-R eRHIC source.
Sub-R&D items:
Achieve and measure XHV
High power laser
Ion back bombardment
Surface charge limit measurement
Lifetime as the function of charge
Beam halo reduction studies
Cathode cooling
BNL 1ST inverted gun in fabrication

## Slide 31: Vacuum
Cathode system 10-12 torr
Gun 10-12 torr
Beam line near the gun low 10-11 torr
Linac 10-11 torr
SIP+NEG

## Slide 32: eSource Lab in CAD
Necessary to build a polarized electron source onsite.
Most of the floor space is dedicated for the ATF-II project. Recently it was determined the second experimental hall of the ATF-II project will not be constructed for at least the next 5 years. CAD management has agreed to lend this space to be used as the polarized source laboratory.
The Electron Source R&D facility will be located in the same building as other important facilities that will support it’s efforts.
  Two class 100 particle free clean rooms
  Large In-vacuum bake out oven
  Deionized water source and large high pressure rinsing facilities.
  2K system and Cryogenic refrigerator
  Technical work force
  Large overhead crane

## Slide 33: eSource Lab layout
160 ft
136 ft
Cathode
Clean room
Gun enclosure
Control room
Accum. Ring
Laser room
40 ft