## Slide 1: Jefferson Lab’s EIC Design
Fanglei Lin
on behalf of JLEIC collaboration
EIC Accelerator Collaboration Meeting
October 29 - November 1, 2018
Outline:
  Introduction
  Design Concepts & Performance
  Reference pCDR Design
  Alternative Baseline Design
  Summary

## Slide 2: JLEIC Collaboration
S. Benson, A. Bogacz, P. Brindza, A. Camsonne, P. Degtyarenko, E. Daly, Ya. Derbenev, M. Diefenthaler, K. Deitrick, D. Douglas, R. Ent, R. Fair, Y. Furletova, R. Gamage, D. Gaskell, R. Geng, P. Ghoshal, J. Grames, K. Jorden, J. Guo, F. Hanna, L. Harwood, T. Hiatt, H. Huang, A. Hutton, K. Jordan, A. Kimber, D. Kashy, G. Krafft, R. Lessiter, R. Li, F. Lin, M. Mamum, F. Marhauser, R. McKeown, T. Michalski, V. Morozov, E. Nissen, G. Park, H. Park, M. Poelker, T. Powers, R. Rajput-Ghoshal, R. Rimmer, Y. Roblin, T. Satogata, A. Seryi, M. Spata, R. Suleiman, A. Sy, C. Tennant, H. Wang, S. Wang, G. Wei, C. Weiss, M. Wiseman, R. Yoshida, H. Zhang, S. Zhang, Y. Zhang – JLab
Y. Cai, J. Fox, Y. Nosochkov, G. Stupakov, M. Sullivan, C. Tsai, M. Wang - SLAC
M. Blaskiewicz, H. Huang, Y. Luo, Q. Wu, F. Willeke – BNL J. Qiang, G. Sabbi - LBNL
Z. Conway, B. Mustapha, U. Wienands, A. Zholents – ANL D. Barber – DESY
Y. Hao, P. Ostroumov, A. Plastun , R. York - Michigan State University
S. Abeyratne, B. Erdelyi - Northern Illinois Univ., Z. Zhao - Duke Univ.
J. Delayen, C. Hyde, S. De Silva, S. Sosa, B. Terzic - Old Dominion Univ.
J. Gerity, T. Mann, P. McIntyre, N. Pogue, A. Sattarov - Texas A&M Univ.
P. Nadel-Turonski, - Stony Brook Univ., V. Dudnikov, R. Johnson - Muons, Inc.,
D. Abell, D. Bruhwiler, I. Pogorelov - Radiasoft, G. Bell, J. Cary - Tech-X Corp.,
A. Kondratenko, M. Kondratenko - Sci. & Tech. Laboratory Zaryad, Russia
Yu. Filatov - Moscow Institute of Physics and Technology, Russia
Y. Huang, X. Ma, L. Mao, Y. Yuan, H. Zhao, H.W. Zhao – IMP, China
F. Pilat – ORNL

## Slide 3: Highlights on JLEIC Design Study
The design concepts (luminosity and polarization) have been stable over the last ~9 years
 It indicates they are mature and believed best for an EIC at Jefferson Lab
Implementation and choice of parameters have been continuously improved for better performance and reduction of technical risks
Latest major design optimization includes
  Replacing super-ferric magnets by conventional cos-theta type SC magnets
  ( risk reduction & CM energy increase)
  Considered/studied/evaluated new magnets for the electron ring
  ( performance enhancement)
Significant progress in many other areas of design study:
  Booster redesign; electron vertical chicane for IR;
  Polarized beam design/simulations; beam-beam simulations; analyses of collective effects;
  Bunched beam cooling experiment; developed a magnetized photo gun; high current, high power ERL/circulator ring (found a technical solution for transporting 1.6 nC (half the design value) bunch in the ERL/circulator ring)
Explored an alternative baseline design for JLEIC to reach a 100 GeV CM energy
Yves Roblin’s talk
Rui Li’s talk

## Slide 4: Key Design Concepts
High luminosity: high collision rate of short
modest-charge low-emittance bunches
  Small beam size
    Small β*  Short bunch length  Low bunch charge, high repetition rate
    Small emittance  Cooling
  Similar to lepton colliders such as KEK-B
  with L > 21034 cm-2s-1
High polarization: figure-8 ring design
  Net spin precession zero
  Spin easily controlled by small magnetic fields for any particle species
Full acceptance primary detector including far-forward acceptance
Beam Design
High repetition rate
Low bunch charge
Short bunch length
Small emittance
IR Design
Small β*
Large beam-beam
Crab crossing
Damping Design
Synch. radiation
Beam cooling

## Slide 5: JLEIC pre-CDR
Objectives:
  Document JLEIC self-consistent design (√s = 65 GeV)
  Update, integrate, expand previous documents
  Document enough detail for reasonable cost estimates
  Establish infrastructure to maintain consistency
  Establish documentation trail and reference tech note series
  Balance deliverable scope with resources
399 page document delivered to lab leadership on Oct. 1, reviewed by external visitors Oct. 1-5
  12 chapters  reference pCDR design
  Appendix A: Higher Center-of-Mass Energy Alternative
    with CM energy up to 100 and 140 GeV
Reference pCDR design has many strengths:
  high polarization
  high luminosity
  high figure of merit
  well-integrated hadron facility and IR for physics goals
Develop energy reach and optimize √s=100 GeV

## Slide 6: Achieved Goals in Reference pCDR Design
Energy
  Coverage of CM energy from 15 to 65 GeV
  Electrons 3-12 GeV, protons 20-100 GeV, ions 12-40 GeV/u
Ion species
  Polarized light ions: p, d, 3He, and possibly Li
  Un-polarized light to heavy ions up to A above 200 (Au, Pb)
Support 2 detectors
  Full acceptance capability is critical for the primary detector
Luminosity
  1033 to 1034 cm-2s-1 per IP in a broad CM energy range
Polarization
  At IP: longitudinal for both beams, transverse for ions only
  All polarizations >70%
Capability for upgrade to higher CM energy ~ 140 GeV
  Consistent with the EIC White Paper requirements
EIC Science White Paper
JLEIC pCDR

## Slide 7: JLEIC e-p Parameters and Luminosity Performance
CM energy | GeV | 21.9 (low) |  | 44.7 (medium) |  | 63.3 (high) | 
 |  | p | e | p | e | p | e
Beam energy | GeV | 40 | 3 | 100 | 5 | 100 | 10
Collision frequency | MHz | 476 |  | 476 |  | 476 | 
Particles per bunch | 1010 | 0.98 | 3.7 | 0.98 | 3.7 | 0.98 | 0.93
Beam current | A | 0.75 | 2.8 | 0.75 | 2.8 | 0.75 | 0.71
Polarization | % | 80 | 80 | 80 | 80 | 80 | 75
Bunch length, RMS | cm | 1 | 1 | 1 | 1 | 1 | 1
Norm. emitt., horiz./vert. | μm | 0.3 | 24 | 0.5/ 0.1 | 54/ 10.8 | 0.9/ 0.18 | 432/ 86.4
Horiz, & verti. β* | cm | 8/8 | 13.5/ 13.5 | 6/1.2 | 5.1/1 | 10.5/2.1 | 4/0.8
Vert. beam-beam param. |  | 0.015 | 0.09 | 0.015 | 0.068 | 0.002 | 0.009
Laslett tune-shift |  | 0.06 |  | 0.055 |  | 0.03 | 
Detector space, up/down | m | 3.6/7 | 2.96/2.2 | 3.6/7 | 2.96/2.2 | 3.6/7 | 2.96/2.2
Hourglass(HG) reduction |  | 1 |  | 0.87 |  | 0.86 | 
Lumi./IP, w/HG, 1033 | cm-2s-1 | 2.5 |  | 21.4 |  | 1.7 | 
Similar high performance for electron-ion (e-A) collisions
Space charge limit
Beam-beam limit
Syn. Rad. limit
Reference pCDR design

## Slide 8: JLEIC Layout
Electron complex
  CEBAF as a full energy injector
  Electron collider ring
Ion complex
  Ion source
  SRF linac
  Booster
  Ion collider ring

## Slide 9: 12 GeV CEBAF as a Full Energy Injector
Extensive fixed-target science program
  Fixed-target program compatible with concurrent JLEIC operations
JLEIC injector
  Fast fill of collider ring
  Full energy
  ~90% polarization
  Enables top-off
New operation mode but no hardware modifications
Up to 12 GeV
to JLEIC
Electron injection scheme --- Jiquan Guo’s talk

## Slide 10: Electron Collider Ring Layout
Possible cost reduction by reusing PEP-II RF cavities, power sources and vacuum pipe
e-
R=155m
Spin rotator
Spin rotator
Arc, 257.4
77.4
Forward e- detection and polarimetry
IP
Tune trombone & Straight FODOs
Future 2nd IP
Spin rotator
Spin rotator
RF inserted
Electron collider ring --- Vasiliy Morozov’s talk

## Slide 11: Electron Beam Dynamics
Linear optics
w/o errors
Global chromaticity compensation
Side-view layout
Dynamic aperture (w/ PEP-II systematic and random field errors)

## Slide 12: Electron Beam
Electron beam
  3 A at up to 6 GeV
  Normalized horizontal emittance 44 µm @ 5 GeV
  Synchrotron power density < 10 kW/m
  Total power up to 10 MW
Beam energy | GeV | 3 | 5 | 6.9 | 9 | 10 | 12
Beam current | A | 3 | 3 | 2.6 | 1 | 0.67 | 0.17
Total SR power | MW | 0.4 | 2.9 | 8.8 | 9.8 | 10.0 | 5.3
Energy loss per turn | MeV | 0.12 | 0.93 | 3.4 | 9.8 | 14.9 | 30.8
Energy spread | 10-4 | 2.8 | 4.6 | 6.4 | 8.3 | 9.3 | 11.1
Transverse damping time | ms | 375 | 81 | 31 | 14 | 10 | 6
Longitudinal damping time | ms | 187 | 40 | 15 | 7 | 5 | 3
Normalized hor. emittance | um | 9.6 | 44 | 116 | 258 | 354 | 612
Normalized ver. emittance | um | 1.1 | 5.0 | 13.1 | 28.9 | 39.7 | 68.6
Nominal
SR limit
Chart: Beam energy (GeV)
| 3 | 3.08 | 3.27 | 3.27 | 3.7 | 4 | 4.5999999999999996 | 5.37 | 5.37 | 6 | 6.8819999999999997 | 7.4 | 7.4 | 8.4700000000000006 | 9.4499999999999993 | 9.4499999999999993 | 10 | 11 | 11.5
I ring (A) | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 2.2443 | 2.2443 | 1.3076 | 0.84389 | 0.84389 | 0.673 | 0.45967 | 0.38479
Iext pulsed with ffwd(mA) | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Tinj with ffwd (min) | 18.75 | 17.3266 | 14.4784 | 14.4784 | 9.9945 | 7.9102 | 5.2011 | 3.2692 | 3.2692 | 2.3438 | 1.5532 | 0.93462 | 0.93462 | 0.36323 | 0.23441 | 0.23441 | 0.18694 | 0.12769 | 0.10689

## Slide 13: Electron Polarization
Two highly polarized bunch trains maintained by top-off
Universal spin rotator
  Sequence of solenoid and dipole sections
  Makes the spin longitudinal in the straights
  Basic spin match
  Lifetimes are the same for both states
Advantage of figure-8 geometry: minimum depolarization demonstrated by spin tracking
Optimum Spin Tune 0.01 with a 1 T.m solenoid
Spin tune
Time (hours)
Average injected current (nA)
Pequ/P0 (%)
Energy (GeV) | 3 | 5 | 7 | 9 | 12
Lifetime (hours) | 116 | 9 | 1.7 | 0.5 | 0.1
Electron polarization --- Fanglei Lin’s talk
Electron polarimetry in EIC --- David Gaskell’s talk

## Slide 14: Ion Injector Complex Overview
Ion injector complex relies on demonstrated technologies for sources and injectors
  Atomic Beam Polarized Ion Source (ABPIS) for polarized or unpolarized light ions, Electron Beam Ion Source (EBIS) and/or Electron Cyclotron Resonance (ECR) ion source for unpolarized heavy ions
  SRF linac is based on ANL design
  8 GeV Booster with no transition energy crossing
  Injection/extraction lines to/from Booster are designed
Booster (280 MeV- 8 GeV)
Ion linac (280 MeV H-)
Ion sources

## Slide 15: Ion Injector Linac Design
Two RFQs: One for light ions (A/q  2) and one for heavy ions (A/q  7)
  Different emittances and voltage requirements for polarized light ions and heavy ions
Separate LEBTs and MEBTs for light and heavy ions
RT Structure: IH-DTL with FODO Focusing Lattice
Stripper section for heavy-ions followed by an SRF section
Pulsed Linac: up to 10 Hz repetition rate and ~ 0.5 ms pulse length
JLEIC SRF --- Robert Rimmer’s talk
(Pb67+) 100 MeV/u
(H-). 280 MeV
Normal conducting
Superconducting
200 MHz
100 MHz

## Slide 16: Booster
8 GeV/c Booster serves for
  Accumulation of ions injected
  from Linac Cooling
  Acceleration of ions
  Extraction and transfer of ions to the collider ring
  Electron cooling for heavy ions
Injection
  single pulse charge stripping at 280 MeV (pulse length is 0.5 ms long or 305 turns)
  Phase-space painting
Design
  Circumference of 313 m
  No transition energy crossing,
  Figure-8 shape for preserving ion polarization
Ion booster --- Edy Nissen’s talk

## Slide 17: Ion Collider Ring Layout
Protons: 100 GeV/u (63 GeV/u in COM with 10 GeV e) Lead: 40 GeV/u (40 GeV/u in COM with 10 GeV e)
3 T conventional superconducting magnets
R = 155.5 m
Arc, 257.4
IP
disp. supp./
geom. match #3
disp. supp./
geom. match #1
disp. supp./
geom. match #2
disp. supp./
geom. match #3
det. elem.
disp. supp.
norm.+
SRF
tune
tromb.+
match
beam exp./
match
elec. cool.
ions
77.4
future 2nd IP
Polarimeter
Ion collider ring --- Vasiliy Morozov’s talk
Ion beam bunching splitting --- Randika Gamage’s talk

## Slide 18: Ion Beam Dynamics
Linear optics
Momentum acceptance
Chromaticity compensation
Dynamic aperture
IP
-12 -6 0 6 12
p/p
±50
with errors and correction 10 seeds
collaboration with SLAC

## Slide 19: Ion Polarization
Figure-8 concept: Spin precession in one arc is exactly cancelled in the other
Spin stabilization by small fields: ~3 Tm vs. < 400 Tm for deuterons at 100 GeV
  Criterion: induced spin rotation >> spin rotation due to orbit errors
3D spin rotator: combination of small rotations about different axes provides any polarization orientation at any point in the collider ring
No effect on the orbit
Polarized deuterons
Frequent adiabatic spin flips
Ion polarization --- Fanglei Lin’s talk
Spin transparency study and test --- Vasiliy Morozov’s talk
n = 0
 = 0

## Slide 20: Start-to-End Proton and Deuteron Acceleration in Ion Collider Ring
Three protons with and accelerated at ~3 T/min in lattice with 100 m rms CO excursion, (1.2 Tm solenoid)
Coherent resonance strength component
Three deuterons with and accelerated at ~3 T/min in lattice with 100 m rms closed orbit excursion,
Deuteron spin is highly stable in figure-8 rings, which can be used for high precision experiments
(Zgoubi simulation)
Analytic prediction
Zgoubi simulation
Analytic prediction
Zgoubi simulation

## Slide 21: 3D Spin Rotator in Ion Collider Ring
Provides control of the radial, vertical, and longitudinal spin components
Module for control of the radial component (fixed radial orbit bump)
Module for control of the vertical component (fixed vertical orbit bump)
Module for control of the longitudinal component
ions
3D spin rotator
IP

## Slide 22: Polarization Control in Ion Collider Ring
100 GeV/c figure-8 ion collider ring with transverse quadrupole misalignments
Example of vertical proton polarization at IP. The 1st 3D rotator:  = 10-2 , ny=1. The 2nd 3D rotator is used for compensation of coherent part of the zero-integer spin resonance strength
2nd 3D rotator for compensation
1st 3D rotator for control
with compensation
without compensation

## Slide 23: Crab Crossing
Electron and ion beams have to cross at an angle in an EIC
  Create space for independent electron and ion IR magnets
  Avoid parasitic collisions of shortly-spaces bunches
  Improves detections
  Improves detector background
Without compensation, geometric luminosity loss is about a factor of 12 and there is potential for dynamic instabilities
Crabbing restores effective head-on collisions
Local compensation scheme
  Set of crab cavities upstream and downstream of IP
Deflective crabbing
  Demonstrated at KEK-B
  Tested with ions at LHC
  Prototype developed at ODU
Crab-cavity tests of hadron beams in SPS --- HyeKyoung Park ’s talk

## Slide 24: Crab Crossing Scheme of JLEIC
Local compensation scheme: set of crab cavities upstream and downstream of IP
Locations of horizontal chromatic sextupoles are also adequate for crab cavities:
  Right phase advance
  High values
Found that sextupoles between crab cavities may lead to emittance increase, avoid them
Dispersion at the crab cavities satisfies the beam stability criterion

## Slide 25: Multi-Step Cooling Scheme
Cooling of JLEIC proton/ion beams for
  Achieving small emittance (~10x reduction)
  Reaching short bunch length ~1 cm (with SRF)
  Suppressing IBS induced emittance degradation
Ring | Functions | Kinetic energy (GeV / MeV) |  |  | Cooler type
 |  | Proton | Lead ion | Electron | 
booster ring | Accumulation of positive ions |  | 0.1 (injection) | 0.054 | DC
collider ring | Maintain emitt. during stacking | 7.9 (injection) | 2 (injection) | 4.3 (for proton) 1.1 (for lead) | DC
 | Pre-cooling for emitt. reduction | 7.9 (injection) | 7.9 (ramp to) | 4.3 | DC
 | Maintain emitt. during collision | Up to 100 | Up to 40 | Up to 54.5 | BBC/ERL
Pre-cool when energy is low
Cool when emittance is small
(after pre-cool at low energy)
Booster
0.280 to 8 GeV
Collider ring
8 to 100 GeV

## Slide 26: Cooling Ring Fed by ERL
Same-cell energy recovery in 952.6 MHz SRF cavities
Uses harmonic kicker to inject and extract from CCR (divide by 11)
Assumes high charge, low rep-rate injector (w/ subharmonic acceleration and bunching)
Use magnetization flips to compensate ion spin effects
Development of ERL electron cooler --- Stephen Benson’s talk
Bunched beam electron cooling --- Haipeng Wang’s talk
Magnetized electron source --- Md Abdullah Mamun’s talk
Beam dynamics in CCR --- Christ Tennant’s talk
Harmonic kicker --- Gunn Park’s talk
Straight merger test --- Kirsten Deitrick’s talk
Electron cooling simulation --- He Zhang’s talk
ERL cooler beam test at FAST --- Phillipe Piot’s talk

## Slide 27: Interaction Region Concept
Ion beamline
Electron beamline
Possible to get ~100% acceptance for the whole event
Central Detector/Solenoid
Dipole
Dipole
Forward (Ion) Detector
Scattered Electron
Particles Associated
with Initial Ion
Particles Associated with struck parton
EIC detector requirement --- Rik Yoshida’s talk

## Slide 28: Detector Region
Integrated detector region design developed satisfying requirements of detection, beam dynamics and geometric match
GEANT4 detector model developed, simulations in progress
Forward hadron spectrometer
low-Q2 electron detection
and Compton polarimeter
p
(top view in GEANT4)
e
ZDC
IP
e
ions
forward e detection
Compton polarimetry
dispersion suppressor/
geometric match
spectrometers
forward ion detection
JLEIC IR design update --- Vasiliy Morozov’s talk
IR magnet layout/design – JLEIC --- Tim Michalski’s talk
Validation of EIC IR magnets --- Tim Michalski’s talk
Forward tagging --- Amy Sy’s talk

## Slide 29: Exploration of High Energy JLEIC
Motivation: high CM energy √s=100 GeV expands science reach
Strategy: based on the same design concepts in pCDR (luminosity, polarization, IR)
Straightforward approach:
  Electron collider ring: no change
  Ion collider ring: double arc SC dipole field to 6 T
    Proton: 200 GeV  CM energy: ~100 GeV
  No changes to ERL cooling
Explored HE-JLEIC associated accelerator issues
  ion ring SC magnet 6 T
  high energy electron cooling
  ion polarization
  interaction region and detection acceptance
  ion injection scheme and ion injector
  RF system
  crab crossing
Conclusion :
  Transition to a high energy JLEIC should be straightforward
  No show-stopper, there are technical solutions for all studied issues.
  Same accelerator R&D, some of them are more challenging;

## Slide 30: √s=100 GeV Energy Reach vs Luminosity Optimization
Luminosity curve for JLEIC is complex, it relies on
  electron vs ion energy two-dimensional
  ion beam size, beam-beam, ion cooling, electron SR power limited in various regions
  tradeoffs affect kinematics, acceptance
Optimization efforts
  Ion beam parameters
  High energy cooling vs store lengths
  Fill pattern, bunch length, beam-beam
  Ion ring arc optics, fill factor
With DC and BB cooling +
With DC cooling only ×
Average Luminosity =
Time of running takes into account the beam formation time (25 minutes), detector turning-on time (5 minutes) and effectively operational time (= operational efficiency 0.75).

## Slide 31: Summary
We continued JLEIC design and improved the design performance. Significant progress has been made in many design aspects.
We completed documenting JLEIC self-consistent design with the CM energy up to 65 GeV. This 400-page pCDR has been delivered to lab leadership and reviewed by external visitors.
We explored an alternative baseline design with the CM energy up to 100 GeV. The study shows no show-stopper in all accelerator-associated issues.
Path forward for FY19
  JLEIC with √s = 100 GeV optimization: injector complex, collider ring optimization, filling pattern, bunch parameters, HE electron cooling, etc.
  Continue program development and RD towards CD0

## Slide 32
Thank You for Your Attention !