## Slide 1: Status of RCS eRHIC Injector Design
Vahid Ranjbar
October 29, 2018

## Slide 2: Outline
Requirements
Spin Resonance Review
Concept Overview and Design
  Geometry
  Detector bypass
  Spin resonance strengths
Polarization Performance
  Tolerances for vertical misalignments
  vertical orbit
  Spin imperfection correction scheme
Areas Requiring Additional Effort
Summary

## Slide 3: eRHIC Injector Requirements
A cost effective design to accelerate polarized electrons from 400 MeV  18 GeV
  For injection of 10 nC bunches into storage ring
  Injection rate once per sec. (1Hz)
  Maintain polarization transmission losses < 5%
  Has to fit inside existing RHIC tunnel with bypass for detectors
  Field effects on Storage Ring must be negligible
  Use existing cost effective technologies.
The Rapid Cycling Synchrotron (RCS) design meets these design requirements.

## Slide 4: Spin Resonance Review
Spinor Form

## Slide 5: Spin Resonance Driving terms

## Slide 6: Concept Overview: Spin Resonance Free Lattice
Both the strong intrinsic and imperfection resonances occur at:
  K = nP +/- Qy
  K = nP +/- [Qy] (integer part of tune)
To accelerate from 400 MeV to 18 GeV requires the spin tune ramping from
  0.907 < Gϒ < 41.
If we use a periodicity of P=96 and a tune with an integer value of 50 then our first two intrinsic resonances will occur outside of the range of our spin tunes
  K1 = 50+νy (νy is the fractional part of the tune)
  K2 = 96 – (50+νy ) =46-νy
  Also our imperfection will follow suit with the first major one occurring at K2 = 96 – 50 = 46

## Slide 7: How to make this work in the RHIC tunnel?
It is easy to accomplish this with a perfectly circular ring. Just construct a series of FODO cells with bending magnets so that we have total periodicity of 96.
The problem is that the RHIC tunnel is not circular and has an inherent six fold symmetry.
The solution make the spin resonances integrals over the straight sections equal to zero.

## Slide 8: Project onto the RHIC tunnel
RHIC Tunnel

## Slide 9: Calculating Spin Resonances
No polarization loss from cumulative effective of intrinsic spin resonances for distributions with rms normalized emittance > 1000 mm-rad (100 msec ramp rate).
At 200 mm-mrad rms normalized emittance, we can tolerate beyond 2% field errors and still maintain above 95% polarization transmission.
Issue to control: Imperfection spin resonances ~ vertical rms orbit 0.5 mm to keep losses < 5%.
Extraction
Extraction

## Slide 10: RCS Design Parameters

## Slide 11: Bypass: Detector and other
We have added a bypass option to the straight sections.
Consists of moving last bend magnets in arc to center of straight section
Achieves 3-4 meter bypass at the IP.
Impacts symmetry of lattice.
  However by optimizing the quad strengths in the bypass region we can recover low intrinsic losses

## Slide 12: Polarization Performance
Intrinsic resonance as calculated by DEPOL yield no cumulative depolarization loss for a beam with below 1,000 mm-mrad rms normalized emittance.
Imperfections could however potentially cause greater than 5% losses during ramp.
  Due primarily to quadrupole misalignment and dipole rolls.
  Survey estimates are 0.2 mm rms with a 2 sigma cut off and +/- 1 1 mrad rolls. This yields an estimated rms orbit distortion of between 3-6 mm rms.
  Extracting at 10 GeV RCS can handle > 3 mm RMS orbit with < 5% pol. Loss and 2 mrad uncorrected rolls.
  With appropriate BPM and corrector pairs this can be corrected down to below 0.5 mm rms and push our polarization losses below 5% extracting at 18 GeV.
  Once corrected, dynamical changes of the relative field strength in the quads and dipoles of greater than 0.5% can be tolerated with little effect on polarization transmission.
  Orthogonal imperfection bump scheme to fix any remaining losses beyond SVD orbit smoothing.

## Slide 13: Studies with SVD orbit correction: Quadrupole Misalignments
Polarization Transmission to 18 GeV for random gaussian quadrupole misalignments with SVD orbit correction for 4 different random seeds. * indicates tests with bpm misalignments of 0.2 mm rms

## Slide 14: Studies with SVD orbit correction: Dipole Rolls
Polarization Transmission to 18 GeV for random gaussian dipole rolls with SVD orbit correction for 2 different random seeds. (calculated using spin tracking in Zgoubi)

## Slide 15: Dynamical Orbit Effects Example: NSLS-II Booster
Thanks :Wang, Guimei
400 msec Ramp, 8M Turns to 3 GeV
Randomly collected 50 shots over 1 hr.
Shot to shot variation ~ 70 microns.
Transient dynamics die after 1st 50 msec :
  Equivalent to below 10 GeV in RCS
  In RCS tolerate > 3 mm RMS orbit below 10 GeV
After 50 msec variation on ramp peak swing 0.1 mm over 50 msec.
   0.02 mrad kick at quads. This is well within the existing bandwidth of our corrector system (swing +/- 1 Amp 20Hz) Possible to achieve 200 Hz ~ 5 msec

## Slide 16: Orthogonal Imperfection Bump
Static imperfection bumps at any imperfection resonance location on the ramp.
Bumps are orthogonal to each other and localized in energy space  no required bandwidth beyond what is needed to ramp the dipoles with the energy.
Example Shown on Right: 10 to 15% (0.005 res.) Depolarization Kick Imaginary and Real no kicks anywhere else.

## Slide 17: Summary
Resonances in this lattice are driven by imperfections
Intrinsic resonances are so weak that even large field distortions don’t hurt.
Resilient to misalignments, dipole rolls and orbit distortions:
- Up to 0.4 mm quadrupole misalignments and 2.5 mrad dipole
rolls are tolerable provided the orbit is corrected to 0.5 mm RMS level.
- Assume orbit correction using SVD algorithm with a corrector and a BPM next to each quadrupole.
- within state-of-the art orbit control hard-and software
This will result in > 95% polarization transmission.
To provide additional margin we show that fixed orthogonal imperfection bumps are capable of removing any residual polarization losses.