## Slide 1: JLEIC Collider Rings
Vasiliy Morozov on behalf of JLEIC collaboration
EIC Accelerator Collaboration Meeting
October 29 - November 1, 2018
Supported in part by DoE NP EIC R&D FOA funds

## Slide 2: Outline
Electron collider ring
  Requirements, overview, and main parameters
  Interaction region
  Optimized spin rotator
  Non-linear dynamics
Ion collider ring
  Requirements, overview, and main parameters
  Interaction region
  Electron cooling section
  Chromaticity compensation block housing crab cavities
  Spin rotator
  Non-linear dynamics
  Path towards 200 GeV design

## Slide 3: Electron Collider Ring Design Requirements
Provide the necessary beam parameters
  3-12 GeV electron
  3A beam current up to 6-7 GeV, small emittance, short bunch length ~1cm, focusing at the IP
    Support luminosities above 1034 cm-2s-1
  Sufficient beam and luminosity lifetime
  Less than 10 MW total synchrotron radiation power
Capability of operating multiple detectors
  One full-acceptance detector incorporated
  Incorporate crossing angle and crabbing system
  Space for a second detector reserved
Maintain high polarization >80%
  Longitudinal polarization at the IP
  Sufficient polarization lifetime
Non-linear dynamics correction
  Distributed chromaticity correction scheme
  No extra space required, no emittance growth
Geometry
  Doglegs for vertical stacking with the ion collider ring in the arcs

## Slide 4: Electron Collider Ring Layout
Circumference 2256.6 m, arc 893.0 m, straight 235.3 m
Integrated IR
Spin rotators combined with doglegs for vertical stacking with the ion collider ring
e-
R=155.5 m
Spin rotator + dogleg
Spin rotator
+ dogleg
Arc, 257.4
77.4
Forward e- detection and polarimetry
IP
Space for 2nd IP
Space for
Spin rotator
Space for
Spin rotator
RF
RF

## Slide 5: Electron Beam Parameters
Electron beam
  3 A at up to 7 GeV
  Normalized emittance 58 µm @ 5 GeV
  Synchrotron power density < 10 kW/m
  Total power up to 10 MW
Beam energy | GeV | 3 | 5 | 6.9 | 9 | 10 | 12
Beam current | A | 3 | 3 | 3 | 1 | 0.69 | 0.33
Total SR power | MW | 0.4 | 2.7 | 9.6 | 9.3 | 9.8 | 9.7
Energy loss per turn | MeV | 0.12 | 0.88 | 3.2 | 9.3 | 14.2 | 29.4
Energy spread | 10-4 | 2.8 | 4.6 | 6.4 | 8.4 | 9.3 | 11.1
Transverse damping time | ms | 389 | 84 | 32 | 14 | 11 | 6
Longitudinal damping time | ms | 194 | 42 | 16 | 7 | 5 | 3
Normalized Emittance | um | 13 | 58 | 152 | 337 | 462 | 799

## Slide 6: Complete Optics of Electron Collider Ring

## Slide 7: Parameters of Electron Collider Ring
and scale as and can be adjusted as necessary, e.g. cm m
Electron beam momentum | GeV/c | 5
Beta stars at IP  | cm | 10/2
Maximum horizontal / vertical functions  | m | 487 / 438
Maximum horizontal / vertical dispersion | m | 0.44 / 0.47
Horizontal / vertical betatron tunes  |  | 57(.22) / 50(.16)
Horizontal / vertical chromaticities |  | -124 / -129
Momentum compaction factor |  | 9.97  10-4
Transition energy  |  | 31.67
Electron beam momentum | GeV/c | 5
 | cm | 10/2
 | m | 487 / 438
 | m | 0.44 / 0.47
 |  | 57(.22) / 50(.16)
 |  | -124 / -129
 |  | 9.97  10-4
 |  | 31.67

## Slide 8: Electron IR Optics
IP
electrons
FFB
FFB
Dipole chicane
Compton polarimeter
Low- tagger
Secondary focus

## Slide 9: Electron Spin Rotators with Doglegs
Universal spin rotator
  Minimizes spin diffusion by switching polarization between vertical in arcs and longitudinal in straights
  Sequence of solenoid and dipole sections
  Geometry independent of energy
Sol. 1 + dec. skew quads + matching quads
Vertical dogleg 1
Horizontal DBA 1
Vertical dogleg 2
Sol. 2 + dec. skew quads + matching quads
Horizontal DBA 2
IP
Arc
Vertical dogleg 1
Vertical dogleg 2

## Slide 10: Geometry of Electron Collider Ring
IP
Top view
Side view
77.4
Arc
R=155.5 m
Spin rotator
Spin rotator
1.2 m

## Slide 11: Non-Linear Dynamics in Electron Collider Ring
Distributed chromaticity compensation scheme
Working point (57.22, 50.16)

## Slide 12: Dynamic Aperture of Electron Collider Ring
Bare lattice for different momentum offsets
PEP-II measured systematic and random non-linear field errors in all magnets for 10 random seeds
Solid black: no errors

## Slide 13: Ion Collider Ring Design Requirements
Provide the necessary beam parameters
  20(8)-200 GeV protons, 12-80 GeV/u ions
  Focusing at the IP that supports luminosities above 1034 cm-2s-1
  Incorporate electron cooling
  Sufficient beam and luminosity lifetime
Capability of operating multiple detectors
  One full-acceptance detector incorporated
  Incorporate crossing angle and crab system
  Space for a second detector reserved
Polarization preservation and control using figure-8 geometry
  Light ion (p, d, 3He, and possibly Li) polarization above 70%
  Transverse and longitudinal polarization orientations adjustable at the IP
  Sufficient polarization lifetime
Match the electron collider ring geometry
  Same tunnel
Non-linear dynamics correction
  Local chromaticity correction scheme

## Slide 14: Ion Collider Ring Layout
Same circumference as the electron collider ring of 2256.6 m
6 T cos superconducting magnets supporting proton momentum of 200 GeV/c
R = 155.5 m
Arc, 257.4
IP
disp. supp./
geom. match #3
disp. supp./
geom. match #1
disp. supp./
geom. match #2
disp. supp./
geom. match #3
det. elem.
disp. supp.
norm.+
SRF
tune
tromb.+
match
beam exp./
match
elec. cool.
ions
77.4
space for 2nd IP
Polarimeter
CCB
Crab cavities
CCB
Crab cavities

## Slide 15: Complete Collision Optics of Ion Collider Ring
CCB
CCB
IP
ions
Crab cavities
Crab cavities

## Slide 16: Parameters of Ion Collider Ring
and scale as and can be adjusted as necessary, e.g. cm m
Electron beam momentum | GeV/c | 100
Beta stars at IP  | cm | 10/2
Maximum horizontal / vertical functions  | m | 2500 / 2500
Maximum horizontal | m | 5.4
Horizontal / vertical betatron tunes  |  | 24(.22) / 23(.16)
Horizontal / vertical chromaticities |  | -107 / -127
Momentum compaction factor |  | 
Transition energy  |  | 12.78
Electron beam momentum | GeV/c | 100
 | cm | 10/2
 | m | 2500 / 2500
 | m | 5.4
 |  | 24(.22) / 23(.16)
 |  | -107 / -127
 |  | 12.78

## Slide 17: Ion IR Optics
FFB
FFB
Far-forward detection
Geometric match and dispersion suppression
ions
cm
m
mrad
IP
Secondary
focus
IP
iBDS2
iBDS3
iBDS1
37 cm
m
m
rad

## Slide 18: IR Layout
Electron IR
  No net bend or transverse shift
Ion IR
  50 mrad crossing angle produced by shaping upstream ion arc
  Spectrometer and geometry matching dipoles provide net 50 mrad bend and ajust the separation of the ion and electron beam lines to 1.5 m
IP
e
ions
forward e detection
Compton polarimetry
dispersion suppressor/
geometric match
spectrometers
forward ion detection

## Slide 19: Ion Arc Ends
Provide dispersion suppression and geometric match to the electron ring
Arc end upstream of IP
  Shaped to provide 50 mrad crossing angle at the IP
Arc end downstream of IP
  Shaped to provide 1.5 m separation
ions
IP
20 m
5 m
ions
10 m
2 m

## Slide 20: Electron Cooling Section
Four 15 m 1 T opposite-field cooling solenoids separated by 5 m
Large -functions in the cooling section
Matching section
Matching section

## Slide 21: Chromaticity Compensation Block with Space for Crab Cavities
Vertical sextupoles
Horizontal sextupoles
Crab cavities
10 m reserved for crab cavities
Optics and space can be optimized for crab crossing

## Slide 22: 3D Spin Rotator in Ion Collider Ring
IP
ions
3D spin rotator
Provides control of the radial, vertical, and longitudinal spin components
Module for control of radial component (fixed radial orbit bump)
Module for control of vertical component (fixed vertical orbit bump)
Module for control of longitudinal component
Can be placed anywhere and has no effect on optics

## Slide 23: Non-Linear Dynamics in Ion Collider Ring
Dynamic aperture
Chromaticity compensation
Momentum acceptance
Linear-x sext
FF sext

## Slide 24: Towards 200 GeV Ion Complex
Not simply doubling of ion collider magnetic fields from 3 to 6 T
Consider crab cavity and bunching RF voltages
Consider impact on electron cooling
Doubling of FFQ lengths to preserve detector acceptance and keep their maximum fields at 6 T (to be discuss in more detail during the IR/MDI session)
Modification of ion spin rotators to use transverse fields for polarization control at higher energy

## Slide 25: Conclusions
Optimization of the electron collider ring continued
  Spin rotator has been further optimized and now includes vertical doglegs
  Adopted distributed chromaticity compensation scheme
Further work on the electron collider ring
  Development of crab system
  Spin matching and spin tracking
  Non-linear dynamics design and optimization
  Development of the orbit diagnostics and control systems
Updates in the ion collider ring
  Optimization of electron cooling section
  Further development of the crab crossing system
  IR further optimized for detection requirements
Further work on the ion collider ring
  Update of the IR design for 200 GeV and its further optimization
  Further development of FFQ specifications
  Optimization of the crab crossing system
  Geometric match to the electron collider ring