## Slide 1: JLEIC Ion and Electron Polarization
Fanglei Lin
Collaborators:
Ya.S. Derbenev, V. Morozov, Y. Zhang (JLab), A.M. Kondratenko, M.A. Kondratenko (Zaryad), Yu.N. Filatov (MIPT), D. Barber (DESY)
EIC Accelerator Collaboration Meeting
October 29 - November 1, 2018

## Slide 2: Polarization Requirements
Ion polarization design requirements
  High polarization (> 70%) of protons and light ions (d, 3He++, and possibly 6Li+++)
  Both longitudinal and transverse polarization orientations available at all IPs
  Sufficiently long polarization lifetime
  Spin flipping
Electron polarization design requirements
  High polarization (> 70%)
  Longitudinal polarization orientation at all IPs
  Sufficiently long polarization lifetime
  Opposite polarization states

## Slide 3: Spin Resonances
Spin tune (number of spin precession per turn) in a conventional ring
A spin resonance occurs whenever the spin precession becomes synchronized with the frequency of spin perturbing fields
  Imperfection resonances due to alignment and field errors
  Intrinsic resonances due to betatron oscillations
  Coupling and higher-order resonances
As changes during acceleration, many resonances are crossed causing depolarization
Even at a fixed energy, a finite spread of may overlap higher-order resonances limiting polarization lifetime

## Slide 4: Siberian Snake
Device rotating spin by some angle about an axis in horizontal plane
  A “full” Siberian snake rotates the spin by 180
  Overcomes all imperfection and most intrinsic resonances
Spin tune with a snake
Solenoidal Siberian snake at low energies
  No orbit excursion
  Field integral grows with momentum
Dipole Siberian snake at high energies
  Orbit excursion is inversely proportional to momentum
  Almost energy-independent field integral
  In reality, orbit control requirements lead to an increase of the field integral by a factor of or so, e.g. to as in RHIC
  Medium energies are still a problem
  Full deuteron Siberian snake is not practical for medium to high energies

## Slide 5: Figure-8 Scheme
Figure-8 ring is transparent to the spin motion: in an ideal structure, spin precession in one arc is cancelled by the other
Without additional fields, spin rotation is a priori unknown and occurs only due to closed orbit excursion and beam emittances
Additional fields are introduced to stabilize the spin motion by producing a spin rotation that is much greater than that due to imperfections
Required integrals of the additional fields are almost two orders of magnitude lower than those of full Siberian snakes
  e.g. ~3 Tm vs. < 400 Tm for deuterons at 100 GeV
Figure-8 is an indispensable solution for deuterons in the whole EIC energy range and protons in the low-to-medium energy range as well as an excellent alternative solutions for high-energy protons and electrons
n = 0
 = 0

## Slide 6: Zero-Integer Spin Resonance and Spin Stability Criterion
Total zero-integer spin resonance strength
is composed of
  coherent part due to closed orbit excursions (due to imperfections); it does not lead to depolarization but causes coherent spin rotation about a priori unknown direction
  incoherent part due to transverse and longitudinal emittances (proportional to beam emittance), it causes spin tune spread potentially leading to depolarization
Spin stability criterion
  the spin tune induced by a spin rotator must significantly exceed the strength of the incoherent part of the zero-integer spin resonance
  for proton beam
  for deuteron beam

## Slide 7: Ion Booster
Polarization in Booster stabilized and preserved by a single weak solenoid
  0.6 Tm at 8 GeV/c
  d / p = 0.003 / 0.01
Longitudinal polarization in the straight with the solenoid
Conventional 8 GeV accelerators require B||L of ~30 Tm for protons and ~100 Tm for deuterons
beam from Linac
Booster
to Collider Ring
BIIL

## Slide 8: Spin Dynamics in Booster
Acceleration in figure-8 booster with transverse quadrupole misalignments
0.3 Tm (maximum) spin stabilizing solenoid
Spin tracking simulation using Zgoubi
protons
x0 = y0 = 1 cm
p/p = -0.1%, 0, +0.1%
deuterons
x0 = y0 = 1 cm
p/p = 0

## Slide 9: Start-to-End Proton Acceleration in Ion Collider Ring
Three protons with and accelerated at ~3 T/min in lattice with 100 m rms closed orbit excursion,
Coherent resonance strength component
Zgoubi simulation
Analytic prediction
Zgoubi
simulation

## Slide 10: Start-to-End Deuteron Acceleration in Ion Collider Ring
Three deuterons with and accelerated at ~3 T/min in lattice with 100 m rms closed orbit excursion,
Deuteron spin is highly stable in figure-8 rings, which can be used for high precision experiments
Analytic prediction
(Zgoubi simulation)

## Slide 11: 3D Spin Rotator in Ion Collider Ring
Provides control of the radial, vertical, and longitudinal spin components
Module for control of the radial component (fixed radial orbit bump)
Module for control of the vertical component (fixed vertical orbit bump)
Module for control of the longitudinal component
ions
3D spin rotator
IP

## Slide 12: Polarization Control in Ion Collider Ring
100 GeV/c figure-8 ion collider ring with transverse quadrupole misalignments
Example of vertical proton polarization at IP. The 1st 3D rotator:  = 10-2 , ny=1. The 2nd 3D rotator is used for compensation of coherent part of the zero-integer spin resonance strength
2nd 3D rotator for compensation
1st 3D rotator for control
with compensation
without compensation

## Slide 13: Spin Flipping
Adiabaticity criterion: spin reversal time must be much longer than spin precession period  flip >> 1 ms for protons and 0.1 s for deuterons
Vertical (hy) & longitudinal (hz) spin field components as set by the spin rotator vs time  Spin tune vs time (changes due to piece-wise linear shape)
is the number of particle turns
Vertical & longitudinal components of proton polarization vs time at 100 GeV/c
Zgoubi
simulation

## Slide 14: Radiative Polarization Effects
Sokolov-Ternov polarization change rate
is the invariant spin field, a 1-turn periodic unit 3-vector field over the phase space satisfying the T-BMT equation along particle trajectories, is a unit vector along the particle velocity, and is Planck’s constant.
Depolarization rate due to spin diffusion
is the spin-orbit coupling function
Total polarization change rate
Equilibrium polarization
where is the value of ensemble average of independent of and is the initial polarization

## Slide 15: Electron Polarization Strategies
Highly vertically polarized electron beams are injected from CEBAF
  avoid spin decoherence, simplify spin transport from CEBAF to MEIC, alleviate the detector background
Polarization is designed to be vertical in the JLEIC arc to avoid spin diffusion and longitudinal at collision points using spin rotators
Universal spin rotator (fixed orbit) rotates the electron polarization from 3 to 12GeV
Desired spin flipping is implemented by changing the source polarization
Polarization configuration with figure-8 geometry removes electron spin tune energy dependence, significantly suppress the synchrotron sideband resonance
Continuous injection of highly-polarized electrons from CEBAF is considered to maintain high equilibrium polarization
Spin matching in some key regions is considered to improve polarization lifetime
Compton polarimeter provides non-invasive measurements of the electron polarization
…
…
…
…
Empty buckets
Empty buckets
2.1 ns
476 MHz
Polarization (Up)
Polarization (Down)
bunch train & polarization pattern (in arcs)
IP
Spin Rotator
Magnetic field
Polarization
Polarization configuration
e-

## Slide 16: Universal Spin Rotator
Changes polarization from vertical in the arcs to longitudinal in the straights
Sequence of solenoid and dipole sections
Geometry independent of energy
Dispersion suppressed in solenoids and each solenoid is individually decoupled
Two polarization states with equal lifetimes
IP
Arc
E | Solenoid 1 |  | Dipole set 1 | Solenoid 2 |  | Dipole set 2
 | Spin Rotation | BDL | Spin Rotation | Spin Rotation | BDL | Spin Rotation
GeV | rad | T·m | rad | rad | T·m | Rad
3 | π/2 | 15.7 | π/3 | 0 | 0 | π/6
4.5 | π/4 | 11.8 | π/2 | π/2 | 23.6 | π/4
6 | 0.62 | 12.3 | 2π/3 | 1.91 | 38.2 | π/3
9 | π/6 | 15.7 | π | 2π/3 | 62.8 | π/2
12 | 0.62 | 24.6 | 4π/3 | 1.91 | 76.4 | 2π/3
1st sol. + decoup. skew quads
2nd sol. + decoup. skew quads
Dipole set
Dipole set
Vertical dogleg
Vertical dogleg

## Slide 17: Spin Tracking
Spin tune scan using a spin tuning solenoid in SLICK/SLICKTRACK
Demonstrates suppression of synchrotron sideband spin resonances
Verified by Zgoubi’s Monte-Carlo spin tracking
s=0.01 (optimum spin tune)
s=0.027 (synchrtron tune)
Spin tracking using ZGOUBI.
~ 3x,y
Spin tune scan using SLICKTRACK
Synchrotron sideband spin resonances suppressed compared to a racetrack
Spin tuning solenoid

## Slide 18: Polarization Lifetime and Continuous Injection
Estimated polarization lifetime
Constant polarization is maintained by continuous injection of highly polarized electron beam from CEBAF
Equilibrium polarization
A relatively low average injected beam current of tens-of-nA level can maintain a high equilibrium polarization in the whole energy range
Beam lifetime must be balanced with the beam injection rate and
Energy (GeV) | 3 | 5 | 7 | 9 | 12
Lifetime (hours) | 116 | 9 | 1.7 | 0.5 | 0.1

## Slide 19: Impact of Ion Energy Increase on Ion Polarization
Zero-integer spin resonance (see slide 6 for the detail)
  incoherent part
    due to transverse and longitudinal emittance
  coherent part
    due to closed orbit excursion
Spin stability criterion
  spin tune induced by a spin rotator must significantly exceed the strength of the incoherent part of the zero-integer spin resonance
The coherent part of the zero-integer spin resonance does not depolarize the beam. But it determines the spin direction. In order to manipulate the polarization direction, the spin tune induced by the spin rotators must be sufficient to “compensate” the coherent part the zero-integer spin resonance.

## Slide 20: Incoherent Part of Zero-Integer Spin Resonance Strength
Assuming normalized vertical beam emittance of 0.07 m rad
, at 200 GeV/c are sufficient to stabilize the polarization
Protons
Deuterons

## Slide 21: Coherent Part of Zero Integer Spin Resonance Strength
Protons
Deuterons
Assuming RMS closed orbit distortion of ~200 m
Above ~100 GeV/c, the 3D spin rotator strength may not be sufficient to compensate the coherent part of the resonance strength that determines the polarization orientation
  can consider a 3D spin rotator based on transverse fields
  can consider a pair of compact longitudinal-axis transverse-field Siberian snakes for protons

## Slide 22: Deuteron Spin Rotator Utilizing Longitudinal Fields
Longitudinal Polarization at IP
Radial Polarization at IP
4.4o
4.4o

## Slide 23: Proton Spin Rotator Utilizing Transverse Fields
Longitudinal Polarization at IP
Radial Polarization at IP

## Slide 24: Summary
JLEIC rings adopt a figure-8 shape for better preservation and control of polarization by taking advantage of a spin transparency mode
Ion and electron polarization schemes have been designed. Spin tracking numerically validated a figure-8 based polarization control schemes for the whole JLEIC complex
  Both ion and electron polarizations > 80% can be reached
Spin transparency mode will be studied in RHIC
Ion polarization with an energy increase up to 200 GeV (proton) can still be preserved and controlled. Preliminary designs of new spin rotators for both protons and deuterons are presented and will be further optimized

## Slide 25
Thank you for your attention !

## Slide 26
Back Up

## Slide 27: Spin Response Function
The periodic spin response function is the spin Green’s function; it describes spin response to a local perturbing radial field and resulting closed orbit excursion
is determined by ideal linear lattice. For an uncoupled flat ring, it is expressed through the Floquet function of vertical betatron oscillations :
As orbit, spin is most sensitive to perturbations in large- areas
Beam-beam effect on the spin can be suppressed by minimizing the spin response function at IP
Contribution of a periodic radial perturbing field to the coherent part of the resonance strength
  dipole roll
  vertical quadrupole misalignment

## Slide 28: Statistical Model
The rms strength of the spin resonance due to uncorrelated segments of length with radial fields normalized to where is the average radius for circumference
The rms vertical excursion of the closed orbit
Based on the expected closed orbit excursion, one can estimate the expected coherent component of the zero-integer spin resonance strength

## Slide 29: Ion Polarization Measurement Strategy
Ion Polarimeter located downstream of IP
Orbital bending angle between the IP and polarimeter should be as small as possible to minimize polarization measurement error
Since ion polarimeter measures only transverse polarization component, complete “spin dance” to calibrate the polarization orientation at the polarimeter as a function of 3D spin rotator settings
Measure polarization of bunch trains that have identical polarizations of individual bunches
Calibrate fast polarimeter against absolute polarimeter
IP
e
ions
forward e detection
Compton polarimetry
dispersion suppressor/
geometric match
spectrometers
forward ion detection
80 m
ion polarimeter

## Slide 30: Compton Polarimeter
Dipole chicane immediately downstream of the IP for detection of low-Q2 electrons
Compton polarimeter located in the middle of the chicane
  same polarization at the laser as at the IP due to zero net bend
  non-invasive continuous monitoring of electron polarization
c
Laser + Fabry Perot cavity
e- beam from IP
Low-Q2 tagger for low-energy electrons
Low-Q2 tagger for high-energy electrons
Compton electron
tracking detector
Compton photon
calorimeter
Compton- and low-Q2 electrons are kinematically separated!
Photons from IP
e- beam to spin rotator
Luminosity monitor

## Slide 31: RF feed-forward to correct voltage drooping
25.4µs, 6 turns-0.88µs in CEBAF NL (4.375µs per turn)
17-375ms
0.88µs
Each bunch train 3.5µs
P0=0.97kW
P1=8.1kW
Flat Vc=10.4MV, Ipulse=0.7mA, ΔV/V≈0 within bunch train
17-375ms
Pulsed RF input for a typical NL C100 cavity with feed-forward
(assuming on-resonance, need more power for off resonance)
Pulse-to-pulse feed-back will help to find the correct power level with microphonics etc.
If ~0.2% droop is allowed, the estimated extraction beam current will be ~2mA at various energy, depending on cavity coupling and microphonics.
Chart: Beam energy (GeV)
| 3 | 3.08 | 3.27 | 3.27 | 3.7 | 4 | 4.5999999999999996 | 5.37 | 5.37 | 6 | 6.8819999999999997 | 7.4 | 7.4 | 8.4700000000000006 | 9.4499999999999993 | 9.4499999999999993 | 10 | 11 | 11.5
I ring (A) | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 2.2443 | 2.2443 | 1.3076 | 0.84389 | 0.84389 | 0.673 | 0.45967 | 0.38479
Iext pulsed with ffwd(mA) | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Tinj with ffwd (min) | 18.75 | 17.3266 | 14.4784 | 14.4784 | 9.9945 | 7.9102 | 5.2011 | 3.2692 | 3.2692 | 2.3438 | 1.5532 | 0.93462 | 0.93462 | 0.36323 | 0.23441 | 0.23441 | 0.18694 | 0.12769 | 0.10689
Estimated JLEIC pulsed injection current and injection time (limited by injector current only) with RF feed-forward and varying number of passes
Assumes maximum kicker repetition rate 60 Hz
Assumes head-tail energy droop of 0.2% (1/2 of the ±0.2% arc acceptance)
Chart: Beam energy (GeV)
| 3 | 3.08 | 3.27 | 3.27 | 3.7 | 4 | 4.5999999999999996 | 5.37 | 5.37 | 6 | 6.8819999999999997 | 7.4 | 7.4 | 8.4700000000000006 | 9.4499999999999993 | 9.4499999999999993 | 10 | 11 | 11.5
Iext pulsed with ffwd(mA) | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Iext avg with feed-forward (nA) | 18.6133 | 20.1425 | 24.1048 | 24.1048 | 34.9193 | 44.1205 | 67.1018 | 106.7538 | 106.7538 | 148.9067 | 224.7007 | 279.3544 | 279.3544 | 418.8 | 418.8 | 418.8 | 418.8 | 418.8 | 418.8
From Jiquan Guo’s talk