## Slide 1: IR/MDI requirements for the EIC
M. Sullivan
for the
EIC Accelerator Collaboration Meeting
October 29 – Nov 1, 2018

## Slide 2: Outline
Introduction
Accelerator Issues
Detector Issues
Engineering Issues
Final Focus Magnets
Backgrounds
Other issues
Summary

## Slide 3: Introduction
The interaction region is one of the more challenging parts of any accelerator design
There are many different (and usually conflicting) constraints from both the accelerator and from the detector
I will try to touch on some of these issues

## Slide 4: Physics
As I understand it, the EIC will be used to measure how the proton surface (or near surface) works
Somehow, the strong force fades to zero at the proton radius
We want to study events that scatter with small momentum transfers (low q2 – very forward events)
Polarization is another physics requirement

## Slide 5: Accelerator
The accelerator must deliver the beams to a collision point that maximizes the luminosity
  The collision is inside a detector that has a large solenoidal magnetic field
Also, to maximize the luminosity the final focus magnets must be a close as possible to the IP
The beam currents are generally high (~1 A)
Usually there is a crossing angle in order to get the beams quickly in and out of collision
Polarization of the beams

## Slide 6: Detector
The detector must be efficient in order to collect as much of the delivered luminosity as possible
For the EIC, the very forward acceptance is crucial
  This is where most of the events of interest are located
The detector and the accelerator no longer have a well defined boundary
  Detector components are spread out all along the outgoing beam trajectories
Measuring the polarization usually needs to be near the IP

## Slide 7: Energy Range
The physics requires a range of energies for both beams
This complicates the overall accelerator design and, in particular, the IR design
  The IR must be able to handle a lower-energy high-current as well as a higher-energy low-current electron beam
  These two configurations have different IR issues
    Synchrotron radiation at the electron beam high-energy setting
    Beam current and beam bunch heating at the electron low-energy setting
    Beam current and bunch heating for the proton beam

## Slide 8: Engineering
With the detector and the machine components intertwined the engineering challenges become more interesting
  Detector wants minimal material for supports and maximal acceptance for low angle events
    Minimal outer size for final focus magnets
    Maximal aperture size inside the final focus
  Accelerator stability and force compensation require strong supports for accelerator elements
    Cuts into detector acceptance and sometimes increases the size of the final focus magnets
    Sometimes detectors can be placed in front of obstructions or in front of magnets

## Slide 9: Final Focus Magnets
The large beam energy asymmetry and the different beams (e and P/ion) means the final focus magnets can be separated in Z for each beam
  Allows for magnets to be closer transversely (not overlapping in Z)
The magnets still need to be as small as possible (radially) for maximum detector acceptance
  Ion beam magnets can not affect the electron beam (too much perturbation)
  Vice Versa for perturbations on the ion beam?

## Slide 10: Backgrounds
Quick list of various backgrounds that must be studied
  Synchrotron radiation (SR) from the electron beam
    Upstream and downstream
    Beam tail distributions
  Beam-gas Bremsstrahlung
  Coulomb scattering
  Touschek scattering
  Luminosity related backgrounds
    Radiative electron scattering
    Low-energy ee production
    Neutron production

## Slide 11: Beam Tails
All electron storage rings have a beam tail
  Interactions with gas molecules
  IBS (Touschek, etc.)
  Beam tune shift
  Nearby resonances in the tune plane
  Other…
Usually sets the beam lifetime
The tail can be up to a few percent of the core distribution

## Slide 12: Beam Tails
The collimators in the ring need to be set to a beam sigma that is smaller than the IP apertures
  Else the IP becomes the tight spot in the ring and collects all of the beam backgrounds
So if the BSC in the IR is 15 sigma then the collimators must be ~12 sigma
The collimators will then set the electron beam lifetime
Based on recent super KEKB and Belle II experience beam tail distributions appear to be a significant source of detector background

## Slide 13: Beam Tails
1 day
1 hr = ~15
10 min =~13
X beam tail
Y beam tail
gaussian
gaussian
10 min =~40
1 hr = ~45
x
y
M. Sands 6 pt.
The background distribution is a 2nd lower and wider gaussian
Where a = 8.5×10-3 and
b = 0.3 for x and
0.1 for y
The integral of the background distribution is about 0.3% of the total.
This might be on the low side especially for a new accelerator.
The tails in the plots here are the ones I use for synchrotron radiation background calculations

## Slide 14: Some other Issues
Here I list various other issues that need to be included in the IR design
  Vacuum pumping
  Heating issues from the electron beam
    Including SR
    Less of a problem for the P/ion beam
  Thin windows for the low-angle particles produced in the interaction
  Supports
  Solenoidal field compensation
  Ion beamline magnetic field compensation for the electron beam

## Slide 15: Summary and Conclusion
The accelerator and detector teams will have to work closely together in order to achieve a good design for the IR
The EIC IR is more complicated than ordinary IRs due to the need for maximum acceptance in the forward direction
The machine and detector design are intertwined now making the first point above even more important
This is an exciting new accelerator with many challenges and the physics is compelling!