## Slide 1
Northern Illinois Center for Accelerator
and Detector Development
ERL cooler beam tests at the FAST facility
Fermilab: J. Ruan, P. Piot
Northern Illinois University: A. Fetterman*, C. Marshall*, P. Piot
Collaborators at JLab: S. Benson, J. Gubeli, F. Hannon, K. Jordan, S. Wang
* Graduate students

## Slide 2: Introduction
High-charge magnetized beam:
  Production of high-charge (3.2 nC) magnetized beam
  characterization of magnetization
  Transport + manipulation over long beamline including use of locally non-symmetric optics
High-current magnetized beams → understanding halo
  Explore halo formation in magnetized beam using a long-dynamical range diagnostics (LDRD)
New merger concept:
  Tests of merger concept combining RF deflector and magnetic coil proposed by A. Hutton -- augmenting recent test at Cornell.
YEAR 1
YEAR 2

## Slide 3: The FAST facility infrastructure
superconducting linac
superconducting
accelerating cavities
50-MeV injector
section
RF gun
e- dump
BC1
300-MeV area
FAST facility accelerator vault
IR pulse train before SHG1
UV pulse train (electron beam)
Green pulse train before SHG2
1.2 ms
110 meters
SHG2
SHG1
FAST photocathode laser system
`
Integrable-optics
Test accelerator (IOTA)
LDRD

## Slide 4: Relevance of FAST injector to EIC e- cooling
AS
parameter | JLEIC | FAST | units
energy | 20-55 | <50 | MeV
bunch length | 2 | 0.3* | cm
thermal emittance | <19 | ~1 | µm
cathode spot rad. | 2.2 | ~1* | mm
B-field on cathode | 0.1 | 0.09 | T
rms energy spread | 0.03 | 0.1 | %
Bunch charge | 3.2 | 2* | nC
* Parameter can be varied
Nominal operating point
magnetized-beam
next run
EIC requirement
are data points from Winter-2017 run

## Slide 5: Magnetized beams in the FAST injector
The FAST injector includes
  1+1/2 RF gun
  High quantum efficiency Cs2Te photocathode
  A symmetrical solenoid configuration can provides substantial field on cathode up to 0.15 T
Magnetized beam is characterized by the magnetization parameter
Drift emittance is
L1 L2
(for JLEIC )
B field on cathode
Laser-spot size on cathode

## Slide 6: Magnetized beams generation at FAST
During the winter 2017 run we did some low-charge (pC) magnetized beam
Inferred the magnetization via measurement of the kinetic angular momentum
(A. Halavanau, in preparation)
beam at
slits
beam at observation point

## Slide 7: Alternative measurement via decoupling
A set of three quadrupole magnets can decoupled an incoming magnetized beam
In the process the magnetized beam eigen-emittances are mapped into conventional transverse emittances
R. Brinkmann et al., PRSTAB 4, 053501 (2001)
Y. Derbenev, University of Michigan report UM-HE-98-04 (1998)
(drift emittance)
skew quadrupole
magnets
magnetized
beam
magnetized
beam

## Slide 8: Decoupling into flat beams @ FAST (preliminary)
Low charge experiment (pC) performed in Winter 2017
Demonstrated flat-beam emittance repartition
magnetized
(A. Halavanau, in preparation)
IMPACT-T
experiment

## Slide 9: Formation of high-charge magnetized beams I
Simulation to demonstrate FAST photo-injector can produce JLEIC-like emittances (mm, nC)
(run # 002787)
dominated by
an be elongated via laser pulse stacking or bunch decompression

## Slide 10: Formation of high-charge magnetized beams II
Started with thermal emittance associated to Cs2Te photocathode
Eigen-emittance partition consistent with required value for JLEIC ERL cooler
Magnetization at cathode is
Next step is to understand mapping to real conventional emittance using RFBT
drift emittance: 37.07 mm
4D emittance
cyclotron emittance: 1.04 mm

## Slide 11: Going to higher charge
Experiment on high-charge magnetized beam generation in preparation
Some challenges being addressed:
  Laser-distribution control (transverse + longitudinal if needed)
So far up to 2.8 nC was produced (limited by the laser setting)
2.8 nC

## Slide 12: Halo formation in magnetized beams
Halo could cause beam loss which would ultimately limit the average current of the ERL cooler
Various source of halo (some could be mimicked with laser shaping)
Large-dynamical-range diagnostics developed at Jlab (P. Evtushenko and J. Gubeli):
  Wire scanner with high-dynamical range electronic or PMT (measured projections only)
  YaG:Ce screen with dual-sensor detection system.
wire scanner assembly
YAG screen

## Slide 13: Measurement of halo at fraction
Detection optics
Magnetized beam will be transported for 50-70 m and halo diagnosed
Mapping of eigen-emittance will be done in 45-deg frame (w. normal quad)
CCD #1
CCD #2
L1
L2
L3
L3
e- beam
BS
mask
CCD #1
CCD #2
P. Evtushenko

## Slide 14: Test of a new merger concept (during year 2)
Straight merger concept (see talk by K. Deitrick):
  RF deflecting cavity with superimposed magnetostatic fields.
  Separation of injector and recirculated beam with angular separation sufficient for septum magnet.
Preliminary tests done at Cornell
Follow up tests at FAST:
  beam degradation due to RF field
  Impact on magnetization
  Depending on location; RF cavity will also be used as a longitudinal phase space diagnostics
(from A. Hutton)
RF+B

## Slide 15: Summary
High-charge magnetized beam:
  Simulation of 3.2 nC magnetized beam with parameters consistent with JLEIC mostly done; need to understand limiting effects associated with mapping into conventional emittances (flat-beam transform).
  Simulations of transport of magnetized beams started.
  Beam experiment on magnetized beam formation & characterization in preparation.
High-current magnetized beams
  Possible locations for the LDRD identified, final locations to be selected based on simulations (1.b).
New merger concept
  planned in year 2, identified a 1.3-GHz power supply, location of experiment not yet decided.