## Slide 1: JLEIC IR Design Update
Vasiliy Morozov on behalf of JLEIC collaboration
EIC Accelerator Collaboration Meeting
October 29 - November 1, 2018
Supported in part by DoE NP EIC R&D FOA funds

## Slide 2: Outline
Full-acceptance detector concept
Forward hadron detection
Low- tagger
IR magnets
Background studies
Geometry tagging
IR optimization for 200 GeV/c

## Slide 3: Full Acceptance Detector Concept
Would like to get ~100% acceptance for the whole event
Ion beamline
Electron beamline
Central Detector/Solenoid
Dipole
Dipole
Forward (Ion) Detector
Scattered Electron
Particles Associated
with Initial Ion
Particles Associated with struck parton

## Slide 4: Schematic of Full-Acceptance Detector
50 mrad crossing angle
Forward hadron detection in three stages
  Endcap
  Small dipole covering angles up to ~2-3
  Far forward, up to ~10 mrad, for particles passing through accelerator quads
Low-Q2 tagger
  Small-angle electron detection

## Slide 5: JLEIC Interaction Region Layout
Design of the IR has been stable for a few years with only minor modifications
Recent focus has been on reconciling detection requirements and engineering constraints
GEMC model has been developed and is being used for simulations
Forward hadron spectrometer
low-Q2 electron detection
and Compton polarimeter
p
(top view in GEANT4)
e
ZDC
IP
e
ions
forward e detection
Compton polarimetry
dispersion suppressor/
geometric match
spectrometers
forward ion detection

## Slide 6: Forward Hadron Detection
Electron and ion beams have to cross at an angle in an EIC, JLEIC: 50 mrad
  Create space for independent electron and ion IR magnets
  Avoid parasitic collisions of shortly-spaces bunches
  Improves detections
  Improves detector background
Two forward charged hadron detector regions:
  Region 1: Forward, small dipole covering scattering angles from 0.5 up to ~2-3 (before quads)
  Region 2: Far forward, up to ~10 mrad, for particles passing through (large aperture) accelerator quads. Subsequent dipoles for precision measurements.
Neutrals are detected in a zero-degree calorimeter (ZDC)
Region 1: ~7 m
Region 2: ~45 m

## Slide 7: Ion IR Optics
FFB
FFB
Far-forward detection
Geometric match and dispersion suppression
ions
cm
m
mrad
IP
Secondary
focus
IP
iBDS2
iBDS3
iBDS1
37 cm
m
m
rad
Pole-tip fields are limited to 6 T

## Slide 8: Ion Beam Envelope and 0.99 Trajectory
Assuming beam momentum of 100 GeV/c, ultimate normalized emittances of 0.35/0.07 m, and ultimate momentum spread of
The horizontal size includes both betatron and dispersive components

## Slide 9: Momentum & Angular Resolution
Protons with spread are launched at different angles to nominal trajectory
Resulting deflection is observed at the second focal point
Particles with large deflections can be detected closer to the dipole
Crab tilt at the second focus may reduce momentum acceptance to

## Slide 10: Electron IR Optics
IP
electrons
FFB
FFB
Dipole chicane
Compton polarimeter
Low- tagger
Secondary focus

## Slide 11: Low Tagger in JLEIC
Dipole chicane for high-resolution detection of low-Q2 electrons
Compton polarimetry has been integrated to the interaction region design
  same polarization at laser as at IP due to zero net bend
  non-invasive monitoring of electron polarization

## Slide 12: Development of IR Magnet Specifications (DoE FOA project)
IR magnet engineering design/analysis
  Design of the multipole correction scheme in the IR region, relate LARP experience
  Identify limits in magnet parameters which directly affect the IR performance
  Relate existing magnet data to the EIC performance requirements including scaling to the IR design
  Heat and radiation loads on IR magnets
  Perform magnetic analysis and initial optimization, considering LARP design, BNL EIC IR quadrupole prototype, and others
  Mechanical and magnetic design of an optimized IR quadrupole
  Incorporate optimized IR quadrupole lessons/features and finalize IR layout
See talk by Tim Michalski

## Slide 13: Background Studies (Supported by Generic EIC Detector R&D)
Project leads: Latifa Elouadrhiri and Charles Hyde

## Slide 14: Geometry Tagging for Heavy Ions (Completed JLab LDRD Project)
Simulation of detector performance for saturation and hadronization studies
See talk by Amy Sy

## Slide 15: Streamlining IR Updates
With many parties involved, need to find a way to reliably synchronize the IR models between accelerator, detector and engineering groups.
Accelerator Lattice
MAD-X
Detector Model
GEMC
Engineering Design
CAD
Largely
automated
Largely
automated

## Slide 16: Modifying IR Design for 200 GeV/c
Constraints
  Maximum pole-tip fields at 200 GeV/c of 6 T
  Minimum impact on the forward hadron acceptance compared to the 100 GeV/c design
  Minimum impact on the luminosity performance compared to the 100 GeV/c design
  Minimum impact on the beam dynamics compared to the 100 GeV/c design
Options explored
  Reduced FF Quad Apertures
  Doubled Detector Space and Halved Crossing Angle
  Doubled Quad Lengths
  1.5x Quad Lengths and 2/3 Crossing Angle


## Slide 17: Doubled Quad Lengths
Keep maximum -functions at ~2500 m  same maximum beam size
Quad apertures  6 T / at 200 GeV/c = 85 / 152 / 196 mm (radius)
Quad aperture / distance from IP to quad’s far end = 9.1 / 10.0 / 10.5 mrad
= 18 / 2.15 cm  , at roman pot = 0.97 m

## Slide 18: Performance Optimization at Lower Energies
Cut first FFQ in half and use the halves as the first and second FFQs at lower energies
Can run in this mode up to 65 GeV/c proton momentum
= 7.5 / 2 cm  luminosity improvement by a factor of 1.15 (up to 65 GeV/c)

## Slide 19: Conclusions
The full-acceptance detector concept has been stable for the last few years, there have been only minor lattice modifications
Recent focus has been on
  Engineering design (talk by Tim Michalski)
  Background studies (lead by Latifa Elouadrhiri and Charles Hyde)
  Detector simulations (see e.g. talk by Amy Sy)
We are currently developing a procedure to quickly synchronize the accelerator, detector and engineering IR models
Have a path forward to modify the IR design for 200 GeV with minimum impact on performance and without introducing additional risks