## Slide 1: eRHIC Machine Design Overview
Christoph Montag, BNL
8th Workshop of the APS Topical Group on Hadronic Physics
April 10-12, 2019

## Slide 2: RHIC
Two superconducting storage rings
3.8km circumference
Energy up to 255 GeV protons, or 100 GeV/n gold
110 bunches/beam
60% proton polarization – world’s only polarized proton collider
6 interaction regions, 2 detectors
In operation since 2001

## Slide 3: Requirements for the EIC
Requirements for an Electron-Ion Collider are defined in the White Paper:
High luminosity: L = 1033 to 1034 cm-2sec-1
Large range of center-of-mass energies Ecm= 20 to 140 GeV
Polarized beams with flexible spin patterns
Favorable condition for detector acceptance such as pT =200 MeV
Large range of hadron species: protons ….Uranium
Collisions of electrons with polarized protons and light ions (h3He, hd,…)

eRHIC meets or exceeds the requirements formulated in the
White Paper on EIC

## Slide 4: Design Concept
eRHIC is based on the RHIC complex: Storage ring (Yellow Ring), injectors, ion sources, infrastructure; needs only relatively few modifications and upgrades
Todays RHIC beam parameters are close to what is required for eRHIC (except number of bunches, 3 times higher beam current, and vertical emittance)
A 5 to 18 GeV electron storage ring & its injectors are added to the RHIC complex  Full center-of-mass energy range of Ecm = 29 to 141 GeV from the start
Design aims to meet the goals formulated in the EIC WHITE PAPER, in particular the high luminosity of L = 1034cm-2s-1.
Design is optimized under the assumption that each beam will have the parameters (in particular beam-beam tune shift) as demonstrated in collisions between equal species (HERA Concept).
The requirement to store electron beams with a variable spin pattern requires an on-energy, spin transparent injector.
The total synchrotron radiation power of the electron beam is assumed to be limited to 10 MW. This is a design choice, not a technical limitation.

## Slide 5: Facility layout
Electron complex to be installed in existing RHIC tunnel – cost effective
Large 3.8 km circumference allows for high electron energies of 18 GeV

## Slide 6: Maximum Luminosity Parameters
High beam currents
Many bunches
Large beam-beam tune-shift
Flat beams
Need strong hadron
cooling
Short hadron bunches
22 mrad crossing angle
with crab cavities
 Large Luminosity
No problem
Challenge
Difficult/R&D required
0.10

## Slide 7: Luminosity versus Center-of-Mass Energy

## Slide 8: Strong Hadron Cooling
2 hour IBS emittance growth time requires strong hadron cooling – otherwise store length would be limited to ~2h
Several methods of strong hadron cooling have been studied.
Bunched Beam Electron Cooling with an electron storage ring
Coherent electron cooling with FEL amplifier or micro-bunching amplifier – essentially a stochastic cooling concept using an electron beam as pick-up and kicker
 The most promising approach at this point is micro-bunched electron beam cooling with 2 plasma amplification stages.
Achievable cooling rates with 100 mA electron current and flat beams are in the order of
1 h which would be sufficient for eRHIC.
Analytical calculation of the
cooling rate agrees well with
simulations within the 1-D model.

## Slide 9: Mitigation of Strong Hadron Cooling Risk
Solution with L = 0.44·1034cm-2s-1 and IBS growth rates of 9 h

## Slide 10: Electron Storage Ring
Composed of six FODO arcs with 60º /cell for 5-10 GeV
90º /cell for 18 GeV
Super-bends for 5 to 10 GeV for emittance control
5 straight sections with simple layout, plus IR straight
Radiate approx. 10 MW for maximum luminosity parameters at 10GeV
 14 superconducting 2-cell 591 MHz RF cavities
Storage
Ring

## Slide 11: Beam-Beam Physics
Operate electron ring just above integer resonance to benefit from dynamic focusing and to stay away from half-integer spin resonance
Concerns:
Slow hadron emittance growth,
examined using long term weak-strong
simulations
No evidence in head-on collisions; optimum choice of crab cavity frequency on-going
Coherent beam-beam instability,
examined by strong-strong simulations
using several codes
Threshold found
at twice the design intensities
No strong dependence of beam-beam parameter on radiation damping decrement found

## Slide 12: Dynamic Aperture Assessment
Requirements: Hadrons DA> 5 s (RHIC experience)
Long terms tracking in eRHIC hadron ring
with beam-beam effect
with multipole errors
Beam-beam has a strong impact on DA
Systematic multipole errors in the IR should not
exceed 2 units of 10-4 @ 25mm
High demand of IR magnet design

## Slide 13: Electron Ring Dynamic Aperture
Requirement: > 10 s in all three planes (lifetime)
Main issue: 2nd order chromaticity (local IR xx,y = -30)
Sextupole scheme: A-B-E-A-B-A-B-C-A-B-C-A-B-E-A-B
Off-momentum DA still limited at 0.7% (12s) by
2nd order vertical chromaticity
On-momentum DA ~ 20 s, limited by tune shift with
amplitude
No results with beam-beam and imperfections yet
No optimization of non-chromatic sextupoles yet

## Slide 14: Electron Storage Ring Polarization
Need to store bunches with 85% initial polarization and spins parallel ↑ ↑ and spins antiparallel ↑↓ to guide field in the arc.
Need to replace bunches with parallel spin ↑ ↑ with a rate of up to 1/(5 minutes) because of Sokolov-Ternov depolarization (defines the injection chain – Rapid Cycling Synchrotron)
Equilibrium polarization P∞ = 50% in eRHIC sufficient
to maintain polarization with <P> = 63% (spin ↑↓ 80%)
Higher vertical tune better due to easier orbit control
(beam-beam feasibility to be checked))
Spin matching between rotators essential
Conclusion:
Polarization is ok
More improvements expected by longitudinal spin matching, harmonic bumps, BBA, etc
Polarization with realistic machine errors
↑ 50% reachable

## Slide 15: Rapid Cycling Synchrotron with Spin Resonance Free Lattice as Full Energy Polarized Injector
Both the strong intrinsic and imperfection resonances occur at spin tunes:
  = nP +/- Qy
  Gϒ = nP +/- [Qy] (integer part of tune)
To accelerate from 400 MeV to 18 GeV requires the spin tune ramping from
  0.907 < Gϒ < 41.
If we use a periodicity of P=96 and a tune Qy with an integer value of 50 then our first two intrinsic resonances will occur outside of the range of our spin tunes
  Gϒ1 = 50+νy (νy is the fractional part of the tune)
  Gϒ2 = 96 – (50+νy ) =46-νy
  Also our imperfection resonances will follow suit with the first major one occurring at Gϒ2 = 96 – 50 = 46

## Slide 16: Spin Tracking in the Rapid-Cycling Synchrotron
Blue asterisk: 200 ms ramp time
High quasi-symmetry
 Good spin transparency properties

## Slide 17: IR Layout
Design meets all requirements
 Very constrained systems, requires novel types of magnets in the IR
IR design requirements:
  Small b* for high luminosity
  Limited IR chromaticity contributions
  Large final focus quadrupole aperture
  Large detector acceptance
   Large quadrupole aperture, limited beam divergence
  Accommodate dipole spectrometer in the low-b optics
  No accelerator magnets +/-4.5 m
  22 mrad crossing angle, crab crossing, crab cavities 90° from IP
  Avoid synchrotron radiation:
  - no electron bends on the forward side
  - absorb SR far from IP
  - need mask against backscattered SR photons
  Accommodate spin rotators, spin matching
  Space for luminosity monitor, neutron detector, “Roman Pots”
REAR
Forward

## Slide 18
Multi-stage separation:
Electrons from protons
Protons from neutrons
Electrons from Bethe-Heitler photons (luminosity monitor)
Currently working on increasing crossing angle from 22 to 25 mrad to ease magnet design

## Slide 19: Summary
eRHIC design reaches a peak luminosity of
L= 1.05·1034cm-2s-1
However, this can only be achieved with strong hadron cooling, which is beyond state of the art, and is a topic of ongoing R&D.
The corresponding design risk is mitigated by R&D, exploring variants for hadron cooling and by a fall-back solution with a respectable luminosity of
L= 0.44·1034cm-2s-1
eRHIC design has progressed very well and a tremendous amount of design work was accomplished.
There are still critical beam dynamic issues which require more effort. They could have an impact on achievable luminosity but do not constitute a risk of missing the EIC White Paper Requirement
While a large amount of work is still ahead to arrive at a Conceptual Design, we believe that the present state of the eRHIC design matches well the expectations of a Pre-Conceptual Design

## Slide 20
Pre-Conceptual Design Report delivered to DOE on August 20, 2018 – soon to be published
~800 pages, with many subsystems already beyond pre-conceptual stage
Active R&D program on strong hadron cooling

## Slide 21: Backup slides