## Slide 1: Design Study for a sPHENIX based EIC Detector Progress on streaming demonstrations for EIC
Jin Huang (BNL)

## Slide 2: Evolution of the RHIC 1008 Interaction region
~2000
2017→2023, CD-1/3A Approved
>2025
Time
PHENIX experiment
An EIC detector
16y+ operation
Broad spectrum of physics 180+ physics papers with 25k citations
1.4-M channel streaming
Comprehensive central upgrade base on previous BaBar magnet
Rich jet and HF physics program → Microscopic nature of QGP
Path of PHENIX upgrade leads to a capable EIC detector
Large coverage of tracking, calorimetry and PID
Full streaming DAQ based on sPHENIX
RHIC: A+A, spin-polarized p+p, spin-polarized p+A
EIC: e+p, e+A
arXiv:1501.06197 [nucl-ex]
arXiv:1402.1209 [nucl-ex] Update: sPH-cQCD-2018-001

## Slide 3: PHENIX/FVTX Streaming FEE
Online display
PHENIX event builder
/ Data storage
Standalone data
(calibration, etc.)
FPHX Chip
Sensor
HDI
Ionizing Hit
384 Wedges
1.4M channel 3-bit flash ADC
24 Readout cards (ROC)
IR
DAQ Room
48 FEM
6 DCM II
5x PCIe cards on
5 SEB Servers
768 fibers
1.9 Tb/s
17k LVDS
3.2 Tb/s
8 fibers
Data cable/bandwidth shown on this slide only
Flash ADC & free streaming
Triggered data to disks
Streaming data processing on FPGA for b-by-b luminosity & Transverse SSA (AN)
Notes: SEB – sub-event builder

## Slide 4: PHENIX Data validation & data processing in near-real-time
PHENIX validate data and perform majority calibration in near-real-time via online system using a subset of raw data prior to disk write
PHENIX has enough CPU to final process all data in real-time, but the limitation is usually special data need and manpower for calibration
0 – 5% Most Central
0 – 10% Most Central
0 – 20% Most Central
J/Psi spectrum in Cu+Au @ sqrtS = 200 GeV via run-time data production & analysis, Run 12 weekly report : https://www.c-ad.bnl.gov/esfd/Scheduling_Physicist/Time_Meetings/2012/tm120619/tm120619.htm

## Slide 5
2016: Scientific review and DOE mission need Status (CD-0)
2018: Cost/schedule review and DOE approval for production start of long lead-time items (CD-1/3A)
2022: installation in RHIC 1008 Hall; 2023: First data
Φ ~ 5m
Outer HCal
SC Magnet
EMCal
TPC
INTT
15 kHz trigger
>10 GB/s data
MVTX
Inner HCal
Detector
All tracker front end support streaming readout.
DAQ disk throughput for 9M particle/s + pile ups (> EIC ~4M particle/s)
Notes: 15kHz matched to collision rate.

## Slide 6: Selection of streaming and triggered front end
For calorimeter triggered FEE, (signal collision rate 15kHz x signal span 200ns) << 1: No need for streaming readout which significantly reduce front-end transmission rate
For TPC and MVTX tracker FEE supports full streaming: (signal collision rate 15kHz x integration time 10-20us) ~ 1: Streaming readout fits this scenario. Consider late stage data reduction by trigger-based filtering
Data Concentration
Rack Room
Interaction Region
Rack Room
Computing
Facility
Rack Room
DCM
DCM
DCM
DCM2
SEB
SEB
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Buffer Box
DCM
DCM
DCM
DCM2
DCM
DCM
DCM
DCM2
DCM
DCM
DCM
FEM
DCM
DCM
DCM
FEM
DCM
DCM
DCM
FEM
SEB
EBDC
DAM
EBDC
DAM
EBDC
DAM
10+ Gigabit
Network
Switch
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
Buffer Box
Buffer Box
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
TPC
MVTX
O(1000) SFP(+) fiber links Multi-Tbps to DAQ room
Commodity network ~200 Gbps to disk

## Slide 7: sPHENIX Time projection chamber (TPC)
Next-gen TPC w/ gateless and continuous readout: δp/p < 2% for pT<10 GeV/c
Ne-based gas for fast drift (13us). qGEM amplification and zigzag mini-pads.
160k channels 10b flash ADC @ 20MHz with SAMPA ASIC -> 2 Tbps stream rate.
Diameter ~ 1.6 m
MVTX
INTT
TPC
Server
BNL-712 v2 (FELIX2)
FELIX in server
MTP <-> LC Breakout
(To be built into TPC)
FEE Prototype

## Slide 8: TPC DAQ in streaming mode
600 Fibers @ 600x 6 Gbps
Commodity networking @ 200 Gbps

## Slide 9: sPHENIX MVTX
Active length ~ 30 cm
Diameter ~ 8 cm
Sensor test with sPHENIX extension
Readout Unit v2
BNL-712 v2 (FELIX2)
200M pixel monolithic active pixel sensors (MAPS) vertex tracker (MVTX) → 5μm position resolution, 0.3% X0 / layer → <50 μ m DCA @ 1 GeV/c
In close collaboration with ALICE & ATLAS phase-1 upgrades
MVTX
INTT
TPC
Exp. Hall DAQ room
192 GBT fiber links
Thickness ~ 50 μm, 30x30 μm pixels
Notes: 48 staves + 100% spares
30-um-pitch, 200 M pixel, 0.3% X0/layer, 4-10 us integration time

## Slide 10: Highlight of sPHENIX prototypes in action
MVTX Hit Spatial Resolution: < 5 um
Feb-July 2018 FermiLab Test beam facility, test of each sPHENIX detector subsystem
4x MVTX sensor in beam sPHENIX DAQ
INTT
MVTX EMCal HCal
TPC

## Slide 11: A EIC detector concept based sPHENIX and its streaming DAQ
Detector concept
Rate estimation
DAQ strategy
DAQ interface

## Slide 12: An EIC detector concept based on sPHENIX
Using sPHENIX as a foundation with further instrumentation of tracker, calorimeter and PID
Reuse and upgrade the streaming parts of sPHENIX Readout & DAQ
Letter of intent in 2014: arXiv:1402.1209 [nucl-ex]
On-going design study in public note: sPH-cQCD-2018-001 @ https://indico.bnl.gov/event/5283/

## Slide 13: sPHENIX rate VS EIC charge track rate
sPHENIX AuAu dNch/dη ~200, |η|<1
Streaming readout @ 200 kHz collision : 80 M Nch/s
DAQ throughput @ trigger rate 15 kHz: 6 M Nch/s + pile up
Multiplicity, e+p 20+250 GeV/c, 50μb https://wiki.bnl.gov/eic/index.php/Detector_Design_Requirements
EIC 20+250 GeV/c dNch/dη ~1, |η|<4
Streaming readout @ 500kHz collision (1034 cm-2 s-1) : 4 M Nch/s << sPHENIX
DAQ throughput, full stream: 4 M Nch/s <~ sPHENIX
Charged multiplicity, Au+Au, 100 + 100 GeV/c
HIJING event generator

## Slide 14: More quantitative? Take a look in EIC simulation
e+p collision 18+275 GeV/c DIS @ Q2 ~ 100 (GeV/c)2

## Slide 15: Full detector “Minimal bias” EIC events in sPHENIX framework: quick first look
Multiplicity check for all particles Minimal bias Pythia6 e+p 20 GeV + 250 GeV
53 µb cross section
BNL EIC taskforce studies https://wiki.bnl.gov/eic/index.php/Detector_Design_Requirements
  Based on BNL EIC task-force eRHIC-pythia6 event-gen set

## Slide 16: GEANT4-based detector simulation for DAQ simulation: tracker
Raw data: 16 bit / MAPS hit
Raw data: 3x5 10 bit / TPC hit + headers (60 bits)
Raw data: 3x5 10 bit / GEM hit + headers (60 bits)

## Slide 17: GEANT4-based detector simulation for DAQ simulation: central calorimeters
Raw data: 31x 14 bit / active tower +padding + headers ~ 512 bits / active tower

## Slide 18: GEANT4-based detector simulation for DAQ simulation: forward calorimeters
Raw data: 31x 14 bit / active tower +padding + headers ~ 512 bits / active tower

## Slide 19: EIC preliminary data rate summary
Tracker + calorimeter ~ 40 Gbps
+ PID detector + 2x for noise ~ 100 Gbps
Signal-collision data rate of 100 Gbps seems quite manageable,
  < sPHENIX TPC disk rate of 200 Gbps
Machine background and noise would be critical in finalizing the total data rate
  From on-going sPHENIX R&D prototyping will show noise level from state-of-art MAPS and SAMPA ASICs
  Prevision for noise filtering in EIC online system

## Slide 20: sPHENIX-EIC DAQ Strategy
Full streaming readout → DAQ interface to commodity computing via PCIe-based FPGA cards (e.g. BNL-712/FELIX series) → Disk streaming raw data → Event tagging in offline production
Why streaming readout?
  Versatility of EIC event topology make it challenging to design a trigger on all interested event. e.g. new diffractive-type events below, and new type of events not yet envisioned?
  Many EIC measurement, e.g. SF, are systematic driven. Streaming minimizing systematics by avoiding hardware trigger decision + keep background and history
  At 500kHz collision rate, many detector would require streaming, e.g. TPC, MAPS
Why BNL-712/FELIX series DAQ interface? [More on next slides]
  0.5 Tbps x bi-direction IO to FEE <-> large FPGA <-> 100 Gbps to commodity computing
  O($100) / 10Gbps bidirectional link
Why keep raw data?
  At 100 Gbps < sPHENIX rate, we can disk all raw data: If you can, always keep raw data.
  Achieve final minimal systematics may require refining calibration with integrated and special (e.g. z.f.) data.
  Calibration in real-time for final production in real-time requires considerable manpower for preparation (100 FTE?) and risky to fit in initial running years.
Diffractive (general)
Diffractive di-”jet” : Promising new channel to access OAM

## Slide 21: A streaming DAQ architecture
Using PCIe FPGA card bridging stream-readout FEE on detector and commodity online computing
  Similar approach taken at ATLAS, LHCb, ALICE phase-1+ upgrades and sPHENIX
Implementation: BNL-712-series FPGA-PCIe card
  2x 0.5-Tbps optical link to FEE: 48x bi-directional 10-Gbps optical links via MniPODs and 48-core MTP fiber
  100 Gbps to host server: PCIe Gen3 x16
  Large FPGA: Xilinx Kintex-7 Ultra-scale (XCKU115), 1.4 M LC
  Bridge μs-level FEE buffer length with seconds level DAQ time scale
  Interface to multiple timing protocols (SPF+, White Rabbit, TTC)
  Developed at BNL for ATLAS Phase-1 FELIX upgrade, down selection to use for streaming FEE readout in sPHENIX, proto-DUNE, CBM
  Continued development to upgrade to 25-Gbps optical links, Vertex7 FPGA and PCIe-Gen4
Server
COST Network & Online Computing
Server
Server
Server
....
FEE
FEE
FEE
FEE
....
Exp. Hall
DAQ room
10-100 Gbps
Network
48x 10-Gbps fibers per FELIX
EIC Timing
FELIX Card – BNL712 - v2.0
FELIX timing interface mezzanine
FELIX-server test stands at BNL

## Slide 22: Productions for BNL-712v2/FELIXv2
Ongoing FY19 BNL-712v2/FELIXv2 card production from BNL covering sPHENIX advanced R&D
  CBM working on joining this production and adopting this architecture for 2020 campaign too.
  2nd sPHENIX production planned after sPHENIX CD-3B (FY20?)
  BNL produced 40x cards in various versions of FELIX in ATLAS pre-productions, which will continue too.
Synergies from further EIC stream readout R&D welcomed too
Courtesy of C. Stum, D. Emschermann (GSI)
See also talk of Dr. Volker Friese (GSI)

## Slide 23: Recent highlights
GEM & TPC streaming FEE – SAMPA
Timing distribution
BNL LDRD on high throughput DAQ

## Slide 24
Readout of the eRD6 GEM + zigzag pad with SAMPA FEE + FELIX test stand
sPHENIX also initiate engineering and production for a special version of SAMPA with ½ current min shaping time (→80ns) @ University of São Paulo & TSMC
SAMPA test stand with EIC RD GEM tracker
Fe-55 x-ray on q-GEM (Ar-based)
Raw data, decoder, clustering & Ana.

## Slide 25: SAMPA test stand with EIC RD GEM tracker
Raw data & Ana.
X-ray src, eRD6 GEM + zigzag pad
8x SAMPA FEE
BNL-711 (→ BNL-712v2)
Commodity server
Picture embedded in raw data stream (animation)
Reconstructed GEM hits from SAMPA data

## Slide 26: Timing distributions
All PHENIX/sPHENIX FEE are synced to beam clock/counter. Expecting similar for EIC detector
BNL-712/FELIX can receive clock of multiple protocols (SPF+, White Rabbit, TTC, …) via a timing mezzanine card
SI5345 jitter cleaner control jitter to <0.1 ps
BNL-712/FELIX carries 48x 10 Gbps downlink fiber for control data to FEE. Beam clock and sync word can be encoded on fiber (e.g. 8b10b encoding)
For EIC hadron beam RF, extra cautious need to be taken for hadron machine ramp from low gamma to high gamma, which leads to clock frequency variation [next slide].
Courtesy of Kai Chen (BNL)
timing mezzanine cards
Server
COST Network & Online Computing
Server
Server
Server
....
FEE
FEE
FEE
FEE
....
Exp. Hall
DAQ room
10-100 Gbps
Network
48x 10-Gbps fibers per FELIX
EIC Timing

## Slide 27: Embedded clock demo with variable beam clock frequency
Demo FELIX Kintex-7 Ultrascale
Demo FEE Atrix-7
Uplink: 4.8 Gb/s, fixed clock
Downlink: 4.8 Gb/s
Multiples of RHIC clock (9.4 MHz)
Recover clock from 8b/10b
Optical Links
Function generator mimic repeated RHIC clock ramping (triangle pattern)
Test recovered “RHIC” clock
Kintex 7 (eval board for now) -> Atrix 7 (eval board)
Uplink iBERT @ DAM: 1.46e-13
Downlink iBERT @ FEE: 1. 023e-13
RHIC frequency spread (due to ramp) is large, 9.362 MHz ±22 kHz

## Slide 28: Future explorations, BNL LDRD 19-026: Common development for Advanced DAQ
BELLE-II
EIC detectors
DUNE far detector
nEXO
21-cm digital interferometer
Common challenge cross multi-discipline of BNL: Advance DAQ with high throughput @ 100 Gbps
Solution: FELIX-based DAQ, the architecture used
in the LHC upgrades in the 2020s
Deliverable: test stand & firmware for each case
Co-PIs: Kai Chen (BNL/ATLAS), Jin Huang (BNL/sPHENIX)
Strong contribution from BNL instrumentation
BNL 712 – series PCIe Card
Commodity Computing

## Slide 29: Summary
PHENIX and sPHENIX builds long experience for streaming readout front-end
We are exploring one way to build EIC detector streaming readout and trigger-less DAQ based on architecture of sPHENIX DAQ. Looks promising
  Preliminary simulation show disk rate for EIC collision signal (100 Gbps) expected lower than sPHENIX disk rate (200 Gbps)
  Controlling background for high-L low-σ collisions would be important for collider, detector and DAQ designs.
BNL-712/FELIX-type DAQ architecture fits EIC purpose. Similar architecture have wide support in 2020+ for high throughput DAQ e.g. ATLAS, ALICE, LHCb, CBM, Bell-2, and cost effectively bridges custom front-end with commodity computing
Productions planned for BNL-712/FELIX DAQ interface, more EIC R&D interests welcomed
PHENIX/FVTX streaming readout sPHENIX SAMPA+FELIX DAQ chain reading out EIC GEM detectors