## Slide 1: Asymmetric ERL for compact source of coherent radiation – design and preliminary experiments I.V. Konoplev1, M. Topp-Mugglestone1, Ya. Shashkov4, G. Burt2, F. Marhauser3 and A. Seryi3 1 John Adams Institute, Department of Physics, University of Oxford, Oxford, UK 2 Cockcroft Institute, Lancaster University, Lancaster, UK 3Thomas Jefferson National Accelerator Facility, Newport News, VA 23606, USA 4National Research Nuclear University MEPhI, Moscow, Russia

## Slide 2: Asymmetric ERL
Introduction
  Asymmetric Energy Recovery LINAC
    Basic concept
    Experimental Studies of RF cavity
    Cavity optimisation
  Conclusion

## Slide 3: Motivation
Original:
Ultra-High Intensity source of coherent
THz radiation:
-up to 1MW tunable from 0.1 THz to 10 THz
No industrial company can currently produce high power THz in this range, therefore a unique product. Non-contact imaging of coatings, composites, drug formulation, non-destructive sources and material/medical diagnostics research market. Replacing X-ray scanners: the global security screening market is expected to reach $9.10 Billion by 2020.
EUV radiation:
Generating electron beams of typical energy of 10-30 MeV; average current above 1A.
Aim to generate 1kW power radiation at 7-13 nm wavelength for lithography and ~120nm for QA.
Lithography for the £332 billion Semiconductor Industry: $7 billion market in 2014.
New:
Research which may benefit from high current ERL or multi-axis configuration
Recirculating ERL like PERLE and CBETA
FELs and other electron beam driven radiation sources
Electron beam cooling for EIC

## Slide 4: UH- FLUX Ultra high flux compact source of THz and X-ray
Very large current designs Oxford Design: AERL
100 metre +
5 metre

## Slide 5
UH-FLUX: AERL

## Slide 6
UH-FLUX: AERL
[1] A. Seryi, Patent PCT Application No. PCT/GB2012/052632 (24 Oct 2012)
[2] R. Ainsworth, G. Burt, I. V. Konoplev, and A. Seryi, Patent PCT Application No. PCT/GB2015/053565 (24 Nov 2015).
[3] I. Konoplev, ”Charged particle beam targets” US Patent App. 14/651,693, (2015)

## Slide 7
UH-FLUX: AERL
Acc. mode
One of transverse modes
Decoupling all modes except the accelerating mode to maximize the beam current
Problem: BBU instability development due to HOM in the cavity
Suggested solution:
HOMs localisation to maximise the BBU instability start current and separation of accelerating and decelerating sections; plus single pass
Partial mode of accel. section
Partial mode of decel. section

## Slide 8
UH-FLUX: AERL
Operating field flatness @1.3GHz
Electric field contour plot of dipole eigenmode at 1.73GHz
Electric field contour plot of resonant coupler eigenmode at 1.48GHz
Electric field contour plot of operating eigenmode at 1.3GHz
Small deviations of the cell geometrical parameters which do not affect the operating mode led to desired field distributions.
Unfortunately: pass-band modes are also not affected
First numerical studies of 11 cells cavity using ACE3P/Omega3P/T3P software packages

## Slide 9: Eigenmodes of the asymmetric cavity
First numerical studies of 11 cells cavity using ACE3P/Omega3P/T3P software packages

## Slide 10
Experimental studies: proof of the concept
  Aluminium 7 cells cavity (manufactured in 2015 studied summer 2016 and summer 2017)
Aim:
- to identify the cavity modes: operating and HOMs
- To compare with numerical data

## Slide 11: Scaled down prototype of the cavity
7 cells cavity: 3- accelerating; 3 decelerating and coupling cavity
Bead pull RF measurements test bench
VNA
Bead pull pillars
7 cells asymmetric cavity made from 2 blocks of solid aluminium

## Slide 12: Preliminary experimental and numerical results (CST MW studio)
Operating mode
Parasitic LOM
Mode type-1
Parasitic LOM
Mode type-2
First comparison of the operating mode measured (solid line) with the numerical predictions dashed line. The measurements were carried out at a single axis.

## Slide 13: Pass band modes: experiment and theory
First comparison of the pass band modes measured (solid line) with the numerical predictions dashed line. The measurements were carried out at a single axis.

## Slide 14: Pass band modes experimental studies at two axes
Red line active axis
Blue line passive axis
The RF coupler is located on one axis (active) while the field measurements are conducted on both axes

## Slide 15: HOMs measurements
The RF coupler is located on one axis (active) while the field measurements are conducted on both axes
Red line active axis
Blue line passive axis
HOMs localisation at one or another axis

## Slide 16: Cavity optimisation
Tesla like cavity (TT)
Low Loss like cavity (LL)
Risk points due to high field intensity on the surface
Other risk factors:
Multipacting
Proximity on modes to operating mode
Cost

## Slide 17: Cavity optimisation
TT&LL cavity with the original bridge
Original cavity TT&TT
& - indicate bridge

## Slide 18: Cavity optimisation
TT&LL cavity
LL&TT+LL cavity
TT&LL+TT cavity

## Slide 19: Cavity optimisation
- Improved but did not resolve completely high field risk
- Improved but did not resolved the modes proximity
- Did not resolve the chalenge with multipacting

## Slide 20
JLAB dual axis cavity
The cavity was used as a prototype during the optimisation
It was considered as an indication that such structure can be machined

## Slide 21
Bridge optimisation
- Resolved high field risk
- Improved the modes proximity
- Resolve the challenge with multipacting

## Slide 22: Conclusion
Motivation for a new ERL capable of driving Ampere level average electron beam current has been discussed
Design and studies of the dual axis asymmetric cavity has demonstrated
Results of cavity optimisation have been shown
Proposal to build and test the cavity at JLAB has been submitted to STFC UKRI on 31st of October.
We will know the final decision by the end of Spring 2019.

## Slide 23
Future plans
01-October-2019 Start of the project
- Evaluation of the cavity design and technical drawings of the cavity - 3 months
- Machining, assembling and preparation of the cavity – 12 months
- Room temperature RF tests and RF tests with LHe -3 months
Thank you
Future
Can this development be interesting and useful for EIC (beam cooling perhaps)?
If there are positive outcomes of the studies can it be used for EIC?
HP RF Experiments with such cavity
Building high-current ERL