## Slide 1
ERL EIC Workshop | Jefferson Laboratory | November 2, 2018
Requirements for Magnetized Bunched-Beam Cooling
Speaker: Chris Tennant, Jefferson Laboratory

## Slide 2: Introduction
top level requirements are “standard” for an ERL
  generate, accelerate, and deliver a properly configured beam to the user
  recover (possibly degraded) beam after use
  preserve beam quality, avoid instabilities and limit losses
unique features of JLEIC cooling system:
  magnetized beam
    axially symmetric transport
  high charge
    collective effects aggravated
  long bunch
    samples large(r) part of RF waveform
  small momentum spread
    susceptible to wake-induced distortion

## Slide 3: Strong Cooling
harmonic kicker exchanges every 11th CCR bunch between ERL and CCR
Beam Exchange (side)
CCR
ERL
DC & RF kicker
chirper
chirper
injected bunch orbit
extracted bunch orbit
dipole
dipole
DC & RF kicker
CCR (top)
ion beam
cooling solenoids
magnetization flip
septum
magnetization flip
DC & RF kicker
DC & RF kicker
ERL (bottom)
magnetized gun
booster
linac
beam dump
chirper
chirper
dipole
dipole

## Slide 4: Getting From Here to There
state-of-art performance for SRF-driven ERLs:
  decoupled beam (but with fully coupled transport/phase space exchange)
  Qbunch ≈ 100 pC
  Iave ≈ 10 mA
  Pbeam ≈ 1 MW
JLEIC cooler requirements:
  magnetized beam (coupled)
  Qbunch ≈ 3 nC
  Iave ≈ 100 mA (ERL) – 1 A (CCR)
  Pbeam ≈ 10 MW (ERL) – 100 MW (CCR)
(courtesy D. Douglas)
required performance orders of magnitude beyond state-of-art
  (30x)
  (10-100x)
  (10-100x)

## Slide 5: ERL Landscape
1 kW
10 kW
100 kW
1 MW
10 MW
100 MW
1 GW

## Slide 6: Summary: Beam Dynamics Issues
BEFORE: a premium on short bunch length and transverse emittance (i.e. FELs)
NOW: bunch lengths are long and the metric of interest is the energy spread
high charge, high power transport that preserves
magnetization and small energy spread
power management: understand sources of, and manage, losses
CSR, space charge, mBI: machine lives in unique part of parameter space
beam breakup (BBU): well understood, need full system to assess impact
halo: serious operational problem, formation via many processes
(collimation: not demonstrated in high power, CW operation)
ion trapping: potential problem
these items represent only the things about which we know,
not the things we know we don’t know

## Slide 7: Outlook & Points of Discussion
historically, SRF-driven ERLs have taken advantage of high repetition rates and modest bunch charges to achieve high power  moving into a regime of high repetition rate, high bunch charge
unlikely we will have a high power ERL testbed in the near future
how can we leverage currently available accelerators to help our understanding of high power machines?
(S. Nagaitsev)

## Slide 8: The Elephant in the Room

## Slide 9: Table of Parameters
(courtesy S. Peggs)

## Slide 11: What to Do, Where to Go?
multiple generations separate state of art system readiness from required performance
need development in many areas, including:
  CW/high charge magnetized source
  merger
    management of CSR/space charge/microbunching
  modeling with CSR and space charge
    model validation (1D, 2D, 3D…)
    validate treatment of ends of bunches
    simulation dynamic range (part per million statistics => trillion particle simulation…)
  CSR shielding
  methods for mB gain control
  LSC wake control/compensation
    nonlinear longitudinal matching
  magnetization-preserving beam transport
  high-rep-rate beam transfer
  halo (simulation statistics inadequate…)
    formation mechanisms (scattering: IBS, Touschek, beam/gas,…; dynamical)
    characterization (LDR diagnostics, tomography…)
    control (suppression, collimation, matching (linear and nonlinear…)
  power scaling
    100x state of art
(courtesy D. Douglas)

## Slide 12: Effect of CSR on Longitudinal Phase Space
no CSR
CSR
CSR “corrected”

## Slide 13: CSR Shielding
shielding of CSR is effective when the full aperture size is less than where R is the bend radius and sz is the rms bunch length
for R = 0.53 m and sz = 4.95 mm, the (full) aperture needs to be less than ~2 inches (5.04 cm)
for sz = 4.95 mm
with CSR + shielding
with CSR

## Slide 14: Why Magnetized Electron Cooler?
Tremendous reduction (by a factor 20 – 30) of the regional and global deleterious Space Charge transverse impact to dynamics in CCR (tune shift)
Strong mitigation (suppression) of the CSR microbunching/ energy spread growth
Suppression of deleterious impacts of high electron transverse velocity spread and short-wave misalignments to cooling rates (thanks to ion collisions with “frozen” electrons at large impact parameters)
At cathode immersed in solenoid, a gun generates almost parallel (laminar) beam state of a large size (electron Larmor orbits are very small compared to beam size)
This beam state is then transplanted to the solenoid in cooling section
(while preserving the canonical emittances: the drift and the Larmor
emittances)
The solenoid field can be controlled to make e-beam size properly match the ion beam size
Magnetization results in the following critical advantages
(compared to a non-magnetized gun/cooling solenoid):
Notes: At cathode immersed in solenoid, one can generate almost parallel (laminar) beam state after the gun

## Slide 15: Where to go: Existing Opportunities
ASTA/IOTA/FAST can support single bunch studies
  3.2 nC magnetized bunch  can initiate evaluation of single-bunch dynamics & evolution
  could IOTA offer a CW analog?
JLab UITF & LERF, ELBE at HZD can support low power/low charge CW tests for hardware and dynamics
  JLab ERLs down for LCLS-II module tests through 2018
No “true” (Pbeam>>PRF) SRF ERLs in operation at this time
  no immediate opportunity for high power testing in SRF enviroment
  BINP capable of high charge/current/CW at low energy…
2019: three SRF ERL facilities available: Cb, bERLinPRO, Jlab
  complementary capabilities/limitations
    JLab is legacy generation (low charge, MW class) but fully commissioned and operationally flexible
    Cb is “next generation”, but experimental design may be operationally challenging (FFAG)
    bERLinPRO  high current/power; design charge low but SRF gun offers possibility for high charge, but no magnetization 
(courtesy D. Douglas)